## Slide 1: IEEE P802.15 Wireless Personal Area Network
Description of Proposed Structure for Draft MAC and PHY Standards
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 2: IEEE 802 Structure

## Slide 3: The Project 802 Domain

## Slide 4: Original Bluetooth to IEEE 802.15
Notes: Appears to be a fairly good correspondence, except for Audio.
(discussion)

## Slide 5: New Understanding of Bluetooth/IEEE Correspondence

## Slide 6: Taxonomy of an 802 Standard
Notes: Communications are performed via Service Access Points (SAPs)
1) Logical Link Control -- Three types of operation: connectionless with no ACK; connection-oriented; and connectionless with ACK
Communicates with upper layers via a set of primitives:
* Request
* Indication
* Response
* Confirm
Communicates with MAC via frames
2) Media Access Control -- Performs access control functions for the shared medium in support of the LLC.
* Addressing and recognition of frames
* frame check sequence generation and checking
* LLC protocol data unit (PDU) delimiting
3) MAC Management -- managed objects and controls for MAC protocol
4) Physical Layer Convergence Procedure -- Medium-independent physical layer: receives Messages, hands over bits to PMD
5) Physical Medium Dependent layer takes bits and (in our case) turns them into radio waves
6) PHY Management -- managed objects and controls for PHY protocol
7) Station Management -- Set of tools that allow performance of
* Configuration management
* Fault management
* Performance management
* Security management
* Accounting management

## Slide 7: Outline of Standard Main Text
1) Overview
2) Normative References
3) Definitions
4) Abbreviations and Acronyms
5) General Description
6) Medium Access Control (MAC)
7) Physical Layer (PHY)
8) Layer Management

## Slide 8: Outline of Standard Appendix
A. Protocol Implementation Conformance Statement (PICS) proforma
B. Formal Description of MAC operation
C. Formal Description of PHY operation
D. MAC Management Information Base
E. PHY Management Information Base
F. Bibliography

## Slide 9: Clause 1
Overview
  Scope
  Purpose

## Slide 10: Clause 2
Normative References
  Other documents (IEEE, ISO, ITU…)

## Slide 11: Clause 3
Definitions
  Terms specific to this Standard

## Slide 12: Clause 4
Abbreviations and Acronyms

## Slide 13: Clause 5
General Description
  Architecture
  Components
  Services

## Slide 14: Clause 6
Medium Access Control
The part of the data link layer that supports topology-dependent functions and uses the services of the physical layer to provide service to the logical link control (LLC) sublayer. In ISO/IEC 8802, the combined set of functions in the DQDB Layer that support the MAC Sublayer service to the logical link control (LLC) sublayer .

## Slide 15: Clause 6.1
MAC Service Definition (MAC_SAP)
  Overview
  Service Specification
The unconfirmed connectionless-mode MAC service defined in ISO/IEC 10039, as an abstraction of the features common to a number of specific MAC services for Local Area Networks .

## Slide 16: Clause 6.2
MAC Frame Formats
  Conventions
  General Frame Formats
  Format of Individual Frame Types

## Slide 17: MAC Frame Format Conventions
The sequence of octets in the fields of the MAC frame forms an octet stream at the MAC/PLCP sublayer boundary. The leftmost octet in each field of the MAC frame is passed across the MAC/PLCP boundary first.
Fields that are longer than a single octet are depicted with the least significant octet on the left. The least significant bit of each octet is defined as bit 0 for that octet and is the leftmost bit of the octet. Fields that are less than one octet in length are ordered with the least significant bit to the left.
MAC addresses are assigned as ordered sequences of bits. The Individual/Group bit is always transferred first and is the least significant bit of the first octet.
Values specified in decimal are coded in natural binary unless otherwise stated.
Reserved fields and subfields are set to 0 upon transmission and are ignored on reception.
802.11 Example

## Slide 18: MAC General Frame Formats
Fields common to all frames declared first
All possible optional fields follow
When present, they occur in specified order
802.11 Example

## Slide 19: Format of Individual MAC Frame Types
Specify purpose of frame and fields
Define fields used
Specify default values (if any)
Reserved fields

## Slide 20: Clause 6.3
MAC Layer Functional Description
  Authentication and Privacy
  Fragmentation/Defragmentation
  Frame Exchange Sequences
  Audio

## Slide 21: Clause 7
Physical Layer

## Slide 22: Clause 7.1
PHY Layer Functional Description

## Slide 23: Clause 7.1 (continued)
The Physical Layer is the first layer of the seven-layer OSI model; responsible for transporting bits between adjacent systems. Note: This layer accepts a bit stream, called a frame, from the data link layer and places it on the media. It also performs the inverse operation of extracting a bit stream from the physical media and passes it to the data link layer. This layer describes mechanical and electrical characteristics of the connection, as well as the required interchange circuits.

## Slide 24: Clause 7.2
PHY Service Specification
  Overview
  Service Specification

## Slide 25: Clause 7.2 (Service Specification)
The subdivision that provides the protocol to allow transfer of slot octets, management information octets, and DQDB Layer timing information over the transmission link between DQDB Layer subsystems at adjacent nodes. The Physical Layer provides the service to the DQDB Layer.

## Slide 26: Clause 7.3
PHY Frame Formats
  Conventions
  General Frame Formats
  Format of Individual Frame Types

## Slide 27: Clause 8
Layer Management
  Overview
  MAC Layer Management Entity
  Physical Layer Management Entity
  Station Management Entity

## Slide 28: Management Primitives
The GET and SET primitives in fact are represented as REQUESTs with associated CONFIRM primitives. These primitives are prefixed by MLME or PLME
    XXGET.request (MIBattribute)
    XXGET.confirm (status, MIBattribute, MIBattributevalue)
    XXSET.request (MIBattribute, MIBattributevalue)
    XXSET.confirm (status, MIBattribute)

## Slide 29: Clause 8.1
Overview
Both MAC and PHY layers conceptually include management entities, called MAC subLayer Management and PHY Layer Management Entities (MLME and PLME). These entities provide the layer management service interfaces through which layer management functions may be invoked.

## Slide 30: Clause 8.2
MAC Layer Management Entity

## Slide 31: Clause 8.3
Physical Layer Management Entity

## Slide 32: Clause 8.4
Station Management Entity
The SME is a layer-independent entity which may be viewed as residing in a separate management plane or as residing "off to the side". The exact functions of the SME are not specified in this standard, but in general this entity may be viewed as responsible for such functions as the gathering of layer-dependent status from the various layer management entities, and similarly setting the value of layer-specific parameters. SME would typically perform such functions on behalf of general system management entities and would implement standard management protocols.
802.11 Example

## Slide 33: Appendices
A. Protocol Implementation Conformance Statement (PICS) proforma
B. Formal Description of MAC operation
C. Formal Description of PHY operation
D. MAC Management Information Base
E. PHY Management Information Base
F. Bibliography

## Slide 34: Protocol Implementation Conformace Statement proforma
The PICS is a description of an implementation claim. It specifies:
  Who implemented
  What was implemented
  Mandatory capabilities were satisfied
  Which options were chosen

## Slide 35: Formal Definitions
Formal definitions are represented in Specification and Description Language (SDL)
ITU-T Recommendation Z.100
REF: Ellsberger, J., SDL Formal Object-Oriented Language for Communicating Systems, Hertfordshire, Prentice Hall Europe, 1997 (ISBN 0-13-621384-7)

## Slide 36: Management Information Base
MIBs are abstract representation of data
They are represented in ASN.1
  Abstract Syntax Notation One
  ITU-T Recommendations
    X.280
    X.680-683
    Z.105
REF: SDL Formal Object-Oriented Language for Communicating Systems

## Slide 37: LLC Discussion
Research needed

## Slide 38: MAC Bridging
Not applicable (?)

## Slide 39: Proposed Work Areas

## Slide 40: END OF PRESENTATION
(backup slides follow)

## Slide 41: Bluetooth and IEEE Structure
Notes: Correspondence of Bluetooth to the ISO Open Standards Interface (OSI) model and how the IEEE standards map to them.
Note that IEEE has only two layers of the ISO-OSI while Bluetooth (as you well know) covers all of them. What is not indicated by this graph is that the normal place for the LLC layer is in a separate committee, 802.2. This standard is common to 802 stacks, but each MAC may have some medium-specific clauses in the 802.2 standard. Due to the unique nature of the wireless medium, we will need to evaluate if there is sufficient flexibility for a Bluetooth-based standard to follow this model. Other options can be considered.

## Slide 42: Distributed Queue Dual Bus (1 of 2)
IEEE Std 802.6-1994. Information Technology Telecommunications And Information Exchange Between Systems Local And Metropolitan Area Networks Specific Requirements—Part 6: Distributed Queue Dual Bus (DQDB) Access Method And Physical Layer Specifications. This standard is part of a family of standards for local area networks (LANs) and metropolitan area networks (MANs) that deals with the Physical and Data Link Layers as defined by the ISO Open Systems Interconnection Reference Model. It defines a high-speed shared medium access protocol for use over a dual, counterflowing, unidirectional bus subnetwork. The Physical Layer and Distributed Queue Dual Bus (DQDB) Layer are required to support a Logical Link Control (LLC) Sublayer by means of a connectionless Medium Access Control (MAC) Sublayer service in a manner consistent with other IEEE 802 networks. Additional DQDB Layer functions are specified as a framework for other services. These additional functions will support Isochronous Service Users and Connection-Oriented Data Service Users, but their implementation is not required for conformance.

## Slide 43: Distributed Queue Dual Bus (2 of 2)
IEEE Std 802.6j-1995. Local and Metropolitan Area Networks: Supplement to 802.6: Connection-Oriented Service on a Distributed Queue Dual Bus (DQDB) Subnetwork of a Metropolitan Area Network (MAN). Enhanced Queued Arbitrated (QA) Functions, which can support applications requiring bandwidth guarantees and delay limits on a DQDB subnetwork, are specified. Connection-Oriented Convergence Functions (COCFs) using the enhanced QA Functions, which are necessary to support connection-oriented service, are also specified
return

## Slide 44: Service Access Point
service access point (SAP)
(1) The point at which services are provided by one layer (or sublayer) to the layer (or sublayer) immediately above it (ISO 7498), ISO 8802-6-1994
(2) An address that identifies a user of the services of a protocol entity. 610.7-1995
individual address
(1) An address that identifies a single source or destination service access point. ISO 8802-6-1994
return

## Slide 45: Encryption Question
How does the 128 bit encryption requirement impact USA export restrictions?
return

## Slide 46: Bluetooth Classes of Services
Audio
Synch
Bridging
Network
HID
Still Image
Comm Port App.
WAP
RF
A
U
D
I
O
BB
LM
L2CAP
Audio
Ctrl
TS0710
TCP/IP
HID
IrOBEX
PPP
WAP
Still Images
vCard
vCal
UDP