## Slide 1: Wideband FH NPRM Discussion
Ben Manny
Chair, HomeRF Working Group
Intel Corporation < ben.manny@intel.com>
IEEE 802.11&15 Interim Meeting
September 13, 1999 - Santa Rosa, CA
Jul 28, 2026
        doc.: IEEE 802.11-99/201

## Slide 2: Discussion Points
Motivation for proposed rule change
  HomeRF Mission
  Current Usage Scenarios
  Expanded Usage Scenarios
The Requested Rule Change
  Objectives
  Proposed Change
Responding to IEEE objections
Call to Action

## Slide 3: HomeRF™ Working Group Mission Statement
To enable the existence of a broad range of interoperable consumer devices, by establishing an open industry specification for unlicensed RF digital communications for PCs and consumer devices anywhere, in and around the home.
94 Members as of 9/1/99
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Connects Broadband Pipes to Home network
Internet Pipe
Broadband
Mobile display pad
Electronic Program guide
Read & set security system
Home Theater control
Display News headlines
Grandma’s
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
1/2 cup chopped walnuts
minutes.
HOME
INDEX
Fridge Pad
Family Calendar
Recipe Display
Build shopping lists
Voice messaging
Intercom
Office Laptop
Connect to office LAN
Email
Home Printer access
Surf from anywhere
Share files
Ethernet or
HomePNA
Main Home PC
Additional PC(s)
Grandma’s Brownies
3 cups flour
1 cup grated chocolate
1 cup sugar
1 stick butter
Kids Room PC
Printer access
Internet access
File access
Cordless Phone
Remote Speech recognition
Call by name
Build shopping lists
Home PBX
CM

## Slide 5: WBFH Benefits & Expanded Usage
Benefits:
  Backwards compatible with first generation SWAP devices
  Take advantage of HomePNA R2.0 performance
  Increase telecommuting productivity for Laptop users
  Increase the number of DECT handsets from 4 to 8
  Improve compressed video transmissions quality
  Take advantage of future Broadband speed increases
  Increase number of MP3 audio streams
Usage scenarios
  Whole house wireless CD quality audio speakers
  Video intercoms
  Remoting PC screen/keyboard to TV
  SOHO PBX with the expanded DECT channels

## Slide 6: Requested Change Objectives
Aligned with purpose of Part 15
  to enable the “introduction of new services and devices and the enhancement of existing services and devices…[which] will create new jobs, foster economic growth, and improve access to communications by industry and the American public.”
Proposal does not cause additional interference to existing users of the 2.4 GHz band
  The increases in bandwidth are accompanied by proportionate reductions in maximum allowable power
Allows a similar degree of range/performance flexibility for FH systems as recently allowed for DS systems
  Will foster greater offerings at lower costs for consumers
Harmonizes Part 15 FH regulations with most of Europe & Far East

## Slide 7: Requested Change
Maximum 1 MHz channels
  unchanged
Maximum 3 MHz channels
  Maximum power +25 dBm EIRP
  Maximum channel bandwidth 3 MHz
  Maximum channel occupancy 50 mSec
  Minimum number of hops 75
Maximum 5 MHz channels
  Maximum power +23 dBm EIRP
  Maximum channel bandwidth 5 MH
  Maximum channel occupancy 20 mSec
  Minimum number of hops 75
Definition of channel bandwidth remains unchanged
  -20 dBc energy or less out of channel bandwidth
  Two new categories will result in overlapping channels

## Slide 8: Response to IEEE’s Objections
Four points were raised in the letter:
  a) Overlapped channels cause “increased interference”
  b) WBFH rules will require faster hopping, which “represents a more severe interference threat”
  c) The proportional reduction in maximum allowed transmitted RF power will not “effectively offset the impact of wider occupied channels”
  d) Changing the 15.247 rules to allow WBFH is not necessary, since there is “already…a standard for high speed wireless networking” that will meet all of HomeRF’s objectives.
HomeRF would like to clarify our position - we believe there are sound technical and marketing reasons for WBFH

## Slide 9: First-some key points
1: WBFH Home RF systems will be required to fall back to 1MHz channels in the presence of interference or channel impairments
  Will be in the 2.0 spec and required for compliance/logo
  Just like 802.11b, fallback modes increase robustness and provides legacy support
  Unlike 802.11b, fallback modes decrease spectral occupancy, so probability of co- and adjacent channel interference decreases for WBFH---especially significant for Bluetooth interference
    In 802.11b, fallback modes are especially bad for Bluetooth interference, since spectral occupancy remains constant, but packet length increases significantly.

## Slide 10: Key points (2)
2: We believe the FCC’s role is to foster competition when it is in the consumer’s best interest
  The intent of WBFH is to allow FH systems to move to higher speeds just like rule wavers have allowed DS systems to move to higher speeds - §15.247 has always allowed both DS and FH to operate in the 2.4GHz ISM band, and our belief is that the FCC should allow both technologies to compete and drive down prices.
  IEEE 802.11 has both FH and DS standards - both types of systems have advantages and disadvantages and 802.11 has historically recognized that fact
  By favoring an imbalance in §15.247, IEEE 802.11 is abandoning its traditional impartiality
HomeRF believes FH technology is best for home use, and should be allowed to expand to higher speeds, like DS technology

## Slide 11: Response to letter (a-1)
Overlapped channels cause “increased interference”
  WBFH will likely use GMSK, which has most of its energy concentrated near the middle of the channel
    For 5Mb/s w/5MHz channels, WBFH will be -20dB@4MHz
    For 10Mb/s w/5MHz channels, WBFH will be -20dB@5MHz, and -10dB at 3MHz
  Simulation results show that DS systems can operate at 0dB C/I, as long as it has 10dB of processing gain (next slide)
  FH systems such as Bluetooth use limiter/discriminators, and capture effect effectively blocks interference for C/I>11dB (BT)
  WBFH is 5MHz hopping over the entire 83.5MHz band; 802.11b occupies 22MHz continuously per subnet
Interference from WBFH is only significant when C/I is poor - not unique

## Slide 12: Response (a-2)
Pathological case: Matlab simulation of 22MHz DS signal with 5MHz WBFH signal, equal power in DS IF

## Slide 13: Response (a-3)
Input to post-detection correlator
Spreading sequence
Even at 0dB C/I, a DS system with 10dB processing gain can recover the bit stream
Parallel corelator output
Original data sequence

## Slide 14: Response (a-4)
WBFH does not pose a significant interference threat to other FH systems
  Limiter/discriminator systems capture at C/I>10dB or so
  ANY interferer will cause problems at C/I below capture
  HomeRF systems must revert to 1MHz channels under interference or impairments, so situation will be same as today
    Spectral density of WBFH will be lower since power is spread over as much as 5MHz

## Slide 15: Response (a-5)
CCA issues are only relevant for 802.11 systems
  802.11 can only do energy detection for today’s SWAP or BT systems
  Issues in CCA between 802.11FH and DS
  BT doesn’t even do CCA of any type
Self interference of WBFH is not an issue for 802.11 or FCC
  HomeRF hopping sequences are a minimum of 10MHz between adjacent hops
  SWAP devices must negotiate between themselves, like 802.11
    HomeRF doesn’t consider self interference (802.11 with itself or WBFH with itself) as an FCC issue

## Slide 16: Response (b-1)
“In general, a faster hop rate for FHSS systems represents a more severe interference threat than does an FHSS system employing a slower hop rate.”
  Given this statement, Bluetooth would seem to be the worst case, since it hops much faster than WBFH, BUT, according to a study by an 802.11 company:
    “IEEE 802.11 DSSS systems show graceful degradation in the presence of significant levels of BT interference”
    “IEEE 802.11 High Speed WLANs show good reliability even in an environment of fairly dense BT piconet usage”
  If these statements are true, then the slower hop rate of WBFH should make it more benign to 802.11b

## Slide 17: Response (c-1)
c) The proportional reduction in maximum allowed transmitted RF power will not “effectively offset the impact of wider occupied channels”
  The claimed detrimental impact of wider channels has not been substantiated
  Many WLAN vendors DO ship products with RF power >100mW
  If a WBFH system at 200mW over 5MHz but hopping 50 times per second is bad, consider that FCC rules currently allow DS systems to transmit at a single frequency with an RF bandwidth of 5MHz (500kb/s w/10dB of processing gain) at up to 1 Watt, which would appear to be much worse for interference
  A 200mW WBFH system would have the same overall power spectral density over the 83.5MHz as allowed under today’s rules
WBFH offers many advantages - and doesn’t increase PSD over today’s rules

## Slide 18: Response (d-1)
d) Changing the 15.247 rules to allow WBFH is not necessary, since there is “already…a standard for high speed wireless networking” that will meet all of HomeRF’s objectives.
  HomeRF chose FH for SWAP because, compared to DS, FH offers:
    Lower power consumption
    Lower cost
    More graceful degradation in capacity with increasing network density, including multi-family dwellings
  In additon, the HomeRF MRD requires a complete cordless telephony solution, which SWAP gets from DECT
802.11b does not meet the HomeRF MRD, or we would have chosen it
If SWAP and 802.11b are competitive, that’s OK…competition is good!
HomeRF/SWAP was designed for its target market - the home.
802.11b was designed for the enterprise.

## Slide 19: Call To Action
Vote to recall first letter and send in a letter of support for the rule change
  Is aligned with IEEE 802 goals of supporting regulations that permit greatest selection of best technology to meet specific market needs
  It does not impact the performance of existing Part 15 compliant products over current regulations
  It enable US consumers to benefit from new wireless devices that are currently allowed in most other countries but not in the US
Vote to recall first letter and remain neutral
  Let individual companies comment on rule change