## Slide 1: 802.15 Working Group for Wireless Personal Area Networks
A Presentation to the Workshop on WPANs
August 2, 1999
Sponsored By:
Bob Heile, Chair
Thanks to
Tom Siep, Texas Instruments
Bruce Kraemer, Harris
Ian Gifford, M/A-COM
who made contributions to this presentation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 2: Presentation Outline
802 Wireless Vision/Positioning
Brief WPAN/WG background/charter
WPAN-WG Status/Func. Req./Direction
Brief Comparison to 802.11/Bluetooth
Project Timeline
Some Thoughts on the Mission
802.15 Functional Organization
Liaison Activites

## Slide 3
IEEE P802, a Family of Standards

## Slide 4: IEEE 802 Wireless Vision Statement
802.11 Base Standard
  2.4GHz Frequency Hopping Spread Spectrum (1Mbit/s)
  2.4GHZ Direct Sequence Spread Spectrum (2Mbit/s)
  Infrared (1Mbit/s)
802.11a 5GHz Extension (>20Mbit/s)
802.11b 2.4GHz Extension (>8Mbit/s)
802.15 Wireless Personal Area Networks
802.16 Broadband Wireless LANs (LMDS)
“IEEE 802 is the focal point for Wireless LAN standards.” Jim Carlo
Source: Jim Carlo, 802 Chair [JC-802-Consortium.PDF] can be downloaded from the following URL: ftp://ftp.flexipc.com/wearablesgroup/802/

## Slide 5
Data Communication Systems by Network Classification
WAN (Wide Area Network) 802.??
  WANs interconnect facilities in different parts of a country or of the world
MAN (Metropolitan Area Network) 802.16
  MANs shall be capable of operating over an area up to 50 Km in diameter
LAN (Local Area Network) 802.11
  LANs shall be capable of supporting segments at least 100 meters in length.
  LANs composed of segments connected by physical layer inter-networking devices, shall be capable of operating over a physical medium that is at least 2 Km in length.
PAN (Personal Area Network) 802.15
  PANs shall be capable of supporting segments at least 10 meters in length.

## Slide 6: WPAN Positioning Statement
Continuum of needs for wireless products
No one solution can fill all needs
Family of complementary devices
RFID
WPAN
WLANs
High performance,
higher cost
Low performance,
low cost
802.15
802.11
802.16
802.??

## Slide 7: WPAN Project History
Started in 1997 as ‘ad hoc’ group within IEEE Portable Applications Standards Committee (PASC)
At the time, no other Groups or Standards Bodies dealing with the problem
In March 1998 a Study Group was formed within 802.11 to develop a Project Authorization Request (PAR)
In March 1999, IEEE 802.15 Working Group for WPANs established
Kick-off Meeting July5-9 in Montreal-61 people attending, 39 achieved voting status.

## Slide 8: PAN Related Activities
Bluetooth--over 900 Companies Participating Formed May 20, 1998 Spec due-July 99
HomeRF/Firefly-- over 90 Companies Formed March 4, 1998 Spec Dec 98(swap)/Dec 99
802.15-- ~50 Companies Participating Target Standard Nov 00
Others
  Intermec, Motorola, Butterfly, Kodak...

## Slide 9
IEEE 802.15 Charter
Build on emerging industry specifications
Provide an open forum to debate these proposals
Identify substantive issues
Build consensus on solutions
Goal is to create standards that have:
  broad market applicability
  deal with the issues of coexistence and interoperability
  widely used
The IEEE P802.15 WPAN Working Group is chartered with developing Personal Area Network standards for short distance wireless networks.

## Slide 10
Right now the WG is here
~Jun97 - Idea for standard
Mar98 - Find Sponsor
Feb99 - Submit PAR
Mar99 - Approve PAR
Jul99 - Organize working group
3Q99 - Develop draft standard
? - Ballot draft standard
? - Approve draft standard
? - Publish approved standard

## Slide 11
How IEEE 802 Establishes a Standard

## Slide 12
What the WG is doing
Write scope and purpose
Examine related standards and publications
Draft outline
Fill in outline
Revise, revise, revise
Finalize document
You are here

## Slide 13: Current 802.15 WPAN Functional Requirements- “A” List
Worldwide spectrum allocations for unlicensed bands such as 2.4GHz
Low Cost: i.e., relative to target device
Small Size e.g., ~.5 cubic inches( excludes antenna & battery)
Power Management: Very Low current consumption (Average 20mw or less @ 10% Tx/Rx load)
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 14: Current 802.15 WPAN Functional Requirements- “A” List (cont.)
Asynchronous or connection-less data links
Allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Allow coexistence of multiple Wireless Systems such as P802.11 in the same area
WPAN Network Access Control
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 15: Current 802.15 WPAN Functional Requirements- “B” List
Range: 0-10 meters
Networking support for a minimum of 16 devices
Attach: within one (1) second, once within range
Bridge or Gateway connectivity to other data networks
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 16: Current 802.15 WPAN Functional Requirements- “B” List (cont.)
Delivered Data Throughput at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
All devices within a WPAN must be able to communicate with each other
Address QoS to support a variety of traffic types
Synchronous, and connection-oriented links
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 17: Current 802.15 WPAN Functional Requirements- “C” List
No single element of failure
Video
Roaming: hand-off to another PAN
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 18: WPAN Interoperability Classes
Class 4 - Full Compliance to the 802.11 MAC & PHY PICS
Class 3 - Partial Interoperability: there is a way on the medium to exchange data without an intermediate device
  Class 3a Transmit and Receive
  Class 3b Receive Only
  Class 3c Detect Energy
Class 2 - Bridge-like (1 MAC/2 PHYs)
Class 1 - Gateway-like (> 1 MAC)
Class 0 - Non Interoperable

## Slide 19: Coexistence/Interoperability Continuum
Background White noise
Full compliance
Destructive Interference
Significant Degradation
coexistence
Acceptable to 802.11 ?
WPAN proposal ?
interference
interoperable
communication
Spectrum
sharing
etiquette
Data transfer capability
Class 4
Class 3a
Class 3b
Class 3c
WPAN GOAL

## Slide 20
Results of CFPs and Submissions
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
3. November 13, 1998 or sooner
IEEE 802.11
1997
Bluetooth
5/20/98
GTE
5/22/98
Intermec
5/22/98
M/A-COM
5/22/98
1. May 22, 1998 or sooner
HomeRF
3/4/98
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
4. January 15, 1999 or sooner
Kodak
IEEE 802.11
HomeRF Lite
Bluetooth
GTE
Intermec
Motorola
2. July 10, 1998 or sooner
M/A-COM
IEEE 802.11
HomeRF Lite
(Firefly)
Bluetooth
Intermec
5. March 8, 1999 or sooner
Kodak
Wireless Personal Area Networking
Call For Proposals
Liaison
Convergence Achieved
Convergence Happening
Possible Convergence
Bluetooth
6. July 1, 1999 or sooner

## Slide 21: Comparison of 802.15 WPAN Requirements with IEEE 802.11
WPAN
2.4 GHz radio
Freq. Hopping
Spread Spectrum
2.4 GHz radio
Direct Sequence
Spread Spectrum
Infra-Red
1 Mbit/s
2 Mbit/s
2 Mbit/s
1 Mbit/s
1 Mbit/s
2 Mbit/s
Legend: italic (and red) = optional
Higher data rate extension in 2.4 GHz
802.11b
Higher data rate extension in 5 GHz
802.11a
11 & 5.5 Mbit/s
6-12-18...54 Mbit/s
MAC
Lower data rate extension in 2.4 GHz
802.11x
<1Mbit/s
MAC Lite

## Slide 22: 802 focuses only on the Lower Layers
Medium Access Control Sub Layer
Physical Layer
Physical
Data Link
Network
Transport
Session
Presentation
Application
ISO/OSI Reference Model
Area
of
Focus
}
LLC (802.2) and Bridging (802.1)

## Slide 23
How do we map the Bluetooth Specification to the “MAC, PHY, & LLC”?
MAC Sublayer
PLCP Sublayer
PMD Sublayer
MAC Layer
Management
PHY Layer
Management
Station
Management
LLC
MAC
PHY
Physical
Data Link
Network
Transport
Session
Presentation
Application
ISO/OSI
RM
IEEE
802

## Slide 24: Bluetooth and IEEE 802

## Slide 25
802.15 Proposed Timeline for Initial Standard & Beyond
Jul 1999 - Initial Discussion on Proposal submissions
Sep 1999 - Review initial draft standard. If Bluetooth specification is the only complete proposal, understand and present what problems, if any, it will create for other 802 standards. If minimal, base draft on BT spec.
Sept 1999-Initiate Call for Interest and form Study Group(s) to quickly initiate new PARs for other distinct functional classes of WPANs (HRF, Kodak, low end, etc)
Nov 1999 - Initial draft ready for WG ballot. New PAR(s) reviewed by Excom
Jan 2000 - First Ballot complete, second ballot kicked off. Parallel TG(s) formed
Mar 2000 - Draft ready for IEEE sponsor ballot.
Jul 2000
Nov 2000
Dec 2000 - Approval by IEEE Standards Board

## Slide 26: 802.15 WPAN Timeline Compared to Other Activities
1998
1999
J
J
A
S
O
N
D
J
F
M
A
M
J
J
A
S
O
N
M
D
11/00
Bluetooth
v1.0
HRF-Lite
v1.0
SWAP-CA
v1.0 Provisional
3/12/98
WPAN SG
Formed
2/4/99
2nd PAR to ExCom
& WG LB17
6/4/98
1st PAR to
ExCom
CFP
CFA
802.15
Call for Proposals
1st Draft of Standard
802.15 Formed

## Slide 27: Thoughts on Objectives/Missions/Timelines
Success means:
To be recognized by companies as the place to go for WPAN functionality in their products
To have users demand P802.15 compliance as a minimum requirement of product functionality

## Slide 28
Thoughts on Objectives/Missions/Timelines
Need a sponsor ballot approved standard sooner than later -target should be Nov 00
Needs to be recognized by Bluetooth, HomeRF and 802.11
Good enough(meets market need for functionality) vs perfect is an acceptable trade-off for speed in delivery of a standard.
Absolutely need coexistence
Have more flexibility on interoperability solutions
Additional PARs are likely for
  HomeRF/Kodak
  Ultra low power/low cost/low data rate requirements
  Bridging
  Coexistence/Interoperability

## Slide 29
P802.15 Functional Organization Chart

## Slide 30: 802.15 WPAN - Proposed Liaisons
Bluetooth Special Interest Group
Home Radio Frequency Working Group (HRFWG)
Infrared Data Association (IrDA)
IEEE P802.11
Internet Engineering Task Force (IETF), MobileIP
MMAC/PC
ETSI Broadband Radio Access Networks (BRAN) Project
ATM Forum Wireless ATM (WATM) Working Group
Wireless LAN Alliance (WLANA)
DoT FHWA ITS DSRC

## Slide 31
Liaison Objectives
Promote the IEEE as a Value Add
Promote the IEEE 802 as a leader in Wireless Standards-Making
Promote P802.15 as an expert in WPANs
Request/Receive Draft Standard Submissions Through our Liaison Activities from External and Internal (IEEE) Sources

## Slide 32
An Example of a Potential Cooperative Standards Scenario
Specification
  Bluetooth L1-7
Standard
  ETSI L3-7
  IEEE 802 L1-2
Physical Layer
(PHY)
Medium Access Layer
(MAC)
Logical Link Control
(LLC)
Physical
Data Link
Network
Transport
Session
Presentation
Application
7
6
5
4
3
2
1
ISO OSI
Layers
IEEE 802
Standards
Hardware
Software
Transport Control Protocol (TCP)
Internet Protocol (IP)
X.400 and X.500 EMAIL

## Slide 33: 802.15 Working Group for WPANs Summary
Chartered to develop PAN standards for short distance wireless networks.
Cognizant of emerging industry specifications and the importance of building on the work of these groups.
Key role in providing an open forum to debate these proposals, identify issues, and build consensus.
Goal is to create standards having broad market appeal and deal effectively with coexistence and interoperability.
Timeframe for first standard is November, 2000.

## Slide 34
802.15 Plenary & Interim Meetings
1999
  July 5-9, 1999 - Queen Elizabeth Hotel, Montreal, PQ, Plenary
  September 13-17, 1999 - Hilton, Santa Rosa, CA, Interim (Alantro)
  November 8-12, 1999 - Hyatt Regency, Kauai, Koloa, HI, Plenary
2000
  January 10-14, 2000 - Israel, Interim (Breezecom)
  March 6-10, 2000 - Hyatt Regency, Albuquerque, NM, Plenary
  May 8-12, 2000 - Seattle, Interim (Boeing)
  July 10-14, 2000 - Hyatt Regency La Jolla, San Diego, CA, Plenary
  September ?-?, 2000 - ?, Interim (?)
  November 6-10, 2000 - Hyatt Regency, Tampa, FL, Plenary
Plenary and Interim Meetings are official meetings whereas Ad Hoc and Liaison Meetings are unofficial
Meetings and as such do not accrue voting rights and no official actions can be taken by the participants.
Source: http://grouper.ieee.org/groups/802/15/pub/Meeting_Plan.html

## Slide 35: Archive, Mailing List, URLs
WPAN Archives
  http://grouper.ieee.org/groups/802/15/
WPAN Mailing List
  stds-802-wpan@majordomo.ieee.org
IEEE 802.11
  http://grouper.ieee.org/groups/802/11/
Bluetooth Special Interest Group
  http://www.bluetooth.com/
Home RF Working Group
  http://www.homerf.org/
To add your name to IEEE mailing list please send an e-mail
to giffordi@amp.com or bheile@bbn.com

## Slide 36
Questions??
Thanks to
Tom Siep, Texas Instruments
Bruce Kraemer, Harris
Ian Gifford, M/A-COM
who made contributions to this presentation

## Slide 37
Back-up Slides

## Slide 38
Structure of IEEE P802 Standards

## Slide 39: PERSONAL AREA NETWORKING: The Problem
Wires are a problem
  Get broken
  Get lost
  Get in the Way
  Get misconnected

## Slide 40: PERSONAL AREA NETWORKING: The Problem (cont.)
People who carry a watch, pager, cell phone, PDA, and personal stereo have at least
  Four displays
  Two input devices
  Four speakers
  One microphone
  Two long range communications links

## Slide 41: PERSONAL AREA NETWORKING: The Problem (cont.)
Unnecessary Duplication of
  Information
  Hardware I/O components
  Software functions
  Data entry

## Slide 42: Bluetooth Mission/Requirements
A global specification for wireless technology.
Bluetooth answers the need for short-range wireless connectivity within three areas:
  Data and Voice access points
  Cable replacement
  Ad hoc networking
Bluetooth is a system solution comprising hardware, software and interoperability requirements. The Bluetooth specifications specify the complete system.
Bluetooth operates in a globally available 2.4 Ghz ISM band, ensuring communication compatibility worldwide.
Source: Bluetooth Webpage

## Slide 43: HomeRF Mission
The mission of the HomeRF Working Group is to enable the existence of a broad range of interoperable consumer devices, by establishing an open industry specification for unlicensed RF digital communications for PCs and consumer devices anywhere, in and around the home.
Source: HomeRF Webpage