## Slide 1: Bluetooth Architecture Overview Dr. Chatschik Bisdikian IBM Research T.J. Watson Research Center Hawthorne, NY 10532, USA bisdik@us.ibm.com

## Slide 2: Overview
Who is Bluetooth?
What is Bluetooth and what does it do for you?
Bluetooth usage scenarios examples
Bluetooth architecture
Interoperability & profiles
Summary

## Slide 3: Who is Bluetooth?
Harald Blaatand “Bluetooth” II
  King of Denmark 940-981 AC
This is one of two Runic stones erected in his capital city of Jelling
  The stone’s inscription (“runes”) says:
    Harald christianized the Danes
    Harald controlled the Danes
    Harald believes that devices shall seamlessly communicate [wirelessly]

## Slide 4: What does Bluetooth do for you?
Personal Ad-hoc Connectivity
Cable Replacement
Landline
Data/Voice Access Points

## Slide 5: A little bit of history
The Bluetooth SIG (Special Interest Group) was formed in February 1998
  Ericsson
  IBM
  Intel
  Nokia
  Toshiba
There are 1100+ adopter companies
The Bluetooth SIG went “public” in May 1998
The Bluetooth SIG work (the spec: >1,500 pages) became public on July 26, 1999

## Slide 6: The Bluetooth program overview
Bluetooth
Promise
Wireless Connections Made Easy
Bluetooth
Values
Freedom, Simplicity, Reliability,
Versatility and Security
Usage
Scenarios
What the technology can do
Specification
Profiles
How to implement the usage scenarios
Certification
Testing
Interoperability
License free IP for adopters: product
testing to ensure interoperability;
protect the Bluetooth brand

## Slide 7: What is Bluetooth?
Application Framework and Support
Link Manager and L2CAP
Radio & Baseband
Host Controller Interface
RF
Baseband
Audio
Link Manager
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control
A hardware/software description
An application framework

## Slide 8: Usage scenarios: Synchronization
Sharing Common Data…
User benefits
Proximity synchronization
Easily maintained database
Common information database

## Slide 9: Usage scenarios: Headset
Wireless Freedom…
User benefits
Multiple device access
Cordless phone benefits
Hand’s free operation

## Slide 10: Usage scenarios: Data access points
PSTN, ISDN, LAN, WAN, xDSL
Remote Connections...
User benefits
No more connectors
Easy internet access
Common connection experience

## Slide 11: Architectural overview
RF
Baseband
Audio
Link Manager
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control
Cover this

## Slide 12: Radio
frequency synthesis: frequency hopping
  2.402 + k MHz, k=0, …, 78
  1,600 hops per second
conversion bits into symbols: modulation
  GFSK (BT = 0.5; 0.28 < h < 0.35);
  1 MSymbols/s
transmit power
  0 dbm (up to 20dbm with power control)
receiver sensitivity
  -70dBm @ 0.1% BER

## Slide 13: The Bluetooth network topology
M
M
S
S
S
S
P
sb
sb
P
P
Radio designation
  Connected radios can be master or slave
  Radios are symmetric (same radio can be master or slave)
Piconet
  Master can connect to 7 simultaneous or 200+ inactive (parked) slaves per piconet
  Each piconet has maximum capacity (1 Mbps)
  Unique hopping pattern/ID
Scatternet
  High capacity system
  Minimal impact with up to 10 piconets within range
  Radios can share piconets!

## Slide 14: Baseband protocol
Standby
  Waiting to join a piconet
Inquire
  Ask about radios to connect to
Page
  Connect to a specific radio
Connected
  Actively on a piconet (master or slave)
Park/Hold
  Low-power connected states
Inquiry
Page
Connected
AMA
Transmit
data
AMA
HOLD
AMA
PARK
PMA
T =2ms
tpcl
Low-power
states
Active
states
Standby
Connecting
states
Unconnected:
Standby
Detach
T =2ms
tpcl
T =0.6s
tpcl
T =2s
tpcl
releases
AMA address

## Slide 15: Baseband link types
Polling-based (TDD) packet transmissions
  1 slot: 0.625msec (max 1600 slots/sec)
  master/slave slots (even-/odd-numbered slots)
  polling: master always “polls” slaves
Synchronous connection-oriented (SCO) link
  “circuit-switched”
    periodic single-slot packet assignment
  symmetric 64Kbps full-duplex
Asynchronous connection-less (ACL) link
  packet switching
  asymmetric bandwidth
    variable packet size (1-5 slots)
      max. 721 kbps (57.6 kbps return channel)
      108.8 - 432.6 kbps (symmetric)
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22
SCO
ACL
master
slave

## Slide 16: Bluetooth security features
Fast frequency hopping (79 channels)
Low transmit power (range <= 10m)
Authentication of remote device
  based on link key (128 Bit)
  May be performed in both directions
Encryption of payload data
  Stream cipher algorithm ( 128 Bit)
  Affects all traffic on a link
Initialization
  PIN entry by user

## Slide 17: Key generation and usage
PIN
E2
Link Key
Encryption Key
E3
Encryption
Authentication
PIN
E2
Link Key
Encryption Key
E3
User Input
(Initialization)
(possibly)
Permanent
Storage
Temporary
Storage

## Slide 18: Architectural overview
RF
Baseband
Audio
Link Manager
L2CAP
TCS
SDP
RFCOMM
Applications
Data
Control
Cover This
HCI

## Slide 19: Software architecture goals
Support the target usage scenarios
Support a variety of hardware platforms
Good out of box user experience
  Enable legacy applications
  Utilize existing protocols where possible

## Slide 20: Bluetooth protocols
Host Controller Interface (HCI)
  provides a common interface between the Bluetooth host and a Bluetooth module
    Interfaces in spec 1.0: USB; UART; RS-232
Link Layer Control & Adaptation (L2CAP)
  A simple data link protocol on top of the baseband
    connection-oriented & connectionless
    protocol multiplexing
    segmentation & reassembly
    QoS flow specification per connection (channel)
    group abstraction

## Slide 21: Bluetooth protocols
Service Discovery Protocol (SDP)
  Defines a service record format
    Information about services provided by attributes
    Attributes composed of an ID (name) and a value
    IDs may be universally unique identifiers (UUIDs)
  Defines an inquiry/response protocol for discovering services
    Searching for and browsing services

## Slide 22: Bluetooth protocols
RFCOMM (based on GSM TS07.10)
  emulates a serial-port to support a large base of legacy (serial-port-based) applications
  allows multiple “ports” over a single physical channel between two devices
Telephony Control Protocol Spec (TCS)
  call control (setup & release)
  group management for gateway serving multiple devices
Legacy protocol reuse
  reuse existing protocols, e.g., IrDA’s OBEX, or WAP for interacting with applications on phones

## Slide 23: Interoperability & Profiles
Profiles
Protocols
Applications
Represents default solution for a usage model
Vertical slice through the protocol stack
Basis for interoperability and logo requirements
Each Bluetooth device supports one or more profiles

## Slide 24: Profiles
Generic Access Profile
  Service Discovery Application Profile
  Serial Port Profile
    Dial-up Networking Profile
    Fax Profile
    Headset Profile
    LAN Access Profile (using PPP)
    Generic Object Exchange Profile
      File Transfer Profile
      Object Push Profile
      Synchronization Profile
  TCS_BIN-based profiles
    Cordless Telephony Profile
    Intercom Profile

## Slide 25: Synchronization
Sharing Common Data…
User benefits
Proximity synchronization
Easily maintained database
Common information database

## Slide 26: Synchronization profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
IrOBEX
IrMC

## Slide 27: Headset profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
Audio
Stream
AT Commands

## Slide 28: LAN access point profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
PPP

## Slide 29: Summary
Bluetooth is a global, RF-based (ISM band: 2.4GHz), short-range, connectivity technology & solution for portable, personal devices
  it is not just a radio
  create piconets on-the-fly (appr. 1Mbps)
    piconets may overlap in time and space for high aggregate bandwidth
The Bluetooth spec comprises
  a HW & SW protocol specification
  usage case scenario profiles and interoperability requirements
1999 Discover Magazine Awards finalist
To learn more: http://www.bluetooth.com