## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Physical Model Sub-Group Discussion and Questions
Date Submitted: 09 November, 1999
Source: [Kevin Marquess] Company [CETECOM Inc.]
Address [1120 Fulton Place, Fremont, CA 94539, USA]
Voice:[(510) 252-1700x 338 or (510) 387-9080], FAX: [(510) 252-1700], E-Mail:[kevin.marquess@cetecomusa.com]
Re: [99098r0802-15 Reliability of 802.11 WLANs in the Presence of Bluetooth Radios (Jim Zyren)]
Abstract: Review of the PHY layer issues and begin discussions and questioning
Purpose: Call for work in Coexistence Study Group and a review of the work to date.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area Networks
Coexistence Study Group - Physical Model Team Report

## Slide 3: Needs for PHY model
Assumptions
PHY Questions
Need for input from the academic community
  IEEE 802.15 drafted letter?
  (Reply) Chair will review the letter before release.
Compile current research to have centralized discussion
  Bibliography

## Slide 4: Assumptions -- From Jim Zyren’s White-paper -98r0
Network Topology and User Density
Propagation Model
Load (Usage models) for 802.11 and Bluetooth Devices
  MAC related and will be dealt with by MAC subgroup (David Cypher)

## Slide 5: Network Topology and User Density
802.11 Network
1 BT piconet co-located w/ each WLAN node
STA (Wireless STAtion) may be 20m from AP (Access Point)
Average density for BSS (Basic Service Set) is 1 STA every 25m2.
  BSS = AP and its STAs
Transmitter power for both STAs and the AP is +20dBm
        translates to
50 STAs w/ 1 AP
Bluetooth Network
1 BT piconet (= 2 or more BT devices in the piconet) co-located w/ each 802.11 STA
# of BT piconets is dependent on usage scenarios
40 m
IEEE 802.11 AP
IEEE 802.11 STA
BT Piconet

## Slide 6
Simplified indoor model has been proposed -- A. Kamerman (see Bibliography slide)
LOS (Line Of Sight) propagation is assumed 8m
L.O.S. , range  8m
r3.3 , range > 8m
Lpath = 20 log (4  r /  ) r < 8m
= 58.5 + 33 log( r/8 ) r > 8m
where:
 = wavelength @ 2.45 GHz (0.1224 m)
r = range (m)
Binary threshold
  SIR (Signal-to-Interference Ratio)
  BlueTooth Interference = BTI
  BTI < 10 dB SIR -- will not cause significant interference
  BTI  dB SIR -- the DSSS STA will experience a dropped packet provided there is an overlap in time & frequency
Therefore the # of BTI to which a DSSS node is exposed depends on the range from the AP
Propagation Model

## Slide 7
Physical Layer Model and Questions for Discussion
PHY
1) Is the Signal-to-Jammer Ratio (SJR) that was used in the previous analysis of the effect of Bluetooth
on 802.11b of 10dB accurate?
2) Should we use a binary threshold model in the SJR or should we use a more complex model?
--Currently it assumes that the system breaks with a SJR below 10dB and it works fine above 10 dB.
3) We are currently approximating the IF filter as an ideal “brick-wall” filter. Is that a reasonable model?
4) How does power behave as a function of distance? We are interested in how power drops off as a
function of distance in an indoor environment. (Are there any “standard” indoor models that are used?

## Slide 8
G. Ennis, “Impact of Bluetooth on 802.11 Direct Sequence Wireless LANs,” Doc IEEE 802.11-98/319a, Sept. 1998
J. Zyren, “Extension of Bluetooth and 802.11 Direct Sequence Interference Model,” Doc IEEE 802.11-98/378, Nov. 1998
A. Kamerman, “Coexistence between Bluetooth and 802.11 CCK Solution to Avoid Mutual Interference,” Lucent Technologies, Jan 1999
Bibliography