## Slide 1: 802.15 Working Group for Wireless Personal Area Networks
Dr. Robert F. Heile
GTE Technology Organization
Chairman, IEEE 802.15
May 7, 1999
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 2: Outline
IEEE 802 Wireless Vision Statement
WPAN Market Need/Vision
WPAN Project History
WPAN Functional Requirements
Liaison Activities
Summary

## Slide 3: IEEE 802 Wireless Vision Statement
802.11 Base Standard
  2.4GHz Frequency Hopping Spread Spectrum (1Mbit/s)
  2.4GHZ Direct Sequence Spread Spectrum (2Mbit/s)
  Infrared (1Mbit/s)
802.11a 5GHz Extension (>20Mbit/s)
802.11b 2.4GHz Extension (>8Mbit/s)
802.15 Wireless Personal Area Networks
802.16 Broadband Wireless LANs (LMDS)
“IEEE 802 is the focal point for Wireless LAN standards.” Jim Carlo
Source: Jim Carlo, 802 Chair [JC-802-Consortium.PDF] can be downloaded from the following URL: ftp://ftp.flexipc.com/wearablesgroup/802/

## Slide 4: PERSONAL AREA NETWORKING: The Need
Used to interconnect portable computers and/or devices like peripherals and sensors
These devices may be carried or worn by a person and/or may be located nearby
Home/Office computers, printers, phones, LANs, GPS or other car resources can be connected as needed.

## Slide 5: PERSONAL AREA NETWORKING: The Problem
Wires are a problem
  Get broken
  Get lost
  Get in the Way
  Get misconnected

## Slide 6: PERSONAL AREA NETWORKING: The Problem (cont.)
People who carry a watch, pager, cell phone, PDA, and personal stereo have at least
  Four displays
  Two input devices
  Four speakers
  One microphone
  Two long range communications links

## Slide 7: PERSONAL AREA NETWORKING: The Problem (cont.)
Unnecessary Duplication of
  Information
  Hardware I/O components
  Software functions
  Data entry

## Slide 8: PERSONAL AREA NETWORKING: The Solution
Cost effective and efficient embedded wireless connectivity for devices within an area of about 10 meters of each other.
  This area is defined as a Personal Area Network (PAN)
  The PAN is the next domain in the WAN-MAN-LAN hierarchy.

## Slide 9: WPAN Vision Statement
Continuum of needs for wireless products
No one product which can fill all needs
Family of complementary devices
RFID
WPAN
WLANs
High performance,
higher cost
Low performance,
low cost

## Slide 10: WPAN Project History
Started in 1997 as ‘ad hoc’ group within IEEE Portable Applications Standards Committee (PASC)
At the time, no other Groups or Standards Bodies dealing with the problem
In March 1998 a Study Group was formed within 802.11 to develop a Project Authorization Request (PAR)
In March 1999, IEEE 802.15 Working Group for WPANs established

## Slide 11: WPAN: Other Groups Developing Similar Specifications
March 4, 1998
May 20, 1998
1997
Source: doc.: IEEE 802.11-98/58 (Bob Heile, GTE)
HomeRF -formed March 4, 1998
Bluetooth -formed May 20, 1998
Infrared Data Association

## Slide 12: Bluetooth Mission/Requirements
A global specification for wireless technology.
Bluetooth answers the need for short-range wireless connectivity within three areas:
  Data and Voice access points
  Cable replacement
  Ad hoc networking
Bluetooth is a system solution comprising hardware, software and interoperability requirements. The Bluetooth specifications specify the complete system.
Bluetooth operates in a globally available 2.4 Ghz ISM band, ensuring communication compatibility worldwide.
Source: Bluetooth Webpage

## Slide 13: HomeRF Mission
The mission of the HomeRF Working Group is to enable the existence of a broad range of interoperable consumer devices, by establishing an open industry specification for unlicensed RF digital communications for PCs and consumer devices anywhere, in and around the home.
Source: HomeRF Webpage

## Slide 14: Company Participation as of March 1999 in WPAN Related Activities
~504 Bluetooth Adopters,
SIG Members
~50 Attendees
~82 HomeRF Adopters,
Participants/Core Members

## Slide 15: 802 focuses only on the Lower Layers
Medium Access Control Sub Layer
Physical Layer
Physical
Data Link
Network
Transport
Session
Presentation
Application
ISO/OSI Reference Model
Area
of
Focus
}

## Slide 16: 802.15 WPAN Working Group Charter
Establish WPAN functional requirements
Provide an open forum to debate and critique proposals
Develop MAC and PHY standards for short range embedded wireless networking of PCs, PDAs, peripherals, cell phones, pagers, consumer electronic devices, sensors, actuators, and the like.

## Slide 17: 802.15 WPAN Working Group Mission
Work closely with and build consensus among groups having an interest in WPANs like Bluetooth, HomeRF, and 802.11.
Create Standards that meet the requirements of WPANs and have broad market appeal.
Deal effectively with coexistence and interoperability in a shared medium.

## Slide 18: Current 802.15 WPAN Functional Requirements- “A” List
Worldwide spectrum allocations for unlicensed bands such as 2.4GHz
Low Cost: i.e., relative to target device
Small Size e.g., ~.5 cubic inches( excludes antenna & battery)
Power Management: Very Low current consumption (Average 20mw or less @ 10% Tx/Rx load)
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 19: Current 802.15 WPAN Functional Requirements- “A” List (cont.)
Asynchronous or connection-less data links
Allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Allow coexistence of multiple Wireless Systems such as P802.11 in the same area
WPAN Network Access Control
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 20: Current 802.15 WPAN Functional Requirements- “B” List
Range: 0-10 meters
Networking support for a minimum of 16 devices
Attach: within one (1) second, once within range
Bridge or Gateway connectivity to other data networks
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 21: Current 802.15 WPAN Functional Requirements- “B” List (cont.)
Delivered Data Throughput at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
All devices within a WPAN must be able to communicate with each other
Address QoS to support a variety of traffic types
Synchronous or connection-oriented links
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 22: Current 802.15 WPAN Functional Requirements- “C” List
No single element of failure
Video
Roaming: hand-off to another PAN
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 23: WPAN Interoperability Classes
Class 4 - Full Compliance to the 802.11 MAC & PHY PICS
Class 3 - Partial Interoperability: there is a way on the medium to exchange data without an intermediate device
  Class 3a Transmit and Receive
  Class 3b Receive Only
  Class 3c Detect Energy
Class 2 - Bridge-like (1 MAC/2 PHYs)
Class 1 - Gateway-like (> 1 MAC)
Class 0 - Non Interoperable

## Slide 24: Coexistence/Interoperability Continuum
Background White noise
Full compliance
Destructive Interference
Significant Degradation
coexistence
Acceptable to 802.11 ?
WPAN proposal ?
interference
interoperable
communication
Spectrum
sharing
etiquette
Data transfer capability
Class 4
Class 3a
Class 3b
Class 3c
WPAN GOAL

## Slide 25: 802.15 WPAN - Proposed Liaisons
Bluetooth Special Interest Group
Home Radio Frequency Working Group (HRFWG)
Infrared Data Association (IrDA)
IEEE P802.11
MMAC/PC
ETSI Broadband Radio Access Networks (BRAN) Project
Internet Engineering Task Force (IETF), MobileIP
ATM Forum Wireless ATM (WATM) Working Group
Wireless LAN Alliance (WLANA)

## Slide 26: Comparison of 802.15 WPAN Requirements with IEEE 802.11
WPAN
2.4 GHz radio
Freq. Hopping
Spread Spectrum
2.4 GHz radio
Direct Sequence
Spread Spectrum
Infra-Red
1 Mbit/s
2 Mbit/s
2 Mbit/s
1 Mbit/s
1 Mbit/s
2 Mbit/s
Legend: italic (and red) = optional
Higher data rate extension in 2.4 GHz
802.11b
Higher data rate extension in 5 GHz
802.11a
11 & 5.5 Mbit/s
6-12-18...54 Mbit/s
MAC
Lower data rate extension in 2.4 GHz
802.11x
<1Mbit/s
MAC Lite

## Slide 27: 802.15 WPAN Timeline Compared to Other Activities
1998
1999
J
J
A
S
O
N
D
J
F
M
A
M
J
J
A
S
O
N
M
D
11/00
Bluetooth
v1.0
HRF-Lite
v1.0
SWAP-CA
v1.0 Provisional
3/12/98
WPAN SG
Formed
2/4/99
2nd PAR to ExCom
& WG LB17
6/4/98
1st PAR to
ExCom
CFP
CFA
802.15
Call for Proposals
1st Draft of Standard
802.15 Formed

## Slide 28: Standards should be written between the two elephants
Activity
Research
Investment
Standards
Time
Source: “Apocalypse of the two Elephants”, David Clark, MIT
Today
Today
Today

## Slide 29: 802.15 Working Group for WPANs Summary
Chartered to develop PAN standards for short distance wireless networks.
Cognizant of emerging industry specifications and the importance of building on the work of these groups.
Key role in providing an open forum to debate these proposals, identify issues, and build consensus.
Goal is to create standards having broad market appeal and deal effectively with coexistence and interoperability.
Timeframe for first standard is November, 2000.

## Slide 30: Archive, Mailing List, URLs
WPAN Archives
  http://grouper.ieee.org/groups/802/15/
WPAN Mailing List
  stds-802-wpan@majordomo.ieee.org
IEEE 802.11
  http://grouper.ieee.org/groups/802/11/
Bluetooth Special Interest Group
  http://www.bluetooth.com/
Home RF Working Group
  http://www.homerf.org/
To add your name to IEEE mailing list please send an e-mail
to Ian Gifford giffordi@amp.com

## Slide 31: Thank-you