## Slide 1: Reliability of IEEE 802.11 WLANs in Presence of Bluetooth Radios
Jim Zyren
jzyren@harris.com

## Slide 2: Conditions for Collision
Frequency Overlap
  Probability of collision is reduced by using a narrower occupied channel width
Time Overlap
  Probability of collision is reduced by minimizing transmit time (ie transmit at higher data rate)
Sufficient Interference Energy
  Interference energy can be reduced by:
    spatial separation
    tighter filtering
    processing gain

## Slide 3: FHSS and DSSS Power Spectral Densities
2.400 GHz
t0
t2
t1
FHSS Networks are Frequency Agile
2.4835 GHz
2.400 GHz
DSSS Networks typically use 3 fixed non-overlapping Channels
2.4835 GHz

## Slide 4: DSSS vs. Bluetooth
Early study of impact of Bluetooth on IEEE 802.11 DSSS system
  IEEE 802.11 DSSS WLAN @ 11 Mbps
  Dense environment of BT piconets
    one DSSS WLAN node per 25 m2 of office space
    BT piconet co-located with each DSSS node
  0 dBm BT tx power
  +20 dBm DSSS tx power

## Slide 5: Enterprise Environment
40 m
IEEE 802.11 AP
IEEE 802.11 STA
BT Piconet
Composite BT/DSSS
Network Topology
L.O.S. , range < 8m
r3.3 , range > 8m
Lpath = 20 log (4  r /  ) r < 8m
= 58.5 + 33 log( r/8 ) r > 8m
where:
 = wavelength @ 2.45 GHz (0.1224 m)
r = range (m)
Simplified Propagation
Model

## Slide 6: Impact of BT Interference Depends on Range from AP
20 m
4 m
10 m
IEEE 802.11 AP
IEEE 802.11 STA
BT Piconet

## Slide 7: BT Piconet User Model
BT Single Piconet Utilization
BT Composite Effects

## Slide 8: Interference Model
1.94 dwell periods
625

sec
259

sec
BT Transmission slots
1500 byte DSSS Hi Rate Packet
(1210 sec)

## Slide 9: Thruput of DSSS WLAN vs. Piconet Load
Effects shown are for a single BT Piconet operating in close proximity
to IEEE 802.11 DSSS WLAN.

## Slide 10: Availability Curve for DSSS WLAN (r = 4 m)
For r = 4m, only one BT piconet is close enough to cause interference

## Slide 11: Availability Curve for DSSS WLAN (r =10 m)
At r = 10 m, 2 piconets are close enough to interfere with DSSS receiver

## Slide 12: Availability Curve for DSSS WLAN (r = 20 m)
At r = 20 m, 13 piconets are close enough to interfere with DSSS reception. IEEE
802.11 Hi Rate WLAN can still provide peak THROUGHPUT (7.2 Mbps) with 75%
certainty, and 3.5 Mbps THROUGHPUT with over 99% certainty

## Slide 13: Average Effect Over 8 Hour Day
Average Effect over 8 hour working day is shown as a function of range from
DSSS node to DSSS AP.

## Slide 14: Summary of BT/DSSS Results
Degree of BT interference depends on:
    local propagation conditions
    density of BT piconets
    BT piconet loading
DSSS susceptibility to BT interference increases as a function of range from DSSS node to DSSS AP
DSSS Hi Rate systems retain high throughput and have graceful degradation in the presence of BT interference
Based on these user models, DSSS Hi Rate WLANs are very reliable in the presence of significant BT interference
Results are preliminary. Must be verified by lab tests.

## Slide 15: IEEE 802.11 FHSS vs. Bluetooth
Preliminary evaluation
  interaction between single BT transmitter and an IEEE 802.11 FHSS link
  0 dBm BT Tx power, +20 dBm IEEE 802.11 tx power
  Impact estimated under specific BT conditions:
    Bluetooth idle (establish baseline IEEE 802.11 throughput)
    BT telephony w/HV3 packet (33% BT piconet load)
    BT file transfer w/DH1 packet (100% BT piconet load)
    BT in PAGE mode (worst case)
  Influence of Range and receiver filtering
    IF filtering determines bandwidth of susceptibility to BT interference (about 3 MHz for IEEE 802.11 FHSS Rx)

## Slide 16: Rx Desense Values (2FSK)
(1) Vales stated in terms of interference-to-signal ratio
(2) Interim values. To be finalized within 18 mos. after release

## Slide 17: Influence of Range (1 Mbps)
Signal-to-Interference Ratio depends on:
- relative BT and IEEE 802.11 Tx power
- Range from IEEE 802.11 node to AP
- Range from IEEE 802.11 node to BT Tx
At 1 Mbps and 0 dBm BT Tx Power:
- Bandwidth of interference susceptibility is 3 MHz
- BT Tx must be approximately 50% closer to node than AP
(0 dBm BT Tx power, +20 dBm IEEE 802.11FH Tx Power)
802.11 FH AP
802.11 FH
Node
Link Distance (D)
BT Tx
Interference Range (D/2)

## Slide 18: Throughput of WLAN Operating @ 1Mbps (2FSK) vs BT Load
Note: Raw data rate for 2FSK = 1 Mbps

## Slide 19: Influence of Range (2 Mbps)
At 2 Mbps and 0 dBm BT Tx Power:
- Bandwidth of interference susceptibility is 3 MHz
- BT Tx must be within roughly same distance to node as AP
(0 dBm BT Tx power, +20 dBm IEEE 802.11FH Tx Power)
802.11 FH
Access Point
802.11 FH
Node
Link Distance (D)
BT Tx
Interference Range (D)

## Slide 20: Throughput of WLAN Operating @ 2 Mbps (4FSK) vs BT Load
Note: Raw data rate for 4FSK = 2 Mbps

## Slide 21: Summary of FHSS/BT Results
Narrow channel width of FHSS systems help avoid interference in frequency domain
  Occupied channel for FHSS is about 1 MHz under current FCC rules (same width for 2FSK and 4FSK)
Slower transmission rate requires longer transmit time
  increases chances BT will hop into channel during transmission and collide (advantage for 4FSK)
Multi-level FSK more susceptible to ACI/CCI
  4FSK transmission can be jammed by a weaker BT signal (advantage 2FSK)