## Slide 1
Proposal for a Wireless Personal Area Network Physical Layer and Medium Access Control Protocol
Allen Heberling
Eastman Kodak Co.
66 Eastman Ave.
Rochester, NY 14650-2015
phone: 716-588-1939
e-mail: heberlin@kodak.com

## Slide 2
Agenda
Review CFA (doc:IEEE 802.11-98/352)
  Applications
  Requirements
Physical Layer Proposal (doc:IEEE 802.11-99/006)
Medium Access Control Protocol Proposal
Questions

## Slide 3
Application Scenarios for WPAN and Digital Cameras
Digital Cameras able to communicate via RF to:
each other
printers
PCs or Set Top Boxes
kiosks
beacons

## Slide 4
Requirements Summary
RF Enabled Digital Imaging Devices require:
  Ease of use. Digital Image data transfers need to be easy to initiate and take less than 15 seconds.
  ad-hoc network capability. Should be able to enter, join or leave a network easily. User doesn’t need to know IP addresses. It just happens.

## Slide 5
Requirements Summary cont...
  a communications range 60 meters or less.
  dual transmit power levels ( High/Low).
  low power consumption.
  well defined (transmit)/(no transmit) boundary, based on RF energy strength.
  no roaming or hand-off between networks.

## Slide 6
Requirements Summary cont...
Support 12-20 Mbps Data Transfers
Data types:
  Bulk transfers ( Megabyte sized image files)
  Isochronous data ( Packetized Video streams)
  Asynchronous data ( e.g. interactive sessions )
Low cost for consumer applications

## Slide 7
RF PHY Characteristics
2.54 GHz License Free Band. Allows multiple channels in North America & Europe.
Bi-directional, half Duplex
Robust in the face of Microwave Oven Interference
Inexpensive

## Slide 8
MAC Characteristics
MAC protocol layer must:
be RF multi-user friendly( e.g. Carrier Sense/Collision Avoidance).
be able to select & negotiate the use of one of several available RF channels.
support the creation of an ad hoc network.
support high effective data rates.

## Slide 9
MAC Characteristics cont. ...
support bulk data, asynchronous data, and isochronous data transfers.
support power management (e.g. Awake or Asleep).
be transparent to upper layer protocols (e.g. TCP/IP).
be inexpensive

## Slide 10
Multi-Media-ISM (MM-ISM) Physical Layer Proposal

## Slide 11
Proposed MM-ISM Physical Layer Attributes
Operating Frequency Range
  2.4 GHz to 2.5 GHz ISM Band
RF Modulation
  Wideband CP-BFSK
Baseband signal
  Serial NRZ data stream

## Slide 12
Proposed MM-ISM Physical Layer Attributes cont...
Radio Power Consumption
  < 300 milliwatts ( Transmit)
  ~ 100 milliwatts (Receive)
Bit Rate Modes
  20 Mbps
  1 Mbps

## Slide 13
Proposed MM-ISM Physical Layer Attributes cont...
Channel Bandwidth
  27 MHz ( 20 Mbps )
  1.33 MHz ( 1 Mbps)
Number of Operating Channels
  11 overlapping 20 Mbps channels
  3 non-overlapping 20 Mbps channels
  41 non-overlapping 1 Mbps channels

## Slide 14
2.4 GHz ISM Band Channelization to Support 20 Mbps Data Rate

## Slide 15
2.4 GHz ISM Band Channelization to Support 1 Mbps Data Rate

## Slide 16
Proposed MM-ISM Physical Layer Attributes cont...
TxRxTurnAroundTime < 10 usec
RxTxTurnAroundTime < 10 usec
EnergyDetectTime = 10 usec
Slot Time < 20 usec
  SlotTime = RxTxTurnAroundTime + EnergyDetectTime

## Slide 17
Proposed MM-ISM Physical Layer Transmit Specification
Transmit Power Levels
  Maximum 10mW (10dBm) or -20dBW e.i.r.p
  Reduced power mode
    15 dB below max. peak power of 10 dBm
Transmit Spectrum Masks for:
  20Mbps
  1 Mbps

## Slide 20
Proposed MM-ISM Physical Layer Receiver Specification
Minimum Input Level Sensitivity
< 10E-06 BER with -80dBm measured at antenna
Maximum Input Level
< 10E-06 BER with -10dBm measured at the antenna
Receiver Adjacent Channel Rejection
  20 Mbps
  1 Mbps

## Slide 23
MM-ISM Physical Layer PICS Proforma A.4.6

## Slide 24
MM-ISM Physical Layer PICS Proforma A.4.6 cont...

## Slide 25
MM-ISM Physical Layer PICS Proforma A.4.6 cont...

## Slide 26
Proposed MM-ISM Physical Layer Attributes - Interoperability OK = Fully Interoperable X = No Interoperability 1 = There is sensing (CCA) that another BSS is functioning

## Slide 27
Proposed MM-ISM Physical Layer Attributes cont... - Co-existence OK = Co-exist w/o interference(defer) OK’ = Co-exist with interference C = Co-exist by deferring on CCA

## Slide 28
Multi-Media ISM (MM-ISM) Medium Access Control Protocol Proposal

## Slide 29
Two MAC Layer proposals:
1) Adopt a Full Featured 802.11 MAC.
or
2) Develop and Adopt an 802.11 MAC Lite

## Slide 30
Full Featured 802.11 MAC Protocol Pros & Cons
Pros
IEEE 802.11 Standards support.
Full featured MACs are available.
Cons
Current implementations do not support 20Mbps data rates.
Cost to implement in a HW architecture.

## Slide 31
802.11 MAC Lite Protocol Pros & Cons
Pros
Less complexity.
Potentially less expensive to implement.
Maintains Frame formats.
Cons
reduced capability
time to develop

## Slide 32
802.11 MAC Lite Protocol Capabilites A.4.4.1 Preliminary

## Slide 33
802.11 MAC Lite Protocol Capabilites A.4.4.1 cont...

## Slide 34
802.11 MAC Lite Protocol Capabilites A.4.4.1 cont...

## Slide 35
802.11 MAC Lite Protocol Capabilites A.4.4.1 cont...

## Slide 36
802.11 MAC Lite Protocol Capabilites A.4.4.1 cont...