## Slide 1: Bluetooth Architecture Overview Dr. Chatschik Bisdikian IBM Research T.J. Watson Research Center Hawthorne, NY 10532, USA bisdik@us.ibm.com

## Slide 2: Acknowledgement: I would like to acknowledge J. Haartsen, J. Inouye, J. Kardach, T. Muller and J. Webb for assisting me in the preparation of this presentation.

## Slide 3: Overview
Part A:
Who is Bluetooth?
What is Bluetooth and what does it do for you?
Bluetooth usage scenarios examples
Bluetooth architecture
Interoperability & profiles
Summary
Part B:
Bluetooth status (modules, certification, etc.)
IEEE802.15 and Bluetooth spec mapping
2.4GHz coexistence studies

## Slide 4: Who is Bluetooth?
Harald Blaatand “Bluetooth” II
  King of Denmark 940-981 AC
This is one of two Runic stones erected in his capital city of Jelling
  The stone’s inscription (“runes”) says:
    Harald christianized the Danes
    Harald controlled the Danes
    Harald believes that devices shall seamlessly communicate [wirelessly]

## Slide 5: What does Bluetooth do for you?
Personal Ad-hoc Networks
Cable Replacement
Landline
Data/Voice Access Points

## Slide 6: A little bit of history
The Bluetooth SIG (Special Interest Group) was formed in February 1998
  Ericsson
  IBM
  Intel
  Nokia
  Toshiba
There are over 1036 adopter companies
The Bluetooth SIG went “public” in May 1998
The Bluetooth SIG work (the spec: >1,500 pages) became public on July 26, 1999

## Slide 7: The Bluetooth program overview
Bluetooth
Promise
Wireless Connections Made Easy
Bluetooth
Values
Freedom, Simplicity, Reliability,
Versatility and Security
Usage
Scenarios
What the technology can do
Specification
Profiles
How to implement the usage scenarios
Certification
Testing
Interoperability
License free IP for adopters: product
testing to ensure interoperability;
protect the Bluetooth brand

## Slide 8: What is Bluetooth?
Application Framework and Support
Link Manager and L2CAP
Radio & Baseband
Host Controller Interface
RF
Baseband
Audio
Link Manager
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control
A hardware/software description
An application framework

## Slide 9: Usage scenarios: Synchronization
Sharing Common Data…
User benefits
Proximity synchronization
Easily maintained database
Common information database

## Slide 10: Usage scenarios: Headset
Wireless Freedom…
User benefits
Multiple device access
Cordless phone benefits
Hand’s free operation

## Slide 11: Usage scenarios: Data access points
PSTN, ISDN, LAN, WAN, xDSL
Remote Connections...
User benefits
No more connectors
Easy internet access
Common connection experience

## Slide 12: Architectural overview
RF
Baseband
Audio
Link Manager
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control
Cover mostly this

## Slide 13: Radio
frequency synthesis: frequency hopping
  2.402 + k MHz, k=0, …, 78
  1,600 hops per second
conversion bits into symbols: modulation
  GFSK (BT = 0.5; 0.28 < h < 0.35);
  1 MSymbols/s
transmit power
  0 dbm (up to 20dbm with power control)
receiver sensitivity
  -70dBm @ 0.1% BER

## Slide 14: The Bluetooth network topology
M
M
S
S
S
S
P
sb
sb
P
P
Radio designation
  Connected radios can be master or slave
  Radios are symmetric (same radio can be master or slave)
Piconet
  Master can connect to 7 simultaneous or 200+ active slaves per piconet
  Each piconet has maximum capacity (1 MSps)
  Unique hopping pattern/ID
Scatternet
  High capacity system
  Minimal impact with up to 10 piconets within range
  Radios can share piconets!

## Slide 15: The piconet
or
A
D
C
B
E
All devices in a piconet hop together
  To form a piconet: master gives slaves its clock and device ID
    Hopping pattern determined by device ID (48-bit)
    Phase in hopping pattern determined by Clock
Non-piconet devices are in standby
Piconet Addressing
  Active Member Address (AMA, 3-bits)
  Parked Member Address (PMA, 8-bits)

## Slide 16: Baseband protocol
Standby
  Waiting to join a piconet
Inquire
  Ask about radios to connect to
Page
  Connect to a specific radio
Connected
  Actively on a piconet (master or slave)
Park/Hold
  Low-power connected states
Inquiry
Page
Connected
AMA
Transmit
data
AMA
HOLD
AMA
PARK
PMA
T =2ms
tpcl
Low-power
states
Active
states
Standby
Connecting
states
Unconnected:
Standby
Detach
T =2ms
tpcl
T =0.6s
tpcl
T =2s
tpcl
releases
AMA address

## Slide 17: Power consciousness
Standby current < 0.3 mA
  3 months(*)
Voice mode 8-30 mA
  75 hours
Data mode average 5 mA (0.3-30mA, 20 kbps, 25%)
  120 hours
Low-power architecture
  Programmable data length (else radio sleeps)
  Hold and Park modes: 60 µA
    Devices connected but not participating
    Hold retains AMA address, Park releases AMA, gets PMA address
    Device can participate within 2 ms
(*)Estimates calculated with 600 mAh battery and internal amplifier, power will vary with implementation

## Slide 18: Baseband link types
Polling-based packet transmissions
  1 slot: 0.625msec (max 1600 slots/sec)
  master/slave slots (even-/odd-numbered slots)
  polling: master always “polls” slaves
Synchronous connection-oriented (SCO) link
  “circuit-switched”
    periodic single-slot packet assignment
  symmetric 64Kbps full-duplex
Asynchronous connection-less (ACL) link
  packet switching
  asymmetric bandwidth
    variable packet size (1-5 slots)
      max. 721 kbps (57.6 kbps return channel)
      108.8 - 432.6 kbps (symmetric)
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22
SCO
ACL
master
slave

## Slide 19: Error handling
Forward-error correction (FEC)
  headers are protected with 1/3 rate FEC and HEC
  payloads may be FEC protected
    1/3 rate: simple bit repetition (SCO packets only)
    2/3 rate: (10,15) shortened Hamming code
    3/3 rate: no FEC
ARQ (ACL packets only)
  16-bit CRC (CRC-CCITT) & 1-bit ACK/NACK
  1-bit sequence number
access code
header
payload
72b
54b
0-2745b

## Slide 20: Bluetooth security features
Fast frequency hopping (79 channels)
Low transmit power (range <= 10m)
Authentication of remote device
  based on link key (128 Bit)
  May be performed in both directions
Encryption of payload data
  Stream cipher algorithm ( 128 Bit)
  Affects all traffic on a link
Initialization
  PIN entry by user

## Slide 21: Link keys in a piconet
KAD
A
B
C
D
M
KMC
KMA
KMD
KMB
Link keys are generated via a PIN entry
A different link key for each pair of devices is allowed
Authentication:
  Challenge-Response Scheme
Permanent storage of link keys

## Slide 22: Key generation and usage
PIN
E2
Link Key
Encryption Key
E3
Encryption
Authentication
PIN
E2
Link Key
Encryption Key
E3
User Input
(Initialization)
(possibly)
Permanent
Storage
Temporary
Storage

## Slide 23: Application level security
Builds on-top of link-level security
  creates trusted device groups
Security levels for services
  authorization required
  authentication required
  encryption required
Different or higher security requirements could be added:
  Personal authentication
  Higher security level
  Public key

## Slide 24: Architectural overview
RF
Baseband
Audio
Link Manager
L2CAP
TCS
SDP
RFCOMM
Applications
Data
Control
Cover This
HCI

## Slide 25: Software architecture goals
Support the target usage scenarios
Support a variety of hardware platforms
Good out of box user experience
  Enable legacy applications
  Utilize existing protocols where possible

## Slide 26: Bluetooth protocols
L2CAP
OBEX
WAP
Printing
Host Controller Interface
vCard/vCal
WAE
Still Image
Audio
TCP/UDP
RFCOMM
TCS
HID
IP
Service Discovery
PPP

## Slide 27: Bluetooth protocols
Host Controller Interface (HCI)
  provides a common interface between the Bluetooth host and a Bluetooth module
    Interfaces in spec 1.0: USB; UART; RS-232
Link Layer Control & Adaptation (L2CAP)
  A simple data link protocol on top of the baseband
    connection-oriented & connectionless
    protocol multiplexing
    segmentation & reassembly
    QoS flow specification per connection (channel)
    group abstraction

## Slide 28: Bluetooth protocols
Service Discovery Protocol (SDP)
  Defines a service record format
    Information about services provided by attributes
    Attributes composed of an ID (name) and a value
    IDs may be universally unique identifiers (UUIDs)
  Defines an inquiry/response protocol for discovering services
    Searching for and browsing services

## Slide 29: Bluetooth protocols
RFCOMM (based on GSM TS07.10)
  emulates a serial-port to support a large base of legacy (serial-port-based) applications
  allows multiple “ports” over a single physical channel between two devices
Telephony Control Protocol Spec (TCS)
  call control (setup & release)
  group management for gateway serving multiple devices
Legacy protocol reuse
  resuse existing protocols, e.g., IrDA’s OBEX, or WAP for interacting with applications on phones

## Slide 30: Interoperability & Profiles
Profiles
Protocols
Applications
Represents default solution for a usage model
Vertical slice through the protocol stack
Basis for interoperability and logo requirements
Each Bluetooth device supports one or more profiles

## Slide 31: Profiles
Generic Access Profile
  Service Discovery Application Profile
  Serial Port Profile
    Dial-up Networking Profile
    Fax Profile
    Headset Profile
    LAN Access Profile (using PPP)
    Generic Object Exchange Profile
      File Transfer Profile
      Object Push Profile
      Synchronization Profile
  TCS_BIN-based profiles
    Cordless Telephony Profile
    Intercom Profile

## Slide 32: Synchronization
Sharing Common Data…
User benefits
Proximity synchronization
Easily maintained database
Common information database

## Slide 33: Synchronization profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
IrOBEX
IrMC

## Slide 34: Headset profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
Audio
Stream
AT Commands

## Slide 35: LAN access point profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
PPP

## Slide 36: The Bluetooth program overview
Bluetooth
Promise
Wireless Connections Made Easy
Bluetooth
Values
Freedom, Simplicity, Reliability,
Versatility and Security
Usage
Scenarios
What the technology can do
Specification
Profiles
How to implement the usage scenarios
Certification
Testing
Interoperability
License free IP for adopters: product
testing to ensure interoperability;
protect the Bluetooth brand

## Slide 37: Summary
Bluetooth is a global, RF-based (ISM band: 2.4GHz), short-range, connectivity technology & solution for portable, personal devices
  it is not just a radio
  create piconets on-the-fly (appr. 1Mbps)
    piconets may overlap in time and space for high aggregate bandwidth
The Bluetooth spec comprises
  a HW & SW protocol specification
  usage case scenario profiles and interoperability requirements
1999 Discover Magazine Awards finalist
To learn more: http://www.bluetooth.com

## Slide 38: Bluetooth modules
The presentation on Bluetooth Modules (Thomas Mueller) is made here

## Slide 39: The Bluetooth spec and IEEE802.15 (1)
Bluetooth is not only a link (connectivity) solution but an end-to-end (e2e)solution
The Bluetooth e2e solution is built on-top of a core of low level transport protocols
The Bluetooth “brand-name” is highly dependent on the presence of the core protocols in all devices claiming to be Bluetooth devices
The draft standard must contain: RF, BB, LM, & L2CAP Bluetooth protocols
  Higher level services (including LLC) can/shall be built on top of L2CAP
  The GAP (Generic Access Profile) can serve as a guideline for establishing Bluetooth links between host devices

## Slide 40: The Bluetooth spec and IEEE802.15 (2)
HCI
Control
Data
Cover this
Audio
TCP/IP
HID
RFCOMM
Applications
RF
Baseband
Link Manager
L2CAP

## Slide 41: IEEE802.15 & Bluetooth Mapping
The presentation on the Bluetooth/IEEE802.15 mapping (Tom Siep) is made here

## Slide 42: Coexistence studies
The presentation on 2.4GHz radio coexistence (Jim Zyren) is made here

## Slide 43: Protocol layering
“upper” layers
L2CAP
ACL layer
(LM)
BB(MAC)
BB(PHY)+radio
UL_PDU
L2CAP_PDU
LM_SDUs
LM_PDUs
L2CAP_SDU
BB_PDUs
. . . .
BB_SDU
protocol layer
headers
PDU:
protocol data unit
SDU:
service data unit
. . . .
. . .
802.15 MAC

## Slide 44: L2CAP PDU components
L2CAP header
4 (or 6) octets
L2CAP payload
0 to 64K-1 (or -3) octets
L2CAP header
L2CAP payload
  when channelID=‘0x0001’ the L2CAP payload is generated and interpreted by the L2CAP layer itself
  else, the payload is passed to the appropriate higher layer
(*) present only for connectionless traffic (channelID=`0x0001’)
LSB
MSB

## Slide 45: ACL PDU (ACLP) components
ACLP header
1 (or 2) octets
ACLP payload
0 to 339 octets
ACLP header
ACLP payload
  when L_CH=‘b11’ the ACLP payload is generated and interpreted by the ACLP layer itself
    Link Manager (LM) PDUs
  else, the payload is passed to the appropriate higher layer (L2CAP)
(*) for multislot baseband packets (**) present only when length is 9 bits
LSB
MSB

## Slide 46: Baseband PDU components
BB header
18 bits
BB payload
0 to 339 octets
BB header (encoded with 1/3-rate FEC)
BB payload (+CRC encoded with {1,2,3}/3-rate FEC)
  when PDU_type=Dxy, HVx, DV, AUX1 the BB payload is passed to the appropriate higher layer (LM for ACL packets, an application for SCO packets, AUX1?)
  else, header information or in the FHS payload is used to facilitate & manage baseband transmissions
CRC: present only in non-AUX, ACL packets
LSB
MSB
CRC
2 octets

## Slide 47: Baseband PDU type alternatives
AC
header
ACL or SCO payload
72
54 (1/3FEC)
0-2744 (uniform FEC)
AC
FHS payload
68
240 (2/3 FEC(**))
(bit-count)
AC
AC
header
72
54 (1/3FEC(*))
ID
POLL/NULL
72
FHS
ACL/SCO
AC
header
SCO payload
72
54 (1/3FEC)
(*) Bit-counts with FEC references are for bit-counts after FEC has been applied.
(**) When 2/3 FEC encoding is used, the original payload may be
appended (trailed) with 0’s until a multiple of 10-bits is achieved.
ACL payload
80
32-150 (2/3 FEC)
DV
LSB
MSB
header
54 (1/3FEC)

## Slide 48: Baseband PDU components
AC
72
preamble
synch word
trailer
4
68
4
header
54 (1/3FEC*)
AM_ADDR
PDU type
flags
HEC
3
4
3
8
SCO payload
SCO data
FEC ({1,2}/3) applied whenever appropriate
ACL payload
header
body
CRC
FEC (2/3) applied whenever appropriate

## Slide 49: Baseband PDU processing
HEC
whitening
FEC
HEC
whitening
FEC
TX header (apply/add)
RX header (de-apply/remove)
CRC
encryption
whitening
FEC
whitening
FEC
encryption
CRC
TX payload (apply/add)(*)
RX payload (apply/add)
RF-interface
(*) transmission of the “payload” bits follow immediately behind the transmission of the corresponding header bits
insert access code
remove access code
air
transmission