## Slide 1: A Proposal for 802.11b and Bluetooth Coexistence in Enterprise Environments
Carlos Rios
September 13, 1999
Abstract
Operational Scenario
Coexistence
Obvious Questions
Extension to Small Business
Summary
Notes: Introduction
WLAN Market Update
  Status
  Dynamics
  Industry Players
3Com Approach
  Target Market Segments
  Project Approach
  Risks
Summary Note: This presentation contains company revenue information obtained under non-disclosure.

## Slide 2: Abstract
A scheme for simultaneous, collocated IEEE 802.11High Rate DSSS and Bluetooth (BT) communications in environments managed by an MIS infrastructure
  Typically a large enterprise
The concept is to guarantee frequency orthogonality at all times
Applicable to next generation products
  Bluetooth 2.0 (BTv2), as modification of present protocols is required
  802.11b APs need configurability, manageability mods also
Some possible implementations require no modification of the presently envisioned, first generation hardware
  “Just firmware changes…”

## Slide 3: Operational Scenario
Assume an enterprise with installed wired and (2.4 GHz) wireless LANs providing high speed connectivity
Both managed by a common NMS, maintained by the MIS/IT folk
  NMS monitors and configures fixed nodes, APs and mobile clients
  Controls network access
  Gathers statistics, gauges trends, monitors traffic
The MIS department “owns the airwaves”
  Has the charter to provide reliable, secure, uninterrupted wireless network access, microwave ovens notwithstanding
  Typically engage in “search and destroy” missions to ferret out interfering clandestine WLANs and cordless telephones
To these MIS managers, Bluetooth devices would be decidedly unwelcome
  BT is an excellent 802.11b jammer
  Post “No Bluetooth” decals at building entrances?

## Slide 4: But,
Nobody really wants that
Bluetooth is compelling in the enterprise
  BT enabled PDA connectivity to the internet, corporate email, intranet
  BT enabled laptops in a conference room sharing files, presentation materials over one or more piconets
  BT enabled WAN access independent of the corporate net
Bluetooth Access Points are coming
  Complement to the WLAN APs
  Act as either master or slave in BT piconets
  Located in conference rooms, meeting areas, cafeterias and other high traffic areas to provide access to the corporate net, gateways
  Are key to Bluetooth and 802.11 coexistence in the enterprise

## Slide 5: Enterprise BT and 802.11 Coexistence
10/100 BASE-T
Ethernet Hub/Switch
Network
Management
System
802.11b
Access
Point
802.11b Clients
BT Clients
Bluetooth
Access
Point
Notes: Explain WLAN product suite

## Slide 6: Harmonic Coexistence, part 1
Modify the Bluetooth 1.0 air protocols such that the hopping sequence avoids, using adaptive FH, designated 25 MHz sections of the spectrum
  Define 5 sets of BT “forbidden FH channels” that happily coincide with the North American and European non overlapping 802.11b DS (.11bv2) channel spacings (chs 1, 6, 7, 11, 13)
  Derive 5 BTv2 “Optional Hop Modes (OHMs)” from these sets, yielding hopping sequences that occupy 59 (84 - 25) channels only
  Rather than hopping into a “forbidden FH channel” the BTv2 frequency would be mapped to one of the other 59 “permitted” channels
Configure the BTv2 and .11bv2 emitters to operate in the complementary OHMs and DS channels at any given time
  The .11bv2 signals blithely occupy the 25 Mhz vacated by BTv2
  There are no throughput hits to either wireless network

## Slide 7: Harmonic Coexistence, part 2
However, need to keep the FCC folks happy with the FH average time of occupancy requirements
  FH emitters need occupy a minimum 75 channels for no more than 400 ms total over a 30 second interval
So, hop the .11bv2 emitters over the 3 non overlapping US DS channels, switching between them every 10 seconds
  Existing 802.11 beacon mechanisms support this
In concert, alternate BTv2 hopping between the corresponding 3 OHMs that provide the frequency orthogonality with the .11bv2 set
Compliance with the FCC occupancy time requirements is assured with a judicious BTv2 frequency mapping algorithm taken over the 3 nonoverlapping OHMs
  Simplest idea is “shell game” where the 25 OHM1 forbidden frequencies map into those of OHM2, the OHM2 forbidden channels map into OHM3’s, and then OHM3’s map back into OHM1’s

## Slide 8: Obvious Questions
How to bind BTv2 and .11bv2 networks in a sensible manner?
  Pair BTv2 and .11bv2 APs on a one to one basis, perhaps with only enough physical separation to avoid desensitization and ACI
  Configure the Bluetooth AP as a “BTv2 Pilot” associated with its “.11bv2 Partner” AP
“BTv2 Pilot”?
  Need to preclude activation of full band FH emissions by BT radios wandering about in their standby state, without a priori knowledge of the specific spectrum sharing protocol at any given location
  With no BT nets established, the BTv2 Pilot operates exclusively in Inquire mode, issuing continuous, successive pages in order to locate all BT radios in range as they emerge from standby.
    BTv2 pages need to incorporate OHM data for proper response by waking radios
    BTv2 pages will be subject to mapping out of Inquiry Hop Frequency Set
  BT radios respond to the Pilot, piconets are established and the Pilot remains connected in order to, as a minimum, relay OHM cycling information to the piconet participants

## Slide 9: More Obvious Questions
And the “.11bv2 Partner”?
  Provides the successive Optional Hopping Mode cycle data (“Next Up, OHM mode 3”) and necessary timing marks (“Engage now”) to the BTv2 Pilot, consistent with its own agile channel changes.
Just how would the OHM and DSSS frequency agility be coordinated?
  Best left as an exercise to the implementer
  Likely first option is use the wireline backbone to link paired BTv2 and .11bv2 APs. The resulting timing uncertainty due to propagation through the network may not be critical if OHMs cycle only every 10 seconds
  Or, implement a short wired connection (RS-232?) between paired APs.
And coordination of all interacting 802.11APs within one building?
  If organized in the classic non overlapping 3 cell structure, likely have the NMS centrally coordinate the .11bv2 AP frequency agility, with the same attendant timing concerns as above
  Maybe OK to not hop 802.11 APs if they are not paired with a BTv2 AP
    Would overlap only 1/3 of the time with a contiguous, hopping .11bv2 AP- the throughput hit due to mutual CCA deferrals could be acceptable

## Slide 10: Extension to Small Business
Small businesses don’t have MIS departments or sophisticated NMS systems
Are probably more likely than enterprises to want both BT and 802.11 networks on site
Networks are much smaller in scale
Possible implementation scenario
  One “master” .11bv2 AP would be configurable to coordinate the frequency agility of its brother 802.11 APs.
  Hopping coordination propagates from AP to AP through the wired backbone, or also over the air to “Wireless APs” and/or repeaters
  Frequency coordination propagates to the BTv2 APs via their .11bv2 Partners, as in the enterprise

## Slide 11: Summary
A method for providing simultaneous, collocated enterprise 802.11b and Bluetooth communications was presented
Modifications to the existing Bluetooth 1.0 spec are needed to make it work
The existing 802.11b specs needs no change
Coordination of 802.11b AP frequency agility is needed at the network level. These APs would in turn coordinate complementary hopping of Bluetooth piconets.
All the above are conceivably implementable without changes to first generation hardware
An extension to small business environments was also thrown in