## Slide 1: Bluetooth Architecture Overview James Kardach Principle Engineer Bluetooth SIG Program Manager Intel Corporation
Copyright © 1998 Intel Corporation

## Slide 2: Agenda
What does Bluetooth do for you?
  Usage model
What is Bluetooth?
  Compliance, compatibility
What does Bluetooth do?
  Technical points
Who is Bluetooth?
  History
Architectural Overview of Bluetooth

## Slide 3: What does Bluetooth do for you?
Personal Ad-hoc Networks
Cable Replacement
Landline
Data/Voice Access Points

## Slide 4: What is Bluetooth?
A hardware description
An application framework
Application Framework and Support
Link Manager and L2CAP
Radio & Baseband
Host Controller Interface
RF
Baseband
Audio
Link Manager
LMP
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control
Latest Version on
Bluetooth Website:
www.Bluetooth.com

## Slide 5: What is Bluetooth?
A hardware description
An application framework
Modules
Software
RF
Baseband
Audio
Link Manager
LMP
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control

## Slide 6: Testing to Specification
Bluetooth devices will be tested against the specification
Basic Layer Certification
Application Framework Certification
RF
Baseband
Audio
Link Manager
LMP
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control

## Slide 7: What does Bluetooth Do?
Cable Replacement

## Slide 8: Who is Bluetooth?
Harald Blaatand “Bluetooth” II
King of Denmark 940-981
  Son of Gorm the Old (King of Denmark) and Thyra Danebod (daughter of King Ethelred of England)
This is one of two Runic stones erected in his capitol city of Jelling (central Jutland)
  This is the front of the stone depicting the chivalry of Harald.
  The stone’s inscription (“runes”) say:
    Harald christianized the Danes
    Harald controlled Denmark and Norway
    Harald thinks notebooks and cellular phones should seamlessly communicate

## Slide 9: Architectural Overview
Cover This
And a bit of this
RF
Baseband
Audio
Link Manager
LMP
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control

## Slide 10: Bluetooth RF Specifications
Specified for low cost, single chip implementation
  Noise floor margin for substrate noise and low current LNA
  Linearity set by near-far problem
  In-band image allows low-cost low IF
  VCO phase noise enables integrated VCO
  TX-RX turn around time enables single synthesizer
  2.4 ISM band chosen for global use and process capabilities

## Slide 11: Basic Baseband Protocol
Spread spectrum frequency hopping radio
  79/23 one MHz channels
  Hops every packet
    Packets are 1, 3 or 5 slots long
  Frame consists of two packets
    Transmit followed by receive
  Nominally hops at 1600 times a second (1 slot packets)

## Slide 12: Network Topology
Radio Designation
  Connected radios can be master or slave
  Radios are symmetric (same radio can be master or slave)
Piconet
  Master can connect to 7 simultaneous or 200+ active slaves per piconet
  Each piconet has maximum capacity (1 MSPS)
    Unique hopping pattern/ID
Scatternet
  High capacity system
    Minimal impact with up to 10 piconets within range
  Radios can share piconets!
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: The Piconet
All devices in a piconet hop together
  In forming a piconet, master gives slaves its clock and device ID
    Hopping pattern determined by device ID (48-bit)
    Phase in hopping pattern determined by Clock
Non-piconet devices are in standby
Piconet Addressing
  Active Member Address (AMA, 3-bits)
  Parked Member Address (PMA, 8-bits)
or

## Slide 14: Functional Overview
Standby
  Waiting to join a piconet
Inquire
  Ask about radios to connect to
Page
  Connect to a specific radio
Connected
  Actively on a piconet (master or slave)
Park/Hold
  Low Power connected states

## Slide 15: Page and Inquire Scans
A radio must be enabled to accept pages or inquires
  Consumes 18 slots every 1.25 s (or so) for each scan
    slot is 0.625 ms

## Slide 16: Inquiring for Radios
Radio Wants to find other radios in the area

## Slide 17: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A issues an Inquire (pages with the Inquire ID)
    Radios B, C and D are doing an Inquire Scan
Inquire

## Slide 18: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A issues an Inquire (pages with the Inquire ID)
    Radios B, C and D are doing a Inquire Scan
  Radio B recognizes Inquire and responds with an FHS packet
    Has slave’s Device ID and Clock

## Slide 19: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A issues an Inquire (pages with the Inquire ID)
    Radios B, C and D are doing a Inquire Scan
  Radio B recognizes Inquire and responds with an FHS packet
    Has slave’s Device ID and Clock
Inquire

## Slide 20: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A Issues an Inquire (again)
  Radios C and D respond with FHS packets
    As radios C & D respond simultaneously packets are corrupted and Radio A won’t respond
    Each radio waits a random number of slots and listens

## Slide 21: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A Issues an Inquire (again)
Inquire

## Slide 22: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A Issues an Inquire (again)
  Radios C respond with FHS packets

## Slide 23: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A Issues an Inquire (again)
Inquire

## Slide 24: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A Issues an Inquire (again)
  Radios D respond with FHS packets

## Slide 25: Inquiring for Radios
Radio Wants to find other radios in the area
  Radio A Issues an Inquire (again)
  Radios D respond with FHS packets
  Radio A now has information of all radios within range

## Slide 26: Inquiry Procedure
Inquiry has unique device address (all BT radio use)
  Unique set of “Inquiry” hop frequencies
Any device can inquire by paging the Inquiry address
Correlater hit causes slave to respond with FHS packet
  Device ID
  Clock
625 s
fk+1
fk
fk+1
FHS
f’k+1
f’k
fk+4
INQUIRER
STANDBY

## Slide 27: Inquiry Procedure
Multiple slaves are expected to respond
  Correlater hit causes slave to
    respond with FHS packet
    Wait a random number of slots
    Wait for another Inquiry page and repeat
Master should end up with a list of slave FHS packets in area
train A
A
A
A
B
10 ms
INQUIRER
STANDBY
11.25 ms
A
FHS
scan fk
sleep RAND2
fk+1
1.25ms
fk
A
fk+1
FHS
fk+2
sleep RAND1
A
A
A
A
A
A
A

## Slide 28: Inquire Summary
Paging radio Issues page packet with Inquire ID
Any radio doing an Inquire scan will respond with an FHS packet
  FHS packet gives Inquiring radio information to page
    Device ID
    Clock
  If there is a collision then radios wait a random number of slots before responding to the page inquire
After process is done, Inquiring radio has Device IDs and Clocks of all radios in range

## Slide 29: Master Paging a Slave
Paging assumes master has slaves Device ID and an idea of its Clock

## Slide 30: Master Paging a Slave
Paging assumes master has slaves Device ID and an idea of its Clock
  A pages C with C’s Device ID
Page

## Slide 31: Master Paging a Slave
Paging assumes master has slaves Device ID and an idea of its Clock
  A pages C with C’s Device ID
  C Replies to A with C’s Device ID

## Slide 32: Master Paging a Slave
Paging assumes master has slaves Device ID and an idea of its Clock
  A pages C with C’s Device ID
  C Replies to A with C’s Device ID
  A sends C its Device ID and Clock (FHS packet)

## Slide 33: Master Paging a Slave
Paging assumes master has slaves Device ID and an idea of its Clock
  A pages C with C’s Device ID
  C Replies to A with C’s Device ID
  A sends C its Device ID and Clock (FHS packet)
  A connects as a master to C

## Slide 34: Master Paging a slave
Master pages slave (packet has slave ID) at slave page frequency (1 of 32)
  Master sends page train of 16 most likely frequencies in slave hop set
    Slave ID sent twice a transmit slot on slave page frequency
    Master listens twice at receive slot for a response
  If misses, master sends second train on remaining 16 frequencies
Slave listens for 11 ms (page scan)
  If correlater triggers, slave wakes-up and relays packet at response frequency
  Master responds with FHS packet (provides master’s Device ID and Clock)
  Slave joins piconet
625 s
fm
fk+2
Master
Slave
fk+1
fk
fk+1
f’k+1
f’k
FHS
fk+2

## Slide 35: Paging Procedure
Each slave page scans on unique sequence of 32 channels fk
  Master pages 16 most likely channels for entire sleep period (nominally 1.25 seconds)
If clocks are off, then second train sent on last 16 frequencies for entire sleep period
train A
A
A
A
B
B
10 ms
Pager
Paged
11.25 ms
B
B
FHS
scan fk
sleep
CONNECTION
fk+1
1.25ms

## Slide 36: PHYSICAL LINK DEFINITION (II)
circuit switching
symmetric, synchronous services
slot reservation at fixed intervals
packet switching
(a)symmetric, asynchronous services
polling access scheme
SYNCHRONOUS CONNECTION-ORIENTED (SCO) LINK
ASYNCHRONOUS CONNECTION-LESS (ACL) LINK

## Slide 37: Packet Types/Data Rates
0000
0001
0010
0011
NULL
POLL
FHS
DM1
NULL
POLL
FHS
DM1
1
0100
0101
0110
0111
HV1
HV2
HV3
DH1
2
DV
1000
1001
1010
1011
1100
DM3
DH3
3
1101
1110
1111
DM5
DH5
4
TYPE
SEGMENT
ACL link
SCO link
AUX1
DM1
DH1
DM3
DH3
DM5
DH5
108.8
172.8
256.0
384.0
286.7
432.6
108.8
172.8
384.0
576.0
477.8
721.0
108.8
172.8
54.4
86.4
36.3
57.6
TYPE
symmetric
asymmetric
Data Rates (Kbps)
Packet Types

## Slide 38: Mobile = Battery life
Low power consumption*
  Standby current < 0.3 mA
    3 months
  Voice mode 8-30 mA
    75 hours
  Data mode average 5 mA
  (0.3-30mA, 20 kbit/s, 25%)
     hours
Low Power Architecture
  Programmable data length (else radio sleeps)
  Hold and Park modes 60 µA
    Devices connected but not participating
    Hold retains AMA address, Park releases AMA, gets PMA address
    Device can participate within 2 ms
  * Estimates calculated with 600 mAh battery and internal amplifier, power will vary with implementation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 39: Bluetooth Security
Provides link layer security between any two Bluetooth radios
  Authentication (E1 algorithm)
    Challenge/Response system
  Encryption (privacy)
    Encrypts data between two devices
    Stream cipher with E0 algorithm
  Key management and usage
    Configurable Encryption key length (0-16 bytes)
      Government export regulations
      Radio negotiate key size
    Key generation with E2-E3 algorithms
      Authentication and Encryption keys

## Slide 40: Bluetooth Radio Modules
Complete radio on a module
  Designed to meet “Limited Module Compliance” requirements
    Pre-certified to meet global regulatory requirements
    Allows devices assembled with modules to be “self-certified”
  USB or Serial Interface
  Solder-ball connections
  External Antennae
25 mm dia
17x33mm
19x35mm
25x25mm
36x43mm
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 41: The international 2.4 GHz ISM band
Requirements
  Channel bandwidth limited to 1 MHz
  Spectrum spreading must be employed
  Multiple uncoordinated networks may exist and cause interference
  Microwave ovens also use this band
  2.4 GHz IC electronics must run at high current levels
Bluetooth solution
  1 Mb/s symbol rate exploits maximum channel bandwidth
  Fast frequency hopping and short data packets avoids interference
  CVSD voice coding enables operation at high bit error rates
  Air interface tailored to minimize current consumption
  Relaxed link budget supports low cost single chip integration
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 42: Bluetooth is global
One version for the world
  Architecture compliant with global emission rules (2.4 GHz ISM band)
    Working through FCC, EC, MPT for spectrum and power harmonization
  Architecture compliant and safe for use on airlines
    Working with FAA, JAA, FCC, airplane manufacturers and airlines
  Reviewing security architecture with affected countries
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 43: Software Goals
Good out of box experience
  Should provide value with existing applications
    Utilize existing APIs and protocols where possible
  Should be introduced with hardware that provides value
    Notebooks
    Cellphones
    Handhelds
  Should support the usage model
    Data access points (POTs Modem, cellphone, …)
    Cable replacement (Speaking laptop, instant postcard, …)
    Ad-hoc networking (File exchange, …)

## Slide 44: Example Software Implementation
PC Windows* example supporting the Bluetooth usage model
  WDM Driver
    Windows* 2000
    Windows 98*

## Slide 45: Summary
Bluetooth is a radio system (not a radio)
  Hardware
  Software framework
  Interoperability requirements
Bluetooth Radio System is optimized for mobility
  Primarily cable replacement
    NOT a WLAN technology
  Targeted for Global use by mobile users
Notes: Page <number>
        <footer>
<header>
<date/time>