## Slide 1: 802.15 Working Group for Wireless Personal Area Networks
A Presentation to the MobileIP Work Group at IETF45
July 16, 1999
Bob Heile, Chair
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 2: Presentation Outline
Brief WPAN/WG background/charter
WPAN Functional Requirements
Brief Comparison to 802.11/Bluetooth
Project Timeline
802.15 Functional Organization
Liaison Activites

## Slide 3: IEEE 802 Wireless Vision Statement
802.11 Base Standard
  2.4GHz Frequency Hopping Spread Spectrum (1Mbit/s)
  2.4GHZ Direct Sequence Spread Spectrum (2Mbit/s)
  Infrared (1Mbit/s)
802.11a 5GHz Extension (>20Mbit/s)
802.11b 2.4GHz Extension (>8Mbit/s)
802.15 Wireless Personal Area Networks
802.16 Broadband Wireless LANs (LMDS)
“IEEE 802 is the focal point for Wireless LAN standards.” Jim Carlo
Source: Jim Carlo, 802 Chair [JC-802-Consortium.PDF] can be downloaded from the following URL: ftp://ftp.flexipc.com/wearablesgroup/802/

## Slide 4: WPAN Project History
Started in 1997 as ‘ad hoc’ group within IEEE Portable Applications Standards Committee (PASC)
At the time, no other Groups or Standards Bodies dealing with the problem
In March 1998 a Study Group was formed within 802.11 to develop a Project Authorization Request (PAR)
In March 1999, IEEE 802.15 Working Group for WPANs established
Kick-off Meeting July5-9 in Montreal-61 people attending, 39 achieved voting status.

## Slide 5: WPAN Positioning Statement
Continuum of needs for wireless products
No one product which can fill all needs
Family of complementary devices
RFID
WPAN
WLANs
High performance,
higher cost
Low performance,
low cost

## Slide 6: PAN Related Activities
Bluetooth--over 900 Companies Participating Formed May 20, 1998 Spec due-July 99
HomeRF/Firefly-- over 90 Companies Formed March 4, 1998 Spec Dec 98(swap)/Dec 99
802.15-- ~50 Companies Participating Target Standard Nov 00
Others
  Intermec, Motorola, Butterfly, Kodak...

## Slide 7
IEEE 802.15 Charter
Build on emerging industry specifications
Provide an open forum to debate these proposals
Identify substantive issues
Build consensus on solutions
Goal is to create standards that have:
  broad market applicability
  deal with the issues of coexistence and interoperability
  widely used
The IEEE P802.15 WPAN Working Group is chartered with developing Personal Area Network standards for short distance wireless networks.

## Slide 8: Current 802.15 WPAN Functional Requirements- “A” List
Worldwide spectrum allocations for unlicensed bands such as 2.4GHz
Low Cost: i.e., relative to target device
Small Size e.g., ~.5 cubic inches( excludes antenna & battery)
Power Management: Very Low current consumption (Average 20mw or less @ 10% Tx/Rx load)
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 9: Current 802.15 WPAN Functional Requirements- “A” List (cont.)
Asynchronous or connection-less data links
Allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Allow coexistence of multiple Wireless Systems such as P802.11 in the same area
WPAN Network Access Control
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 10: Current 802.15 WPAN Functional Requirements- “B” List
Range: 0-10 meters
Networking support for a minimum of 16 devices
Attach: within one (1) second, once within range
Bridge or Gateway connectivity to other data networks
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 11: Current 802.15 WPAN Functional Requirements- “B” List (cont.)
Delivered Data Throughput at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
All devices within a WPAN must be able to communicate with each other
Address QoS to support a variety of traffic types
Synchronous, and connection-oriented links
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 12: Current 802.15 WPAN Functional Requirements- “C” List
No single element of failure
Video
Roaming: hand-off to another PAN
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 13: Comparison of 802.15 WPAN Requirements with IEEE 802.11
WPAN
2.4 GHz radio
Freq. Hopping
Spread Spectrum
2.4 GHz radio
Direct Sequence
Spread Spectrum
Infra-Red
1 Mbit/s
2 Mbit/s
2 Mbit/s
1 Mbit/s
1 Mbit/s
2 Mbit/s
Legend: italic (and red) = optional
Higher data rate extension in 2.4 GHz
802.11b
Higher data rate extension in 5 GHz
802.11a
11 & 5.5 Mbit/s
6-12-18...54 Mbit/s
MAC
Lower data rate extension in 2.4 GHz
802.11x
<1Mbit/s
MAC Lite

## Slide 14: 802 focuses only on the Lower Layers
Medium Access Control Sub Layer
Physical Layer
Physical
Data Link
Network
Transport
Session
Presentation
Application
ISO/OSI Reference Model
Area
of
Focus
}

## Slide 15: Bluetooth and IEEE 802
Notes: Correspondence of Bluetooth to the ISO Open Standards Interface (OSI) model and how the IEEE standards map to them.
Note that IEEE has only two layers of the ISO-OSI while Bluetooth (as you well know) covers all of them. What is not indicated by this graph is that the normal place for the LLC layer is in a separate committee, 802.2. This standard is common to 802 stacks, but each MAC may have some medium-specific clauses in the 802.2 standard. Due to the unique nature of the wireless medium, 802.15 will evaluate if there is sufficient flexibility for a Bluetooth-based standard to follow this model.

## Slide 16: Bluetooth and IEEE 802

## Slide 17
802.15 Proposed Timeline Initial Standard & Beyond
Jul 1999 - Initial Discussion on Proposal submissions
Sep 1999 - Review initial draft standard. If Bluetooth specification is the only complete proposal, understand and present what problems, if any, it will create for other 802 standards. If minimal, base draft on BT spec.
Sept 1999-Initiate Call for Interest and form Study Group(s) to quickly initiate new PARs for other distinct functional classes of WPANs (HRF, Kodak, low end, etc)
Nov 1999 - Initial draft ready for WG ballot. New PAR(s) reviewed by Excom
Jan 2000 - First Ballot complete, second ballot kicked off. Parallel TG(s) formed
Mar 2000 - Draft ready for IEEE sponsor ballot.
Jul 2000
Nov 2000
Dec 2000 - Approval by IEEE Standards Board

## Slide 18: 802.15 WPAN Timeline Compared to Other Activities
1998
1999
J
J
A
S
O
N
D
J
F
M
A
M
J
J
A
S
O
N
M
D
11/00
Bluetooth
v1.0
HRF-Lite
v1.0
SWAP-CA
v1.0 Provisional
3/12/98
WPAN SG
Formed
2/4/99
2nd PAR to ExCom
& WG LB17
6/4/98
1st PAR to
ExCom
CFP
CFA
802.15
Call for Proposals
1st Draft of Standard
802.15 Formed

## Slide 19: Thoughts on Objectives/Missions/Timelines
Success means:
To be recognized by companies as the place to go for WPAN functionality in their products
To have users demand P802.15 compliance as a minimum requirement of product functionality

## Slide 20
Thoughts on Objectives/Missions/Timelines
Need a sponsor ballot approved standard sooner than later -target should be Nov 00
Needs to be recognized by Bluetooth, HomeRF and 802.11
Good enough(meets market need for functionality) vs perfect is an acceptable trade-off for speed in delivery of a standard.
Absolutely need coexistence
Have more flexibility on interoperability solutions
Additional PARs are likely for
  HomeRF/Kodak
  Ultra low power/low cost/low data rate requirements
  Bridging
  Coexistence/Interoperability

## Slide 21
P802.15 Functional Organization Chart

## Slide 22: 802.15 WPAN - Proposed Liaisons
Bluetooth Special Interest Group
Home Radio Frequency Working Group (HRFWG)
Infrared Data Association (IrDA)
IEEE P802.11
Internet Engineering Task Force (IETF), MobileIP
MMAC/PC
ETSI Broadband Radio Access Networks (BRAN) Project
ATM Forum Wireless ATM (WATM) Working Group
Wireless LAN Alliance (WLANA)
DoT FHWA ITS DSRC

## Slide 23
Liaison Objectives
Promote the IEEE as a Value Add
Promote the IEEE 802 as a leader in Wireless Standards-Making
Promote P802.15 as an expert in WPANs
Request/Receive Draft Standard Submissions Through our Liaison Activities from External and Internal (IEEE) Sources

## Slide 24
An Example of a Potential Cooperative Standards Scenario
Specification
  Bluetooth L1-7
Standard
  ETSI L3-7
  IEEE 802 L1-2
Physical Layer
(PHY)
Medium Access Layer
(MAC)
Logical Link Control
(LLC)
Physical
Data Link
Network
Transport
Session
Presentation
Application
7
6
5
4
3
2
1
ISO OSI
Layers
IEEE 802
Standards
Hardware
Software
Transport Control Protocol (TCP)
Internet Protocol (IP)
X.400 and X.500 EMAIL

## Slide 25: 802.15 Working Group for WPANs Summary
Chartered to develop PAN standards for short distance wireless networks.
Cognizant of emerging industry specifications and the importance of building on the work of these groups.
Key role in providing an open forum to debate these proposals, identify issues, and build consensus.
Goal is to create standards having broad market appeal and deal effectively with coexistence and interoperability.
Timeframe for first standard is November, 2000.

## Slide 26: Archive, Mailing List, URLs
WPAN Archives
  http://grouper.ieee.org/groups/802/15/
WPAN Mailing List
  stds-802-wpan@majordomo.ieee.org
IEEE 802.11
  http://grouper.ieee.org/groups/802/11/
Bluetooth Special Interest Group
  http://www.bluetooth.com/
Home RF Working Group
  http://www.homerf.org/
To add your name to IEEE mailing list please send an e-mail
to Ian Gifford giffordi@amp.com

## Slide 27
Questions??
Thanks to
Tom Siep, Texas Instruments
Bruce Kraemer, Harris
Ian Gifford, M/A-COM
who made contributions to this presentation

## Slide 28
Back-up Slides

## Slide 29: PERSONAL AREA NETWORKING: The Problem
Wires are a problem
  Get broken
  Get lost
  Get in the Way
  Get misconnected

## Slide 30: PERSONAL AREA NETWORKING: The Problem (cont.)
People who carry a watch, pager, cell phone, PDA, and personal stereo have at least
  Four displays
  Two input devices
  Four speakers
  One microphone
  Two long range communications links

## Slide 31: PERSONAL AREA NETWORKING: The Problem (cont.)
Unnecessary Duplication of
  Information
  Hardware I/O components
  Software functions
  Data entry

## Slide 32: WPAN Interoperability Classes
Class 4 - Full Compliance to the 802.11 MAC & PHY PICS
Class 3 - Partial Interoperability: there is a way on the medium to exchange data without an intermediate device
  Class 3a Transmit and Receive
  Class 3b Receive Only
  Class 3c Detect Energy
Class 2 - Bridge-like (1 MAC/2 PHYs)
Class 1 - Gateway-like (> 1 MAC)
Class 0 - Non Interoperable

## Slide 33: Coexistence/Interoperability Continuum
Background White noise
Full compliance
Destructive Interference
Significant Degradation
coexistence
Acceptable to 802.11 ?
WPAN proposal ?
interference
interoperable
communication
Spectrum
sharing
etiquette
Data transfer capability
Class 4
Class 3a
Class 3b
Class 3c
WPAN GOAL

## Slide 34: Bluetooth Mission/Requirements
A global specification for wireless technology.
Bluetooth answers the need for short-range wireless connectivity within three areas:
  Data and Voice access points
  Cable replacement
  Ad hoc networking
Bluetooth is a system solution comprising hardware, software and interoperability requirements. The Bluetooth specifications specify the complete system.
Bluetooth operates in a globally available 2.4 Ghz ISM band, ensuring communication compatibility worldwide.
Source: Bluetooth Webpage

## Slide 35: HomeRF Mission
The mission of the HomeRF Working Group is to enable the existence of a broad range of interoperable consumer devices, by establishing an open industry specification for unlicensed RF digital communications for PCs and consumer devices anywhere, in and around the home.
Source: HomeRF Webpage

## Slide 36
WPAN Liaison & Submissions
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
3. November 13, 1998 or sooner
IEEE 802.11
1997
Bluetooth
5/20/98
GTE
5/22/98
Intermec
5/22/98
M/A-COM
5/22/98
1. May 22, 1998 or sooner
HomeRF
3/4/98
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
4. January 15, 1999 or sooner
Kodak
IEEE 802.11
HomeRF Lite
Bluetooth
GTE
Intermec
Motorola
2. July 10, 1998 or sooner
M/A-COM
IEEE 802.11
HomeRF Lite
Bluetooth
Intermec
5. March 8, 1999 or sooner
Kodak
Wireless Personal Area Networking
Call For Proposals
Liaison
Convergence Achieved
Convergence Happening
Possible Convergence
Bluetooth
6. July 1, 1999 or sooner