## Slide 1
IEEE 802.15 Charter
Build on emerging industry specifications
Provide an open forum to debate these proposals
Identify substantive issues
Build consensus on solutions
Goal is to create standards that have:
  broad market applicability
  deal with the issues of coexistence and interoperability
  widely used
The IEEE P802.15 WPAN Working Group is chartered with developing Personal Area Network standards for short distance wireless networks.

## Slide 2: 802.15 WPAN Working Group Scope of First PAR
Establish WPAN functional requirements
Develop MAC and PHY standards for short range embedded wireless networking of PCs, PDAs, peripherals, cell phones, pagers, consumer electronic devices, sensors, actuators, and the like.

## Slide 3: Thoughts on Objectives/Missions/Timelines
Success means:
To be recognized by companies as the place to go for WPAN functionality in their products
To have users demand P802.15 compliance as a minimum requirement of product functionality

## Slide 4
Thoughts on Objectives/Missions/Timelines
Need a sponsor ballot approved standard sooner than later -target should be Nov 00
Needs to be recognized by Bluetooth, HomeRF and 802.11
Good enough(meets market need for functionality) vs perfect is an acceptable trade-off for speed in delivery of a standard.
Absolutely need coexistance
Have more flexibility on interoperability solutions
Additional PARs are likely for
  HomeRF/Kodak
  Ultra low power/low cost/low data rate requirements
  Bridging
  Coexistence/Interoperability

## Slide 5: WPAN Vision Statement
Continuum of needs for wireless products
No one product which can fill all needs
Family of complementary devices
RFID
WPAN
WLANs
High performance,
higher cost
Low performance,
low cost

## Slide 6: 802.15 WPAN Working Group Mission
Work closely with and build consensus among groups having an interest in WPANs like Bluetooth, HomeRF, and 802.11.
Create Standards that meet the requirements of WPANs and have broad market appeal.
Deal effectively with coexistence and interoperability in a shared medium.

## Slide 7: Bluetooth Mission/Requirements
A global specification for wireless technology.
Bluetooth answers the need for short-range wireless connectivity within three areas:
  Data and Voice access points
  Cable replacement
  Ad hoc networking
Bluetooth is a system solution comprising hardware, software and interoperability requirements. The Bluetooth specifications specify the complete system.
Bluetooth operates in a globally available 2.4 Ghz ISM band, ensuring communication compatibility worldwide.
Source: Bluetooth Webpage

## Slide 8: HomeRF Mission
The mission of the HomeRF Working Group is to enable the existence of a broad range of interoperable consumer devices, by establishing an open industry specification for unlicensed RF digital communications for PCs and consumer devices anywhere, in and around the home.
Source: HomeRF Webpage

## Slide 9: Possible Coalescence of Standards
Achieve coverage through aggregation of networking capabilities rather than through power levels
Evaluate all mechanisms that will promote coexistence (including CSMA)

## Slide 10: 802.15 Structure

## Slide 11: 802.15 Structure
Workings Groups may be organized along applications (WLANs, WPANs, BWA, etc)
Working Groups may have multiple base standards vs one
Working Groups may have multiple MACs

## Slide 12
802.15 Proposed Timeline Initial Standard & Beyond
Jul 1999 - Initial Discussion on Proposal submissions
Sep 1999 - Review initial draft standard. If Bluetooth specification is the only complete proposal, understand and present what problems, if any, it will create for other 802 standards. If minimal, base draft on BT spec.
Sept 1999-Initiate Call for Interest and form Study Group(s) to quickly initiate new PARs for other distinct functional classes of WPANs (HRF, Kodak, low end, etc)
Nov 1999 - Initial draft ready for WG ballot. New PAR(s) reviewed by Excom
Jan 2000 - First Ballot complete, second ballot kicked off. Parallel TG(s) formed
Mar 2000 - Draft ready for IEEE sponsor ballot.
Jul 2000
Nov 2000
Dec 2000 - Approval by IEEE Standards Board

## Slide 14: 802 focuses only on the Lower Layers
Medium Access Control Sub Layer
Physical Layer
Physical
Data Link
Network
Transport
Session
Presentation
Application
ISO/OSI Reference Model
Area
of
Focus
}

## Slide 15: Current 802.15 WPAN Functional Requirements- “A” List
Worldwide spectrum allocations for unlicensed bands such as 2.4GHz
Low Cost: i.e., relative to target device
Small Size e.g., ~.5 cubic inches( excludes antenna & battery)
Power Management: Very Low current consumption (Average 20mw or less @ 10% Tx/Rx load)
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 16: Current 802.15 WPAN Functional Requirements- “A” List (cont.)
Asynchronous or connection-less data links
Allow coexistence of multiple Wireless PAN’s in the same area (20 within 400 square feet)
Allow coexistence of multiple Wireless Systems such as P802.11 in the same area
WPAN Network Access Control
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 17: Current 802.15 WPAN Functional Requirements- “B” List
Range: 0-10 meters
Networking support for a minimum of 16 devices
Attach: within one (1) second, once within range
Bridge or Gateway connectivity to other data networks
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 18: Current 802.15 WPAN Functional Requirements- “B” List (cont.)
Delivered Data Throughput at the MAC SAP: (19.2 - 100) kbit/s (actual 1 device to 1 device)
All devices within a WPAN must be able to communicate with each other
Address QoS to support a variety of traffic types
Synchronous, and connection-oriented links
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 19: Current 802.15 WPAN Functional Requirements- “C” List
No single element of failure
Video
Roaming: hand-off to another PAN
Source:doc.: IEEE 802.11-98/160r2 (Ian Gifford, M/A-COM)

## Slide 20: 802.15 Working Group for WPANs Summary
Chartered to develop PAN standards for short distance wireless networks.
Cognizant of emerging industry specifications and the importance of building on the work of these groups.
Key role in providing an open forum to debate these proposals, identify issues, and build consensus.
Goal is to create standards having broad market appeal and deal effectively with coexistence and interoperability.
Timeframe for first standard is November, 2000.