## Slide 1: Time Modulated Ultra-Wideband Technology
Paul Withington
Senior Technologist
Time Domain Corporation
6700 Odyssey Drive
Huntsville, Alabama 35806 USA
TEL: 256 922 9229
FAX: 256 922 0387
E-M: paul.withington@tdsi.com

## Slide 2: Time Modulated Ultra-Wideband Technology
Brief technical overview of TM-UWB
The value of TM-UWB
The status of TM-UWB R&D
Sources of information

## Slide 3: Defining “UWB”
Large relative bandwidth signal:
Large processing gain
BW=
fu-fl
fu+fl


## Slide 4: Time Modulated UWB
75% to 100% relative bandwidths
  One or two zero crossing monocycle waveforms
Noise-like signal in both time and frequency domains
  High pulse repetition frequencies (typically > 10 MHz)
  Interpulse period varied in accordance with a pseudo-noise code (time hopping)
Coherent Matched Filter Correlating Receiver
  Correlation process converts UWB RF to baseband signal
Applications
  High performance wireless communications
  Sub-centimeter distance measuring
  High resolution radar sensing

## Slide 5: TM-UWB Transmitted Waveform
Not a sinewave, but millions of pulses per second
Time coded to make noise-like
Pulse position modulation
500 ps
Time
Randomized Time Coding
Amplitude


ps
“0”
“1”
Power Spectral Density (dB)
-80
-40
0
Frequency (GHz)
1
2
3
4
5
Frequency (GHz)
Random noise signal

## Slide 6: Coherent Reception Concept
-2
-1
0
1
2
Time
ns
V
-2
-1
0
1
2
Time
ns
V
An analog process
  Linear multiplication
  Integration
Result depends on time offset between
  Received waveform
  Template waveform
  In-band noise
Collapses UWB RF signal to baseband signal
  Duty cycle processing gain
  Baseband BW = 1/2 PRF
-2
-1
0
1
2
Time
ns
V
-2
-1
0
1
2
Time
ns
V
-2
-1
0
1
2
Time
ns
V
-2
-1
0
1
2
Time
ns
V

## Slide 7: Baseband Signal Processing
TM-UWB does not send one symbol per pulse
TM-UWB depends on coherent pulse integration for additional processing gain
  For a 10 Mpps system transmitting 10 kbps, one pulse is spread over 1000 pulses
  10 Log (1000) = 30 dB additional processing gain
Total processing gain
  Duty cycle gain + pulse integration gain

## Slide 8: Multipath Advantage
RAYLEIGH FADING : A Continuous Wave Phenomenon
  Conventional Radios Overcome Fading with Power
  High Power Transmitter are Detectable and Consumed Batteries
TM-UWB Does Not Use Continuous Waves
No Rayleigh fading
No high power transmission required to overcome Rayleigh fading
Direct Path
Path 2
Path 1
Direct Path
Path 2
Path 1
Interfering
Receive
Window
(500 ps)
•
•
Non-Interfering

## Slide 9: Real-World Multipath
Unobstructed 10 meter LOS Path
Obstructed 8 meter Path
Baseband Amplitue
Baseband Amplitue
Baseband Amplitue
Baseband Amplitue
Time (ns)
Time (ns)
Time (ns)
Time (ns)

## Slide 10: High Performance Rake Combining
Power variations minimized
Maximal performance enhancements from rake receiver architecture
1 correlator
10 correlators

## Slide 11: Value of Technology
High performance communications in cluttered environment
Synchronous with timing uncertainty on the order of 20 ps RMS
High resolution radar sensor
Fused functionality
Low cost

## Slide 12: Technology Status
Time Domain funded development of two SiGe chips
  Synchronous programmable time delay
  Multiple correlator ASIC
Chips are fabricated by IBM under contract
Third chip (in development)
  DSP/controller is necessary for signal processing and system control
  Standard CMOS
  Application specific

## Slide 13: Radar Prototype
Through wall motion sensing for law enforcement
Ranging
SAR imaging demonstrations

## Slide 14: Communications Prototypes
10 kbps up to 2.5 Mbps
  Full duplex
  Half duplex
  Peer-to-peer networking
Inherent ranging demonstrated to better than 1/2 cm
New generation of SiGe chips under development

## Slide 15: Sources of Additional Information
www.time-domain.com
  IEEE papers by Prof. R.A. Scholtz, USC and others
  Time Domain papers
www.uwb.org
  Other UWB companies
  September Conference in Washington, DC