## Slide 1: Integration of Bluetooth into LAN Environments
Simon Baatz, Matthias Frank, Peter Martini
University of Bonn, Institute of Computer Science IV, Germany
E-Mail: {baatz, matthew, martini}@cs.uni-bonn.de

## Slide 2: Who are we?
Slide <number>
<footer>
<date/time>
Institute of Computer Science IV
University of Bonn
http://www.cs.uni-bonn.de/IV
Research on computer networks and distributed systems
Focus on IP based communication protocols
Bluetooth SIG member
  Current work on IP network layer mobility support for Bluetooth

## Slide 3: Bluetooth Usage Scenarios
GSM
BT
BT
BT
Data/Voice Access Points
Ad Hoc Networking
Cable Replacement

## Slide 4: Reminder: Bluetooth key characteristics
P
FHSS (Frequency Hopping Spread Spectrum)
  up to 1600 Hops/s
  79 channels in the 2.4 GHz ISM band (similar to 802.11 FHSS PHY)
MAC: Link Oriented TDMA Scheme
  Master: Defines hopping pattern
  Slaves: Synchronized with master
    Up to 7 simultaneous active slaves
    More in “Park” mode
Scatternets
  Devices can participate in several piconets
Piconet
P
Master
Slave
Parked Slave

## Slide 5: Reminder: Bluetooth key characteristics
Support for two Link Types:
  Synchronous Connection Oriented (SCO) (typically voice)
  Asynchronous Connectionless (ACL)
Link Setup
  Page Scan: Find device with known ID
  Inquire Scan: Find other radios in range
Sophisticated Power Management
Sniff
Hold
Park
Power efficiency

## Slide 6: Suitability for WPAN
Fulfills most of the functional requirements of the second WPAN Call For Proposals, e.g.:
  Use of unlicensed bands
  Low cost, low power, small size
  Range 0-10 meters
  Asynchronous and synchronous links, voice, QoS
Some need further examination:
    Coexistence with other wireless systems
    Bridge or gateway connectivity to other data networks
    Roaming between piconets
*
*
* covered in the following

## Slide 7: Is Handoff Support Needed?
BT is not designed as a cellular system
  No base station required
  No seamless handoff, Inquiry Scan can last for several seconds
But: Slow handoff is sufficient for many applications
  Stock-control palmtop moving around a warehouse
  Office usage: Prevent discontinuation of work due to room changes (log out off/log into network, need to close applications)
  Access to local/remote information in public places (airport terminal, department store, ...)

## Slide 8: Functionality Required for Handoff Support
AP
BT
BT
BT
BT
. . .
. . .
AP
BT
BT
Public Network
(Internet)
GW
Portal
Routing Updates
AP
Server
Path of Device
Session Information

## Slide 9: A Network Layer Solution: Cellular IP
Internet
Gateway
Router
BT Device
All packets coming from BT devices are routed to the gateway
Base Station
Base Station

## Slide 10: A Network Layer Solution: Cellular IP
Internet
Gateway
Router
BT Device
Base Station
Base Station
All packets coming from BT devices are routed to the gateway
Packets update the routing tables on their way to the gateway

## Slide 11: A Network Layer Solution: Cellular IP
Internet
Gateway
Router
BT Device
Base Station
Base Station
All packets coming from BT devices are routed to the gateway
Packets update the routing tables on their way to the gateway
Packets can be sent on multiple interfaces on their way down

## Slide 12: A Network Layer Solution: Cellular IP
Internet
Gateway
Router
BT Device
Base Station
Base Station
All packets coming from BT devices are routed to the gateway
Packets update the routing tables on their way to the gateway
Packets can be sent on multiple interfaces on their way down
Routes disappear if not updated regularly

## Slide 13: Access Points from a MAC Layer Perspective
802.11
Bluetooth
STA
STA
AP
Distribution System
To DS
From DS
Data
Poll/Data
Data
Distribution System
Master
Slaves
Header signaling communication through access points
Optional contention free periods
AP indicates to STAs in power save state that data is pending
Strict master/slave communication
Master has full control of medium access: QoS guarantees possible
Master can activate slaves in power save states if data is pending

## Slide 14: Possible Approaches for LAN Access
RADIO
BASEBAND
LINK MANAGER (LM)
(Connection state management, etc.)
AUDIO
LOGICAL LINK CONTROL (LLC)
(Segmentation, Reassembly, Multiplexing)
RFCOMM
(Serial Cable Emulation)
TCP/IP
Implement network layers with support for mobility
“Adaptation” protocol
Change LLC layer or add another protocol above LM
Bluetooth Master/Slave MAC
PPP
Standard PPP support
(Bluetooth profile for LAN access)
TCP/IP
...

## Slide 15: Comparison of the Approaches (1)
Already studied in some detail:

## Slide 16: Comparison of the Approaches (2)
Approaches with conceivable implications to an upcoming MAC & PHY standard:

## Slide 17: Summary and Open Questions
PPP over
virtual serial ports
Direct IP support
  Mobile IP
  Cellular IP
Direct support for a DS
  Bridge like
Seamless LAN integration
Open Questions:
  Which level of integration has to be achieved?
  Which aspects of LAN integration has 802.15 to deal with if Bluetooth becomes a candidate for standardization?