## Slide 1: IEEE 802.15 TG2 Coexistence Tel-Aviv January 13, 2000
Oren Eliezer
Texas Instruments Israel
OrenE@ti.com

## Slide 2: Definition
The realization and consideration of another wireless system in the shared environment of operation
Interoperability, in contrast

## Slide 3: A Measure of Coexistence
Reception Sensitivity Degradation in dB (additional dBs necessary to maintain the same reception quality in terms of BER or other link quality measure)
System Performance Degradation in throughput (in bits/second)
User perception of the damage is most important!

## Slide 4: Susceptibility to Interference
Different wireless applications have different sensitivities to interference (in terms of user perception of the link quality)
Various coexistence policies to suit the different needs

## Slide 5: Sources of Interference
Communication systems (in-band, out-of-band, etc.)
Non-communication systems (such as microwave ovens)

## Slide 6: Levels and Effects of RF Interference
Receiver front-end compression (saturation)
Blocking of the entire band or portions of it
3rd order intermodulation
Single channel jamming
Collisions without interference or with manageable interference

## Slide 7: Coexistence Scenarios
At least 4 units are involved
Symmetrical Interference
Non-symmetrical Interference
Various system layouts are possible resulting in different interference scenarios