## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Comment Resolution Discussion]
Date Submitted: [11 January 2000]
Source: [Tom Siep] Company [Texas Instruments]
Address [12500 TI Blvd, m/s 8723, Dallas, TX 75243, USA]
Voice:[214.480.6786], FAX: [972.761.5581], E-Mail:[Siep@ti.com]
Re: [P802.15/D0.6 Letter Ballot Commnets -99/172 & -99/173]
Abstract: [Items from Technical Comments on D0.6 that need to be discussed in TG1. On 10-11Jan00
the TG1 met and began resolution of the LB1 comments. The first and second pass were conducted very
fast and therefore we did not dwell on any one Technical Comment (T & t) this submission is therefore
just to capture the post cleanup on the Technical Comments during the Tel-Aviv session. ]
Purpose: [Consideration of response to author/disposition of comments]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Letter Ballot #1 Comment Resolution For Technical Comments (T,t) defined as “Discussion”
Tom Siep
siep@ti.com

## Slide 3: Comment Codes
Planned
  TG1 Concurs
Research
  TG1 needs to do more research
Discussion
  TG1 needs to discuss in more detail
Clarification
  TG1 will request more detail from the Author
BSIG Discussion
  TG1 needs to discuss the comment w/ BSIG
Decline
  TG1 declines the comment from the Author
Verify
  TG1 we need to review Bluetooth Specification(s) v1.0 B
Defer
  TG1 requires and Bluetooth has not determined need

## Slide 4: Comment Coding Summary for the “Discussion” definitions

## Slide 5: Golmie NG006
1.1 T Y [2nd paragraph]The sentence, “Coexistence is defined as the trait of reducing the amount of mutual degradation to the lowest degree feasible.”, is not appropriate, nor does it match the current one for 802.15 TG2
Delete this sentence.
Accepted, also delete sentence before this one.

## Slide 6: Shellhammer Sjs01
1.1 T Y The definition of coexistence that includes the phrase “reduce the amount of mutual degradation to the lowest degree feasible” may not make commercial sense and is clearly not implemented in the 802.15.1 standard. It could clearly be reduced more.
Change definition.
Definition will be deleted.

## Slide 7: Shellhammer Sjs06
5.4 T Y I think it is in appropriate to say that the WPAN uses circuit switched channels. I think a more accurate statement is that it uses connection-oriented packet-switched channels.
Rewrite
Concur. Redo to add connection-oriented and connectionless terms

## Slide 8: Alborzi hxa17
5.4.1 t N A unit can participate in more than one piconet. Hence it synchronizes to the piconet partially.
2nd paragraph, change “All units” to “All active units”
Decline

## Slide 9: Golmie NG057
5.4.2 t Y The statement “These are high capacity systems.” Is not true. A scatternet is made from individual piconets. The capacity is not aggregated in a piconet. In fact if interpiconet traffic is supported, it is a lower capacity than a single piconet
Delete this sentence.
Decline

## Slide 10: Alborzi hxa32
6.3.2.1 t N The pseudo random data pattern is not specified.
Specify one if possible.
decline

## Slide 11: Alborzi hxa34
6.3.2.1 t N Ambiguity in case of devices with power calss 1, and their transmit power in adjacent channels. FCC requires 20 dB less, and the standard requires less than –20dBm. Which one is correct?
Add the clause:“Adjacent channel Radiation of devices in power class 1 and 2 should comply with that of table 4”
Decline. The answer to the question is yes.

## Slide 12: Kinney pwk 15
6.4.5 T Y No spec defining the maximum signal strength before device destruction
Add a signal strength, eg +20 dBm, where, up to this value, no destruction will take place
BTSIG Discussion -- Pat K lead

## Slide 13: Heberling ADH01
7.2 T Y 4th Paragraph: The Bluetooth system consists of a radio unit, a link control unit, …Comment: Where is the link control unit specified? The link control unit is indirectly specified in various sections of Clause 7.2. However, it is not specified in one concise subclause as to what it’s functions are.
Consequently, I recommend that a subclause 7.2.x or clause 7.X be added to the current specification to rectify this short coming.
BT SIG Discussion -- Alan H. lead

## Slide 14: Heberling ADH02
7.2 T Y 4th Paragraph, 1rst sentence: The Bluetooth system consists of a radio unit, … and host terminal interface functions, … Comment: Where are the Host terminal functions specified? Do these correspond to the Host Controller Interface specification?
Either delete the reference to the <host terminal interface functions> or provide a Clause that describes what these functions are. Requires discussion in TG1 to decide
White paper Alan/Tom

## Slide 15: Alborzi hxa40
7.2 t N A master can be a slave in more than one piconet.
Change the sentence in last paragraph of the 7.2“In addition, a master in one piconet can be a slave in another piconet” to “In addition, a master in one piconet can be a slave in other piconets”
Decline: current text sufficiently describes system behavior

## Slide 16: Heberling ADH81
7.2.10.3 t N Page 92, 2nd sentence: The BlueTooth clock is derived from a free running native clock which is never adjusted and is never turned off.
Comment: So the BT clock is never turned off, even when power is turned off? Please clarify.
BT Discussion one page or less -- Alan H.

## Slide 17: Heberling ADH120
7.2.11.1 T Y Page 117, Figure 56 Hop selection scheme in CONNECTION state: Comments: Diagram needs to be more illustrative of what the text is trying to describe.
Please provide more graphical detail to better illustrate the Hop selection scheme.
Alan to re-review

## Slide 18: Golmie NG111
7.2.12.4.1 t Y [& 7.2.12.4.2]Refers to a website. What/which website?
List the URL and link to which it refers.
Research then go to BTSIG if necessary Ian to do research.

## Slide 19: Golmie NG112
7.2.12.4.2 T Y The term “64 ksamples/s” is not correct or is it? -- There are 8000 samples/second or -- 64,000 bits/second if samples equal 8 bits.
Need clarification from author -- Ian

## Slide 20: Alborzi hxa44
7.2.2.2 t N Mention the fact that in the worst case SCO links should be resynchronized before CLK27 switches back to its initial value at the time of SCO link establishment. This could be happen anytime between one half of cycle time to a full cycle time. (around 11 hours to 23 hours). Not doing so may result in interference with another SCO link.
Decline, implementation differentiator

## Slide 21: Golmie NG088
7.2.3.4.1.1 T Y The ID is not a packet as defined in this section. Make this distinction, so its placement and importance is clearly understood.
Add -- This ID packet is really not a packet as listed here, since it does not carry a packet header identifying it as one of the sixteen packet types. However, it carries information that is interpreted as a special type of packet received, which is acted upon similarly to true packets.
BT SIG discussion

## Slide 22: Golmie NG146
7.4.2.4 T Y Clause refers to HCI See previous comment on HCI
Do we include HCI in 802.15?
Alan/Tom to do white paper

## Slide 23: Golmie NG164
7.4.4.2 t Y HCI is again referenced
Alan/Tom to do white paper