## Slide 1: Intermec’s PicoLink WPAN
MAC Overview

## Slide 2
Initial Targeted Applications for PicoLink
Cable replacement (point to point)
  Barcode scanner to portable/mobile computer
  Printer to portable/mobile computer
Personal area connectivity (peer to peer)
  hand held computer to numerous peripheral devices including scanners, printers, wide area network radios, etc.
PEN*KEY 6500
Picking Application
Scan Item 000123456
Description: Tide Liq., 50oz.
Scan Location: BAY 31
Enter Quantity: 40
Take to Location: Dock 5A
Keyboard
Keypad
Help
Exit

## Slide 3
High Rate WPANs
Existing WPANs
Newly Targeted Applications

## Slide 4
WPAN Solution Requirements
Very low cost
Low power consumption
Small size
Minimal attach/detach times
Interference immunity
Ease of use
Standardized interfaces
Unlicensed, international usability

## Slide 5
PicoLink Concept
Complementary to WLAN/IEEE 802.11 devices
  some of the WLAN’s areas of performance have been sacrificed for cost/size/current drain
    reduced range, roaming is not optimum
Lower complexity than WLAN devices
  reduced RF specifications
  reduced MAC/PHY complexity
    this MAC has similarities to the 802.11 IBSS/adhoc
Features which do not add recurring costs
  peer to peer with up to 10 nodes per PAN

## Slide 6
Picolink Configurations
Personal
Area
Network
Infrastructured
Network
Access Point
PowerShip terminal
Astra Printer
DADS Terminal
EST
PowerPad
Ethernet

## Slide 7: Picolink Configurations
Personal
Area
Network
PowerShip terminal
Astra Printer
DADS Terminal
EST
PowerPad
Personal Area Network (PAN; Peer-to-Peer)
  Multiple Networks co-habitate (20 or more have been tested, but this attribute is dependent upon the PHY)
  Up to 10 devices in a single PAN
  Dynamic PAN and device IDs with network initiation
  Network maintained devices coming and going
  Temporary devices and NETWORKS also supported

## Slide 8
Picolink Configurations
Limited Infrastructured
Network
Access Point
Ethernet
Limited Infrastructured Network
  Main device (access point) typically has power at all times (for fast access)
  Support for up to 10 devices
  Ethernet access points with higher layer protocol

## Slide 9: MAC Protocol Criteria
Transparent to Upper Layer Protocols
Ease of Use
  Unique 48 bit address
  Simple network join/un-join procedure
  Device registration

## Slide 10: MAC Protocol Criteria
Delivered Data Throughput
  For the proposed aggregate rate of 22 Mbps a throughput of 14 Mbps is anticipated but depends upon the PHY (e.g. reducing Rx-Tx to 10µS increases throughput to 17Mbps with 2048 byte frames)
Fast Response
  Average response time for small packets is under 5 mS for current 1 Mbps system, projected to be less at higher data rate

## Slide 11: MAC Protocol Criteria
Data Transfer Types
  Asynchronous
    short response times
    CSMA/CA; collision sense/collision avoidance (very much like 802.11)
  Isochronous (we propose a timebounded service to provide a level of QoS although CSMA presents bandwidth limitation for Isochronous operation
  Mixed traffic load management

## Slide 12: MAC Protocol Criteria
Topology
  Minimum number of active connections
    Up to 10 nodes per network
  Ad hoc network
    Fully supported
    Temporal ad-hoc networks are also supported
  Access to portal
    Any node on the network can provide a portal to another network

## Slide 13: MAC Protocol Criteria
Reliability
  Master redundancy
    Any node on the network can assume the master(coordinator) role either by request from the master or by disappearance of the master
  Loss of connection
    The proposed system does provide a method for detection and recovering from the loss of a link
    System has options allowing it to conserve current drain by allowing periodic searches for link re-establishment rather than continuous searches

## Slide 14: MAC Protocol Criteria
Power Management Types
  Sleeping
    Multiple time increments for sleeping are selectable, e.g. 1,2…beacon periods
  Wakeup
    Schedule service intervals allow the MAC to adapt to various PHY wakeup times
  Polling
    Beacons are scheduled and allow the nodes to wakeup listen for any pending messages and then go back to sleep if there are no messages

## Slide 15: MAC Protocol Criteria
Power Consumption of MAC controller
  Transmit: 20 mA
  Receive: 30 mA
  Sleep: .3 mA
  Other Power Consumption Features
    programmable search duty cycle during loss of connect
    Slave to slave links require less energy in a Peer to Peer topology than a Master/Slave topology

## Slide 16: MAC Protocol Criteria
Security
  Authentication. Propose a modified Safer algorithm be used, as in Bluetooth
  Privacy. Propose the use of the Bluetooth algorithm
Quality of Service
  Will be a function of environment congestion

## Slide 17: MAC Protocol Criteria
Cost/Complexity
  Baseband controller
    functionality described for the HR MAC is estimated at 10,000 gates (6,000 gates w/o security), not including µP which has been quoted at 3k gates.
  Code size
    under 32 Kbytes (excluding security)