## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Supergold Encoding for High Rate WPAN Physical Layer ]
Date Submitted: [ 7 July 2000 ]
Source: [ T O’Farrell & L.E. Aguado] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 2332004 ], FAX: [ +44 113 2332032 ], E-Mail:[ enrique@supergold.com ]
Re: [ Physical layer modulation proposal for the IEEE P802.15.3 High Rate Wireless Personal Area Networks Standard.ref 00210P802.15]
Abstract: [ This contribution presents a coded modulation proposal for the physical layer part of the High Rate WPAN standard. This scheme is evaluated based on the Pugh criteria. ]
Purpose: [ Proposal for PHY part of IEEE P802.15.3 standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Supergold Communication
Supergold Communication is a campus start up company that specialises in solutions for wireless communications:
  Sequence Coded Modulation
  Sequence/Code Design
  Synchronisation

## Slide 3: Supergold Communication
By efficiently exploiting the distance properties of sequences/codes, Supergold’s solutions balance the trade-off between bandwidth efficiency, BER performance and complexity.
Supergold’s solutions can be beneficially applied in
  WPAN
  WLAN
  Wireless Infrared
  Cellular Mobile

## Slide 4: Sequence Coded Modulation for High Rate WPAN PHY
QPSK / OQPSK chip modulation  constant amplitude
M-ary symbol modulation
Single error correcting concatenated RS code
> 3 dB coding gain over QPSK @ 10-6 BER
High bandwidth efficiency: 22 Mbit/s in 25MHz bandwidth
Propose to operate in 2.4 GHz ISM band (can operate in 5 GHz band)

## Slide 5: Properties of the sequence coded modulation (cont.)
Based on pre-existing technology
  Feasible solution
  Short Development time
Works in the 2.4 GHz ISM band
  Cost effective
  Allows for 802.11 - 802.15.1 and 802.15.3 interoperability
Very low baseband complexity
Meets robustness criteria

## Slide 6: Channelisation of the 2.4 GHz ISM Band
Propose three 25 MHz channels in 2.4 GHz ISM band
Channel spacing 27 MHz
25 MHz
25 MHz
25 MHz
2400 MHz
2483.5 MHz
Channel 1
Channel 2
Channel 3
Transmit Spectrum Mask
0 dBr
-30 dBr
-50 dBr
Unfiltered sinx/x
2.4 GHz ISM band

## Slide 7: Example of Link Budget for Two-Ray Model
[based on: IEEE 802.15-00/050r1, Rick Roberts, Intersil]
Rx Noise Figure: 15 dB (inexpensive implementation)
Rx Noise Bandwidth: 25 MHz
Rx Noise Floor: -174+10*log(25*106)+15 = -85 dBm
Implementation Loss Margin: 4 dB
Antenna Gain: 0 dB

## Slide 8: Example of Link Budget for Two-Ray Model (Cont.)
Maximum Second Ray Delay: 25 ns
Maximum Second Ray Refflection Coefficient: -6 dB
Required Direct Ray Range: 10 m
Loss Equation (dB): L = 32.5+20log(dmeters)+20log(FGHz)
At 2.4 GHz, assuming the direct ray is blocked, the loss of the reflected ray path (17.4 m) is:
L = 32.5+24.8+7.6+6 = 70.9 dB (6 dB reflection coefficient)
Including antenna gain and implementation loss:
Total Loss Budget: L + 2*0 + 4 = 74.9 dB
Operating SNR is 10 dB for 10 -6 BER
Tx Power: Noise Floor + SNR + Loss = -85 dBm + 10 dB + 74.9 dB
Tx Power  0 dBm

## Slide 9: Evaluation of Criteria
Evaluation Methodology
  The proposal has been evaluated by the simulation of baseband models.
  Evaluations including the RF chain are pending

## Slide 10: General Solution Criteria
Unit Manufacturing Cost
  Similar architecture to IEEE 802.11
  Much simpler baseband processing than 802.11b
  Low power PA (0 dBm Tx Power)
  Similar to 802.15.1 equivalent UMC

## Slide 11: General Solution Criteria
Signal Robustness
Interference and Susceptibility
  Analysis based on co-channel interference simulation of multiple access and CW interference
  BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S (MAI) = -6 dB co-channel
    J/S (CW) = -7 dB co-channel
  Adjacent+1 channel power atenuation > 50 dB min.
  Interference protection > 40 dB

## Slide 12: General Solution Criteria
Interference and Susceptibility (cont.)
System performance in the presence of interference

## Slide 13: General Solution Criteria
Intermodulation Resistance:
  Evaluation including model of RF chain pending
  Results for interference resistance demonstrate robustness of the sequence coded modulation scheme
  In our model, a 2 KHz AM modulated 802.15.1 signal behaves like a CW interferer with (almost) constant level over a symbol period

## Slide 14: General Solution Criteria
Jamming Resistance
  For a CW interfererer operating in an uncoordinated manner
    BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S = -7 dB co-channel
  For an 802.15.3 connection operating in an uncoordinated manner
    BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S = -6 dB co-channel

## Slide 15: General Solution Criteria
Multiple Access/Coexistence
  Throughput measurements with coordinated same systems and uncoordinated dissimilar systems requires
    software test-bed to model PHY and MAC protocols
    hardware test-bed to measure in real environments
  Implementation of test-beds pending
  TBA by group

## Slide 16: General Solution Criteria
Interoperability
  Dual mode terminal would be required for interoperability with 802.15.1, working at 2.4 GHz, low added cost.
  Common channelisation supports interoperability with 802.11

## Slide 17: General Solution Criteria
Technical Feasibility
Manufactureability
  System architecture utilises pre-existing IEEE 802.11b technology
  Baseband processing functionality similar to existing applications.
Time to Market
  Pre-existence of technology will ensure short development cycle
  Only PHY part proposed
  Date: 1Q2002

## Slide 18: General Solution Criteria
Regulatory Impact
  The proposed scheme is compliant with regulatory standards
Maturity of Solution
  The system technology utilises existing 802.11b technology
  Underlying modulation is constant amplitude QPSK
  Baseband processing less complicated than CCK
  Baseband scheme tested in a general purpose hardware demonstrator

## Slide 19: General Solution Criteria
Scalability
Power Consumption
  AGC would be used to control transmit power
Data Rate
  Throughput can be reduced by increasing the level of coding while enhancing the link quality
Frequency Band of Operation
  This modulation scheme can be applied at both 2.4 GHz and 5 GHz
Cost
  Changing the level of coding would not impact on the unit cost
Function
  Equalisation could be introduced in the scheme to enhance resistance to time dispersive channels - not proposed

## Slide 20: PHY Layer Criteria
Size and Form Factor
  A less complex solution than 802.11:
    Simpler baseband processing
    No legacy modulation implementation
    No equalisation
    802.15.1-type MAC
    Low power PA
  Estimated one or two chip implementation

## Slide 21: PHY Layer Criteria
MAC/PHY Throughput
Minimum MAC/PHY Throughput
  Offered data rate: 22 Mbit/s, 21.65 Mbit/s with enhanced coding
  MAC overhead allowance: 10%, 8.25% with enhanced coding
  Offered MAC/PHY thoughput = 20 Mbit/s
High End MAC/PHY Throughput
  One throughput level is offered

## Slide 22: PHY Layer Criteria
Frequency Band
  This proposal is addressed to the 2.4 GHz ISM band, but would also be applicable to the 5GHz ISM band.
Number of Simultaneously Operating Full Throughput PANs
  The IEEE 802.11 channelisation is adopted
  Up to 3 co-located networks could share the 2.4 GHz ISM band with no co-channel interference
  Up to 5 co-located networks could share the 5 GHz ISM band with no co-channel interference
Range
  For 0 dBm Tx. Power, range > 10 m (for link budget presented)

## Slide 23: PHY Layer Criteria
Sensitivity
BER v. Eb/N0 Performance in the AWGN channel

## Slide 24: PHY Layer Criteria
Sensitivity
BER v. SNR Performance in the AWGN channel

## Slide 25: PHY Layer Criteria
Sensitivity
PER v. SNR Performance in the AWGN channel

## Slide 26: PHY Layer Criteria
Delay Spread Tolerance
  The BER criterion = 10-3 is met for TRMS = 25 ns with no equalisation
  The addition of equalisation would allow longer delay spreads
System Performance in the multipath channel for TRMS = 25 ns

## Slide 27: PHY Layer Criteria
Power Consumption
  Low transmitted power
  Low implementation complexity
   Low power consumption
  Power consumption should be below 0.5 Watts

## Slide 28: Pugh Matrix - General Solution Criteria

## Slide 29: Pugh Matrix - General Solution Criteria

## Slide 30: Pugh Matrix - PHY Layer Criteria

## Slide 31: Pugh Matrix - PHY Layer Criteria