## Slide 2
System Overview of HiperLAN Type 2
Jamshid Khun-Jush
Chairman of ETSI Project BRAN
Ericsson Eurolab Deutschland - Nürnberg
A Presentation to
The Plenary of IEEE 802.15 Working Group
July 12, 2000, San Diego
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3: Agenda
Wireless “Data” Solutions
HiperLAN/2
  Requirements
  Spectrum Allocation
  Operation Modes
  Application Scenarios
  Protocol Architecture
    Convergence Layer
    DLC
    PHY
  Security
Conclusions

## Slide 4: Wireless “Data” Solutions
Mbps
1
10
100
0,1
Outdoor
Stationary
Walk
Vehicle
Indoor
Stationary/ Desktop
Walk
Mobility
HiperLAN/2
IEEE802.11a
User Bitrates
LAN
3G
cellular
Bluetooth
2G cellular
Wide Area Network (WAN)
-Large coverage
-High cost
Personal Area Network (PAN)
- Connectivity
- Cable replacement
-Low cost
Local Area Network/Access
-Hot Spots
- High speed
- Moderate cost
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Requirements - 1
Core network independent with QoS support for real time services (VoIP, Video)
  Support of IP transporting networks, ATM networks, 3rd Generation, Firewire, etc.
  Packet network based on connection-oriented wireless link
Radio access network specifications (physical layer, data link control layer and convergence layer)
  Interoperability standard with conformance test specifications
No frequency planning
  Dynamic Frequency Selection
Capable of handling different interference and propagation situations
  “Link Adaptation” with multiple modulation and channel coding schemes Supporting asymmetrical traffic load fluctuating in uplink and downlink as well as for different users
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Requirements - 2
A cellular multi-cell radio network capable of offering access, switching and management functions within a large coverage area
  A point-to-multipoint topology with mandatory centralized mode and optional direct mode
  Mobility management
  Power management
    Uplink power control, downlink power setting, sleep mode
Usage in indoor and outdoor environments
Multicast and broadcast
Scalable security
  Different key encryption: 56 bit and 168 bit
  Authentication: Optional pre-shared or public key

## Slide 7: Spectrum Allocation at 5 GHz
US
Japan
Europe
Hiperlan
U-NII
U-NII
5200
5400
5600
5800
5100
5300
5500
5700
High Speed Wireless Access
5.15 - 5.35
5.15 - 5.35
5.725 -5.825
5.470 - 5.725
Hiperlan
5.15 - 5.25
Unlicensed
300 MHz
Licensed exempt
455 MHz
100 MHz
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Operation Modes
Infrastructure based network:
Ad-hoc network:
No compromise on QoS in ad-hoc mode!
Fixed network
AP - AP Mobility (link level)
Access Point (AP)
Mobile Terminal (MT)

## Slide 9: Application Scenarios
SGSN
GGSN
IWU
Office
ISP
Home
GPRS/UMTS
Ethernet
Internet
HIPERLAN/2
HIPERLAN/2
HIPERLAN/2
HIPERLAN/2
On the move
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Protocol Architecture
Standardization scope: air interface, service interfaces of the radio access system and the convergence layer functions

## Slide 11: Convergence Layer
Segmentation and re-assembly to / from 48 bytes packets
Priority mapping from IEEE 802.1p
Address mapping from IEEE 802
Multicast & broadcast handling
Flexible amount of QoS classes
Multiple convergence layers
One single convergence layer active at a time
Mapping between higher layer connections/priorities and DLC connections/priorities
Cell based
ATM
CP
Packet based
PPP
Firewire
Ethernet
UMTS
Common Part (CP)
Service Specific
Part
Mapping higher layer
packets onto layers of
HiperLAN/2
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: DLC: Medium Access Control - 1
TDMA/TDD with a fixed frame duration of 2 ms
3 transmission possibilities: AP to MT (Downlink), MT to AP (Uplink) and MT to MT (Direct Link)
Centralized scheduling (not specified)
  Air interface frame creation in the AP
  Resource allocation by the AP
  Resource requests from MTs
  Dynamic assignment of capacity in uplink and downlink - no fixed slot structure is mandatory, but possible for CBR type services
  Could consider QoS and link adaptation modes
  Transmission of Data PDU and ARQ PDU without collisions
Peer-to-peer and multicast support
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: DLC: Medium Access Control - 2
Random access scheme
  Association and resource request transmissions from MTs
  Random access in mobile stations: slotted ALOHA with exponential increase of contention window
  Processing random access in the AP: acknowledgements of random access in the next frame
Sector antenna support

## Slide 14: MAC Frame Channels: Logical Channel - 1
Logical and Transport channels are used to construct MAC frame
Logical Channel:
  A generic term for any distinct data path which describes a specific data transfer service offered by the MAC entity
  Defined by the type of information it carries and the interpretation of the value in the corresponding messages
Some important Logical Channels
  BCCH (Broadcast Control CHannel): used in downlink conveying the necessary broadcast information concerning the whole radio cell e.g. scrambler seed, access point ID, network ID, etc.
  FCCH (Frame Control CHannel): used in downlink conveying information describing the structure of the MAC frame visible at the air interface (resource grant announcement)
  RACH (Random Access CHannel): used by MTs in uplink to send signalling data (resource request, association request) for DLC or RLC.

## Slide 15: MAC Frame Channels: Logical Channel - 2
Some important Logical Channesl: Contd
  RFCH (Random access Feedback CHannel): used in downlink to inform the MTs that have used the RACH in the previous MAC frame about the result of their access attempts.
  RBCH (RLC Broadcast CHannel): used in downlink (when necessary) conveying broadcast CONTROL information concerning the whole radio cell, e.g. broadcast RLC message, MAC ID in the association process, encryption seed, etc.
  DCCH (Dedicated Control Channel): used in downlink, direct link and uplink conveying RLC messages
  LCCH (Link Control CHannel): used bi-directional to transmit ARQ and discard messages between peer error control functions
  UDCH (User Data CHannel): used bi-directional to transmit user data

## Slide 16: MAC Frame Channels: Transport Channel
Logical channels are mapped onto different transport channels which describe the basic message format and are the basic elements for constructing message sequence of each user
  BCH (Broadcast CHannel): carries BCCH transmitted once per MAC frame per sector antenna
  FCH (Frame CHannel): used in downlink for carring FCCH with variable amount of data
  ACH (Access feedback CHannel): used in downlink for transporting RFCH
  LCH (Long Transport CHannel): used for transporting user data and control information
  SCH (Short CHannel): used for transporting short control information
  RCH (Random CHannel): used in uplink for transmitting resource request or association request

## Slide 17: Mapping between Logical and Transport Channels
Downlink
Uplink

## Slide 18: Basic MAC Frame Structure
A single sector system
A multiple sectors system

## Slide 19: DLC: Error Control
Scaleable Error Control: three EC modes
  Acknowledged mode for reliable transmission by using ARQ
  Repetition mode for reliable transmission by repeating LCHs
  Unacknowledged mode for transmissions with low latency
SR-ARQ with partial bitmap
  retransmission efficiency as conventional SR
  Optimized overhead and delay for acknowledgements
    acknowledgements are sent not for every erroneous packet but a bitmap for several ones
    Dynamical management of bitmap packets
    Cumulative Acknowledgement and Flow Control possible
  Discarding capability
    efficient for real time applications
Short MAC frame (2 ms) allows re-transmission even for voice

## Slide 20: Partial Bitmap Basics
Numbering of PDU from 0 to 1023 (Sequence Number)
Grouping 8 PDUs into 1 Block, totally 127 Blocks
ACK of a PDU: BitMap Block (BMB) & BitMap Number (BMN)
In the ARQ C-PDU: 3 BMBs & 3 BMNs
BMN1=Block_Id1, BMN2=Block_Id1 - Block_Id2, BMN3=Block_Id3 - Block_Id2

## Slide 21: Dynamic Acknowledgement
Problems with fixed ACK
  low utilisation of channel capacity
  bottleneck of feedback channel
  deferring retransmissions
Dynamic ACK
  # of ARQ PDUs based on receiver status
  ABIR-bit used by receiver in MT
  high utilisation of channel capacity

## Slide 22: Link Adaptation
Link Adaptation
  Code rate and modulation alphabet (7 modes) adaptive to current propagation and interference environments
Link throughput versus C/I
  Link quality measurements (C/I) in access point and mobile terminal
  rms delay spread 100 ns
  Selective-repeat ARQ,
  ideal link adaptation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 23: DLC: Radio Link Control
Connection handling
  Setup / release of DLC connections
  Peer-to-peer (ad-hoc)
  Multicast
Security
  Authentication
  Encryption key distribution
  Alternative security negotiation
Management functions
  Mobility
    Association / de-association
    Handover
    Location update
  Radio resource management
    Dynamic frequency selection
  Power management
    Sleep mode
    uplink and downlink power control
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 24: HIPERLAN2 & 802.11a PHY - Key Parameters
Multi-carrier modulation by OFDM
Punctured convolutional
code, based on
rate-1/2 code, constraint length 7
Intra-symbol bit interleaving
Block size depends on the sub-carrier modulation
Channel spacing 20 MHz
Cyclic prefix 800 ns (optional 400 ns only in HIPERLAN/2)
Possible delay spread (at least) 250 ns
48 (data) + 4 (pilot) sub-carriers
PSK/QAM (coherent)
Convolutional Code
Interleaving
OFDM Modulation
Scrambler
A length-127
scrambler with
generator
polynomial S(x)=x7+ x4+1

## Slide 25
Physical Layer Modes
Main difference between 802.11a and HIPERLAN/2: Preamble due to different multiple access scheme
Several physical layer modes are provided
  Link adaptation selects the “most appropriate” mode.
Physical layer modes of HIPERLAN/2 & IEEE 802.11a:
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 26: OFDM Modulation
Mapping
Serial
to
parallel
converter
Multiplex
ej2fot
ej2f1t
ej2fN-1t
ej2fN-2t
x(t)
{d}
{Dq,l}
{Dq,o}
{Dq,N-1}
f
20 MHz
4 pilot carriers
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 27: Security Overview
Corporate
network
Authentication & encryption in public access
Authentication & encryption
Wired equivalency
Sufficient in business, residential and public access environments
Supports negotiation of different security levels including:
  encryption (data confidentiality) and authentication (user confidentiality)
Supports mobility (HO)
Low/moderate processing overhead
Exportable
Internet
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28: Security Features
Mobile identity protection
Restricted to the radio access system
  High level security not provided, e.g. user authentication through the Internet to corporate network Link level encryption
  unicast, multicast, broadcast
  for both user data and signaling
  56 bit and 168 bit key encryption based on DES
Mutual authentication based on challenge/response
  Optional pre-shared key or public key
Token based handover authentication
Key generation based on Diffie-Hellman exchange
Regular key refresh
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 29: Principals of HiperLAN/2 Ad-hoc Networking - I
Case 2: two CC-capable WTs are switched on at the same time
WT1
WT2
No beacon detected
start probing
No beacon detected
start probing
Collision Resolution
I am the CC
I am a WT
I am the CC
Case 1: one CC-capable WT is switched on first
WT
CC: Central Controller
Network creation

## Slide 30: Principals of HiperLAN/2 Ad-hoc Networking - II
WT
ASSOCIATE(random No) @ random access
Authentication (user profile, etc)
ASSOCIATE_ACK (MAC_ID, random No) @ broadcast
dedicated control channel (DCCH) established
Beacon every 2 ms
CC
Terminal association

## Slide 31: Principals of HiperLAN/2 Ad-hoc Networking - III
WT2
WT1
SETUP (descriptor) @ DCCH
CONNECT (DLCC-ID) @ DCCH
SETUP_ACK (DLCC-ID) @ DCCH
CC
CONNECT_ACK (DLCC-ID) @ DCCH
CONNECT_ACK (DLCC-ID) @ DCCH
CONNECT_COMPLETE @ DCCH
Connection setup

## Slide 32: Principals of HiperLAN/2 Ad-hoc Networking - IV
CC
WT1
WT2
Broadcast
Downlink
Direct Link
Uplink
Random Access
Resource Request (DLCC-ID, #Slots)
Resource Grant
(DLCC-ID, #Slots, Pointer)
Fixed Slot Allocation
Resource request & resource grant

## Slide 33: CC Responsibility Handover Principal
WT1
Old CC
„You are my successor!“
- No new resource grant
- Fixed slot allocation remains
„Take my database!“
„Generate next MAC frame!“
WT2
New CC

## Slide 34: Conclusions
HiperLAN/2 for Emerging Nomadic Computing
  Scalable User Security
  Wireless LAN and Wireless Access
  Mobile Datacom
    up to 54 Mbps
    Mobility
    Quality of Service
  Environments
    Home
    Office
    Public
  Network Topology
    Infrastructure based networks
    “Ad-hoc” networks

## Slide 35: HiperLAN/2 as WPAN: Some Questions
Which services and user scenarios are envisioned for WPAN in 5 GHz?
can the envisioned services/scenarios be accommodated with HIPERLAN/2?
  E.g. can HIPERLAN/2 support “ad-hoc connectivity”?
Is HIPERLAN/2 “cost-effective” (compared to Bluetooth technology) for such applications?
If not, can a low-cost mode in HIPERLAN/2 be defined?
What are the regulatory issues/problems?
  E.g. could WPAN in 5 GHz jeopardize the current regulatory activities in relation to MSS?
…?

## Slide 36: BRAN Information
HiperLAN/2 Technical Specifications
  Free of charge @ http://www.etsi.org/bran (click on work items)
    PHY: ts_101475v010101
    DLC (basic functions): ts_10176101v010101
    RLC: ts_10176102v010101
    Packet based CL Common Part: ts_10149301v010101
    Packet based CL Ethernet part: ts_10149302v010101
    Cell based CL Common Part: ts_10176301v010101
    Cell based CL UNI Part: ts_10176302v010101
Contacts:
  jamshid.khun-jush@eed.ericsson.se (BRAN Chair & HiperLAN2 Coordinator)