## Slide 1: Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANS)
Submission Title: [Proposal to Add Location Awareness as an Important New Criteria]
Date Submitted: [July 7, 2000]
Source: [Martin Rofheart] Company [XtremeSpectrum] Address [7501 Greenway Center Drive, Suite 760, Greenbelt, MD 20770-3514] Voice [(301) 614-1324], Fax [(301) 614-1327], E-mail [martin@xtremespectrum.com]
Re: [TG3 Call For Proposals]
Abstract: [Location awareness as a WPAN attribute]
Purpose: [for July 2000 plenary]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual or organization. The material in this document is subject to change in form and content after further study. The contributor reserves the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Presented by: Martin Rofheart
(301) 614-1324
martin@xtremespectrum.com
Proposal for Location Awareness
as a WPAN Criteria
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3: Objectives
In response to invitation for new criteria in final call for proposals
  “If the Task Group agrees to a criteria, it can be added to the criteria list for general consideration. This allows learning and improvement of the overall proposal.”
Review of location awareness problem in WPAN
Location is a fundamental and important property of WPAN
  Location is a primary differentiator from WLAN
  It should be incorporated in the WPAN evaluation documents
Proposal
  Definition & value into TG3 Criteria Definitions document (# 00/110)
    Part of General Solution—allow proposers to address as PHY or MAC
  Comparison values -/same/+ values into Pugh Matrix Comparison doc
  Weighting for the Location Awareness Criteria
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Review of Location Awareness Problem in WPAN
Statement of Problem
  Need to wirelessly communicate between two (or many) users in a crowd
    Handheld devices, kiosks, etc.
  Do not want configuration, passwords, PINs, typing etc.
    This is similar to ‘business card beaming’ with personal data assistants
    want to do this with multimedia data types like digital still images, MP3 files etc.
    Just point and shoot
  Goal is simplification/ease of use for device registration
    As a function of relative location of transceivers
  Also want to locate users in office, factory & home
Two users wish to communicate
without involving others nearby
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Proposed Definition and Value For TG3 Criteria Definitions Document
In General Solution section
  Allows for the greatest diversity from proposals
Location Awareness
  Definition
    Location awareness is the ability to determine information about the relative location of one transceiver with respect to another. This data can be used to locate, identify and discriminate amongst users in crowded environments and to simplify device registration in constantly changing piconets. In a WPAN environment with 10m range, location resolution on the order of 10 centimeters is required to do this. Provisions must be made to propagate location information to higher layers of the stack.
  Values
    Resolution in centimeters of the proposed location method
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Proposed Definition and Value For TG3 Criteria Definitions Document
In General Solution section
  Allows for the greatest diversity from proposals
Location Awareness
  Definition
    Location awareness is the ability to determine information about the relative location of one transceiver with respect to another. The purpose is to improve usability of portable devices. This data can be used to locate, identify and discriminate amongst users in crowded environments and to simplify device registration in constantly changing network topology. Provisions must be made to propagate location information to higher layers of the stack.
  Values
    Resolution in centimeters of the proposed location method
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: Comparison Values for Pugh Matrix Comparison Document
CRITERIA
REF.
Comparison Values
-
Same
+
Location Awareness
False
True
Technical requirement
  WPAN has 10m range
  In order to adequately differentiate individual users, resolution on the order of 10 centimeters is required is required from the proposed method to bring best value.
Proposed Pugh Matrix values

## Slide 8: Weighting for Location Awareness Criteria
Location awareness is a fundamental WPAN attribute and differentiator from WLAN
Top weightings from first pass vote without location awareness
Unit Manufacturing Cost | 9.7
Coexistence | 8.9
Interoperability BT 1.0 | 7.2
High end MAC Mbps | 6.1
Power consumption | 5.9
MAC/PHY interface Mbps | 4.6
Sensitivity | 4.2
Time to Market | 3.7
Jamming Resistance | 3.5
Some choices for setting and applying weight
  Determine ranking by vote
  Apply rank as extra credit for proposals meeting the criteria
  Apply scale to previous weights if maintaining 100 point count matters
  Other choices?