## Slide 1: Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANS)
Submission Title: [XtremeSpectrum Multimedia WPAN PHY]
Date Submitted: [July 7, 2000]
Source: [Martin Rofheart] Company [XtremeSpectrum Inc.] Address [7501 Greenway Center Drive, Suite 760, Greenbelt, MD 20770-3514] Voice [(301) 614-1324], Fax [(301) 614-1327], E-mail [martin@xtremespectrum.com]
Re: [TG3 Call For Proposals]
Abstract: [Multimedia data rate ultrawideband WPAN]
Purpose: [for July 2000 plenary]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual or organization. The material in this document is subject to change in form and content after further study. The contributor reserves the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: XtremeSpectrum, Inc. An Ultrawideband Technology Company
Presented by: John McCorkle
(301) 614-1325
martin@xtremespectrum.com
Multimedia WPAN PHY Proposal
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3: Objectives
Describe XtremeSpectrum PHY solution
Propose ranging as an important new criteria
  Range based authentication
  Allows applications to select the closest transceiver as default
    More sophisticated applications can be built beyond the default—e.g. everyone around a conference table—better than IrDA beaming
    Secure algorithms based on range information
  Enables multimedia radio abstractions of ‘business card beaming’ used in personal data assistants (PDA’s)
  Allows the exchange of digital still images, MP3 files, digital video clips between two devices without involving other nearby parties
  IrDA ports can do this because of range and angle limits
    But lack data rate & have angle of orientation and line of sight limitations
  Narrowband RF is problematic because it propagates everywhere & cannot differentiate between users based on position or range
  Allows protocols to transfer digital still images, MP3 files, digital video clips etc. from one handheld device to another in crowded environments without other parties being involved—either selectively or securely
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Technology Description
Extreme spread spectrum radio
Baseband direct sequence spread spectrum
Coded biphase modulated wavelets
Wavelets formed from the edges of gates
  Bandwidth comes from the rise time of the IC process
  Moore’s law radio—channel capacity grows linearly with IC process
  Matches radio to processing, memory, storage & resolution roadmaps
Similar to unintentional emissions from digital devices
High chip rate (GHz) easy to do in silicon & maps to interop w/ BT
Low peak to average waveform easy to do in low-voltage silicon
Provides ultrawideband-RF inbuilding propagation benefits
Crystal
Crystal
Bits
Bits
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Technical Benefits of Biphase Modulated Ultrawideband RF
See our tutorial presented at the March Plenary
  Document 00082r1P802-15_WG-UWB-Tutorial-1-XtremeSpectrum
Multipath fading immune & best penetration for a given BW
  Result of large relative bandwidth (UWB scattering/propagation Physics)
Low order modulation + High Data Rate ==> low cost & power
  Result of large absolute bandwidth (Shannon)
Biphase modulation is superior to time-hopping (PPM)
  Advantage of 3-6dB depending on optimizations – multipath free chan
  Multipath is in-band interference (data modulation) to PPM
Ranging and fine spatial resolution
  Result of large absolute bandwidth
  Enables positioning and ‘beaming’ in applications
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Physics of UWB scattering - Multipath Fading Immunity Benefits
Frequency (MHz)
Deep
Fade
Fading immunity means channel model closely follows R2 rather than R3.5 or R4
Leads to robust in-building operation
Bottom chart shows actual signal strength measured in a typical office environment (blue) along with reference R3.5 (red) and R2 (green) traces
Narrowband systems can confuse multipath with attenuation
The two top charts are time & frequency duals
Wide bandwidth means signal and correlator outputs can be short in time
Result is that multipath components can be separately resolved
Each component can have full bandwidth
Time (nanoseconds)
1
0
-1
-1.5
-1
-.5
0
.5
1
1.5
2
2.5
3
Path-2
Path-1
Range (feet)
Multipath fading immune Exceeds specified delay spread
Reduces Required Link Budget
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: Technical Benefits of Biphase Modulated Ultrawideband RF
See our tutorial presented at the March Plenary
  Document 00082r1P802-15_WG-UWB-Tutorial-1-XtremeSpectrum
Multipath fading immune & best penetration for a given BW
  Result of large relative bandwidth (UWB scattering/propagation Physics)
Low order modulation + High Data Rate ==> low cost & power
  Result of large absolute bandwidth (Shannon)
Biphase modulation is superior to time-hopping (PPM)
  Advantage of 3-6dB depending on optimizations – multipath free chan
  Multipath is in-band interference (data modulation) to PPM
Ranging and fine spatial resolution
  Result of large absolute bandwidth
  Enables positioning and ‘beaming’ in applications
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Information Theory Benefits
High order modulation requires high SNR and allows the data rate capacity C, to go above the channel bandwidth B, BUT… trades at an unfavorable log function with power.
Shannon’s Equation
Large BW  high capacity with low order modulation & low power
Data rate is proportional channel bandwidth B
Bandwidth comes from IC process in the proposed solution
Moore’s Law Radio
Low order modulation and B>>C linearly trades data-rate for range or power –plus it allows software to easily control the integration that pushes bandwidth into the SNR
Regulatory limits provide
for UWB
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Technical Benefits of Biphase Modulated Ultrawideband RF
See our tutorial presented at the March Plenary
  Document 00082r1P802-15_WG-UWB-Tutorial-1-XtremeSpectrum
Multipath fading immune & best penetration for a given BW
  Result of large relative bandwidth (UWB scattering/propagation Physics)
Low order modulation + High Data Rate ==> low cost & power
  Result of large absolute bandwidth (Shannon)
Biphase modulation is superior to time-hopping (PPM)
  Advantage of 3-6dB depending on optimizations – multipath free chan
  Multipath is in-band interference (data modulation) to PPM
Ranging and fine spatial resolution
  Result of large absolute bandwidth
  Enables positioning and ‘beaming’ in applications
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Biphase Modulation Advantage Over Time-Hopping
Biphase modulation has 3-6dB advantage over PPM (time-hopping) depending on optimizations
Greater advantage in multipath since multipath appears as data modulation in PPM
Biphase modulation exhibits a peak-power to average-power ratio of less than 3 (a sine wave is 2)
Low peak to average leads to efficient transmitters and a natural fit to low cost, low voltage IC’s
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: Basic System Blocks
LNA Filter
X
A/D
Filter
PHY
MAC
Synthesizer
OSC
Wavelet Generator
DLL sliding correlator structure
Shared resources UWB and Bluetooth
Frequency of operation
  From 2 GHz to 6 GHz
  Measured 12dB down points from Class B unintentional radiator limits
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: Summary of Solution
Biphase modulated baseband wavelets (ultrawideband RF)
Unit manufacture cost 30-50% greater than BT1.0 standalone
Coexistence 20dB less interference than BT or 802.11b to each other
Bluetooth 1.0 integrated & interoperable solution
Data rate scalable 1-100 Mbps (BER 10-5 10m 100Mbps no FEC)
Power consumption roadmap to ~30mW (3Q02)
Jamming resistance current demonstration >60dB
Multipath fading immune
Time to market—samples ICs 2Q01, limited qty 3Q00, production 4Q01
Maturity of solution
  Current operational 50Mbps discrete component system & IC
Form factor smaller than Compact Flash – 2 IC then 1 IC
Ranging enables multimedia beaming and position location
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: Bluetooth Interoperability & Unit Manufacturing Cost
Integrated and interoperable with Bluetooth
Low peak to average ratio & high chip rate wavelets allows
  Shared analog structures
  LNA, Frequency Synthesizer, mixers, A/D
Shared digital structures
  Partial reuse of PHY layer
  Large reuse of MAC layer from potentially small mods to Bluetooth MAC layer to support high rate
Cost for interoperability is ~30% increase in die size
Solution is Bluetooth/802.15.1 interoperable
Solution UMC is ~30% premium to Bluetooth/802.15.1 alone
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14: Coexistence Analysis
Victim
Transmitter
3
XtremeSpectrum
Transmitter
2
Victim
Receiver
1
Rv
Rx
P12
P13
Pv
Px
Isotropic Antenna on Victim System
Coexistence is 100% for 802.15.1/Bluetooth, 802.11b and 802.11a
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: Coexistence with Bluetooth
The XtremeSpectrum radio does not change the net throughput of a Bluetooth receiver located 3 meters away
  For a pair of Bluetooth radios separated by 10 meters, the received Bluetooth signal power is 42.8 dB larger than the received UWB power
    The XtremeSpectrum radio is 12 dB below Class B limits at 2.4 GHz
There is no detectable change in the net throughput
BER of Bluetooth radio in the absence of XSI radio | BER of Bluetooth radio when an XSI transmitter is 3 meters away
1e-3 | 1.003e-3
1e-9 | 1.035e-9
1e-12 | 1.068e-12
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 16: Coexistence with 802.11b
The XtremeSpectrum radio does not change the net throughput of an 802.11b receiver located 3 meters away
  For a pair of 802.11b radios separated by 100 meters, the received 802.11b signal power is 29.78 dB larger than the received UWB power
  For a pair of 802.11b radios separated by 50 meters, the received 802.11b signal power is 35.8 dB larger than the received UWB power
There is no detectable change in the net throughput in either case
BER of 802.11b receiver in the absence of XSI radio | BER of 802.11b radio communicating at 100 meters when an XSI transmitter is 3 meters away | BER of 802.11b radio communicating at 50 meters when an XSI transmitter is 3 meters away
1e-3 | 1.05e-3 | 1.01e-3
1e-9 | 1.96e-9 | 1.19e-9
1e-12 | 3.48e-12 | 1.38e-12
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Coexistence with 802.11a
The XtremeSpectrum Radio does not change the net throughput of an 802.11a receiver located 3 meters away
  For a pair of 802.11a radios separated by 50 meters, the received 802.11a signal power is 29.8 dB larger than the received UWB power
There is no detectable change in the net throughput
BER of 802.11a radio in the absence of XSI radio | BER of 802.11a radio when an XSI transmitter is 3 meters away
1e-3 | 1.05e-3
1e-9 | 1.95e-9
1e-12 | 1.46e-12
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: Regulatory Impact & Frequency Band
Low power operation—at or below Class B unintentional limits
  Superior coexistence results from gentle underlay of the spectrum
  Requires rules change to do this intentionally
Part 15 rules change for FCC is underway (docket 98-153)
  By definition unlicensed frequency bands (subject to rules)
  3Q 1998 NOI (Notice of Inquiry)
  2Q 2000 NPRM (Notice of Proposed Rule Making)
  2Q 2001 RO (Report & Order) – Expected
NPRM postulates Class B emissions with 12dB roll-off below 2GHz
International regulatory efforts are underway
Unlicensed
Currently at NPRM stage with FCC (98-153)
International efforts are underway
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: Power Consumption Roadmap
Notes
  Digital functions include baseband, PHY and MAC. MAC is assumed 802.15.1 modified to support high rate
  Analog/RF functions with SiGe .35/.8u BiCMOS 1Q01 and .25/.25u 1Q02
  Digital IC with .18u Bulk CMOS 1Q01 and SOI CMOS 1Q02
  Die reduction and power optimization in 3Q01 and 3Q02
 | 1Q01 | 3Q01 | 1Q02 | 3Q02
Analog/RF | 83mW | 66mW | 22mW | 18mW
Digital | 60mW | 48mW | 16mW | 13mW
Total | 143mW | 114mW | 38mW | 31mW
Power consumption with PHY and MAC is much less than 500mW
• • •
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 20: Sensitivity
Not a meaningful parameter because
  Interference dominates
    Multipath/clutter limited
    Other RF signals
  Depends on bandwidth
Customer wants
  In real home/office environments, not outside in the clear
  Goodness measure
    Battery Life X Range2 X Data Rate X log(1/BER) = Goodness
Radio sensitivity is < 108dBm/MHz
Exceeds specified target
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21: Data Rate, Range and Scalability of Solution
Data rate scalable 1-100Mbps
  2 Decades of bandwidth allow applications unprecedented control of performance envelope (method is increased code length)
    Data rate throttles BER, power consumption and range
Range can scale to exceed 10m
  Range=10m with BER=10-5 & rate=100Mbps & margin=10dB & no FEC
  Range can increase for decreased data rate
Power consumption drops with data rate
Cost can be reduced by reducing bandwidth (frequency band)
  Results in decreased range at a given data rate
Functionality can scale
  Removing interoperability constraint reduces cost 30%
Solution exceeds minimum and maximum throughput specifications
Solution scales in data rate, power, range, BW (freq), cost & function
Solution exceeds range specification
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 22: Maturity, Manufacturability & Time to Market

## Slide 23: Maturity, Manufacturability & Time to Market
Maturity of solution
  Though new here, Technology proven in DoD (see doc # 00082r1)
  Operational discrete component systems
  Current is 50Mbps, 10-5 BER, 45 ft TR sep, link margin 10dB, no FEC
  Measurement environment is office & home, not screen room or chamber
Manufacturability
  Key analog/RF IC functions completed and tested
  Taped out 1Q00, tested 2Q00
  Basis of 100Mbps system due 3Q00
Time to market
  Sample chipsets 2Q01
  Limited availability 3Q01
  Production quantity 4Q01
Maturity demonstrated by discrete system
Manufacturability demonstrated by analog ICs
Time to market is 2001
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 24: Multiple Access & Number of Full Throughput WPANs
Solution uses baseband coded wavelets
  Each code operates TDD & TDMA and corresponds to a single piconet
    Allows more than 8 active users per piconet each greater 10Mbps
  Between 3 and 6 piconets (codes) can overlap at full throughput
    Supports between 300Mbps and 600Mbps in a cell
    Technique is S-CDMA
Data rate of 100Mbps allows multiple MPEG2 streams & async data
Number of simultaneous full throughput (20Mbps) PANs
  Supports 5 simultaneous 20Mbps users per piconet
  Supports 15-30 simultaneous 20Mbps users in disjoint overlapping piconets
Multiple access exceeds 8 active users & all specified scenarios
Number of full throughput (20 Mbps) PANs exceeds 5
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 25: Interference & Susceptibility and Intermodulation Resistance
The Demonstration System Performance 50 MB/s, 45 ft, 10-5 BER, no FEC, 10dB link margin
  Measured in a high-rise office building – a high multi-path environment
  Measured in Hot RF environment,
    Channel 58 TV broadcasts from the roof
    Other radio services broadcasting from neighboring office buildings
    Operates with 900 MHz and 1.9 GHz Cellular phones 1 ft (or greater) from the receive antenna – >0 dBm into receiver input port
    Demonstrates over 60 db rejection of jamming signals
  >60 db rejection of the 2.4 GHz, 802.11
Intermodulation resistance – N/A for UWB, not channelized per criteria
  Since the bandwidth is 3:1, the effects of the two fundamental test tones, or the RFI in the real environment, swamp the effects of their intermodulation products.
Interference & Susceptibility: –10dBm at receiver input
  Meets 10^-3 BER before FEC at 10m and 100 Mbps
Interference protection is greater than 60 dB
Intermodulation resistance –10 dBm
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 26: Jamming Resistance
Transmit power to drop the BER from 10^-9 to 10^-3 at 3m
Immune to jamming from all specified devices & scenarios

## Slide 27: General Solution Evaluation Matrix
Criteria | REF. | Weight | Value
Unit Manufacturing Cost | 2.1 | 9.7 | Cost of solution is ~30% greater than Bluetooth 1.0 alone based on additional die size
Interference and Susceptibility | 2.2.2 | 1.4 | Interference Protection is greater than 60 dB
Intermodulation Resistance | 2.2.3 | 0.6 | –10 dBm exceeds comparison by 25 dBm
Jamming Resistance | 2.2.4 | 3.5 | Handles all specified sources
Multiple Access | 2.2.5 | 1.7 | Exceeds all specified scenarios
Coexistence | 2.2.6 | 8.9 | 100% for all specified sources
Interoperability | 2.3 | 7.2 | True. Bluetooth 1.0 interoperable
Manufacturability | 2.4.1 | 1.2 | Operational system. Key IC’s completed.
Time to Market | 2.4.2 | 3.7 | Sample IC’s 2Q01 & production 4Q01
Regulatory Impact | 2.4.3 | 1.6 | False. At NPRM stage in FCC
Maturity of Solution | 2.4.4 | 1.5 | Operational 50Mbps system
Scalability | 2.5 | 2.1 | Solution scales in all areas listed
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 28: PHY Protocol Criteria Evaluation Matrix
Criteria | REF. | Weight | Value
Size and Form Factor | 4.1 | 1.6 | Die and package smaller than Compact flash
Minimum MAC/PHY Throughput | 4.2.1 | 2.5 | True. Exceeds 20Mbps
High End MAC/PHY Throughput | 4.2.2 | 4.6 | 100Mbps (exceeds 40Mbps)
Frequency Band | 4.3 | 1.1 | Unlicensed
Number of Simultaneously Operating Full-Throughput PANS | 4.4 | 1.7 | Exceeds 5
Signal Acquisition Method | 4.5 | 2.2 | DLL Single code acquisition
Range | 4.6 | 2.1 | Exceeds 10m
Sensitivity | 4.7 | 4.2 | < 108dBm/MHz
Delay Spread Tolerance | 4.8.2 | 1.7 | True
Power Consumption | 4.9 | 5.9 | Significantly Below 500mW
Notes: Page <number>
        <footer>
<header>
<date/time>