## Slide 1
Slide <number>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [MAC proposal for the High Rate 802.15 Standard]
Date Submitted: [July 2000]
Source: [Walt Davis] Company: [Motorola]
Address: [1303 E. Algonquin Road, Fourth Floor, Schaumburg, IL 60196]
Voice:[(847) 576-3311], FAX: [(847) 576-5292], E-Mail:[Walt.Davis@email.mot.com]
Re: [ MAC layer submission, in response of the Final Call for Proposal ]
Abstract: [This contribution is a WPAN proposal for a high performance 30 Megabit per second, 5GHz system that addresses the requirements of a large number of wireless multimedia applications. The system is based on proven, low cost RF technology at the Physical Layer level, and on an extension of the BlueTooth TDMA protocol at the MAC layer. It provides for real-time transport of a number of real-time data streams while offering the advantages of quick time to market via the use of proven technology and low system cost due to the use of simple receivers and transmitters. It also provides for the low power drain that is essential for personal portable applications by making extensive use of protocol based battery saving techniques.]
Purpose: [Response to WPAN-HRSG Call for Applications]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Motorola, Inc.
MAC Layer Submission
to the IEEE P802.15
Wireless Personal Area Networks
High Rate Working Group
Notes: Page <number>
<header>
<date/time>

## Slide 3: Wireless Multimedia Application
Basic Requirement:
Enable the high-speed, wireless interconnection of consumer devices to support the transfer of large multi-media data files and high speed, real-time data streams.
Typical Applications:
  Video distribution from set-top boxes to remote
  TV sets, VCR to portable screen, computer to projector, etc.
  In-home Internet connectivity from set-top boxes to
  personal devices and computers
  Wireless video camera linkages
  Wireless Audio and Video distribution for
  Home Theater Systems

## Slide 4: Wireless Multimedia Application
Basic Requirement:
Enable the high-speed, wireless interconnection of consumer devices to support the transfer of large multi-media data files and high speed, real-time data streams.
Applications:
  Low cost, high speed networking
    Communications devices to peripherals
    Computer to computer
    Computer to printer
    Digital camera to printer
    Appliance to appliance

## Slide 5: Application Requirements
Physical Layer
• Operating Frequencies
• RF Range / Coverage
• Number of channels
• Channel Noise Immunity
  Error Tolerance
  Delay Spread
  Tolerance
• Security
• Co-existence / compatibility
with other systems
• Operating frequency /
license requirements
System
• Transparent System
Operation
• QoS
• Data Throughput Rate
• System Range / Coverage
• Cost
• Security
• Low Power
• Low Complexity
• Low Development risk
• Time to Market
Categories
MAC Layer
• QoS
• Security
• Low Complexity
• Low Development risk
• Cost

## Slide 6
System Features
Time shared, collision free channel access
High network utilization and low overhead - 86% to 93% throughput dependent on packet size
Isochronous, multimedia data support
Completely QoS oriented stream support
Mesh network topology supports peer-to-peer, point-to-point and point-to-multipoint operation
Multicast support using shadow client mode
Alternate master devices for master redundancy
Privacy and Security

## Slide 7
Quality of Service (QoS) Features
Packet Sequence Preservation
Dynamic BW negotiation
Guaranteed Bandwidth for Isochronous Streams
Guaranteed Max Latency for Isochronous Streams
Dynamically Configurable Selective ARQ
Traffic Monitoring
Priority Services - Four Levels of Priority
Dynamic Channel Change

## Slide 8
TDMA BASED SIGNALING PROTOCOL
Master
Remote 1
Remote 2
Remote 3
Master
Remote 1
Remote 2
Remote 3
Channel
Activity
Time

## Slide 9
1. .System Operation:
The proposed Medium Access Layer, together with the Physical Layer, form a Wireless Personal Area Network system that is targeted at meeting the requirements of high data rate multi-media applications. In particular, it is focused providing a system that can simultaneously deliver up to 63 streams of data, including:
 Several (at least three) MPEG encoded real-time video streams, plus
 Several channels of digital audio, plus
 Several voice telephony channels, plus
 Several computer data streams that may be associated with an interactive Internet session or with simple data file transfers.
Description of MAC Layer Submission

## Slide 10
Description of MAC Layer Submission
802.15.1
MAC
802.15.1
PHY
802.15.3
MAC
802.15.3
PHY
802.1 Bridging
802.2 LLC
=/>20
Mbit/s
=/<1
Mbit/s

## Slide 11
Description of MAC Layer Submission
reQuest
Slot
Network Frame
Network Frame
Network Frame
One Network Frame
Tx Slot, zoomed to define each device’s tx duration
Tx Slot for device-1
Tx Slot for device-2
Tx Slot for device-n
Packet Body
Radio data frame
Pre
Stream1
Stream2
Stream3
Stream4
Bit
Sync
Source
ID
32 bits
32 bits
48 bits
48 bits
Dest
ID
Lgth
CRC
ECC
16bits
16bits
Structure of the Dynamic TDMA Slot System

## Slide 12
Description of MAC Layer Submission
reQuest
Slot
Radio
data
frame
Network Frame
Isoch-Slot n
1
Non-
Isoch
Slot
n
m
Network Frame
Network Frame
One Network Frame
Tx Slot
Tx Slot for device-1
Tx Slot for device-2
Tx Slot for device-n
Isoch-Slot n
2
Isochronous and Non-Isochronous Data Slots

## Slide 13
Description of MAC Layer Submission
QoS - Dynamically Configurable ARQ
Stream level decision
Selective ARQ request from the receiver
Buffering of non-acknowledged packets at tx
Number of re-tx attempts dynamically negotiable
P1
P2
P3
P4
P5
P2
P5
P6
lost
P2, P5 - Not ACKed
rest ACKed
Re-tx
ACKed
up to P5
Stream n to device i from device j
Stream n to device i from device j
lost

## Slide 14
Description of MAC Layer Submission
Qos - Priority Services

## Slide 15
QoS - Channel Protection
  FEC Features:
    255 Symbol Reed-Solomon Block Coding
      Comparable to DSS Satellite Video Broadcasting FEC
    Improve BER from 10E-6 to 10E-11
      1/1,000,00 to 1/10,000,000,000
    Can be negotiated to increase the protection rate through reduction of FEC block size for the same number of redundancy symbols
Description of MAC Layer Submission

## Slide 16
Description of MAC Layer Submission
Qos - Channel Change Procedure
Frequency Spectrum
Channel 1
Channel 2
(More channels)
All devices measure the channel and send feedback to the master device
Master device decides to change the channel based on the feedback and
its own measurements
Master device informs all the client devices to “remain quiet”
Master device looks for another free channel
If a free channel is found, Master device informs all the client devices to move
over to the new channel
If no other free channel, master device resumes operation in the original channel

## Slide 17
Description of MAC Layer Submission
Alternate Master Device
Master
Client A
Master
Master
Client A
Client B
(Alt Master)
No Single Point of Failure

## Slide 18
Description of MAC Layer Submission
Master
Client - C1
Master in RX mode waiting for request
Client - C2
Network Frame
No Radio Transmit -
Entire Frame is reQuest slot
Network Frame
Network idle, no activity
Theory of Operation

## Slide 19
Description of MAC Layer Submission
Client 1 Requests Video
Master
Client - C1
C1 Requests a video stream
Connection Request
Connection Grant
Master
Client - C1
C1 Receives VIDEO Stream
VIDEO
Control
C
Beacon
V
C
C1
C
Beacon
V
C
C1
reQuest slot
Client 1 views MPEG movie
on Master
Network Frame
Network Frame

## Slide 20
Master
Client - C1
Connection Request
Connection Grant
Master
Client - C2
Acknowledgement
Connection Data
C1 views MPEG movie
on Master
C1 requests Digital Photo
file transfer to
C2’s laser printer
Description of MAC Layer Submission
Client 1 Requests Print File Transfer

## Slide 21
Master
Client - C1
VIDEO
Client - C2
Print Data
Network Frame
C
Beacon
C
Beacon
V
C
C1
V
C
C1
reQuest slot
PD
PD
C
C2
D
C1 views MPEG movie
on Master
C1 prints Digital Photo on
C2’s laser printer
Network Frame
Description of MAC Layer Submission

## Slide 22
Description of Physical Layer Submission
Channel
Source
Encode
Channel
Encode
Tx_Signal
Modulate
Encrypt
Transmit
Rx_Signal
Channel
Decode
Source
Decode
Receive
Demodulate
Decrypt
Physical Layer Data Flow Model