## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Frequency Hopping Multi-Mode QAM Physical Layer Proposal for High Rate WPANs
Date Submitted: 7 July 2000
Source: Jeyhan Karaoguz, Broadcom Corporation
Address: 16215 Alton Parkway, Irvine, CA 92619
Voice: 949 585 6168, FAX: 949 450 0754, E-Mail:jeyhan@broadcom.com
Contributors: Jeyhan Karaoguz, Christopher Hansen, Brima Ibrahim, Reza Rofougaran, Nambi Seshadri, Broadcom Corporation
Re: Call for Proposals for IEEE P802.15.3 High Rate Task Group
Abstract: This proposal describes a 5 MHz frequency hopping physical layer operating in the unlicensed 2.4 and 5 GHz bands. The proposed system provides adaptive data rates of 8, 12, 16, and 20 Mbit/sec depending on the channel and noise conditions.
Purpose: To be considered as a candidate PHY layer technology for IEEE P802.15.3 specification
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Physical Layer Summary
5 MHz Frequency Hopping (FH) transmission system operating in the unlicensed radio spectrum (2.4 GHz and 5 GHz bands)
Multi-mode adaptive Quadrature Amplitude Modulation (8-PSK, 16/32/64 QAM) with Trellis Coding supporting 8-20 Mbit/sec
Adjustable transmit power 1, 10, 100 mW for range and robustness
Minimum Mean Squared Error Decision Feedback Equalization (MMSE-DFE) receiver to combat delay spread
Variable length coded frame size (suitable due to TCM)
Will support existing 802.15 devices in dual mode
PHY layer design based on extensive field test results (up to 17 m indoor coverage, 1 and 10 mW transmit levels) conducted by UCLA Electrical Engineering Department

## Slide 3: Modulation Characteristics
Frequency hopping (1600 Hops/sec) for backward compatibility (w.r.t network synchronization) with the 802.15.1 specification
Multi-Mode QAM PHY layer operates at a modulation rate of 4 MBaud with a 20 dB signal bandwidth of 5 MHz
25% excess bandwidth to achieve low Peak-to-Average-Ratio (PAR)
Simple 8-State/2-D TCM applied to 8-PSK, 16/32/64 QAM signal constellations (spectral efficiencies of 2/3/4/5 bits/symbol)
Adaptive data rates of 8, 12, 16, 20 Mbit/sec
MMSE-DFE equalization at the receiver to combat delay spread
Signal acquisition and equalization are both based on a short preamble

## Slide 4: Considerations for 5 MHz FH System
After a 2-year debate and thorough technical analysis, FCC is likely to approve the use of 5 MHz FH systems for high data rate wireless communications in the unlicensed radio spectrum
Extensive field tests (3600 experiments) conducted by UCLA Electrical Engineering Department showed good performance within 17 m radius for uncoded 5 MHz multi-mode QAM systems supporting 20+ Mbps
5 MHz frequency hopping systems require less power compared to wideband non-hopping systems
Higher SNR and front-end linearity required by multi-level QAM modulation can be offset by simple 8-State TCM, which achieves ~3.5 dB coding gain
Frequency hopping is effective in dealing with narrowband interference

## Slide 5: Signal Constellations
16-QAM TCM (12 Mbit/s)
32-QAM TCM (16 Mbit/s)
64-QAM TCM (20 Mbit/s)
8-PSK TCM (8 Mbit/s)

## Slide 6: 8-State Multi-Mode TCM Encoder
T
+
T
T
+
8-PSK
Encoder
16-QAM
32-QAM
64-QAM
2-D Output
to Pulse Shaping
Filter
C
bo
b1
b2
b3
b4
2,3,4,5
bits/symbol
8/16/32/64 QAM TCM
Mode Selection

## Slide 7: 8-State/ 2D Trellis Coded Modulation
D0
D4
D2
D6
D1
D5
D3
D7
D4
D0
D6
D2
D5
D1
D7
D3
D2
D6
D0
D4
D3
D7
D1
D5
D6
D2
D4
D0
D7
D3
D5
D1
D0
D4
D2
D6
16-QAM Set Partitioning
D0
D4
D2
D6
D1
D5
D7
D3
C0
C2
C1
C3
B1
B0
8-State Trellis Diagram

## Slide 8: Coding Gains for 8-State QAM TCM

## Slide 9: Variable Length Frame Format
Preamble
CRC
Tail
Message Body
3 T
12-18 T
Hopping Boundaries
Preamble: Low overhead preamble for fast packet-by-packet MMSE-DFE equalization
Tail: Beneficial for reaching a known TCM state at the end of a burst transmission

## Slide 10
Simulations for Multipath Immunity
Exponential decaying Rayleigh fading channel
25 ns RMS delay spread
-73 dBm received signal level
  3 dB higher than minimum required sensitivity
Monte Carlo simulation used to evaluate MMSE-DFE performance
  2000 random channels evaluated on two equalizers
  4 Feed-Forward and 4 Feed-Back taps
  8 Feed-Forward and 4 Feed-Back taps
SNR at slicer is sufficient for operation under worst case conditions
  At 99.9 percentile, SNRs of 14.7 dB (4 FF taps) and 17.0 dB (8 FF taps) is achieved
  This corresponds to 12 Mbps and 16 Mbps
  20 Mbps can be achieved at 98th percentile with 8 FF Taps

## Slide 11
Multipath Immunity & Equalizer Performance

## Slide 12: Multi-Mode QAM TCM Transmitter
Randomizer
and CRC
Generator
Preamble
Generator
TCM
Encoder
Transmit Control
I/Q Modulator
DACs and LPFs
Inter-
polator
X 2n
Pulse
Shaping
Filter
X 2n
Data
Control
IF and RF Stages

## Slide 13: High-Speed Wireless Indoor Prototype System
2.4 GHz 5 Mbaud multi-mode QAM (4, 16, 64-QAM) built by UCLA researchers
System implementation and distortion issues such as real-time adaptive equalization, timing and carrier recovery, inter-modulation distortion, and phase noise are reflected in the measurements
Prototype system description and results are published in the IEEE Journal on Selected Areas in Communications, March 2000, “Field Trial Results for High-Speed Wireless Indoor Data Communications” by J.F. Frigon, B. Daneshrad, J. Putnam, E. Berg. R. Kim, T. Sun and H. Samueli.
IF to RF
Up-Converter
RF to IF
Down-Converter
IF to Baseband
Converter
Baseband
to IF Converter
Low IF
Out
Data
CLK
BER
Tester
Out
In
Low IF
In
Data
CLK
Baseband QAM Modulator
Baseband QAM Demodulator
NF = 6.5 dB
IP3 = -36.5 dB
Laptop
PC
fc = 2.44 GHz
BW3dB = 5 MHz

## Slide 14: Field Test Results
Field test environment
  UCLA Engineering building 5th floor laboratories
  Modern construction with reinforced concrete with metal support structures
  Rooms contain a set of lab benches with equipment (square rooms with 9.7 m2 area)
Total of 3600 experiments carried out
  1200 measurements within one room (24.8 ns rms delay spread)
  1200 measurements between rooms (35.4 ns rms delay spread)
  1200 measurements between a room and hallway (31.2 ns rms delay spread)
0 dBm transmit power used for measurement within one room
  -43.5 dBm of measured average received power
  24 dB of measured average SNR (with MMSE-DFE)
  SNR > 14.5 dB for %90 of the time (with MMSE-DFE)
  SNR > 10 dB for %95 of the time (with MMSE-DFE)
  As much as 14 dB SNR degradation observed without an MMSE-DFE in the receiver
Results showed that MMSE-DFE equalized system is not ISI but noise limited
  10 dBm transmit power would eliminate all inadequate SNR conditions for 20 Mbps transmission (requires 19.5 dB SNR)

## Slide 15: Designed System Performance
BER and PER (512 Bytes)
  10-5 (BER) and 4 x 10-2 (PER)
  19.5 dB SNR requires for 64 QAM TCM
Receiver Sensitivity (AWGN5 MHz BW + Noise Figure + SNR10-5 BER)
  -76 dBm for 64-QAM TCM, 20 Mbit/sec
  -79 dBm for 32-QAM TCM, 16 Mbit/sec
  -82 dBm for 16-QAM TCM, 12 Mbit/sec
  -85 dBm for 8 -PSK TCM, 8 Mbit/sec
Inter-modulation Performance
  -35 dBm to -45 dBm inter-modulating signals while receiving at 3 dB above sensitivity level
  Results in input IP3 from -6.5 dBm to -21.5 dBm
Spurious Noise
  -45 dB below carrier power (out of band spurious)
Phase Noise
  -40 dBc (total integrated over 5 MHz signal bandwidth), -85 dBc/Hz @ 50 kHz

## Slide 16: Transmitter Complexity
Digital Baseband Processing
  Randomizer
  Preamble generator
  TCM encoder
  Pulse shaping filter
Analog Front-end
  Dual 6~8-bit DACs (10 Msamples/sec)
  Baseband to RF up-conversion
  0 dBm output on-chip PA (5 dB back-off from 1 dB compression point)
  RF synthesizer block (VCO, PLL, etc) shared with receive section
Power Consumption (Analog + Digital) (0 dBm)
  ~60 mA for .35u, 3.3V technology, ~37 mA for .18u, 1.8V technology

## Slide 17: Receiver Complexity
Digital Baseband Processing
  Square-Root-Raised-Cosine Filter: 25% excess bandwidth
  Feed-forward equalizer: 8 symbol interval span
  Decision feedback filter: 4 taps
  Signal acquisition block
  8-State 2-D Viterbi decoder
Analog Front-end
  Dual 6~8-bit A/D converter (10 Msamples/sec)
  AGC
  RF-to-IF down conversion block
  IF-to-baseband down conversion
  RF synthesizer block (VCO, PLL etc.) shared with transmit section
Power Consumption (Analog + Digital)
  ~125 mA for .35u, 3.3V technology, ~60 mA for .18u, 1.8V technology

## Slide 18
Evaluation Matrix and Summary

## Slide 19
Evaluation Matrix and Summary Cont’d

## Slide 20
Evaluation Matrix and Summary Cont’d