## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [L3C Proposal for High Rate WPAN Combined PHY and MAC ]
Date Submitted: [13 July 2000]
Source: Name [Carlos Rios ] Company [LinCom Wireless, Inc.]
Address [5120 W Goldleaf Circle, Ste 400, Los Angeles, CA 90056]
Voice:[408 202 6294], FAX: [408 399 9704], E-Mail:[riosc@lincom.com]
Re: []
Abstract: [A joint PHY and MAC proposal by LinCom Wireless, 3Com and Philips for a 1 to 40 Mbps WPAN operating in the 2.4 GHz band ]
Purpose: [Response to the High Rate WPAN CFP]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: L3C- A Proposal for a High Data Rate WPAN in the 2.4 GHz Band

## Slide 3: The Wireless Home Network Application
Enable the wireless interconnection of electronic devices within the home
  Low and high speed throughput
  Real time and non-real time data
  Multiple simultaneous connections
  Support prioritization and guaranteed bandwidth, latency
  Enable coexistence, interoperability, coordination between all home wireless devices
  Coexist and perhaps interoperate with “visiting” or legacy devices designed to other standards

## Slide 4: L3C Description
L3C PHY is a “streamlined and extended” 802.11 PHY
Robust nQAM signaling at data rates of 1, 2, 10, 20, 30, 40 Mbps
  Reed Solomon error correction above 10 Mbps (No CCK)
  Adaptive equalization improves range, high end throughput
Low power operation per FCC 15.249
Interoperable with 1, 2 Mbps DSSS, coexists with 5.5, 11 Mbps CCK
“Bluetooth class” device in size, cost, power consumption
L3C MAC is also derived from 802.11, will align with 802.11e
Retains CSMA/CA, DCF and PCF
Adds client to AP “morphing”, direct peer to peer communication
Enhanced security features device authorization, registration, mutual authentication, 128 bit encryption and user transparent key maintenance
Real time voice, audio, video and interactive multimedia support

## Slide 5: L3C PHY
L3C-1 is 1 Mbps (11 chip) Barker encoded DBPSK
L3C-2 is 2 Mbps (11 chip) Barker encoded DQPSK
L3C-10 is 10 Mbps RS(220,200) encoded DBPSK
L3C-20 is 20 Mbps RS(220,200) encoded DQPSK
L3C-30 is 30 Mbps is RS(220,200) encoded 8QAM
L3C-40 is 40 Mbps RS(220,200) encoded 16QAM
All produce 11 MSps 802.11 DSSS-like 22 Mhz spectrum
All use the 802.11 PLCP header, with appropriate service field extensions, and support both long and short preamble
5.5, 11 Mbps CCK, PBCC are not supported
CCA mechanism is identical to 802.11
L3C interoperates with 802.11 DS, coexists with 802.11b

## Slide 6: L3C MAC- General
Modified 802.11 MAC to support High Rate WPANs
Single BSS consisting of one Master (AP) and multiple Slaves (clients). The device initially establishing a network becomes the Master. A Slave may later become the Master, as appropriate, and the roles may be switched
The Master controls 802.11 Association and Disassociation services. Associated Slaves may communicate directly (peer to peer) with each other
The Master uniquely supports any active Portal, and so can support 802.11 Distribution and Integration services
The Master uniquely provides security services: authorization, registration, authentication and privacy
The Master controls all PCF and QOS services

## Slide 7: L3C MAC- Multiple Access
Multiple access protocol remains CSMA/CA with a positive ACK
Supports point/multipoint, point/point and peer/peer links
DCF and (extended, QOS capable) PCF modes are supported with identical 802.11 timing relationships (SIFS, DIFS, PIFS)
Automatic data rate shifting is supported, but may defer to QOS prioritization and guaranteed bandwidth, latency contracts
Power Management support may vary between device types, depending on individual message buffering capability
Roaming, fragmentation, RTS/CTS, 802.11 adhoc are not supported

## Slide 8: L3C MAC- Security
Every L3C-capable device features a unique, secret factory assigned signature in addition to its MAC address
A device “Registers” with the Master upon first network access. Regis-tration may require user intervention at one or both ends.
Upon Registration the device is Authorized to access the network in the future, under the aegis of the Master (ACL)
Upon subsequent network access the device undergoes Authentication to prove he is the authorized accessor, likely with a secure exchange (Diffie Helman) of MAC Address and secret signature
The device may optionally demand “Reverse” or Mutual Authentication from the Master, to ensure that he is indeed accessing the network of interest
A unique, secret shared session key is automatically generated at both ends during Authentication, and is then used to ensure communications privacy by strongly encrypting (128b RC4) exchanged messages

## Slide 9: L3C MAC- QOS
Need to support in-home distribution of voice, audio, video and interactive multimedia
  “Single Portal” model for distribution of content likely originating beyond the single BSS, either real time broadcast or stored/cached
  Prioritization, bandwidth and latency guarantees are needed to mitigate wireless network overhead (framing, gaps, ACKs)
  Enhanced PCF eliminates collisions, backoffs, retries
  QOS-aware Master reduces overhead, prevents collisions and prioritizes incoming traffic
Proposed AT&T, ShareWave and Lucent solution for 802.11e QOS supports these services (and more)
L3C QOS MAC will “streamline” this solution as needed to focus solely on the home wireless multimedia distribution problem

## Slide 10: L3C vs TG3 General Solution Criteria
2.1 Unit Manufacturing Costs
  Are intimately associated with specific MAC, PHY implementation
  Direct BB/RF Conversion architecture minimizes BOM cost
  Present day silicon technology supports single chip integration of
    RFCMOS Zero IF transceivers at 2.4 GHz
    Digital nQAM modems, adaptive equalizers, RS FECs
    80+ MIP processors suitable for software 802.11-like MACs, including encryption, QOS
    High speed SRAM
  .18u CMOS process is available in low cost fabrication facilities
  LC3-20 Module s/b available Q101 for < 2x 802.15.3 cost
  Full LC3-40 Module s/b available Q401 for <1.5x 802.15.3 cost
  Criteria Comparison = +

## Slide 11: L3C vs TG3 General Solution Criteria
2.2.2 Interference and Susceptibility
  Inband, Non-Cochannel, Non-Adjacent Channel > 35 dBc
  Out of Band > 35 dBc
  Criteria Comparison = +
2.2.3 Intermodulation Resistance
  Measured IP3 of representative RF = -3 dBm
  IM level= -99 dBm
  Sensitivity and SOI level, L3C-40= -80 dBm
  SIR, L3C-40= 19 dB
  Criteria Comparison = +

## Slide 12: L3C vs TG3 General Solution Criteria
2.2.4 Jamming Resistance
  Handles devices 4, 5, 6
  Criteria Comparison = Same
2.2.5 Multiple Access
  All scenarios work with L3C-30, 40
  Criteria Comparison = +
2.2.6 Coexistence
  L3C coexists with devices 1,2 per 802.15.2
  L3C-40 coexists 100% with devices 3, 4, 5
  Criteria Comparison = Same
2.3 Interoperability
  L3C does not interoperate with 802.15.1
  L3C does interoperate with 802.11
  Criteria Comparison = Same

## Slide 13: L3C vs TG3 General Solution Criteria
2.4.1 Manufacturability
  802.11b equipment of similar complexity available in Q400
  Criteria Comparison = +
2.4.2 Time to Market
  L3C-20 s/b available Q101, L3C-40 s/b available Q401
  Criteria Comparison = +
2.4.3 Regulatory Compliant with existing FCC (15.249), ETSI
  Criteria Comparison = Same
2.4.4 Maturity of Solution
  L3C is a reduction and extension of 802.11b
  Criteria Comparison = +
2.4.5 Scalability
  L3C is scalable in data rate, frequency band, and function
  Criteria Comparison = +

## Slide 14: L3C vs TG3 MAC Criteria
3.1 Fully Transparent to Upper Protocol Layers
  Criteria Comparison= Same
3.2.1 Unique 48 bit Address
  Criteria Comparison= Same
3.2.2 Simple Network Join/Unjoin
  Enhanced 802.11 style association, disassociation
  Criteria Comparison= +
3.2.3 Device Registration
  Configurable from Automatic Admit-All, to Automatic by Device Type, to various levels of Restricted Access
  Criteria Comparison= +

## Slide 15: L3C vs TG3 MAC Criteria
3.3.2 Minimum Delivered Data Throughput
  Short PHY Header, MAC header, Payload, SIFS, ACK
  L3C-30, 3200 B payload = 20.02 Mbps
  L3C-40, 3200 B payload = 24.02 Mbps
  Criteria Comparison= +
3.3.3 High End Delivered Data Throughput
  Short PHY Header, MAC header, Payload, SIFS, ACK
  L3C-40, 6400 B payload = 30.01 Mbps
  L3C-40, 48000 B payload = 38.3 Mbps
  Criteria Comparison= Same
3.4.2. Data Transfer Types
  Asynchronous, isochronous on a per packet basis
  Criteria Comparison= Same

## Slide 16: L3C vs TG3 MAC Criteria
3.5.1 Topologies supported: point/multipoint, point/point, peer/peer
  Criteria Comparison= +
3.5.2 Maximum number of Active Connections > 10
  Criteria Comparison= +
3.5.3 Ad Hoc Networks supported
  Criteria Comparison= Same
3.5.4 Access to a Portal supported
  Criteria Comparison= Same
3.6.2 Master Redundancy supported
  Criteria Comparison= Same
3.6.3 Loss of Connection Detection and Recovery supported
  Criteria Comparison= Same
3.7 Power Management as in 802.11
  Criteria Comparison= Same

## Slide 17: L3C vs TG3 MAC Criteria
3.8 MAC Controller power consumption
  Consistent with 1.5W system power consumption
  Criteria Comparison= Same
3.9.1 Authentication
  Enhanced (spoof-proof) mutual authentication
  Criteria Comparison= +
3.9.2 Privacy
  Strong Encryption (128b RC4)
  User transparent encryption key generation, distribution, and maintenance
  Criteria Comparison= +
3.10 QOS equivalent to 802.11e supported
  Criteria Comparison= +

## Slide 18: L3C vs TG3 PHY Criteria
4.1 Size and Form Factor
  L3C-20, consistent with Compact Flash Type 1, Q101
  L3C-40, smaller than Compact Flash Type 1, Q401
  Criteria Comparison= +
4.2.1 Minimum Delivered Data Throughput
  L3C-40, 3200 B payload = 24.02 Mbps
  Criteria Comparison= +
4.2.2 High End Delivered Data Throughput
  L3C-40, 48000 B payload = 38.3 Mbps
  Criteria Comparison= Same
4.3 Frequency Band of Operation 2.40-2.483 GHz, unlicensed
  Criteria Comparison= Same
4.4 Number of simultaneously operating full rate WPANs= 3
  Criteria Comparison= -

## Slide 19: L3C vs TG3 PHY Criteria
4.5 Signal Acquisition identical to 802.11
  Criteria Comparison= N/A
4.6 Range not less than 30 meters, indoors (home)
  RS FEC plus equalization provide extended range
  Criteria Comparison= +
4.7 Sensitivity, 10E-5 BER
  L3C-20= -89.1 dBm
  L3C-30= -86.1 dBm
  L3C-40= -82.9 dBm
4.8 Multipath Tolerance
  Chip level adaptive equalizer mitigates > 50ns delay spread
  Criteria Comparison= +
4.9 PHY Power Consumption consistent with 1.5 W system power
  Criteria Comparison= Same

## Slide 20: L3C-20 Performance- AWGN, 50ns DS Multipath

## Slide 21: Summary
L3C provides for robust 10, 20, 30 and 40 Mbps WPAN communications in the 2.4 GHz band
L3C is based upon mature 802.11 technology
L3C is presently manufacturable at Bluetooth cost points
L3C coexists with 802.15.3 and interoperates with 802.11
The basic LC3 MAC provides ease of use, scalability, high data throughput, flexible network topology, and reliable, power efficient communications
The L3C MAC also supports advanced security and QOS
The L3C PHY provides for small, cost effective, high performance and low power digital wireless communication
L3C is the ideal candidate for the 802.15.3 High Rate WPAN standard