## Slide 1: An OFDM based solution granting compatibility between next G of high rate WPANs and WLANs: HIPERPAN?
Marc de Courville, Veronique Buzenac and Michael Dydyk
Broadband Systems and Technologies Research Lab
Motorola Labs - Paris
Communication Systems and Technologies Labs

## Slide 2: Major opportunities and convergence scenario

## Slide 3: WPAN&WLAN shall meet!
Observations:
  foreseen convergence in bitrate requirement between next generation of WPANs (high data rate) and WLANs!
    WPAN: IEEE802.15.3 (20Mbps), Bluetooth SIG2 (2-10Mbps),3 (20Mbps?) > 20Mbps
    WLAN: IEEE802.11a, ETSI BRAN HIPERLAN/2, ARIB MMAC: 6-54Mbps
  no coordination could result in a plurality of competing systems in the same band
    regulatory acceptance issue
    share of spectrum: increased cost of service per Hz for a given technology
  OFDM preferred modulation for local area broadband (large bandwidth transmissions in presence of multipath)
Goal&requirement: address higher bitrate demand for WPAN devices
  anticipate convergence between WPAN&WLAN
  preserve specificity of WPAN: low cost, low range, peer to peer, embeddable
  from coexistence to compatibility: grant interoperability with 5GHz WLANs: e.g. provide a mean to sync devices both in office and home environment
  personal means worldwide operation: access 5GHz band as spectrum opportunity for WPAN (escape mw-oven spurious)
In-Building
Neighborhood
Personal
Satellite
Wide Area
Beyond
Pico
Micro
Femto
Global
Macro
  support for realtime audio and video
BT3.0 Specification:
2.4 or 5 GHz
100% Backward Compatible to Foundation & 2.0 Specification
Higher rate ~20Mbit/s via enhanced modulation e.g., OFDM, UWB or etc.

## Slide 4: HiperPAN: strategy proposal for addressing WPAN&WLAN convergence
A possible solution:
  take the opportunity of worldwide harmonization WLANs PHY layer @ 5GHz
  grant interoperability through integration already @ PHY level
HiperPAN concept!
  Cost effective solution for high speed WPAN = P2P system derived from cut down of IEEE802.11a, HIPERLAN/2, MMAC
  20MHz bandwidth, OFDM based with 52 carriers
Allows:
  more than coexistence: compatibility with worldwide harmonized WLAN standards (IEEE802.11a, ETSI BRAN HIPERLAN/2, ARIB MMAC HiSWAN);
  a maximum silicon reuse by OFDM covering at the same time 3 spaces: office/home/personal!
  to escape from the polluted 2.4GHz band and give access to a larger spectrum at 5GHz band still reserved for HIPERLAN/2 in Europe;

## Slide 5: HIPERPAN TECHNICAL CHARACTERISTICS
Frequency band:
  the worldwide available 5.15-5.25GHz band: enables NOMADICITY, WITHOUT REGULATORY CHANGE.
  Possible extensions in some part of the world:
    whole IEEE802.11 band (5.15-5.35GHz and 5.725-5.825GHz) in US
    whole HIPERLAN/2 band (5.15-5.35GHz and 5.470-5.725GHz) in Europe
Data Link Control (DLC) sketch
  Proposal: reuse as a basis for the IEEE802.15.3 MAC/RLC/ARQ (DLC) specification all possible parts of the existing HIPERLAN/2 Home Environment DLC extension
  ad-hoc networking capabilities provided by HIPERLAN/2 Home Environment DLC extension, by the means of dynamic Central Controller selection
  Direct Link concept direct reuse for direct communications between two HIPERPAN devices.

## Slide 6: HIPERPAN BASEBAND PARAMETERS (1)
OFDM modulation advantages:
  spectral efficiency, since the information bit train is divided in several bit trains transmitted on different overlapping subcarriers, which are orthogonal to ensure the information retrieving at the receiver;
  multipath immunity, by using a guard interval which “absorbs” the channel effects, allowing information retrieval using a very simple (complexity wise) equalization scheme;
  modularity, which favors both scalability and silicon reuse;
OFDM parameters:
  64 subcarriers, including 48 information subcarriers , 4 pilot subcarriers used for phase channel tracking and 12 zero subcarriers for avoiding adjacent channels interferences;
  channel spacing is 20Mhz;
  sampling frequency: 20Mhz;
  the guard interval is reduced to 400ns (i.e. eight samples) since WPAN channel impulse responses are quite short (accommodating more than 50ns RMS delay spread);
  OFDM symbol duration: 3.6s (including the guard interval).

## Slide 7: HIPERPAN BASEBAND PARAMETERS (2)
Subcarrier modulation
  BPSK for signaling (required for compatibility with 5GHz WLANs standards)
  QPSK for the payload.
Coding scheme
  same Forward Error Correction (FEC) scheme as IEEE802.11a or HIPERLAN/2: rate ½ convolutional code (generator polynomial: 133, 171)
  puncturing for providing a user data coding rate of ¾
  in some short range Line Of Sight (LOS) transmissions, no coding
4 different PHY modes:
  BPSK + coding rate ½: 6Mbps
    used for signaling, as in IEEE802.11a or HIPERLAN/2;
  QPSK + coding rate ½: 13Mbps
    used for user information data in severe conditions;
  QPSK + coding rate ¾: 20Mbps
    used for user information data in normal conditions;
  QPSK without FEC: 29Mbps
    used for user information data in good conditions (short range LOS channels);

## Slide 8: HOW DOES HIPERPAN MEETS THE PHY CRITERIA?

## Slide 9: Why OFDM as a modulation: some answers to technical issues raised in previous meetings
Back-off/Linearity of the PA: not an issue with robust constellations, certain amount of clipping tolerable (out of band being filtered), relaxing battery drain
OFDM insures good coverage and good performance even in NLOS situations
The acquisition time is of course much less than the frame length: <2ms which enables bursty traffics and provides good interactivity
Differential demodulation IS POSSIBLE (DQPSK on top of OFDM)
Typical PAN channels are less than 50ns RMS delay spread which represents impulse responses realizations of length 200ns. 400ns guard time in OFDM enables complete absorption of the multipath resulting in a complete immunity

## Slide 10: Where the reduction of cost is expected in comparison with WLANs
maximum reuse of IP blocks from WLAN for addressing a broader market: WPAN
specific relaxed RFFE requirements for WPANs:
  oscillators & ADC accuracy spec is less demanding
reduction of range (10m) resulting in power consumption savings (PA linearity)
single chip implementation (BB+RFFE) possible

## Slide 11: (SOME OF) THE GENERAL SOLUTION CRITERIA
Time to the market: HIPERPAN should be available no later than first 5GHz OFDM WLANs products (IEEE802.11a and HIPERLAN/2). Expected to appear Q3 2001.
Maturity of the solution: high, since based on 5GHz OFDM WLANs already standardized.
Regulatory impact: no change required.
Scalability: this is one of the main advantages offered by OFDM: data rate, cost, consumption, function are all scalable. Frequency band is also an area of scalability since OFDM can easily be operated in higher/lower frequency bands.