## Slide 1: Berkeley Wireless Research Center An Overview July 11, 2000
http://bwrc.eecs.berkeley.edu/bwrc

## Slide 2: BWRC –Mission Statement
Provide an environment for research into the design issues necessary to support future wireless communication systems.The focus will be on highly integrated CMOS implementations which have the lowest possible energy consumption and lowest cost while using advanced communication algorithms. The evaluation of these components will be made in a realistic test environment.

## Slide 3: The Design Goal: System on a Chip CMOS Radio
A
D
Analog RF
Timing
recovery
phone
book
Java
VM
ARQ
Keypad,
Display
Control
Filters
Adaptive Antenna
Algorithms
Equalizers
MUD
Accelerators
(bit level)
analog
digital
Direct Mapped Logic & DSP cores
uC Core
(ARM/Tensilica)
Four Basic Components
Logic
Configurable and
Dedicated Logic

## Slide 4: BWRC Faculty
Technology
Comm Engineering
& Protocols
Analog & Digital
Circuits
Radio
Architecture
David Tse
Alberto S-V
K. Ramchandran
Jan Rabaey
Bob Brodersen
Bora Nikolic
Paul Gray
Bob Meyer
Paul Wright
Chenming Hu

## Slide 5: Center Industrial Members
Cadence Design Systems
Ericsson Radio Systems
Agilent Technologies
Lucent Technologies
STMicroelectronics
Texas Instruments
Intel Corporation

## Slide 6: BWRC Funding
Operating Budget: $3.5M/yr
Infrastructure: $600 - 800K/yr
  Member companies
Research: $2.0 - 2.5M/yr
  Member companies
  DARPA programs
    Low power PicoRadio Networks
    Mixed signal CAD for single chip-radios
  Office of Naval Research (ONR)
    Ultra-Wideband Radios
  Pending
    DARPA: Defense Advanced Research Projects Agency
    NSF: National Science Foundation
    DOE: Department of Energy
    ONR: Office of Naval Research

## Slide 7: Intellectual Property
Aggressively publish research results
The center will pursue an active policy of placing research results in the public domain as determined by the Center Scientific Directors
Non-member companies have access to the public domain results, but do not directly participate in center research

## Slide 8: Facilities
Very Effective Hub
for Wireless Research
  Excellent and efficient
  working environment
Cubicle usage at capacity
  Virtual user mode
  Online reservation system
  Wireless laptops for overflow
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Facilities Continued
Laboratory
  Capabilities; Complete chip
  and system level testing
    RF
    Digital
    Analog
    Networked Instruments
    Laptop Controllers
  Installed Cascade semi-automatic
  probe station, 40 GHz wafer/die level probing
  Lab capital expansion ~ $100-200K/yr minus donations
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Computer System
Computer System
  Windows NT Desktop (~50 clients) with Unix Compute Servers (X Windows),
  GB fiber network back-plane
    3 NT Servers
    6 Unix Servers
  Network Appliance filer, 450GB
  DS3 fiber link to campus with T1 backup
  SpectraLogic tape backup
  Lucent WaveLan for Laptops
  Migrating to Windows 2000
Design Tools
  Cadence
  Synopsys
  Mentor
  Viewlogic
  HSPICE
  EESoft ADS
  Telelogic
  The MathWorks
  Tensilica
  Sonics
  Opnet
  Cygnus RTOS
  Sente
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: BWRC Focal Areas
Spectrum
Sharing
PicoRadio
Comm. Algorithms
Signal Processing
Protocols
Networking
Platforms
Architectures
Circuit Fabrics
Design
Methodology

## Slide 12: Spectrum Sharing
The goal is to determine a flexible way to utilize spectra which can adapt to new technology and applications with maximum capacity and minimum interference
  TFS Algorithm development
  Ultra Wideband (UWB)
  802.15
    Bluetooth/WLAN Coexistence

## Slide 13: TFS approach
Three “types” of dimensionality in signal space
  Frequency
  Time
  Physical Space
Exploit all these degrees of freedom to maximize the number of users and to minimize their interference with each other
Understand complexity issues and implementation strategies

## Slide 14: Once upon a time. . .
Feb 1999
  BWRC opens for business, with the Universal Radio (UR) listed as one of 3 design drivers.
  An ambitious radio design that allows for uncoordinated co-existence with other radios.
  Adapts to provide requested service given type of service, location, and dynamic variations in environment (i.e. number of users).
  Allows for continuous upgrades to support new services as well as advances in communication engineering and implementation technologies.

## Slide 15: The USS era
June 1999
  Spectrum sharing is identified as the key challenge for the UR.
  UR driver evolves from a radio design into a spectrum management initiative, and is renamed "Universal Spectrum Sharing" (USS).
  USS study group is formed to investigate strategy for uncoordinated use of spectra without loss in capacity.
  Simultaneously exploit time, frequency, space.
  Main goal: change the way spectrum is allocated.

## Slide 16: USS Guidelines
Fall, 1999
  Several guidelines proposed for spectrum sharing:
    Use transmit power as a constraint which encourages good behavior
    Good behavior means:
      localization in temporal-frequency-spatial signal space which allows other users to coexist without interference
      stationary or predictable behavior which facilitates adaptation by other users
      alignment to a time and frequency structure which facilitates co-existence

## Slide 17: USS difficulties
Jan, 2000
  We had no rigorous results for the difficult problem of spectrum sharing -- we only had guidelines.
  This may stem from lack of results in information theory. The interference channel has not yet been “solved" by information theorists -- even for the seemingly simple Gaussian case:
  Realized that we needed to refocus our efforts on specific practical problems rather than general theory.
user 1
user 2
n2
n1
a
a

## Slide 18: IEEE 802.15 TG 2 – Coexistence of WPAN’s http://grouper.ieee.org/groups/802/15/pub/TG2.html

## Slide 19: Coexistence
June 2000
  Have begun to look at specific coexistence problems (Bluetooth + 802.11b).
  Will attempt to tackle the problem with analysis, simulation, and real measurements.
  Focused efficient silicon implementation approaches
    Low cost
    Low power
    Ease of design

## Slide 20: Architectural Exploration
MAC
Unit
Addr
Gen

P
Prog Mem
DSP
(e.g. TI 320CXX )
Efficiency
Direct Mapped
Hardware
(MUD)
Embedded
FPGA
Flexibility
Embedded
Processor
(lpArm)
Reconfigurable
Processor
(Maia)

## Slide 21: The Energy-Flexibility Gap
Embedded Processors
SA110
0.4 MIPS/mW
ASIPs
DSPs
2 V DSP: 3 MOPS/mW
Dedicated
HW
Flexibility (Coverage)
Energy Efficiency
MOPS/mW (or MIPS/mW)
0.1
1
10
100
1000
Reconfigurable Processor/Logic
Pleiades
10-50 MOPS/mW

## Slide 22: Adaptive Multiuser Detection Test Chip

Baseband
Signal
Despreading
X
Adaptive
Error
Signal
Tracks changes in channel, environment, and interfering users
Uses common error metrics such as MSE, and algorithms such as LMS
Eliminates co-site interference
Basic building block - adaptive correlator

## Slide 23: The Implementation Trade-off
Signal Update Block
Acquisition and
Timing Recovery
Signal Update Block
Adaptive
Pilot
Correlator
Adaptive
Data
Correlator
C
0
C
L-1
Digital Baseband
S
k
...
Data Out
Receiver
Channel
Coefficient
Estimates
Adaptive
Pilot
Correlator
Data In
300 million multiplications/sec
357 million add-sub’s/sec

## Slide 24: Reconfigurable Computing: Merging Efficiency and Versatility
“Hardware” customized to specifics of problem.
Direct map of problem specific data-flow and control,
Circuits “adapted” as problem requirements change.
Spatially programmed connection of
processing elements.

## Slide 25
Multi-granularity Reconfigurable Architecture: The Berkeley Pleiades Approach
Communication Network
Control
Processor
Arithmetic Processor
Arithmetic Processor
Arithmetic Processor
Configurable
Datapath
Configurable
Logic
Configuration Bus
Network Interface
Dedicated Arithmetic
Configuration
Satellite Processor
Computational kernels are “spawned” to satellite processors
Control processor supports RTOS and reconfiguration
Order(s) of magnitude energy-reduction over traditional
programmable architectures

## Slide 26: Hybrid Reconfigurable Processor Presented at ISSCC 2000
0.25um tech: 5.2mm x 6.7mm
1.2 Million transistors
40 MHz at 1V
  1 ARM-8
  8 SRAMs & 8 AGPs
  2 MACs
  2 ALUs
  4x8 FPGA
  Reconfigurable Interconnect
1.8 mW while running VCELP, compared with 17mW on TMS320C54
ARM8
Baseband Source Coding Processor

## Slide 27: Architecture Comparison
LMS Correlator at 1.67 M Symbols Data Rate
Complexity: 300 Mmacs/sec and 640 Mmem/sec
Note: TMS implementation requires 36 parallel processors to meet data rate - validity questionable
51.69 MOPs/mW!

## Slide 28: The Radio System-on-a-Chip Nightmare
“Femme se coiffant”
Pablo Ruiz Picasso
1940

## Slide 29
Behavioral
Analog Data
Processing
Protocols &
Control
Analog RF, Passives, Mixed Signal (Matlab)
Conceptual
Structural
Physical
Communications Engineering/DSP
Protocols/ Control
Amplifiers, Filters, A/D, PA, Inductors
Dedicated Logic, Pleiades, VHDL, Schematics
Embedded P, Programmable DSP (C, Assembly)
Simulink
Simulink,
Stateflow
VCC, Stateflow
Spectre and Spectre RF
Synopsys,
Cadence, Unicad
ARMulator, ARM Compiler
Specification Matlab, Opnet
Analog Component Libraries (Layout, SKILL)
Func. Modules (RAM, ROM, Mult) Standard Cell Place and Route
Agilent ADS ASITIC
Cadence
Programmable Cores DSP, ARM, FPGA (C, VHDL, Assembly
ARM
FPGAs
Digital Data
Processing
Opnet, VCC
Unicad
Cadence, Mentor
Power & TimeMill
Matlab
Matlab

## Slide 30
A Domain Specific Approach

Fully Automated. Based on
Simulink/Stateflow

Make design decisions at top
level

Primary architecture support is
for Direct
-
Mapped
communication algorithms
Goal:
Provide predictability in the design process and a
fully automated path

## Slide 31: Analog Design Flow
behavioral
structural/physical
Simulink
  system specifications
  rapid end-to-end simulation
SpectreRF
  component performance
  periodic steady-state, envelope analyses
HP ADS
  microwave design
ASITIC
  integrated passive components

## Slide 32: Matlab Simulink Model of Zero-IF Receiver
Techniques used to decrease simulation time:
  Baseband equivalent modeling of RF signals (envelope simulation techniques)
  Compile design using Matlab Real-Time Workshop

## Slide 33: QPSK Constellation With and without MUD
10 users (equal power)
Length 31 M sequence spreading codes
25 Mchips/sec
QPSK
Without MUD
With MUD

## Slide 34: With Analog Impairments
10 users (equal power)
20MHz Butterworth LPF
500kHz DC notch filter
13.5dB receiver NF
82dB gain
4% gain mismatch
2.5° I/Q phase mismatch
IIP2 = -11dBm
IIP3 = -18dBm
PLL: -80dBc/Hz @ 100kHz
10-bit, 200MHz S-D ADC
ideal receiver
real receiver

## Slide 35: Conclusion
Center opened in February 1999
Computer and network infrastructure in place
Complete set of design flow and tools on network
Research agenda is established
~60 graduate students, 30 Active
Website: http://bwrc.eecs.berkeley.edu/
Third semi-annual research retreat; June 1-2, 2000
  Presentations on Website for members
  Available to non-members after 6 month delay
Next retreat January 2001, Monterey