## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Bluetooth PHY Modeling update]
Date Submitted: [10 July 2000]
Source: [Jim Lansford] Company: [Mobilian Corporation]
Address: [7431 NE Evergreen Rd, Suite 220, Hillsboro, OR 97124]
Voice:[(405) 377-6170], FAX: [ (425) 671-6099], E-Mail:[jimlans@mobilian.com]
Re: [ ]
Abstract: [This presentation is an update to the initial presentation given at the March and May meetings]
Purpose: [To better quantify effects of noise and interference on bit streams emerging from the Bluetooth PHY]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Bluetooth PHY modeling update
Goal: Integrate PHY effects into OpNet MAC model
  “Clean” bits get sent through the model and are returned “dirty” according to environment and hardware
Work has focused on description of attributes needed for function call
  Environmental effects (channel, interference, etc.)
  System effects (filtering impacts, etc.)
Matlab coding in process, not completed yet
A “C” model has generated some preliminary results
Jim Lansford
Mobilian Corporation
jimlans@mobilian.com

## Slide 3: Environment Description
X
Y
Members of own piconet
Other piconet members
802.11b Stations
802.11b APs
Microwave oven
Master
[X1, Y1]
Slave
SCO, HV2
[X2, Y2]
Slave
Park
[X3, Y3]
Slave
ACL, DH1
[X4, Y4]
This environment could be static for the duration of the simulation run,
or change dynamically (preferred). This is an OpNet issue.

## Slide 4: Block diagram
Block of data
from OpNet
Block of data
returned to OpNet
with errors
Environment
Tx Model
(if needed)
Path loss
Rx Model
Activity Generator
Lp=-40-20Log(d), d<=8 meters
Lp=-58.5-33Log(d/8), d>8 meters

## Slide 5: Initial Simulation
Bluetooth node spacing
“Laptop”
AP
WLAN
distance
“Cellphone”
BT2
Simulates typical usage
  Laptop with both Bluetooth & 802.11
  Cellphone near laptop w/varying distance
Distance to AP is critical
Distance between BT1 and STA is critical
BT1
STA

## Slide 6: Preliminary Simulation Run(1)
Asymmetrical traffic AP->STA
BT Throughput
0
50
100
150
200
250
300
350
400
450
1
10
100
1000
WLAN Distance [m]
Throughput [Kbps]
WLAN on
WLAN off

## Slide 7: Preliminary simulation run(2)
Throughput at top of MAC (PHY)
BT2 distance 1 meter
STA to BT1 distance 10 cm
WLAN Throughput
0
1
2
3
4
5
6
7
8
1
10
100
1000
WLAN Distance [m]
Throughput [Mbps]
BT off
BT Active

## Slide 8: Summary
Coding of model is underway
  Preliminary results - more coming!
  Working with NIST to begin integration
Next steps
  Integration with OpNet
  More simulation runs
  Comparison with UNH tests