## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TI PHY Submission to TG3]
Date Submitted: [07 July 2000]
Source: [Anand Dabak] Company [Texas Instruments]
Address [12500 TI Blvd, m/s 8723, Dallas, TX 75243, USA]
Voice:[214.480.4389], FAX: [972.761.6967], E-Mail:[dabak@ti.com]
Re: [original document.]
Abstract: [Submission to Task Group 3 for consideration as the High Rate PHY for 802.15.3]
Purpose: [Evaluation of Proposal.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHYsical Layer Submission to Task Group 3
Anand Dabak
Texas Instruments

## Slide 3: High Speed WPAN
Criteria document specifies the following data rates :
  Audio: 128, 448, 896, 1280, 1450, 1536 kbps
  Video: 2.5, 7.3, 9.8, 18 Mbps
  Computer graphics: 15, 38 Mbps
Propose a 2.4 GHz ISM band high speed WPAN consisting of three modes
  Mode 1: Bluetooth 1.0
  Mode 2: Maximum data rate up to 3.9 Mbps
  Mode 3: Maximum data rate up to 44 Mbps

## Slide 4: High Speed WPAN
Typical system combinations:
  Mode 1 and Mode 2
  Mode 1 and Mode 3
  Mode 1 + Mode 2 + Mode3: Access points
  * Bluetooth specification is -70 dBm
Configuration 1: Lower cost, lower power. Exactly the same protocol as Bluetooth. Audio and internet streaming applications
Mode 1 (Bluetooth)
Mode 2(2.6-3.9 Mbps)
Configuration 2: video, computer graphics applications
Mode 1 (Bluetooth)
Mode 3(22-44 Mbps)

## Slide 5: Salient features
Interoperability with Bluetooth
High throughput: Upto 126 Mbps over the whole ISM band
Coexistence with Bluetooth and 802.11(b).
Resistance to microwave, Bluetooth, 802.11(b) jamming
Low cost:
  (Mode 2+Mode 1) < 1.2 x of Bluetooth,
  (Mode 3+Mode 1) < 1.5 x Bluetooth
Low sensitivity level: -78 dBm for mode 2 and -84 dBm for mode 3
Low power consumption
Designed for FCC compliance
Compatibility with Bluetooth MAC
Low risk approach

## Slide 6: Mode 2 System Specifications
Mode 2:
* Bluetooth specification is -70 dBm
**: Can be achieved with a square root raised cosine filter of  = 0.5

## Slide 7: Mode 2
The master and slave first begin transmission in mode 1 and then negotiate to enter mode 2.
Interoperable with Bluetooth.
Master maintains synchronization of all mode 1 (Bluetooth) devices in the piconet.
Master and slave in mode 1.
Master transmits Sniff and Beacon
for other mode 1 devices.
Negotiate to enter mode 2 of higher
speed transmission.
Master and slave transmit and
receive in mode 2.
Enter back into mode 1
Revert to mode 1 upon extended
loss of connection.

## Slide 8: Mode 2
A master could be talking to several devices in mode 1 while talking to other devices in mode 2: Controlled by the link layer protocol in the Master.
Sniff, Beacon and paging in mode 1.
Full interoperability with Bluetooth
Master
Slave 1
Slave 2
Slave 3
Mode 1
Mode 2
Mode 1
M
M
S3
S1
Mode 1
M
S1
M
S2
M
S2
M
S3
Mode 1
Mode 2
Mode 2
Mode 1
Mode 1
Mode 1
Mode 1
Mode 2
Mode 2
Mode 1
Mode 1

## Slide 9: Throughput comparison of Mode 2 to Bluetooth

## Slide 10: Mode 3 System Specifications

## Slide 11: Mode 3
Begin transmission in mode 1 and identify good 22 MHz bands.
Negotiate to enter mode 3.
After spending a time T2 in mode 3 come back to mode 1 for time T1.
Identify good 22 MHz bands.
Again negotiate to enter mode 3, this time possibly on a different 22 MHz band.
Regulatory issues similar to 802.11
Time allocation T1 and T2 negotiated between the Master and Slave in the beginning depending upon data rate requirements of the Slave.
Master maintains synchronization of all other Mode 1 devices in the piconet
Sniff, Beacon, Paging, for other mode 1 devices.

## Slide 12: Mode 3 (Example)
Achieved data rates:
  Mode 1 (Slaves 1,2 other mode 1 slaves): 70 kbps
  Mode 3 (Slave 3): 20 Mbps
The mode 3 data rates are negotiable
Master
Slave 1
Slave 2
Slave 3
Mode 1
Mode 3
Mode 1
Mode 1
Mode 3
Mode 1
Mode 3
Mode 1
Mode 3
0
25
250
275
500
525
Time (
msec
.)
17.5
msec
7.5
msec
Communicate with other Blueooth devices (paging, sniff, beacon etc.)
Select good 22 MHz band using Probe, listen and select (PLS)
T1
T2

## Slide 13: 19.8 Mbps Video transmission (Example)

## Slide 14: Exponential 802.15.3 channel
Fading across space
Fading across time
TRMS = 25 ns
T2, X
T3, X
T1, X
T, X2
T, X3
T, X1

## Slide 15: Probe, Listen and Select (PLS)
Frequency diversity

## Slide 16: Probe, listen and select (PLS)
Avoids microwave, 802.11(b) interference
Microwave
802.11(b) interference
2402 MHz
2480 MHz
PLS selects this band
for mode 3

## Slide 17: Turbo codes
Serial concatentated convolutional code (SCCC):
  No error floor
  Choose low complexity code. Complexity less than 802.11 (b) convolutional code. Offers better performance compared to 802.11 (b) convolutional code.
  Implemented and tested the Turbo codes.
  4 state outer and 2 state inner code
D
D

D

## Slide 18: Simulations (AWGN)

## Slide 19: Simulations (802.15.3 channel)

## Slide 20: General Criteria evaluation for high speed WPAN
Unit manufacturing cost
  The RF specifications for mode 2 and mode 3 are similar to Bluetooth.
Estimated silicon size for mode 2 base band is 10 % more than mode 1
  Cost of (mode 1 + mode 2) < 1.2 X cost of Bluetooth
Estimated silicon size for mode 3 base band is 40 % more than mode 1
  Cost of (mode 1 + mode 3) < 1.5 X cost of Bluetooth

## Slide 23: Changes to 802.15.1 MAC

## Slide 24: BACKUP SLIDES FOLLOW

## Slide 25: Interference and Susceptibility
Out of band blocking
  Mode 2, Mode 3:
In band:

## Slide 26: General evaluation criteria
Intermodulation resistance (IM3)
  Mode 2: Interfering signals at -47 dBm
  Mode 3: Interfering signals at -45 dBm
Intermodulation resistance (IM2)
  Mode 2: AM modulated signal at -32 dBm
  Mode 3: AM modulated signal at -27 dBm.

## Slide 27: General evaluation criteria
Jamming resistance: Throughput of high speed WPAN as a percentage of nominal throughput with no jamming.
The nominal data rate for 802.15.3 is 22 Mbits/sec.
  Microwave: PLS ensures 100 % throughput
  802.15.1: Collides 20 % of the time, reducing the throughput to 80%.
  802.15.3: Throughput reduced to 98 % due to PLS of the interference.

## Slide 28: General evaluation Criteria
Multiple access: Desired system transmitting MPEG2 9.8 Mb/s video.
Coexistence: Impact on other systems

## Slide 29: Coexistence: Impact on other systems (cont’d)
802.15.1 HV1 voice:
  B1 transmitting to B2: Signal power at B2 = -61 dBm over 1 MHz bandwidth. Interference power at B2 = 4(dBm) - 65(loss) = -61 dBm over 14 MHz bandwidth. The C/I = -61+61+11.5 = 11.5 dB.
  B2 transmitting to B1: Signal power = -61 dBm over 1 MHz bandwidth. Interference power at B1 = 4(dBm) - 50(loss)=-46 dBm over 10 MHz bandwidth. The C/I = -61+46+11.5 = -3.5 dB.
  Hence transmission from B1 to B2 gets through while that from B2 to B1 does not. Since one 802.15.3 channel bandwidth is 1/5th of the total Bluetooth bandwidth, this occurs 20% of the time.
  Hence 802.15.1 throughput reduces to 90%.
Link between
proposed radios
A1
A2
Link between interfering radios
3m
10m
B1
B2
3m

## Slide 30: General evaluation Criteria
Interoperability: Can interoperate with 802.15.1.
Technical feasibility
  Manufacturability: Can be manufactured with proven technologies.
  Time to market: Available 4Q2001.
  Regulatory impact: Full compliance with current international intentional radiator regulatory standards.
  Maturity of solution: Globally accepted concepts that will be quick to market.
  Scalability:

## Slide 31: PHY layer evaluation criteria
Size and form factor:
  Will fit on compact flash type 1 card.
MAC/PHY throughput
  Can achieve 44 Mbps
Frequency band:
  2.4 GHz ISM band
Number of simultaneously operating full throughput PANs
  6 PAN’s operating at 22 Mbps each
  4 PAN’s operating at 22 Mbps each + Bluetooth
Signal acquisition method
  Similar to Bluetooth with packet header

## Slide 32: PHY layer evaluation criteria
Range:
  Greater than 10 meter range
Sensitivity:
  -80 dBm at bit error rate 10-8 and packet error rate 10-4
Multipath immunity:
  Delay spread tolerance more than 50 ns.

## Slide 33: PHY layer evaluation criteria
Power consumption
  Mode 1 (Bluetooth):
    Transmit
      40 mW peak, 20 mW average
    Receive
      65 mW peak, 3 mW average
  Mode 2
    Transmit
      80 mW peak (40 mW RF + 40 mW baseband), 40 mW average
    Receive
      106 mW peak (50 mW RF + 56 mW baseband), 53 mW average
  Mode 3
    Transmit
      135 mW (65 mW RF + 70 mW baseband) peak, 63 mW average
    Receive
      165 mW (65 mW RF + 100 mW Baseband) peak, 83 mW average