## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY layer modeling of Bluetooth]
Date Submitted: [8 March 2000]
Source: [Jim Lansford] Company: [Mobilian Corporation]
Address: [7431 NE Evergreen Rd, Suite 220, Hillsboro, OR 97124]
Voice:[(405) 377-6170], FAX: [ (405) 377-6173], E-Mail:[jimlans@mobilian.com]
Re: [ ]
Abstract: [This presentation summarizes some early work on modeling the Bluetooth physical layer using Matlab. When combined with MAC layer modeling also being done in TG2, it should allow reasonable estimates of system performance to be made.]
Purpose: [To better quantify effects of noise and interference on bit streams emerging from the Bluetooth PHY]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Modeling of Bluetooth
This is an early work in progress
Overall goal is to work with WLAN coexistence WG in the BT SIG to coordinate position papers on performance optimization
May want to convert Matlab to C to plug into Bluetooth MAC modeling being done in Opnet
Lots of work left to do
Jim Lansford
Mobilian Corporation
jimlans@mobilian.com

## Slide 3: A typical Bluetooth block diagram

## Slide 4: PHY modeling issues
How to avoid implementation specific details….
  Homodyne or superhet? IF frequency?
  Channel filter: linear phase or more realistic?
  Discriminator: PLL? Zero crossing? Ratio detector?
Should a model be a “golden receiver,” or a minimally compliant implementation?

## Slide 5: Relevant Specs

## Slide 6: First cut at a model
Modeled at 6MHz IF
  After mixer, before channel filter
    Doesn’t include hopping or synthesizer effects
    Have to either hop the interferer, or back up a step in the model
FIR channel filter
  Linear phase isn’t representative
  differentiator (linear across passband)
Limiter + envelope detector

## Slide 7: Block diagram
Preselector
+
LNA
Synthesizer
Hop sequence
generator
Channel
Filter
Limiter
Discriminator
Bit
Decision
Current Model

## Slide 8: Spectrum
4
4.5
5
5.5
6
6.5
7
7.5
8
x 10
6
-70
-60
-50
-40
-30
-20
-10
0
10
20

## Slide 9: Recovered bit stream
0
100
200
300
400
500
600
-6
-4
-2
0
2
4
6
0
100
200
300
400
500
600
-6
-4
-2
0
2
4
6

## Slide 10: 802.11DS Signal
0
0.5
1
1.5
2
2.5
x 10
7
-30
-20
-10
0
10
20
30
40

## Slide 11: Summary
First steps toward a model
  Can generate soft bit streams
  Allows experimentation with channel filters and discriminators
  Environment allows for noise, multipath, interference, etc.
Not yet ready for real testing
  Doesn’t have hopping modeled adequately

## Slide 12: Next Steps
Include hopping model
Model image effects
Fold in 802.11DS/b signal
Integrate microwave oven, multipath, and other impairments
Calibrate and measure performance against spec
Figure out interface to MAC model
  Does the PHY model need to have specific formats? (ACL, SCO)