## Slide 1: Introduction to PHY and MAC contributions
“Case for DOQPSK High-rate Physical Medium”(077)
and
“Requirements and Recommended Functions in High-rate MAC” (079)
By: Chandos A. Rypinski For: IEEE P802.15.3 Tiburon, CA 94920 March 7, 2000 rypinski@microweb.com Albuquerque, NM

## Slide 2: What is addressed
Obvious: size, cost, power drain, but also:
“Decimegabit” transfer rates
Easily modelable MAC with DETERMINISTIC capacity for connection-type and packet services.
Provides for rate scalable and basic radio modulation
Coordination of MAC and PHY
Constructive use of overlapping coverage
High utilization traffic assignment

## Slide 3: What the PHY paper is about
“Case for DOQPSK High-rate Physical Medium Modulation”
Near constant envelope I and Q parallel data paths
Shape pulse modulation with either Bessel or better FIR filter
Demodulation using prior pulse as a phase reference for current pulse avoiding need for phase locked reference in demodulator
Preamble based acquisition of bit clock with coast through burst interval
Shows the simplicity and flexibility of the implementation.

## Slide 4: PHY paper purpose
Most of it is obvious and is to show additional support
It may not be obvious that the phase lock on the received carrier is not required for demodulation
Models of the radio can be built now without custom parts and in moderate commercial quantities
Integrated antennas for access point and station are essential to FCC type acceptance, and are normalizing influence on system design and simulation

## Slide 6: Main topics in the MAC paper
“Requirements and Recommended Functions in High-Rate MAC”
Paper is a reference on the factors that should be considered--particularly including traffic assumptions, integrated data and services and system plan for frequency reuse
Shows interrelationship between modulation, channel coding and antenna directivity in optimizing frequency reuse
Shows starting point isochronous period frame structure including broadcast header on downlink and provisions for propagation delay through the system
Shows un-novel access methods and multiple uses of polling

## Slide 7: MAC paper purpose--A
Suggest a protocol that might take on;y ten pages of state diagram (not 80)
Show a mostly deterministic access method
To show simplicity of PERMISSION, REQUEST, GRANT, TRANSFER, ACK procedure for all traffic transfers
Asymmetric, complementary protocol makes station simpler, and also the control terminal

## Slide 8: MAC paper purpose--B
The simpler PAN applications are served by subsetting, to functions necessary
Station has constant small vocabulary for any size of infrastructure
Use of polling is appropriate access method for short reach systems
Uses isochronous frame rate with asynchronous transfer within the frame

## Slide 9: MAC paper purpose--C
The down-link frame consists of preamble, broadcast field and traffic field
The first part of the broadcast field contains system identification, frame parameters and other information used by all stations
The next part is ACK/NACK for previous traffic received
The next part broadcasts identification of stations to which traffic will be sent and the index as to where it will appear
The next part broadcasts identification of stations granted access for traffic to be sent up and the index as to where it will appear

## Slide 10: MAC paper purpose--D
Central control shared by many access points provides many important benefits
Any amount of function may be provided to deal with and condition traffic for external networks
Multiple access points may be coordinated to manage redundant coverage as path diversity; and very much faster because all control and status information is at one point
A common data base maintained in real time enables retrieval of facts knowable before a communication is initiated

## Slide 12: MAC paper purpose--E
By concentrating all broadcast and addressed control messages in the first part of the downlink frame, a station may determine whether there is any traffic for it, and then sleep for the remainder of the frame
The shutdown of the LO multiplier and power amplifier chain within the radio is a substantial power saving when compared with radios that must be ready for broadcast messages at all times
This refinement of battery drain reduction is a result of cooperation between MAC and PHY

## Slide 13: MAC paper purpose--F
The default frame period is 6 millisecond which with 48 octets transferred per frame corresponds to a 64 Kbps one way B channel
Other frame periods at 8 and 12 milliseconds are possible and useful
The longer the frame period, the more fixed time losses are diluted down.
For transmitting 54 octet ATM cells, there would be no change in the perion--the burst would just last 6 bits longer

## Slide 14: MAC paper purpose--G
The polling function serves multiple purposes: access point association check, detection of disappeared stations, change of station settings (channel, power), sleep mode control, and non-contending receipt of service requests
The frequency of poll can be adaptive to reduce access delay for active stations
Sleep mode can be software defined and managed to adapt activity level
An open address poll also can solicit association requests

## Slide 15: MAC paper purpose--H
The station message vocabulary contains the following received message types:
  Poll with sleep mode control, settings change
  Poll with solicitation of service request
  Allotment of time for sending and receiving of traffic
and these transmitted message types:
  Association
  Service request
  Ack response to received packet traffic
  Up traffic transfer
and must be able to process the general part of the broadcast header

## Slide 16: MAC paper purpose--I
Segmentation of large files and packets is commonplace for less reliable medium to avoid excessive investment of channel in flawed transfers
Segment size is favorable in the range of 256-512 octets
Using header preamble-based synchronization, segment size is influenced by the accuracy of the radio bit clock crystal-- error determines how long the bit clock can run without refreshing
Use of crystals accurate to 10 ppm is recommended which could be satisfactory for a run of 1000 octets without margin

## Slide 18: Traffic Blocking Characteristics
System behavior must be defined for traffic offered that is in excess of capacity
All possible states resulting from high traffic in combination with source disappearance at the worst possible time must be considered
the service request facility must be out-of-band relative to the traffic carrying bandwidth so that requests can be analyzed and queued for order of arrival service
traffic may be served immediately, delayed and served, or it may be refused and cleared--the queues created enable high utilization of traffic transfer capacity (Erlang C)

## Slide 19: Avoiding Difficulty in MAC Design--1
The entry to all states should be the result of a positive event following a defined state
The delay or absence of an expected event is not a usable logic, but a processed abnormality--Presence or absence of a radio signal is not a usable state
Received signal quality must be measured as window shrinkage tolerance and not by rf level
Minimizing the number of defined states is less important than minimizing the number of undefined states

## Slide 20: Avoiding Difficulty in MAC Design--2
Address space should be generous and far greater than expected traffic capacity in one coverage
Fault detection should be ample and detailed
Logs should be maintained for traffic, faults and temporary overloads to enable diagnosis of system abnormalities
Security against unexpected power loss at the worst time must be provided

## Slide 21: Options on Frequency Reuse
The frequency reuse provision using 4-slot time division can be omitted with zero affect on the station--the provision is entirely an infrastructure function
A frequency reuse provision based on channel coding could probably convert code space to data space to obtain 4-bits per 15/16 bit symbol--this would be a method of greatly increasing delay spread tolerance without frequency reuse
Multi-level modulation will NOT normally provide a capacity advantage in an interference-limited system design

## Slide 22: Options on increased data transfer rate
The best method of doubling is to double the channel bandwidth with some penalty because the power spectral density is not easily (sometimes legally) doubled
Higher order modulations may be used with the same radio circuits
9QPR would increase transfer rate by 1.4, and 16QAM by 2 and at the same time interference susceptibility would be proportionally increased.
A data transfer rate of 20 Mbps in channel 20 MHz wide at 27 db down is a close call but 16 Mbps is conservative--FIR filtering will help

## Slide 23: Differentiating against 802.11 MAC
Deterministic capacity and delay analysis
Provides true connection-type service with reserved future capacity and predictable through-system transit time
Provides bandwidth-on-demand connections suitable for video streams
The user station is identical for systems large and small
The station is simpler (much smaller state diagram)nbecause all the intelligence is in the shared infrastructure

## Slide 24: Differentiating against 802.11a PHY (OFDM)
2.5 vs. 25 millisecond acquisition time ~50 vs. 250+ nanosecond delay spread tolerance
Active time supply power many times greater for OFDM DSP processor for comparable data rate in signal processors--compare DOQPSK vs. QPSK at 18 Mbps
0 vs. 7 db backoff on PA 1 dB compression point