## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Coexistence, Interoperability and Other Terms]
Date Submitted: [6 March, 2000]
Source: [David Cypher] Company [NIST]
Address [100 Bureau Drive, STOP 8920, Gaithersburg, MD 20899-8920]
Voice:[+1 (301) 975 4855], FAX: [+1 (301) 590 0932], E-Mail:[david.cypher@nist.gov]
Re: [Coexistence, Interoperability and Other Terms IEEE 802.15-99/134]
Abstract: [This presentation continues where the previous contribution “left-off”, trying to reach agreement on a definition of coexistence and the performance metrics to define coexistence.]
Purpose: [Agree to finer definitions on coexistence, Define performance criteria to evaluate the protocols/applications, and Define the “level of performance” where systems are defined to coexist]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Coexistence, Interoperability and Other Terms
An attempt to quantify Coexistence/Significantly Impact

## Slide 3: Coexistence, Interoperability and Other Terms
Further clarifications of definitions
Related terms
Discussion of terms
Analogy
Application of terms
Proposals

## Slide 4: Coexistence and Interoperability
Coexistence
Multiple wireless devices are said to “coexist” if they can be collocated without significantly impacting the performance of any of these devices.
The ability of one system to perform a task in a given (shared) environment where other systems may or may not be using the same set of rules.

## Slide 5: Coexistence and Interoperability(continued)
Interoperate - The ability for two or more systems to exchange information and to mutually use the information that has been exchanged
Interoperability - The ability for two systems to perform a given task using a single set of rules.

## Slide 6: Other Terms
Conformance/Conformance Testing/Conforming
Interwork/Interworking
Operability
Performance/Performance Testing
IUT, SUT, repeatability, system

## Slide 7: Discussion
TE
Switch 1
Switch 2
Switch 3
TE
1 Conformance Testing (User side of UNI)
2 Conformance Testing (Network side of UNI)
3 Conformance Testing of NNI (symmetrical)
4a Operability
4b Interworking (UNI to NNI)
5 Interoperability of TE and Switch 1
6 Interoperability of Switch 1 and Switch 2
UNI
UNI
NNI
NNI
(1)
(2)
(3)
(3)
(4b)
(4a)
(5)
(6)

## Slide 8: Interoperability
TE
Switch 1
Switch 2
Switch 3
TE
UNI
UNI
NNI
NNI
End-to-end interoperability
TE
Switch 1
IWF
Switch 3
TE
Interworking

## Slide 9: Analogy (Speech via air)

## Slide 10: In presence of interference

## Slide 11: Translator

## Slide 12: Application (normal environment)

## Slide 13: Application (coexistence environment)

## Slide 14: Proposals
Agree to finer definitions on coexistence and interoperability.
Define performance criteria to evaluate the protocols/applications.
Define the “level of performance” where systems are defined to coexist.

## Slide 15: Issues from Last Presentation
Definition did not specify that both systems had to apply the definition.
Significantly impact is a useless term. A quantity must be specified.

## Slide 16: Revised Definition
The ability of one system to perform a task in a given (shared) environment where other systems may or may not be using the same set of rules. While performing this task the system must not cause more 1/number of systems error rate for the other system(s)
For example if two systems 1/2 = 50%, if three systems 1/3 = 33%, etc