## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TTCN, Protocol Testing on Steroids!]
Date Submitted: [3Mar00]
Source: [Matthew Graney] Company [Telelogic North America Inc.
Address [1798 Technology Drive Suite 231 San Jose, CA 95110 USA]
Voice:[+1 408 451 3161], FAX: [+1 408 573 9799], E-Mail:[matthew.graney@telelogic.com]
Re: [Invited Speaker/IEEE 802 Conference Tutorial #2, 6Mar00 8:00pm to 9:30pm]
Abstract: [Tree and Tabular Combined Notation (TTCN); ISO/IEC 9646-1:1994 Overview]
Purpose: [This 802 Conference Tutorial will provide a technical overview of the Tree and Tabular Combined Notation (TTCN) which is a notation standardized by the ISO [ISO/IEC 9646-1:1994] for the specification of tests for communicating systems, and has been developed within the framework of standardized conformance testing. The Tutorial will specifically overview a TTCN-specified Test Suite which is a collection of various Test Cases together with all the declarations and components needed. The IEEE Projects 802.11 an 802.15 will be referring to and/or actively using these TTCN test suites in the writing and verification of their standards.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Page <number>
        <footer>
<header>
<date/time>
Here is my bio:
Mr. Matthew Graney has worked with Telelogic North America Inc. as an
Applications Consulting Engineer since October 1999. Prior to joining
Telelogic, Mr. Graney worked with Motorola in Australia in the development
of TTCN System Test solutions for GSM (Global System for Communication) and
GPRS (General Packet Radio Service) handsets. Mr. Graney has also worked for
the Australian Submarine Corporation in the field of Systems
Integration/Testing for large scale submarine-based computer systems. He
graduated from the University of Adelaide, Australia with an honours degree
in Computer Systems Engineering in 1993.
Best regards,
Matt
----
Matthew Graney Phone: 408-451-3161
Applications Consulting Engineer Fax: 408-573-9799
Telelogic North America Inc. mailto:matthew.graney@telelogic.com
1798 Technology Drive Web: http://www.telelogic.com
Suite 231
San Jose, CA 95110, USA

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area Networks
TTCN, Protocol Testing on Steroids!
Tutorial #2 8:00pm to 9:30pm
Monday, 6Mar00
Hyatt Regency Albuquerque, NM
Notes: Page <number>
        <footer>
<header>
<date/time>
Outline
I. What is TTCN and why should I care.
II. Where did TTCN come from?
II. What can TTCN do for me? And why would I want to use it?
III. How do I create TTCNs? What tools are available? Give examples of doing it by hand vs. generating TTCNs from SDL models
IV. Demonstrations of various TTCN scenarios
V. Conclusions

## Slide 3: Overview
Conformance Testing
  Behavior Testing
  ISO 9646
Introduction to TTCN
  Why use TTCN?
  ASN.1
  Terminology and Perspective
TTCN in the Real World
  GSM, 3GPP, Bluetooth
  TTCN Executable Test Suites
Demos and Conclusions
Overview
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Why Test Behavior?
Many protocols, many vendors
  interoperability is an issue
Brute force check for interoperability
  test all implementations against all other implementations
Better to use a standard test suite
  all vendors must pass
  does not guarantee interoperability, but increases confidence
product1
product2
product3
product4
TestSuite
product1
product2
productn
productn
?
Conformance Testing
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: Conformance Testing
Definition
  the process of verifying that an implementation performs in accordance (conforms) with a particular standard/specification.
Concerned with...
  external behavior (black box)
  prerequisites for interoperability
  testing of implementations
  but not with performance, reliability, fault tolerance, efficiency, etc.
Enables…
  preparation for interoperability
  comparability and mutual recognition of results
  reduction in the cost of testing
Conformance Testing
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: ISO/IEC 9646
ISO/IEC 9646 (ITU-T X.290)
  Framework and Methodology for Conformance Testing of Implementations of OSI and ITU Protocols
7 part standard
  1. General Concepts
  2. Abstract Test Suite Specification
  3. Tree and Tabular Combined Notation (TTCN)
  4. Test Realization
  5. Conformance Assessment Process
  6. Protocol Profile Test Specification
  7. Implementation Conformance Statement
Conformance Testing
9646
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: Why Use TTCN?
Quality
  a well-tested product increases confidence in the product’s quality
Time/Cost Improvement
  TTCN is a language designed for protocol conformance testing
  TTCN is standardized
  TTCN is fairly simple
Formal
  strict rules, complete BNF and operational semantics
Abstract
  TTCN test suites are independent of an implementation
Introduction to TTCN
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: TTCN Benefits
Standard
  avoids ad-hoc testing solutions
  ISO 9646 provides detailed framework for conformance test
  off-the-shelf test suites
    GSM (ETS 11.10)
    TETRA
    WCDMA
    3GPP
    etc.
Unique functionality for testing
  pre- and post-amble
  separate error handling
  verdicts
  conditional repeated loops
  wild card matching (*, ?)
  optional elements
  timer support
Introduction to TTCN
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: ASN.1
Abstract Syntax Notation One
  language for describing structured information
  standardized internationally (ISO/IEC 8824, ITU-T X.680)
TTCN includes ASN.1
  used for creating data descriptions and constraints
  can be part of TTCN script or imported as a module
SDL also includes ASN.1
  ITU-T Z.105
ASN.1 can be re-used across design and test!
Introduction to TTCN
ASN.1
SDL
TTCN
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Terminology (1)
Introduction to TTCN
Implementation Under Test (IUT)
  black box
System Under Test (SUT)
  the system containing the IUT
Test System
  the system/device performing the test
Abstract Test Suite (ATS)
  the TTCN test suite itself
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: Terminology (2)
Introduction to TTCN
OSI
Conformance Test
SP: Service Primitive
SAP: Service Access Point
PDU: Protocol Data Unit
ASP: Abstract Service Primitive
PCO: Point of Control and Observation
PDU: Protocol Data Unit
Tester: Lower and/or Upper Tester (TTCN scripts)
Layer S
Layer S
Layer T
Layer T
Layer N
Layer N
PDU
Service provided
Service used
SP
SP
SAP
Tester
IUT
Tester
ASP
ASP
ASP
PCO
PCO
PDU
ASP
ASP
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: TTCN Perspective
SUT
PASS, FAIL or
INCONCLUSIVE
TTCN
Test Suite
Result
IUT
Implementation
Under Test
Observe Responses
Send Stimuli
Behavioral testing
  send stimulus, observe response
  was response received within specified time?
Test System
Introduction to TTCN
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: Concurrent TTCN
Master
Test
Component
Parallel
Test
Component
Parallel
Test
Component
sync
sync
IUT
Introduction to TTCN
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14: TTCN in 3GPP
Lessons from GSM
  TTCN ATSs contribute to interoperability
  powerful competitive tool for entry to the global GSM mobile market
  TTCN ATSs widely used within members’ development processes
3GPP
  TTCN in Protocol Conformance Specs
    34.123-1 Prose description of tests
    34.123-2 Implementation Conformance Statement (ICS)
    34.123-3 TTCN Abstract Test Suite
  TTCN will be the normative specification
TTCN in the Real World
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: TTCN and Bluetooth
Bluetooth SIG selected TTCN for...
  definition of Protocol Requirements tests
    interoperability
  definition of Profile Requirements tests
    application interoperability
    end-user expectations
RF
Baseband
Audio
Link Manager
L2CAP
TCP/IP
HID
RFCOMM
Applications
Data
Control
TTCN in the Real World
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 16: Bluetooth Test Architecture
L2CAP Verification
Air
Interface
L2CAP
TCI-L2CAP
TCI
RF
BB
LM
L2CA
RF
BB
LM
L2CA
IUT
Test Suite
Executor
Physical Bus
TCI-L2CAP
Driver
Physical Bus
TCI-L2CAP
Firmware
Test System
Adaptor
TC Firmware
Implementation
dependent interface
TTCN in the Real World
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Example Bluetooth Test Cases
BB
  paging
  inquiry
LM
  authentication
  encryption
  information requests
  link handling
L2CAP
  connect/disconnect
  send/receive data
  group handling
  protocol multiplexing
  segmentation
  reassembly
  QoS parameter values
TTCN in the Real World
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: Executable TTCN
TTCN is abstract
  implementation and platform independent
ISO 9646-3 specifies operational semantics
  semantics defined using a functional approach
  maps ATS concepts to executable model
Executable Test Suite (ETS)
  must implement operational semantics
  one approach:
    compile TTCN to high-level language (C/C++, Java, etc.)
    develop adaptation for mapping TTCN primitives to real world
    link to form ETS
TTCN in the Real World
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: Demos
TTCN Demos
TTCN Language
  structure of a test suite
    Test Suite Overview
    Declarations Part
    Constraints Part
    Dynamic Part
  message definitions
  simple test script
SDL and TTCN
  ASN.1
    module shared by SDL design and TTCN test
  Co-simulation
    TTCN behaves as SDL system’s environment
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 20: Conclusions
TTCN has pedigree
  international standard
  used successfully in key protocols
TTCN has synergy...
  with ASN.1
  with SDL
TTCN can...
  improve time to market
  reduce the “cost of quality”
Thanks
Conclusions
Notes: Page <number>
        <footer>
<header>
<date/time>