## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area Networks
WPAN Coexistence Performance Evaluation:
MAC Simulation Environment and Preliminary Results
N. Golmie and F. Mouveaux
NIST

## Slide 2: Outline
MAC coexistence evaluation platform
Part I: Simulation Environment
  Traffic model
  MAC model
  PHY and RF assumptions
Part II: Preliminary Results
  Sanity check
  Bluetooth reference scenario: LAN Access

## Slide 3: MAC Coexistence Evaluation Platform
Explore different models for the MAC layer coexistence performance evaluation platform.
Invariant: performance results are collected at the MAC layer based on PHY, RF models and assumptions.

## Slide 4: MAC Coexistence: Model I
Heterogeneous set-up where BT and 802.11 are co-located within the same environment as proposed in [1].
Traffic Models
BT MAC
Traffic Models
802.11 MAC
Traffic Models
BT MAC
Traffic Models
802.11 MAC
PHY & RF Layer
Network Topology
in a Coexistence Environment
[1] IEEE 99/117
PHY & RF Layer
PHY & RF Layer
PHY & RF Layer

## Slide 5: MAC Coexistence: Model II
Homogeneous set-up where different devices (BT or 802.11) are considered separately with respect to (accurate) interference models.*
Traffic Models
BT MAC
Traffic Models
BT MAC
Interference Models
based on experimental
measurements, analysis
PHY & RF Layer Assumptions
PHY & RF Layer Assumptions
* IEEE 802.15-99/98r0

## Slide 6: Simulation Environment

## Slide 7: Traffic Models: LAN Access
LAN Access Profile, Bluetooth Spec. V1.0B
PPP connection with LAP in order to gain access to a LAN.
IP
PPP
RFCOMM
TCP/UDP
L2CAP
BB
PPP Networking
PPP
RFCOMM
L2CAP
BB
ME
LAN
IP
TCP/UDP
LAN Access Point: Ethernet, Token Ring, Fiber Channel, Cable Modems, Firewire, Home Networking
Data Terminal: Laptops, Notebooks, desktop PCs and PDAs
LAN

## Slide 8: Traffic Distribution: IP Packet Generation
* IEEE 802.14/96-083r2

## Slide 9: Packet Encapsulation
PPP
FLAG
Address
Control
Protocol
INFO = 0 -1500 bytes
FCS
FLAG
IP
8
8
8
16
16
8
IP Packet: Header + Payload
RFCOMM
Address
Control
Length
INFO =ANY SIZE
FCS
8
8
8-16
8
L2CAP
Channel ID
Length
PAYLOAD = 0 - 65535 bytes
16
16

## Slide 10: Baseband Segmentation
L_CH
Flow
Length
PAYLOAD= 0 - 121 bytes
CRC
2
1
9
L2CAP
Channel ID
Length
PAYLOAD = 0 - 65535 bytes
16
16
DM3
4
16
2/3
FEC
L_CH
Flow
Length
PAYLOAD= 0 - 224 bytes
CRC
2
1
9
DM5
4
16
2/3
FEC
Header
Access Code
PAYLOAD = 0 - 2745 bits
72
54
Baseband

## Slide 11: MAC Model
*OPNET is a Trademark of OPNET Technologies Inc.
Developed a BT MAC device in OPNET*.

## Slide 12: MAC Model Assumptions
Connection mode (no page scan or inquiry)
Master / Slave models
Round Robin master transmission scheduler
Asynchronous Connection Less (ACL) Link
Frequency Hopping
Future Extensions
Synchronous Connection Oriented (SCO) Link
master scheduler
broadcast; L2CAP (?); LMP (?)

## Slide 13: TX Model Attributes*
* OPNET Transmitter model attributes

## Slide 14: TX Parameters
Transmission+Propagation delay: computes the time required to transmit a packet until it reaches its destination.
Closure: determines if a signal can reach a destination and allows dynamic enabling and disabling of links.
Channel match: classifies the transmission as valid, noise, ignore based on frequency, bandwidth, data rate, spreading code etc.
Transmitter antenna gain: computes transmitter antenna gain in the direction of the receiver.

## Slide 15: RX Model Attributes*
* OPNET Receiver model attributes

## Slide 16: RX Parameters
Noise figure:effect of thermal noise on radio transmission.
Ecc threshold/model: Percentage of bit errors allowed in a packet (err/bit).
Power model: computes the received power level for an incoming transmission.
Background noise/ Inoise: computes the background/ interference noise affecting incoming radio transmissions.
SNR/ber models: computes signal-to-noise ratio and expected bit error rates.

## Slide 17: RX Statistics
BER: bit error rate for the packet arriving at the receiving channel.
Packet loss ratio: boolean value corresponding to the acceptance/rejection of packets.
Power: average power of packet arriving at the receiver channel.
Signal/noise ratio: ratio of the average power of a packet received and the combined average power of interference sources.

## Slide 18: Channel Attributes*
* OPNET Channel attributes

## Slide 19: Preliminary Results

## Slide 20: Sanity Check
Number of devices in a piconet:
  2 devices (Master/ Slave).
Distance between devices: 10m
Traffic: DM5 packets symmetric master/slave communication, exponential distribution for packet interarrival rate.
Baseband packet size is:
  72 + 54 + (224 + 2 + 2) * 8 + FEC = 2871 bits
Access Header payload DM5 Header CRC 6 + 915

## Slide 21: Sanity Check (cont.)
Maximum bit rate per device (including headers, CRC, FEC overhead) is:
  2871/(5 * 625 * 2) = 0.45936 Mbits/s
Minimum access delay (master) at low offered load (no packet waiting in buffer) is:
  5 (slots) * 625 (us) = 3.125 ms
Maximum access delay (master) at low offered load (no packet waiting in buffer) is:
  15 (slots) * 625 (us) = 9.375 ms

## Slide 22: Sanity Check Results: Throughput

## Slide 23: Sanity Check Results:Access Delay
*
**
Note: ** Access delays are collected at the slave corresponding to the master traffic access delay.
** Offered load is a percentage of the total channel capacity in both directions

## Slide 24: LAN Access Scenario
Number of devices in a piconet:
  2 devices (Master/ Slave).
Distance between devices: 10m
Traffic: LAN Access (IP traffic distribution)
Average packet size is: 385.1 bytes
  1 DM5 (224 bytes) + 1 DM5 (162 bytes) = 4992 bits
Maximum bit rate per device (including headers, CRC, FEC overhead) is:
  4992/(10 * 625 * 2) = 0.39936 Mbits/s

## Slide 25: LAN Access Results: Throughput

## Slide 26: LAN Access Results:Access Delay
Note: ** Access delays are collected at the slave corresponding to the master traffic access delay.
** Offered load is a percentage of the total channel capacity in both directions
*
**

## Slide 27: Summary
Presented a status report on the BT MAC model development.
Preliminary results:
  sanity check
  BT reference scenario

## Slide 28: Next Step
Results:
  WLAN reference scenario
  Heterogeneous scenario with 2 WLAN devices and 2 BT devices.
Continue the development of the BT MAC model.
Extend the PHY and RF models
Several scenarios to look at with different traffic types, number of devices, configurations.