## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Bluetooth Testing]
Date Submitted: [3 March 2000]
Source: [Mårten Mattsson, M.Sc] Company [Ericsson Mobile Communications AB, c/o BSIG]
Address [Scheelevägen 15 , S-221 83 LUND Sweden]
Voice:[+46 46 194788 ], FAX: [+46 46 194704], E-Mail:[Marten.Mattsson@ecs.ericsson.se]
Re: [N/A]
Abstract: [Bluetooth Testing, c/o Bluetooth Developers Conference, BSIG, and Bluetooth Certification & Verification.]
Purpose: [Provide an overview to the IEEE on the Bluetooth Testing issues.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area Networks
Bluetooth Testing
March 2000, Albuquerque, NM USA

## Slide 3: Bluetooth Testing
By Mårten Mattsson
Ericsson Mobile Communication
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Outline
Present the test strategy for verifying the:
  Radio link quality
    The Bluetooth Radio Link Requirements
  Interoperability between products and brands
    The Bluetooth Protocol Requirements
    The Bluetooth Profile Requirements
Summary
Discussion
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5
First
Present the:
  Test Concept
  Test Configuration
  Test Specification (with Test case examples)
for:
  The Bluetooth Radio Link Requirements
  The Bluetooth Protocol Requirements
  The Bluetooth Profile Requirements
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Bluetooth Radio Link Requirements Test Concept
Goal
  To ensure Bluetooth devices can get in contact with each other
  To ensure the Radio Link performance

## Slide 7
Bluetooth Radio Link Requirements Test Concept
Test Purpose
  To verify the physical layer of the Bluetooth protocol stack, that is RF and parts of BB
Method
  The defined Test Mode in the Bluetooth core specification will be used

## Slide 8: Bluetooth Radio Link Requirements Test Configuration
Notes: Page <number>
        <footer>
<header>
<date/time>
1) Explain the picture
1) IUT - Implementation Under Test
The device we are going to verify
2) Test System - The tester that we will
use for the verification
3) Air interface - The only interface needed
between the tester and the IUT. We uses LMP
commands for Test Mode signalling
4) Locally activation of the Test Mode for the IUT
2) Typical Test Scenario:
1) Operator activates the Test Mode on the IUT
(local activation)
2) Tester establish connection to the IUT
(normal procedure)
3) Tester "forces" or turns the IUT into test mode
(done with LMP signalling)
4) Tester performs measurements
5) Tester leaves test mode
6) Tester disconnect from the IUT

## Slide 9: Bluetooth Radio Link Requirements Test Specification
Based on:
  Part A & Part B of the core specification
    Part A harmonized with ETSI and FCC recommendations
Informal (prose) and contain TCs for
  Transmitter tests
  Transceiver tests
  Receiver tests
  Timing and hopping test

## Slide 10: Bluetooth Radio Link Requirements Example of Test Cases
Transmitter
  Output Power
  TX Output Spectrum
  Initial Carrier Frequency Tolerance
Transceiver
  Out-of-Band spurious emissions
Receiver
  Sensitivity
  C/I performance
  Out-of-Band blocking
Lower Base band
  TX/RX Timing
  Frequency Hopping
  Coding/Decoding
  Error correction

## Slide 11
Next
Present the:
  Test Concept
  Test Configurations
  Test Specification (with Test case examples)
for:
  The Bluetooth Radio Link Requirements
  The Bluetooth Protocol Requirements
  The Bluetooth Profile Requirements

## Slide 12: Bluetooth Protocol Requirements Test Concept
Goal
  To ensure that Bluetooth devices can talk with each other
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13
Bluetooth Protocol Requirements Test Concept
Test Purpose
  To verify the implementation of the
    BB, LM and L2CA layer and HCI, if applicable
Method
  Single-Protocol testing with use of an upper tester (horizontal testing)
  The upper tester accesses the SUT/IUT through the Test Control Interface, TCI (included in version 1.0 of core spec.)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14
Bluetooth Protocol Requirements Test Configuration - BB and LM verification IUT without HCI, physical transport bearer (USB, RS232,UART)
Notes: Page <number>
        <footer>
<header>
<date/time>
1) Explain picture:
1) Implementation Under Test - Device that we are going to verify
2) Test system that will be used for testing - Protocol tester
3) Air interface
4) The Test Control Interface, NEW
- To access the Upper Tester
- Physical Interface /or can be a “SW” interface
- The SW interface must be agreed by the BQTF
5) Test Control Software
- Adapter to TCI
- adapt implementation dependent interface ->TCI
- Bus driver, if physical interface
- Test Software with MMI/GUI if SW interface
2) Why do we need the TCI
IT is needed to be able to access the “upper interface” of the protocols to be able to perform protocol verification.
- The reason is: IUT initiating features.
- We use it to stimulate the IUT
- To shield the tester from different types of interfaces
3) Usage of the interface
- FOR BB AND LM testing TCI = HCI
- ONLY REDUCED SET OF HCI FUNCTIONALLITY
- Semantically and syntactically equal to HCI (we use HCI command and events), but again only a subset of them.
- To stimulate the IUT to initiate signalling
- eg. Authentication/Encryption etc.
4) example test scenario
1) Tester initiate or IUT initiate (Air/TCI)
2) Tester verifies signalling on protocol level (over the air)
3) if information needed form higher layer/host ->
This information can come from the tester (via TCI) or
hard-coded in the TC Software.
5) Other types of transport bearer:
SW version possible : Must be agreed by the BQTF
TC Software -> Test application that include the same functionality as if using TCI over a physical bearer.

## Slide 15
Bluetooth Protocol Requirements Test Configuration - BB, LM & HCI verification IUT with HCI, physical transport bearer (USB, RS232,UART)
Notes: Page <number>
        <footer>
<header>
<date/time>
1) Explain picture again. Same as before
2) Difference when we have a HCI module
- No extra adapter needed
- We use the HCI as the TCI
- No extra burden for the manufacturers of the device IUT
2) Test scenario - same
Although for HCI verification also the HCI signalling itself will be verified
If support for the HCI functionality is clamed by the manufacturer

## Slide 16
Bluetooth Protocol Requirements Test Configuration - L2CAP verification
Notes: Page <number>
        <footer>
<header>
<date/time>
1) Explain the picture again
- This time the TC Software maps the implementation dependent interface to the TCI-L2CAP
2) Explain TCI-L2CAP
- A mapping of L2CAP primitives over HCI
- Uses the same HCI command packet structure
- The same HCI event packet structure
- Same physical bearer as defined for HCI (in core spec)
- Reserved specific event code and Opcode group for testing (included in 1.0 version of HCI specification)
- The mapping of the L2cap primitives described in TCI document (included in core spec version 1.0. Part J:3
3) test scenario as for BB,LM or HCI verification

## Slide 17: Bluetooth Protocol Requirements Test Specification
Based on Part B to Part E of core spec
  Part H if applicable (HCI support)
Informal (prose) and Formal (TTCN)
  Prose version contains
    Test Suite Structure
    Test Purposes with test instructions
  TTCN version contains the Abstract Test Suite, ATS
    Test Cases/Test Steps

## Slide 18: Bluetooth Protocol Requirements Example of Test Cases
BB
  Paging
  Inquiry
LM
  Authentication
  Encryption
  Information requests
  Link Handling
L2CAP
  Connect/Disconnect
  Send/Receive data
  Group handling
  Protocol Multiplexing
  Segmentation
  Reassembly
  QoS parameter values
Notes: Page <number>
        <footer>
<header>
<date/time>
BB
LM
-Authentication
Authentication
Pairing
Creation of the link key
Change link key
- Encryption
Mode
Key size
Start & Stop encryption
- Information requests
Offset (clock/ slot)
Timing accuracy
LMP version
Supported features
Name request
- Link Handling
Connection establishment
Paging scheme
Master/Slave switch
Detach
Hold/Sniff/Park mode
Power control
Quality of Service
SCO link handling
Control of Multi-slot packages
Link Supervision

## Slide 19
Finally
Present the:
  Test Concept
  Test Configurations
  Test Specification (with Test case examples)
for:
  The Bluetooth Radio Link Requirements
  The Bluetooth Protocol Requirements
  The Bluetooth Profile Requirements

## Slide 20: Bluetooth Profile Requirements Test Concept
Goal
  To ensure that Bluetooth devices can execute applications together and meet end-user expectations

## Slide 21
Bluetooth Profile Requirements Test Concept
Test Purpose
  For each profile the Bluetooth product claims to conform to, profile testing will be performed to verify the Bluetooth profile requirements.
Method
  Profile Testing using the MMI of the product as “upper” interface
  Multi-protocol testing (vertical testing)

## Slide 22
Bluetooth Profile Requirements Test Configuration
Notes: Page <number>
        <footer>
<header>
<date/time>
1) Explain picture
- 1 The System Under Test - a product
- 2 The Test System “acting” as the opposite role of the profile
- 3 The Air interface
- 4 The MMI of the product (I.e. can be the button on the headset, the keypad and display on a terminal/cellular phone)
- 5 External application like browsers/file transfer applications etc.
2) Test scenario
If SUT should initiate, the operator will get instructions from the tester to react on the MMI. Operator also feedback results to tester.
Test signalling between the product and the tester (between roles)
NOTE: Early stage since profiles only have been available from version 0.9 of core spec.

## Slide 23: Bluetooth Profile Requirements Test Specification
Based on Part K of the core specification
Both roles of the profile will be handled
Informal (prose) and Formal (TTCN)
  Prose version contains:
    Test Suite Structure and Test Purposes
  TTCN version contains the Abstract Test Suite, ATS:
    The same Test Suite Structure
    Test Cases/Test steps

## Slide 24: Bluetooth Profile Requirements Example of Test Cases
Headset
  Initialisation
  Audio connection
  Connection transfer
  Connection release
Dial-up Networking
  Initialisation
  Data calls
  Command Support
Synchronisation
  Initialisation
  PIM exchange
  Automatic Synchronisation
LAN Access
  Initialisation
  Shutdown
  Establish LAN connection
  Lost LAN connection
  Disconnect LAN connection

## Slide 25: Summary
Testing the BT Radio Link Requirements
  Devices can get in contact with each other
  Verifying the physical layer, RF, parts of BB
  Use of Test Mode
  Informal test specification

## Slide 26
Summary
Testing BT Protocol Requirements
  Get devices to talk with each other
  Verifying BB, LM, L2CAP & HCI (if applicable)
  Single protocol testing, horizontal testing
  Use of an Upper Tester, access with TCI
  Several different test configurations
  Both informal and formal test specification

## Slide 27: Summary
Testing BT Profile Requirements
  Get devices executing applications together
  Verifying conformance to the profiles
  Multi-protocol testing, vertical testing
  Using MMI as upper interface
  Test configuration dependent on profile
  Informal and Formal test specification

## Slide 28: Discussion
Questions ?