## Slide 1: An OFDM based solution anticipating the convergence between next G of high rate WPANs and WLANs: HIPERPAN?
Marc de Courville
Broadband Systems and Technologies Research Lab
Motorola Labs - Paris/ CRM
Communication Systems and Technologies Labs

## Slide 2: Major opportunities and convergence scenario

## Slide 3: WPAN&WLAN shall meet!
Observations:
  foreseen convergence in bitrate requirement between next generation of WPANs (high data rate) and WLANs!
    WPAN: IEEE802.15 HRSG (20Mbps), Bluetooth SIG2 (2-10Mbps) >20Mbps
    WLAN: IEEE802.11a, ETSI BRAN HIPERLAN/2, ARIB MMAC: 6-54Mbps
  no coordination could result in a plurality of competing systems in the same band
  OFDM preferred modulation for local area broadband (large bandwidth transmissions in presence of multipath)
Goal&requirement: address higher bitrate demand for WPAN devices
  anticipate convergence between WPAN&WLAN
  preserve specificity of WPAN: low cost, low range, peer to peer, embeddable
  grant interoperability with 5GHz WLANs: e.g. provide a mean to sync devices both in office and home environment
  access 5GHz band as spectrum opportunity for WPAN (escape mw-oven spurious)
In-Building
Neighborhood
Personal
Satellite
Wide Area
Beyond
Pico
Micro
Femto
Global
Macro
  support for realtime audio and video

## Slide 4: HiperPAN: strategy proposal for addressing WPAN&WLAN convergence
A possible solution:
  take the opportunity of worldwide harmonization WLANs PHY layer @ 5GHz
  grant interoperability through integration already @ PHY level
HiperPAN concept!
  Cost effective solution for high speed WPAN = P2P system derived from cut down of HIPERLAN/2,IEEE802.11a,MMAC
  20MHz bandwidth, OFDM based with 52 carriers
Allows:
  a maximum silicon reuse!
  to relax RFFE impairments (oscillators & ADC accuracy)
  reduction of range (10m?) resulting in power consumption savings (PA linearity)
Technical requirements:
  compatibility requires at minimum ability to decode BPSK 1/2 mode: 6Mbps
  QPSK 3/4 achieves 18Mbps
  Adhoc mode (HIPERLAN/2 Home Environment DLC extension) for self organizing (dynamic Central Controller selection)
  isochronous services support (audio/video)
  perhaps simpler coding scheme for direct link (DILCH)?

## Slide 5: Materializing the concept
3 distinct spaces exist and should be addressed by standard bodies:
  office/home/personal environments
First 2 are already covered by WLANs: HIPERLAN/2, WPAN in EU remains!
Issues/questions:
  HIPERPAN should belong to HIPERLAN/2 family
  What are the extensions required at the DLC level? Is Home Extension sufficient?
  How HIPERPAN should be handled: through creation of new receiver class/transmission mode (restricted to xMbps, revised modulation accuracy)?
Key components of the success
  a must: gain consensus
  strive for a unique platform in the 5GHz band for several wireless applications including WPAN&WLAN
  promote the HIPERPAN concept among the WPAN&WLAN communities
  creation of a HIPERLAN/2 HIPERPAN task force

## Slide 6: The thinking process in a nutshell
  Fact: higher rate demand for next generation of WPANs is 20Mbps
  perhaps not possible to achieve such rate with enough QoS in the 2.4GHz band due to spurious from mw-oven
  foreseeable WPAN community trend: move in the safer 5GHz band and go for dual mode for BT1 backward compatibility
  this approach could result in a fragmentation of standards resulting in competing standards for the same band
  by CEPT regulation, 5GHz band is reserved in Europe for HIPERLANs (DFS/PC)
  in Europe: one standard for all, ETSI BRAN resulting in a good coordination but not yet addressing the PAN space...
  HiperPAN concept: embed WPAN in WLANs HIPERLAN/2 targeting a lower cost solution for WPANs (cut down version)
  benefits: PHY level inter-operability would be granted between WPAN-WLAN in one unique standard worldwide harmonized (PHY layer wise)
  lower cost solutions feasible, sketch of a technical proposal is proposed: same parameters of HL2, but with one lower mode constellation (e.g. QPSK R=3/4 enabling 18Mbps) using parts of home extensions for ad-hoc networking.