## Slide 1
IEEE P802.15 Working Group for Wireless Personal Area Networks
Packet Error Rate of an IEEE 802.11 WLAN in the Presence of Bluetooth
Detailed paper is document IEEE P802.15-00/133r0

## Slide 2: Objective of this Analysis
Develop Theoretical Packet Error Rate equations for an IEEE 802.11 WLAN in the presence of a Bluetooth Piconet.
Prepare for the incorporation of more accurate Physical Layer Models.
Complement the Simulation model that is being developed.

## Slide 3: Previous Work
Greg Ennis, Impact of Bluetooth on 802.11 Direct Sequence, September 1998.
Jim Zyren, Extension of Bluetooth and 802.11 Direct Sequence Model, November 1998.
Jim Zyren, Reliability of IEEE WLANs in the Presence of Bluetooth Radios, September 1999.
A. Kammerman, Coexistence between Bluetooth and IEEE 802.11 CCK Solutions to avoid mutual interference, January 1999

## Slide 4: Description of Packet Timing
WLAN packet is TW seconds long.
I am only considering the case of periodic Bluetooth packets.
Bluetooth interval is TBI. This can be either 625 sec, 1.875 msec, or 3.125 msec.
Bluetooth packet is TBP long.
Offset between WLAN and BT is a random variable, x.

## Slide 5: Timing Figure

## Slide 6: Timing Analysis
Need to calculate the time each Bluetooth packet overlaps with WLAN packet. Call that time: Ti
First packet: T1 = max(TBP - x, 0).
Next packets: Ti = TBP
Last two packets have complicated formula (see paper).

## Slide 7: Probability of WLAN Packet Error
The probability of a packet error is one minus the probability of a good packet.
P(PE) = 1 - P(GP)
Need to condition on random variable x in order to proceed further.
First convert x to a discrete random variable. Its probability mass function is,
px(k) = 1/K k = 1, 2, … K

## Slide 8: Probability of WLAN Packet Error
Probability of a good packet is,
P(GP) =  P(GP|x = k) px(k)
Now we need to find the conditional probability of good packet.
Label the segment of the WLAN packet overlapping each Bluetooth packet as Si
For WLAN packet to be good each segment must be good. GSi means segment Si is good.

## Slide 9: Probability of WLAN Packet Error
Conditional probability is then,
P(GP|x=k) =  P(GSi|x=k)
The frequency of each Bluetooth packet is a uniform random variable.
Pf(j) = 1/79 j = 1, 2, … 79
If we condition on x and f then we can start to figure out if each segment is good.

## Slide 10: Probability of WLAN Packet Error
Condition on x and f,
P(GSi|x=k) = (1/79)  P(GSi |x=k, f = j)
For a fixed value of x and f we need to know the probability of a bad segment.
Determine the number of symbols in that WLAN segment. What is the probability all the symbols in that segment are good?

## Slide 11: Probability of WLAN Packet Error
From Physical Layer Model we need,
pe = P(e | , f = j) = g (, j)
This is the symbol error rate at a given signal-to-interference (SIR) ratio  and Bluetooth channel frequency f = j.
There are mi symbols in segment Si
The mi follow from the Ti from earlier.
Probability of all symbols being good is,
P(GSi | x=k, f=j) = (1 - pe)mi

## Slide 12: Probability of WLAN Packet Error
All these equations can be combined to give the formula for the probability of a WLAN packet error. This is what we refer to as the WLAN Packet Error Rate.
The equations are summarized in the detailed paper IEEE P802-15-00/133r0.

## Slide 13: Simplified 1Mbps FHSS WLAN Example
WLAN packets with 200, 500, and 1000 byte payloads.
Single-slot Bluetooth packets.
Simplified Physical Layer model
pe = 0.5 In one channel
pe = 0 For all 78 other channels

## Slide 14: 1 Mbps FHSS WLAN Results

## Slide 15: Simplified 1 Mbps DSSS WLAN Example
WLAN packets with 200, 500, and 1000 byte payloads.
Single-slot Bluetooth packets.
Simplified Physical Layer model
pe = 0.5 In 22 channels
pe = 0 In all 57 other channels

## Slide 16: 1 Mbps DSSS WLAN Results

## Slide 17: Next Steps
Compare results to those of the Simulation being developed.
Incorporate more accurate Physical Layer Models.
Consider three-slot & five-slot Bluetooth packets.
Consider higher-rate 802.11 systems.