## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area Networks
Update on the MAC Coexistence Modeling Effort
N. Golmie and F. Mouveaux
NIST

## Slide 2: Outline
Objectives
Part I: Progress Report
  Additional Features/ Functionality
  MAC/ PHY Interface
  Example of BER Modeling
Part II: Case Study
  Traffic Model
  Simulation Results

## Slide 3: Objectives
Give a progress update on the MAC modeling effort.
Demonstrate the model capabilities and experiment with different BER distributions.

## Slide 4: Progress Report

## Slide 5: Basic Model 3/00
Connection mode
Round Robin master scheduler
Asynchronous Connection-Less (ACL) Link
Frequency Hopping
Addionnal Features 5/00
L2CAP segmentation and reassembly
Polling
BER modeling
FEC, CRC and HEC
Retransmission (ARQ and SEQN)
Statistics collection

## Slide 6: MAC / PHY Interface
1) A dynamic interface includes 3 steps:
  creation of a bit stream
  function call to PHY model and execution of MATLAB or “C” routine.
  regeneration of Baseband frame (with errors).
2) A parametric interface captures the characteristics of the BER distribution:
  number of errors in a packet
  location of errors in a packet

## Slide 7: Example of BER Modeling
Parametric interface based on a two-state Markov model*.
Error Free
Error
Pge = 0.382
Peg = 0.006
* G. T. Nguyen, R. H. Katz, M. Satyanarayanan, B. Noble, “A Trace-based approach for modeling wireless channel behavior,” Proceedings of the Winter Simulation Conference, pp. 597-604, Orlando Florida, December 1996.
Number of errors:
Fixed percentage with respect to the packet size
Exponentially distributed percentage with respect to the packet size
Placement of errors in packet:
Random (uniformly distributed on the packet length , U(0,1))
Consecutive errors

## Slide 8: Case Study

## Slide 9: Traffic Model: Connectionless Application
Simple ICMP application (i.e ping) is preferred over TCP because it has no error recovery and connection establishment mechanisms.
LAN Access Profile, Bluetooth Spec. V1.0B
PC to PC connection using LAN access.
IP / ICMP
PPP
RFCOMM
UDP
L2CAP
BB
PPP Networking
RFCOMM
L2CAP
BB
ME
LAN
UDP
Data Terminal + LAN Access Point
Data Terminal
IP / ICMP

## Slide 10: Packet Encapsulation
PPP
FLAG
Address
Control
Protocol
INFO = 64/ 72 bytes
FCS
FLAG
ICMP
8
8
8
16
16
8
RFCOMM
Address
Control
Length
INFO =ANY SIZE
FCS
8
8
8-16
8
L2CAP
Channel ID
Length
PAYLOAD = 77 / 85 bytes
16
16
ECHO
ECHO_REPLY
64 x 8
L_CH
Flow
Length
PAYLOAD= 81/ 89 bytes
CRC
2
1
9
DM3
4
16
2/3
FEC
Header
Access Code
PAYLOAD = 1146 / 1251 bits
72
54
Baseband
72 x 8
or

## Slide 11: Master/ Slave Packet Transmission (1)
DM3
Echo
ICMP
L2CAP
BB
DM3
ICMP
L2CAP
BB
MASTER
SLAVE
CHANNEL
NULL
NULL
Echo
DM3
DM1
POLL
1)
2)
3)
DM3
DM1
POLL
Echo R
Echo R
DM3
DM3
Echo R
Echo R
Echo
Echo
POLL
DM3
DM1
NULL
POLL
DM3
DM1
NULL
1)
2)
3)

## Slide 12: Master/ Slave Packet Transmission
DM3
Echo
ICMP
L2CAP
BB
DM3
ICMP
L2CAP
BB
MASTER
SLAVE
CHANNEL
NULL
NULL
Echo
POLL
Choose Option 3)
POLL
Echo R
Echo R
DM3
DM3
Echo R
Echo R
Echo
Echo
POLL
NULL
POLL
NULL
Choose Option 3)
POLL
NULL
POLL
NULL
Repeat n times
Idle Time x

## Slide 13: Simulation Parameters
Number of devices in a piconet:
  2 devices (Master/ Slave).
Distance between devices: 10m.
Traffic: ICMP application:
  n = 2 and x = 0.00625 * n * (1/Load -1)
  where Load is % of max throughput.
100% Throughput = 464160 bits/s.
Measurement are performed at:
  L2CAP for access delay, throughput, and goodput.
  Baseband for packet loss

## Slide 14: BER = 0.25% , Average Delay

## Slide 15: BER = 0.25% , Delay Percentiles

## Slide 16: BER = 0.25%, Coefficient of DelayVariance

## Slide 17: BER = 0.25% , Packet Loss

## Slide 18: BER = 0.25% , Throughput

## Slide 19: BER = 0.25%, Goodput

## Slide 20: BER = 1%, Average Delay

## Slide 21: BER = 1% , Delay Percentiles

## Slide 22: BER = 1%, Coefficient of DelayVariance

## Slide 23: BER = 1% , Packet Loss

## Slide 24: BER = 1% , Throughput

## Slide 25: BER = 1%, Goodput

## Slide 26: Load 50%, Average Delay

## Slide 27: Load = 50% , Delay Percentiles

## Slide 28: Load = 50%, Coefficient of Delay Variance

## Slide 29: Load= 50% , Packet Loss

## Slide 30: Load = 50% , Throughput

## Slide 31: Load = 50%, Goodput

## Slide 32: Next Step
More Results:
  more experiments with different BER, loads, number of devices.
Continue BT MAC model development:
  SCO, master scheduler.
Work on MAC/ PHY interface
  BER modeling.
Presented a status report on the BT MAC model development.
Gave an example of BER modeling
Summary