## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Interference/Coexistence of WLAN/WPANs via SystemView]
Date Submitted : [ 9 May 2000]
Source: [Maurice Schiff] Company: [Elanix, Inc.] and [Michael Dydyk] Company: [Motorola Inc.]
Address: [5655 Lindero Canyon Rd. ,Suite 721, Wetlake Village, CA, 91362]
[8220 E. Roosvelt St., Scottsdale, AZ, 85257]
Voice:[818-597-1414], FAX: [818-597-1427]< E-Mail [maury@elanix.com]
[480-441-2074], FAX: [480-441-0830]< E-Mail [michael.dydyk@motorola.com]
Re: [N/A]
Abstract: [This presentation describes a PC based simulation engine that can be used to investigate
many aspects of the WLAN/WPAN PHY layer performance, including BER performance, effects of
other user interference, etc.]
Purpose:[ To provide WLAN/WPAN developers a means for rapidly and accurately investigating their
system designs.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for
discussion and is not binding on the contributing individual(s) or organization(s). The material in this
document is subject to change in form and content after further study. The contributor(s) reserves(s) the
right to add, amend or withdraw the the material contained within.

## Slide 2: Agenda
Introduction
Overview of SystemView
Bluetooth Model
Interferor Models
  Frequency Hoping Spread Spectrum
  Direct Sequence Spread Spectrum
Results of Simulation
Conclusions

## Slide 3: What is SystemView?
The rapid prototyping tool for system design engineers that want to:
  Implement a design with minimum effort
  Perform trade studies
  Analyze Results
    AND
  Migrate to Hardware

## Slide 4: SystemView Overview
Perform Bit-True, Multi-rate, and Mix-Mode simulations in an efficient manner.
PC Based Software Simulation Tool
  Block diagram editor with Application Specific libraries.
And a “Virtual Work Bench” that offers all the functions of “Real World” laboratory equipment.

## Slide 5: Key SystemView Benefits
Simulate all types of modulation
Add any number of interferers with arbitrary modulation and power levels
Peform complete parameter (BER) studies in a single run
End to end simulations includeing rf and DSP portions of the design (mixed mode)
Easy-to-learn and Ease-of-use
  Be productive rapidly
  Develop and modify sophisticated user models quickly
Notes: SystemView’s key advantage is its ability to model and simulate complex systems, such as multirate and mixed signal applications, while retaining ease-of-use. To create realistic models SystemView enables you to include the effects of noise, limited bit-widths, and fixed-point arithmetic. With SystemView, you can model your system comprehensively and in sufficient detail to optimize and test it thoroughly up front.
Traditional system-design tools are typically rather difficult to use. As a result, designers usually find it is difficult to completely model complex systems. This in turn reduces the effectiveness of design optimization and testing at the system-level, increasing the chances of problems occurring later in the design cycle.

## Slide 6: Block Diagram Editor

## Slide 7: Time Specification Form

## Slide 8: Typical Analysis Displays

## Slide 9: SystemView Filter Design
Filter Design is Included in Basic SystemView
  An extensive filter design window to generate
    FIR Filters
    IIR Filters
    Communications Filters
    Custom Filters
    DSP bit true mode

## Slide 10: Filter Design

## Slide 11
Global Parameter Form

## Slide 12: 802.11 DSSS With Interference

## Slide 13: 802.11 Spectra

## Slide 14
Overlay of DSSS and Interference Spectra

## Slide 15: DSSS Eye Diagram

## Slide 16: Bluetooth Model with DSSS Interference

## Slide 17
Effect of DSSS Interferer on Bluetooth
Performance

## Slide 18: Bluetooth Model With FH Interference

## Slide 19: Effect of FH Interferer on Bluetooth Performance

## Slide 20: GSM Receiver Design

## Slide 21: SystemView Optional Libraries

## Slide 22: Conclusions
Impact on performance of WLAN/WPANs, as related to interference/coexistence, can be predicted apriory using existing simulation tool.