## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Bluetooth PHY Modeling update]
Date Submitted: [11 May 2000]
Source: [Jim Lansford] Company: [Mobilian Corporation]
Address: [7431 NE Evergreen Rd, Suite 220, Hillsboro, OR 97124]
Voice:[(405) 377-6170], FAX: [ (425) 671-6099], E-Mail:[jimlans@mobilian.com]
Re: [ ]
Abstract: [This presentation is an update to the initial presentation given at the March Plenary]
Purpose: [To better quantify effects of noise and interference on bit streams emerging from the Bluetooth PHY]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Bluetooth PHY modeling update
Goal: Integrate PHY effects into OpNet MAC model
  “Clean” bits get sent through the model and are returned “dirty” according to environment and hardware
Work has focused on description of attributes needed for function call
  Environmental effects (channel, interference, etc.)
  System effects (filtering impacts, etc.)
Matlab coding in process, not completed yet
Jim Lansford
Mobilian Corporation
jimlans@mobilian.com

## Slide 3: PHY modeling issues: Environment
Distance to intended device (path loss)
Multipath effects (frequency selective fading)
Number, duty cycle and distance to nearby (<= 10 meters for 0dBm) piconets
Other interference:
  Number, duty cycle, and distance to adjacent 802.11 stations and APs
  Distance from microwave oven (need to allow for multiples, for multifamily dwelling; 50/60Hz?)
Ordered pair for each device for ease of description (2-D or 3-D?)

## Slide 4: PHY modeling issues: Hardware
Sensitivity (-nn dBm for a 10-3 BER; assume normally distributed errors at sensitivity limit?)
Receiver architecture effects
  Co-channel interference
  Adjacent and alternate channel
  Image frequency
  Desensitization
Capture ratio (limiter effects)
Compression of LNA at close proximity

## Slide 5: Environment Description
X
Y
Members of own piconet
Other piconet members
802.11b Stations
802.11b APs
Microwave oven
Master
[X1, Y1]
Slave
SCO, HV2
[X2, Y2]
Slave
Park
[X3, Y3]
Slave
ACL, DH1
[X4, Y4]
This environment could be static for the duration of the simulation run,
or change dynamically (preferred). This is an OpNet issue.

## Slide 6: Block diagram
Block of data
from OpNet
Block of data
returned to OpNet
with errors
Environment
Tx Model
(if needed)
Path losses
(model +multipath?)
Rx Model
Activity Generator
Does node interfere?
Does it compress LNA?
Total contribution due to
Co-channel
Adjacent/Alternate
Image
Does interference at time T1 corrupt bit?
Path loss model?
FSPL for <4 m
Other for indoor
Multipath effects

## Slide 7: Summary
More formal definition of environment and hardware
  Parameters passed to the PHY block from OpNet
Matlab coding is underway, but changes are pretty easy
  Anything else we need to add?
More participation welcomed!

## Slide 8: Next Steps
Complete Rev 1 Matlab
  Finalize microwave oven model (NTIA)
  Finalize 802.11b signal (generic Poisson bursts of Barker coded QPSK?)
Calibrate and measure performance against spec
Figure out with NIST how to integrate with MAC model