## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Bluetooth and 802.11b Physical Layer Coexistence
Date Submitted: 6 November, 2000
Source: Robert E. Van Dyck Company: National Institute of Standards and Technology
Address: 100 Bureau Drive, Mail Stop 8920, Gaithersburg, Maryland, U.S.A.
Voice: 301 975-2923, FAX: 301 590-0932, E-Mail: vandyck@antd.nist.gov
Re: 0
Abstract: Baseband simulations of a bluetooth system and an IEEE 802.11b system are described. Both co-channel and adjacent channel interference of bluetooth devices interfering with bluetooth devices are considered, as well as 802.11b devices interfering with bluetooth.
Purpose: The information in this document should be used to further TG 2 coexistence studies.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Bluetooth and 802.11b Physical Layer Coexistence
Amir Soltanian & Robert E. Van Dyck
National Institute of Standards
and Technology
Gaithersburg, Maryland
November 2000

## Slide 3: Simulations
Additive White Gaussian Noise Channel Model
Mainly Considering Coexistence Scenarios
Signal processing-based implementations
Bluetooth:
Gaussian Frequency Shift Keying
IEEE 802.11b:
Direct Sequence DBPSK
1 Mb/s with 11 Mchips/sec spreading
Baseband Models at 44,000,000 samples/sec

## Slide 4: Baseband Model of Bluetooth GFSK

## Slide 5: Co-channel and Adjacent Channel Interference
Consider Bluetooth as an Interferer
for Bluetooth -- Multiple Piconets
Set Interference Power according to spec.
0 MHz --> 11 dB C/I ratio
1 MHz --> 0 dB
2 MHz --> -30 dB
>= 3 MHz --> -40 dB
Simple Limiter-Discriminator Receiver
Vary the IF Filter Bandwidth

## Slide 6: Bit Error Rate with Co-channel Interference
h = 0.3
AWGN

## Slide 7: BER for Bluetooth Co- and Adjacent Channel Interference

## Slide 8: BER for Bluetooth Co- and Adjacent Channel Interference

## Slide 9: 802.11 Interference
Consider IEEE 802.11b as an Interferer
for Bluetooth – Coexistence Problem
Similar to broadband noise
Use roll-off factor a = 1
Meets transmitter power specification
Evaluate Co-channel and Adjacent
Channel Interference

## Slide 10: IEEE 802.11b Block Diagram

## Slide 11: Spectrum of DS-SS 801.11 Transmitter

## Slide 12: BER for Co-channel 802.11 Interference

## Slide 13: BER for Adjacent Channel 802.11 Interference

## Slide 14: IEEE 802.11b Receiver
Differentially Coherent Detection
1 Mbit/sec mode
Direct Sequence Spread Spectrum
with D-BPSK Modulation
11 Chip Barker PN Sequence
Presently, adding 11 Mbits/sec mode

## Slide 15: BER for SS-DBPSK 802.11 Receiver

## Slide 16: Integration with MAC Layer Model
Consider four node Scenario
Bluetooth transmitter and receiver
802.11b transmitter and receiver
Assume no frequency hopping
Bluetooth radio:
Transmitter power = 1 mW = 0 dBm
Distance = 7 meters
Receiver sensitivity = -80 dBm
802.11 transmitter power = 25 mW = 14 dBm
Distance = 1 meter (to BT receiver)

## Slide 17: BER for Scenario 1

## Slide 18: References
M. K. Simon and C. C. Wang, “Differential vs. limiter-discriminator detection of narrow-band FM,” IEEE Trans. on Comm, pp. 1227-1234, Nov. 1983.
M. K. Simon and C. C. Wang, “Differential detection of Gaussian MSK in a mobile radio environment,” IEEE Trans. On Vehic. Tech., pp. 307-320, Nov. 1984.
P. Varshney and S. Kumar, “Performance of GMSK in a land mobile radio channel,” IEEE Trans. on Vehic. Tech., pp. 607-614, Aug. 1991

## Slide 19: References
J. Proakis, Digital Communications,
McGraw-Hill.
Lee and L. Miller, CDMA Handbook.
T. Ekvetchavit and Z. Zvonar, “Performance of Phase-locked loop receiver in digital FM systems,” IEEE Int. Symp. on PIMRC , pp 381-385, 1998.