## Slide 1: Bluetooth SIG Coexistence Working Group
Tod Sizer
Chair, Coexistence Working Group
Bluetooth Special Interest Group
Bell Laboratories

## Slide 2: Bluetooth SIG Coexistence Working Group
Coexistence Working Group Charter
IEEE/Bluetooth SIG Coordination
Packet Level Simulations
Duty Cycle Assumptions
Coexistence Issues
  Two radios in the same laptop
  Coexistence mechanisms

## Slide 3: Coexistence Working Group Charter
  Work within the Bluetooth™ community as well as with cross industry groups (e.g. IEEE) to quantify the detrimental effects which Bluetooth™ and other wireless products will have on the performance of both. This information will be imperative for members of the Bluetooth community to advise their customers of the realistic performance one can expect in different environments as well a build products which span between Bluetooth™ and other wireless products. In addition, it will be used to disseminate SIG sponsored information on issues of coexistence to regulatory bodies.
  Develop methods of Bluetooth™ operation that will be used to improve coexistence between systems in the shared radio band. These will be issued as Best Practices white papers, improvements to the Bluetooth™ specifications, or formal profiles as necessary.
  To work closely with the Radio 2.0 Working Group to evaluate coexistence issues in new proposed radio designs.

## Slide 4: IEEE 802.15 TG2/ Bluetooth SIG Coexistence Working Group Coordination
Would like to coordinate our efforts with those of the 802.15 Group
Here to work with you on how best to work together and avoid duplication of efforts.
  Recently abandoned efforts to build a MAC layer simulation tool but will rely on the efforts of Nada Golmie and her team.
Rich Ditch of Motorola recently resigned as the liaison from the Working Group to the 802.15 TG2 efforts. Currently Steve Shellhammer and I will be handling these responsibilities.

## Slide 5: Simulation Method
Matlab code created and verified by all in the Coexistence Working Group. All members of the Working Group must have working knowledge of Matlab and the ability to create .m code
Focussing on time/frequency/power considerations to calculate PER (Packet Error Rate)
Initial path loss model uses double slope model typical for indoor propagation.
Rayleigh fading model
Implementation independent.
Completed for Interferers: Bluetooth, 802.11b, HomeRF and WBFH NPRM.
In process for Interferers: Microwave Oven, DECT Cordless (US).

## Slide 6: Interference
Bluetooth Transmitter
Bluetooth Receiver
Interferer
(Ex. Microwave Oven, 802.11, other BT, HomeRF
10m
5m

## Slide 7: Interference Scenario at 100% Duty Cycle
Scenario:
BT voice type hv3 on BT voice type hv3
BT 5m BT 5m hv3 1.3%
1
10
0.045
10
1
0.0
Distance to Interferer (m)
Distance to BT Transmitter (m)

## Slide 8: Interference Scenario at 100% Duty Cycle
Scenario:
HomeRF on BT voice type hv3
BT 5m HomeRF 20m 2.8%
1
10
0.1
50
1
0.0
Distance to Interferer (m)
Distance to BT Transmitter (m)

## Slide 9: What is the correct duty cycle to assume? (1)
Application dependent
  Business users > Home users?
  Continuous bit rate > Variable bit rate?
Duty Cycle Calculations
  802.11b studies* indicate 1% duty cycle over the work day for an end point. (400 Mbytes @ 11 Mbps)
  0.1 erlangs (10% utilization) using Bluetooth hv3 mode will result in 3.3% duty cycle on the Bluetooth link
* Lucent Internal Studies

## Slide 10: What is the correct duty cycle to assume? (2)
What is the best way to advise our users to the reality of the link when duty cycle issues are present?
  100% duty cycle: customer pleased when performance better than expected. But...
  5% duty cycle: customer periodically displeased.
  Descriptions based on usage scenarios

## Slide 11: Two radios in the same laptop/AP
Close radio causes:
  With little/no isolation front end saturation of victim receiver
  With some isolation causes a reduction in range due to high interference values.
Investigating antenna design and layout to provide isolation

## Slide 12: Adaptive Hopping to Avoid Interference
When no interference is detected, hop over the entire frequency band.
When interference is detected at a level which will cause packet errors to Bluetooth, actively avoid these frequency hop locations.
This technique is currently legal for Type 3 Bluetooth units.
The use of intelligence to avoid interference is legal at all powers, however, the required number of hop locations must be maintained.
The Coexistence Working Group feels that adaptive hopping shows great promise in improving the performance of Bluetooth as a Coexistence Mechanism.
2.4 GHz ISM Band
Static Interferer
Bluetooth 1.0
Adaptive Hopping

## Slide 13: Positioning of Adaptive Hopping
Adaptive Hopping could be described in the form of a Coexistence Profile.
Manufacturers which feel that Coexistence issues will be a factor in their success could add this profile to their design.
Examples:
  Laptop Manufacturers deploying 802.11b and Bluetooth in the same laptop.
  Bluetooth Cordless Phones for the home

## Slide 14: Adaptive Hopping
Pros
  Reduction in packet error rate when faced with static Interferers
  Improvement in performance for other wireless systems sharing the band with Bluetooth.
Cons
  A reduction in the number of hopping locations will increase the Bluetooth-Bluetooth interference.

## Slide 15: Examples of Adaptive Hopping Effect
Consider 5 Bluetooth piconets in a given space, one desired piconet with two units separated by 5 meters and the other piconets 10m away. Consider a single 802.11b WLAN unit 20m away. All are operating at 100% duty cycle.
  BT PER without adaptation = 15%
  BT PER with adaptation = 8.4%
Now consider two WLAN units each 20m away, 5 BT Piconets.
  BT PER without adaptation = 23%
  BT PER with adaptation= 14%
Now consider one WLAN unit, 5 BT piconets but with all systems operating at 30% of capacity.
  BT PER without adaptation = 4.7%
  BT PER with adaptation = 2.8%
Now consider one WLAN unit, 5 BT piconets but with BT desired unit only 2m away and at 30% of capacity
  BT PER without adaptation=1.8%
  BT PER with adaptation=0.93%

## Slide 16: Conclusions
Based on Interference Models:
  Coexistence will not be an issue for Bluetooth for low QOS applications
Duty Cycle Issues
  Need a good method for describing this effect to our customers
Adaptive Hopping
  Is an attractive method of improving coexistence with frequency static interferers.
  Microwave ovens and 802.11b are both frequency static
  Bluetooth, Microwave Ovens and 802.11b are likely to be the dominant interferers to Bluetooth in coming years.
  Several companies are currently petitioning the FCC to allow this technique at higher powers than that allowed under 15.249 .