## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: MEHTA: A method for coexistence between co-located 802.11b and Bluetooth systems
Date Submitted: November 7, 2000
Source: Jim Lansford, Ron Nevo, Ephi Zehavi; Company: Mobilian Corporation
Address: 7431 NW Evergreen Pkwy, Suite 220, Hillsboro, OR 97124
Voice:+1.405.377.6170 , FAX: +1 426 671 6099, E-Mail:Jim.Lansford@mobilian.com
Re:
Abstract: This is a proposal to P802.15.2 for a collaborative coexistence mechanism between Bluetooth and 802.11b
Purpose: This document is an overview of a more detailed submission by Mobilian to 802.15.2 (which will be submitted at a later date) of a Recommended Practice for a Collaborative Mechanism that will allow improved coexistence between Bluetooth and 802.11 (DS and 802.11b).
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Coexistence Mechanisms (BT-802.11 specific)
For BT-802.11b distances >2 meters
  Coexistence not really an issue (moderate degradation)
  Not a practical usage model, however
For BT-802.11b distances 0.5-2 meters
  Interference can be significant (depending on implementation)
  Collaboration may be difficult to implement (requires wired backhaul or dual mode radio w/special protocol)
  Non-collaborative mechanisms (such as adaptive hopping) provide some improvement
For co-located BT-802.11b
  Interference most severe; throughput can be nil
  Can fully collaborate; offers best performance improvement
Collaborative
Non-collaborative
No coexistence issues

## Slide 3: Mobilian Collaborative Mechanism: “Mehta Engine” MAC EnHanced Temporal Algorithm
This proposal does not
address PHY or antenna issues
Bluetooth
Baseband
(up to HCI)
802.11b MAC
Bluetooth Radio
802.11b PHY
Mehta
A standardized coexistence interface would be a worthwhile goal for the industry
BT Traffic
802.11 traffic
Mehta-802.11 Interface
Mehta-Bluetooth Interface

## Slide 4: Mehta: Top level overview
Assumes independent RF systems
  Receivers and transmitters share different antennae
  No RF isolation assumed, however
Observes traffic patterns in both systems
  Monitors BT for ACL or SCO
  Monitors 802.11b for beacons, MPDU, ACK, etc
Interface allows flow of data and control information
  Allows exchange of 802.11b channel boundary
  Allows exchange of BT FHS and clock offset
    Same interface concept could be used for BT-BT coordination, if FCC rules are changed to permit
Optimizes timing and duration of traffic
  MAC layer coordination allows precise timing of packet traffic
  802.11b packets can be squeezed between in-band BT slots
  Packet sizes in 802.11b not especially important; 750 byte MPDU is used in this proposal

## Slide 5: BT-802.11b Collision Types
In-band vs Out of band, Tx vs Rx
  Simultaneous Tx is usually ok
    High powered PA can cause problems, such as intermodulation or spurs
    Other BT piconet nodes may have reception problems
  Simultaneous Rx is always ok
    Although other Bluetooth transmitters will usually be close by if BT and 802.11b are co-located
  Problem arises when one is Tx, the other is Rx
    When co-channel (in-band), results are catastrophic for co-located systems
    Outside channel, impact depends on channel filter
      Bluetooth is specified fairly tightly
      802.11b only has to be -35dB outside the channel

## Slide 6: Specific Collision cases
The collision conditions can be mapped out and procedures for each specific case described….
I: BT & WLAN transmit in-band simultaneously
II: BT & WLAN transmit out of band simultaneoulsy
III: WLAN Tx, BT Rx in-band
IV: WLAN Tx, BT Rx out ofband
V: BT Tx, WLAN Rx in-band
VI: WLAN Rx, BT Tx out of band
VII: BT Rx, WLAN Rx in-band
VIII: WLAN Rx, BT Rx out of band
IX: WLAN receives interference in-band from nearby BT device
X: BT receives interference in-band from nearby WLAN device

## Slide 7: Mehta Block Diagram
Assumed MAC structure
  At most one message pending for BT
  At most two messages pending for WLAN
MEHTA
Engine
Frequency
Collision
Map
WLAN Stack
WLAN FIFO2
WLAN FIFO1
WLAN
Modem
WLAN
Modem
Decision
Logic
Decision
Logic
Bluetooth Stack
Backoff &
CCA
Tx
Event
Enable
Enable
Switch
Matrix
Bluetooth FIFO

## Slide 8: Mehta State Machine
In the overall state machine, 5 sub machines need to be described
  State machine actions depend on current traffic and number of messages in queues






## Slide 9: State Machine 1: BT pending
If already receiving in-band WLAN packet, wait until end

## Slide 10: State Machine 2: 1 WLAN msg pending, 1 BT msg pending
If BT is SCO, then it takes priority; else WLAN goes first

## Slide 11: State Machine 3: 1 WLAN msg pending, no BT
Wait for BT to end if in-band (source or dest)

## Slide 12: State Machine 4: 2 WLAN msg pending, 1 BT msg pending
Again, queue messages so that in-band collisions are avoided, giving preference to BT SCO

## Slide 13: State Machine 5: 2 WLAN msg pending, no BT
Send immediately unless BT in-band collision will happen before packet ends

## Slide 14: CFP Evaluation Criteria (1)
Collaborative or non-collaborative?
  Collaborative
Improved performance? (details later)
  802.11b: ACL: 70-80% SCO: ~0%
  Bluetooth: ACL:-25 to +20% SCO: 2-10%
Impact on standards
  None
Regulatory impact
  None
    No known issues in Europe or Japan; believed to meet 15.247 requirements in the US

## Slide 15: CFP Evaluation Criteria (2)
Complexity
  <20,000 gates in addition to existing BT baseband & 802.11b MAC (estimated)
  No PHY changes in this proposal
Interoperability with non-coexistent
  Full interoperability with both systems
Impact on higher layers
  Some perceived latency due to deferral
  Generally small-latencies are rarely more than a few hundred microseconds

## Slide 16: Evaluation Criteria (3)
Classes of operation
  All 802.11b classes except PCF (not implemented)
  All Bluetooth profiles
Voice and data support in Bluetooth
  All ACL and SCO modes supported
Power management
  Supports IEEE 802.11 power management
  Supports Bluetooth pwr management, incl. Park/hold modes
Note: This is a MAC proposal only; additional performance gains are possible with a custom PHY

## Slide 17: Summary
Mehta is an intelligent scheduling algorithm with queuing
  Optimizes for WLAN throughput during BT ACL operation
  Optimizes for packet failure rate during BT SCO operation
  Has full knowledge of BT clock offset and FHS for own piconet
  Meets required WLAN and BT timing constraints (ACK, etc.)
  Allows near-simultaneous operation with existing PHY solutions
  More detailed proposal document will be submitted later
Introduces the concept of standardized coexistence interfaces
  Will facilitate collaborative coexistence between BT and WLAN, as well as among BT piconets/scatternets
  Could take the form of physical interface, logical interface, data protocol interface, or all three
Allows co-location of BT and WLAN
  Stand alone solution between “MACs”
  Can be integrated into existing basebands

## Slide 18: Backups
Simulations

## Slide 19: Simulations
Call for proposals requests 64 simulations
  Only for 11Mb/s; adding 5.5, 2, 1 not included
General simulation types:
  DM5/DM1 or HV1 BT traffic
  0dBm or 20 dBm Bluetooth
  14dBm or 20dBm WLAN
  BT close (1 m) or very close (10 cm) to STA
  Bluetooth performance or 802.11b performance
  Coexistence on or off
These results are based on the 802.15.2 “Stage 0” PHY model and detailed MAC models of BT and WLAN

## Slide 20: Simulation Scenarios (1)

## Slide 21: Simulation Scenarios (2)

## Slide 22: Simulation Results: A1-D4 802.11b Throughput
DM5/DM1
HV1/HV1
Most effective modes;significant WLAN improvement over uncoordinated BT ACL
Mehta attempts to improve SCO performance, even if it reduces WLAN throughput

## Slide 23: Simulation Results: E1-H4 Bluetooth Throughput
DM5/DM1
HV1/HV1
For SCO, packet success rather than throughput; Mehta shows significant improvement in all cases
Mehta attempts to optimize WLAN throughput when ACL BT contends