## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LRSG-RF Lite Overview]
Date Submitted: [6, November, 2000]
Source: [Benno Ritter] Company [Philips Semiconductor]
Address [1109 McKay Drive M/S 48-SJ, San Jose, CA 95131-1706, USA]
Voice:[(408) 474 5116], FAX: [(408) 474 7247], E-Mail:[benno.ritter@philips.com]
Re: [Presentation for Low Rate WPAN Tutorial]
Abstract: [Presenation on RF Lite Applications and Technology]
Purpose: [General Informaton as part of a Low Rate Tutorial to 802]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: RF-Lite a solution for Low Data Rate Wireless Networks 11/6/2000
Benno Ritter
IPMM-Wireless Connectivity
BL-Networking
Philips Semiconductors
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3: Home and Office Network Cluster
Entertainment Cluster
Communications Cluster
PC/Productivity Cluster
Security Systems
Smoke Detectors
Home Appliances
Temperature Control
& Heating
The Home
Network
Internet
Gateway
BBW POTS Sate. xDSL Cable
Home Control/Automation
and Management Cluster

## Slide 4: Example Market Sectors
Consumer
Electronics
Low-End Radio
Devices
PC
Peripherals
Home
Automation
Toys &
Games
Personal
Healthcare
·
TV
·
VCR
·
DVD
·
CD
·
Remote
·
…
·
Mouse
·
Keyboard
·
Joystick
·
Gamepad
·
…
·
Security
·
HVAC
·
Lighting
·
Closures
·
…
·
PETs
·
Gameboys
·
Educational
·
…
·
Monitors
·
Diagnostics
·
Sensors
·
…

## Slide 5: Market Drivers
Extremely low cost
Ease of installation
Reliable data transfer
Reasonable battery life
Short range operation

## Slide 6: Philips Solution
Protocol specification (“PURL”)
Software design and implementation
Air interface design
Baseband and radio IC implementation

## Slide 7: PURL Protocol for Universal Radio Links A Protocol for Low Cost Radio Devices
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: PURL Features
Master/slave topology
Automatic network configuration
Dynamic slave device addressing
Virtual peer-to-peer links (pairing)
Full handshaking for packet transfers
Power management features
Up to 254 (+ master) network nodes
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: PURL Features Cont...
CSMA-CA channel access mechanism
15ms frame structure
TDMA slots can be allocated
10kbps & 115kbps (actual) data throughput
Service discovery (UPnP-Lite)
Low impact internet capability
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10: Data Transfer
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: Frame Structure
Time, ms
t + tf
t
Basic frame:
Network beacon
Contention period
Time, ms
t
t + tf
Slotted frame:
Allocated slot
Notes: Page <number>
        <footer>
<header>
<date/time>
The basic frame shows the contention period during which devices must utilise the CSMA-CA mechanism before transmitting.
The slotted frame still has some portion of contention for those devices which do not have an allocated slot.

## Slide 12: Data Transfers
Network
Beacon
Data
Packet
Data
Handshake
Uplink transfer:
Data
Request
Data
Packet
Data
Handshake
Network
Beacon
Downlink transfer:
From
Slave
From
Master
Message
Transfers
Notes: Page <number>
        <footer>
<header>
<date/time>
Uplink transfers - the slave device listens for the network beacon which identifies the contention period, transmits its packet and the master handshakes it.
Downlink transfers - the master encodes in the network beacon that a particular slave may have a message. When the slave wakes up it listens for the beacon, notices that it may have a message, requests the data, the master sends the appropriate packet and the slave handshakes it.
The key issue here is that the slave has control of the transfers, i.e. it is not a poll/reply system which would mean the slaves would have to know when they need to wake up or would need long wake up sequences.

## Slide 13: Network Management
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14: Network Initiation
Master capable devices only
Listens for network beacons
Attempts to invoke network beacons
Assumes unique network identifier
Starts master operation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: Network Topology
Control flow
Remote
Curtains
DVD
Lamp
STB
Master node
TV
Slave node
Communications flow
Notes: Page <number>
        <footer>
<header>
<date/time>
An example network topology in the area of home (living room) control. A set-top-box is acting as the master with a remote, TV, DVD, lamp and curtains enumerated on the network. This has no functionality since the slaves can only talk to the master. What the consumer actually wants is to be able to control the TV, DVD, lamp and curtains using the remote. In this case there needs to be some virtual peer-to-peer links between the remote and the other devices on the network. The mechanism of creating these links is known as pairing.

## Slide 16: Air Interface Physical Layer
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Frequency Bands
2.4GHz ISM band
  Channel spacing: 3MHz, F = 2404 + 3k MHz with k = 0, 1, …, 25
  Common band:
    USA, Europe including France and Spain
    k = 15, …, 22 F = 2449 – 2470 MHz, 8 channels
915MHz ISM band
  USA only
Direct sequence
  Fast acquisition
  Complexity in digital domain (cheaper)
Spread using length 11 Barker sequence
  Short sequence gives fast acquisition
  Used in IEEE802.11
2.2Mchips/sec
Processing gain of 10.4dB
GFSK, Modulation index h = 0.5, Pre-modulation filterBT = 0.5

## Slide 18: Application Scenarios and System Realisation
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: Applications :- Slave Device
Light Switch
Thermostat
Accessory Control
Security Sensor
Computer Keyboard

## Slide 20: Block Diagram

## Slide 21: Development Platform

## Slide 22: Development Platform

## Slide 23: Demonstration
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 24: Current Demonstration
Internet Connection
WWW
Terminal
STB
Auto-dialler
Fan
Switch
Notes: Page <number>
        <footer>
<header>
<date/time>
In May we will have this demonstration which will use a STB, possibly acting as the master, along with our current demonstration devices. The STB will also implement a web server, allowing us to remotely access and control the devices connected to it. The TV can also be used to display status, such as whether the curtains are opened or closed, etc.

## Slide 25: HomeRF-Lite -> Firefly -> RF-Lite
Low data rate (<200kbps) with fall back for longer range to 20kbps
Very low cost (BOM<$6.00) in 2001 and <$2.50 in 2003
Designed for battery operated systems
Replaces wired solutions that require low data rates
Simple MAC protocol (PURL): master-slave or virtual point-to-point applications, reduces system complexity
Applications: peripherals to PC, temperature control, home security, toys, etc.
Support from growing number of companies
Web Address for RF-Lite committee (http://RF-Lite.com or //12.5.139.199/ )
  Access to the technology through membership in RF-Lite

## Slide 26: Thank You!