## Slide 1: Adaptive Frequency Hopping Implementation Proposals for IEEE 802.15.1/2 WPAN Hongbing Gan, Bijan Treister Bandspeed Pty Ltd

## Slide 2
Outline
What is frequency hopping and why?
Adaptive frequency hopping (AFH) and why
Brief overview of previous work on AFH
Proposals of implementing AFH in IEEE 802.15.1/2 WPAN
Conclusions
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3
Frequency hopping is formed by linearly modulating a train of symbols with a sequence of pseudorandomly generated frequency shifts
What is Frequency Hopping?
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4
To combat frequency-selective fading
To combat narrow-band interference
To protect against intentional jamming and hostile surveillance
f
P
Narrow-band interference
Fading minimum
Why Frequency Hopping?
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5
Fading of Signal vs. Distance and
Frequency in 2.4 GHz ISM Band
Transmit signal at +0dBm
Non-line of sight signal
Room size 400m2 office floor
Measurements done in 3cm increments
Antenna:
  VSWR less than 2.0:1 for all bands
  Linear polarization
  Omni-directional
  Surface mounted
  50 impedance (matched with network analyzer)
All Measurements at Bandspeed Laboratories, Melbourne, Australia

## Slide 6
Channel: 2.45GHz
Modulation: FSK
Symbol Rate: 20Kb/s
Baseband TX sent:
Baseband RX received:
Microwave ON
Baseband TX sent:
Baseband RX received:
Microwave OFF

## Slide 7
Adaptive Frequency Hopping (AFH) and Why
While conventional frequency hopping is blindly passive, adaptive frequency hopping (AFH) classifies channels (say, Good or Bad) and adaptively selects from the pool of ‘Good’ channels.
Advantages:
Active avoidance of narrow-band interference, frequency- selective fading
Better BER performance
Reducing transmitter power, up to 30 dB
Working with adaptive channel equalizers will further enhance system performance
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8
Overview of Previous Work on AFH
FH
Frequency Map
PN generator
FH
Frequency Map
PN generator
LQA
RF Channel
Channel
number
Channel
number
d
Link quality analysis
Zander et al., Radio communication systems laboratory, Royal Institute of Technology, Sweden
30+ dB LESS transmitter power
Low probability of interception by enemies
Results:
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9
Knuth et al. U.S. patent 5418839: Environment adaptive mechanism in cordless telephones
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 10
Knuth et al. U.S. patent 5418839: Environment adaptive mechanism in cordless telephones
Adaptive hopping scheme:
Pre-scanning the channel during idle time, a score is applied to each channel
Selecting preferred channel subset base on score
Channels within the Preferred Channel Subset which experience no or little interference over an extended time is then assigned to Clear Channel Subset
Communication is carried out in Clear Channel Subset
Channel scanning is done periodically
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11
Gillis et al. U.S. patent 5323447:Apparatus and method for modifying a frequency hopping sequence of a cordless telephone system
Adaptive hopping scheme:
Either the base or handset determines the quality of each channel of the First Group of predetermined channels, by measuring the interference level.
Selecting one or more channels from a Second Group of predetermined channels, which is substituted for channels in the First Group upon which the interference is detected
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12
Gillis et al. U.S. patent 5323447:Apparatus and method for modifying a frequency hopping sequence of a cordless telephone system
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13
Lawrey et al. Multiuser OFDM, ISSPA’99, Australia
In a multiuser OFDM system, users are in different locations and have different fading pattern
Each user is allocated carriers which have the best SNR for that user.
Most users can be allocated the best carriers for them with minimal clashes
Carriers are updated every 5 cm. A velocity of 60 km/Hr, update rate is 330 times per second, at 1 GHz.
Adaptive hopping increases received power by 5-20 dB in a frequency-selective fading channel. Adaptive hopping virtually eliminates frequency selective fading
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 14
Lawrey et al. Multiuser OFDM, ISSPA’99, Australia
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15
Current Hop Selection
23/79 mode
Selection box
UAP/LAP
28 bits
Clock
27/28 bits
Hop frequency
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 16
Current Hop Selection
0 2 4 6 62 64 78 1 73 75 77
Segment 1
Segment 3
Segment 2

Segment length 32, =16
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17
Current hopping scheme is blind !!
Adaptive Frequency Hopping could be applied to IEEE 802.15.1/2 to avoid interference from:
Frequency-selective fading
WLAN IEEE 802.11b
HomeRF
Cordless phone
Microwave oven
Baby monitor
etc.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 18: Bandspeed AFH proposals for IEEE 802.15.1/2
A channel classification scheme
  simple, but robust.
Full AFH
  requires ‘Bluetooth enhanced mode’ for full interoperability.
Quasi AFH (adaptive slave TX slot)
  requires no modification of Bluetooth standard for full interoperability.

## Slide 19
A Proposed Channel Classification
Scheme for 802.15.1/2

## Slide 20
Class 1: Clear, first choice of group of channels
Class 2: Good, second choice of group of channels
Class 3: Dead, don’t bother
Default at start - all channels clear.
Upper bound on # of dead channels to adhere to FCC
The dead channel will be visited to see whether it becomes better
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 21
Channel Classification Criterion:
Correlation (Error checking) of channel access code
Error checking of head error control (HEC)
Error checking of cyclic redundancy check (CRC)
BER test by modified LMP
BER test by new packet type (or known sequence)
RSSI
Based on the performance of error checking, each channel is assigned to respective class. Dead channels redeemed after timeout or other scheme.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 22
Proposal 1:
A New Packet Type to Transmit
New Hopping Sequence

## Slide 23
A new packet type is proposed, say type 0101.
The master broadcast this packet to all slaves
The slaves adjust their hopping sequence after a timeout (say, x slots)
After the sequence, either revert to Bluetooth sequence or repeat current sequence.

## Slide 24
Proposal 2:
Master Appends 3 byte to the Payload to Indicate the Channel Number for the Slave to Transmit in Next Time-slot

## Slide 25
Master transmits on regular Bluetooth hopping frequency
Slave transmits on preferred frequency, only master listening to it
Channel classification table regularly updated because master transmits on all frequencies evenly.

## Slide 26
Table of Channel Classification vs. Salves
Complexity can be reduced by grouping channels in chunks of coherence bandwidth
Update of table forced from higher layers, or
Update of dead channels done after a predefined Timeout

## Slide 27
625 s
t
t
Master
Slave X
f(2k)
(regular)
f(2k+2)
(regular)
f’(Clear)
Slave Y
f’(Good)
Next channel
Next channel

## Slide 28
AFH could be applied to 802.15.1/2/3 based on channel classification, as a Non-collaborative Coexistence Mechanism
Channel classification could be based on error checking of CAC, HEC, and CRC, modified LMP or new packet type, etc.
A new packet type is proposed to broadcast hopping sequence information
A quasi-adaptive hopping is also proposed
AFH could potentially avoid interference, lower the transmitting power (important for battery-operated device) and increase throughput.
Bandspeed’s proprietary ‘AFH + equalizer’ could even enhance system performance further
Conclusion
Notes: Page <number>
        <footer>
<header>
<date/time>