## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-PHY-Subcommittee-Report-Tampa]
Date Submitted: [19 September 2000]
Source: [James P. K. Gilb] Company [Mobilian]
Address [11031 Via Frontera, Suite C, San Diego, CA 92127]
Voice:[1-858-451-3438], FAX: [1-858-451-3546], E-Mail:[gilb@ieee.org]
Re: [P802.15-00/110r14_TG3-Criteria-Definitions]
Abstract: [The results of the PHY subcommittee's evaluation of the proposed physical layers for the candidate draft standard.]
Purpose: [Provide a summary of the PHY subcommittee's work.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Evaluation Method
Combination of conference calls and face-to-face meetings in Scottsdale and Tampa
All subcommittee ratings determined by unanimous consent
Number of proposals reduced from 9 to 7
  Two proposals merged (de Courville and Skellern)
  One dropped (Davis, PHY layer only).

## Slide 3: Sub-subcommittees
3 sub-subcommittees, the results are in the annex of P802.15-00/110r14
  Delay spread tolerance: Anand Dabak and Stanley Ling
    Developed new definition that uniquely defined the theoretical delay spread environment
    2 criteria, 90% and 95% of channels
  Microwave oven model: Anand Dabak
    Researched models in literature, summarized results for use in 2.2.4
  Harmony: Carlos Rios
    Low interest at this time, could be brought up later

## Slide 4: Pugh Matrix, Section 2
Proposer | 2.1 Unit Manufacturing Cost | 2.2.2 Interference and Susceptibility | 2.2.3 Intermodulation
de Courville/ Skellern | 0 | +1 | +1
Allen/ Carlson | +1 | +1 | +1
O'Farrell | +1 | +1 | +1
Dabak | +1 | +1 | +1
McCorkle/ Rofheart | +1 | +1 | +1
Karaoguz | +1 | +1 | 0
Rios | +1 | +1 | +1

## Slide 5: Pugh Matrix, Section 2
Proposer | 2.2.4 Jamming Resistance | 2.2.5 Multiple Access | 2.2.6 Coexistence
de Courville/ Skellern | +1 | +1 | +1
Allen/ Carlson | +1 | +1 | +1
O'Farrell | +1 | +1 | +1
Dabak | +1 | +1 | +1
McCorkle/ Rofheart | +1 | +1 | +1
Karaoguz | +1 | +1 | +1
Rios | +1 | +1 | +1

## Slide 6: Pugh Matrix, Section 2
Proposer | 2.3 Interoperability | 2.4.1 Manufacturability | 2.4.2 Time to Market
de Courville/ Skellern | 0 | +1 | +1
Allen/ Carlson | 0 | +1 | +1
O'Farrell | 0 | +1 | +1
Dabak | 0 | +1 | +1
McCorkle/ Rofheart | 0 | +1 | +1
Karaoguz | 0 | +1 | +1
Rios | 0 | +1 | +1

## Slide 7: Pugh Matrix, Section 2
Proposer | 2.4.3 Regulatory Impact | 2.4.4 Maturity of Solution
de Courville/ Skellern | 0 | +1
Allen/ Carlson | 0 | +1
O'Farrell | 0 | +1
Dabak | 0 | +1
McCorkle/ Rofheart | -1 | +1
Karaoguz | 0 | +1
Rios | 0 | +1

## Slide 8: Pugh Matrix, Section 2
Proposer | 2.5 Scalability | 2.6 Location Awareness
de Courville/ Skellern | +1 | 0
Allen/ Carlson | +1 | 0
O'Farrell | +1 | 0
Dabak | +1 | 0
McCorkle/ Rofheart | +1 | +1
Karaoguz | +1 | 0
Rios | +1 | 0

## Slide 9: Ratings Not in Matrix
Some criteria only requested the reporting of the information, the results were not to be graded in the Pugh matrix. For section 4, these were:
  4.3 Frequency band
  4.5 Signal Acquisition
  4.7 Sensitivity
The Pugh matrix numbers for these sections are 0 (same) for all proposals

## Slide 10: Ratings Not in Matrix (cont.)
4.2.1 Minimum MAC/PHY throughput
4.2.2 High End MAC/PHY throughput
  Evaluation came up with more than one number for the MAC overhead, depending on the MAC/PHY combination.
  The results are given in the P802.15-00/110r14 annex
4.8.2 Delay Spread Tolerance
  Original definition flawed, a new definition, with 2 criteria was developed
  Results presented in P802.15-00/110r14 annex

## Slide 11: Pugh Matrix, PHY section
Proposer | 4.1 Size and Form Factor | 4.3 Frequency Band
de Courville/ Skellern | +1 | 5-6 GHz
Allen/ Carlson | +1 | 2.4-2.5 GHz
O'Farrell | +1 | 2.4-2.5 GHz
Dabak | +1 | 2.4-2.5 GHz
McCorkle/ Rofheart | +1 | 2.4-2.5 GHz
Karaoguz | +1 | 2.4-2.5 GHz
Rios | +1 | 2.4-2.5 GHz

## Slide 12: Pugh Matrix, PHY section (cont.)
Proposer | 4.4 Number of Simultaneously Operating Full-Throughput PANs | 4.6 Range | 4.9 Power Consumption
de Courville/ Skellern | +1 | 0 | +1
Allen/ Carlson | 0 | 0 | +1
O'Farrell | 0 | 0 | +1
Dabak | 0 | 0 | +1
McCorkle/ Rofheart | +1 | 0 | +1
Karaoguz | -1 | 0 | +1
Rios | 0 | 0 | +1

## Slide 13: Annex: Intermodulation Resistance
Proposer | 2.2.3 Intermodulation resistance (relative to sensitivity) | 2.2.6 Coexistence (with 100 mW 802.15.1)
de Courville/ Skellern | +1 | +1
Allen/ Carlson | +1 | +1
O'Farrell | +1 | +1
Dabak | +1 | +1
McCorkle/ Rofheart | +1 | +1
Karaoguz | +1 | +1
Rios | +1 | +1

## Slide 14: Annex: Delay Spread Tolerance
 | 4.8.2 Delay Spread Tolerance | 
Proposer | T_RMS, 90 % of channels | T_RMS, 95 % of channels
de Courville/ Skellern | 50 ns | 50 ns
Allen/ Carlson | No response | 33 ns
O'Farrell | 30 ns | 33 ns
Dabak | 25 ns | 25 ns
McCorkle/ Rofheart | 40 ns | No response
Karaoguz | 150 ns | 105 ns
Rios | 50 ns | 25 ns

## Slide 15: Enhancements to Proposals
3 Proposals provided enhanced modes to improve ratings
The details were available too late for the PHY subcommittee to fully evaluate
However, the PHY subcommittee was able to come to some conclusions

## Slide 16: Enhancements for Karaoguz
Karaoguz has presented enhancements to the proposal (8 Mbaud, non hopping) which he believes would improve the overall score. The self ratings would be
  4.2.1 Minimum MAC/PHY throughput (24, 32 and 40 Mb/s raw) +1
  4.4 Number of simultaneously operating full throughput PAN's (8) +1
Without adversely affecting any of the other ratings
The PHY subcommittee believes that the proposed enhancements appear to be reasonable, but did not have sufficient time to review them in depth.

## Slide 17: Enhancements for Allen/Carlson
Allen/Carlson has presented enhancements to the proposal which they believe would improve the overall scores. The self-ratings would be
  4.2.1 Minimum MAC/PHY throughput (33, 44 Mb/s raw) +1
  4.2.2 High end MAC/PHY throughput (33, 44 Mb/s raw) +1
Without adversely affecting any of the other ratings
The proposed enhancements (coding from O'Farrell and 16 QAM from Dabak) have individually been evaluated by the PHY subcommittee for other proposals.
PHY subcommittee did not have sufficient time to review the impact of the combination of the modes to the system performance, although each of the proposed enhancements have been individually evaluated.

## Slide 18: Enhancements for O'Farrell
O'Farrell has presented enhancements to the proposal which he believes would improve the overall score. The self ratings would be
  4.2.1 Minimum MAC/PHY throughput +1
Without adversely affecting any of the other ratings
The proposed enhancement (33 Mb/s, MBCK 16-QAM) appears to be reasonable. However, the PHY subcommittee did not have sufficient time to review the proposed enhancement in depth.