## Slide 1
Notes: From: IWCS [admin@iwcs.org]
Sent: Friday, September 22, 2000 10:30 AM
To: Gifford, Ian C.
Subject: Re: Hotel Reservation 2nd Reply
What I should have asked was what time are you flying in. The Speaker's
Orientation Breakfast is at 7:30 am but it looks like you'll miss that. I
hope you will get in sometime in the morning as you have to turn you power
point file in at the registration desk so that it can be loaded onto the
computer before the afternoon session.
Regards,
Pat Hudak
"Gifford, Ian C." wrote:
> Hi Pat,
>
> I did not make a reservation. I will arrive for the early afternoon panel
> and leave the same day...I have a 3 month old at home and my wife has a
> short leash on me :). Not to worry I it is a short flight from Boston to
> ALC.
>
> Regards,
>
> --
> Ian Gifford
> giffordi@tycoelectronics.com
>
> -----Original Message-----
> From: IWCS [mailto:admin@iwcs.org]
> Sent: Wednesday, September 20, 2000 4:17 PM
> To: Gifford, Ian C.
> Subject: Hotel Reservation
> Importance: High
>
> Dear Mr. Gifford,
>
> Mr. Godwin had blocked rooms for the speakers at the Taj Mahal. Did you
>
> mail the hotel envelope we provided to you or did you call and make
> reservations? We need to know so we can unblock some of these rooms.
> Also, if you did make reservations, did you receive a confirmation from
> the hotel?
>
> Please respond by telling me how reservations were made (by envelope or
> telephone) and if confirmation was received. Waiting for your immediate
> response.
>
> Regards,
>
> Ms. Pat Hudak
> Admin Asst
> IWCS, Inc.
> 174 Main Street
> Eatontown, NJ 07724
> Tel: 732-389-0990
> Fax: 732-389-0991
> Website: www.iwcs.org
>
> P.S. Also for your information, the program is posted on our website.

## Slide 2: 49th International Wire and Cable Symposium (IWCS) 2000 Wireless Access Systems - An Alternative to Wireline Solutions Panel Session 12, Wednesday, November 15, 2000, 2:00-4:30 PM
Bluetooth™, A Cable Replacement Overview
Mr. Ian C. Gifford
Vice Chair, IEEE 802.15 WG for WPANs
Director of Standards, M/A-COM, Inc.
<giffordi@ieee.org>
Notes: From: Wichansky, Howard A CECOM RDEC STCD
[Howard.Wichansky@mail1.monmouth.army.mil]
Sent: Wednesday, July 19, 2000 11:58 AM
To: 'Ian Gifford'
Subject: FW: Wireless Seminar
Mr. Gifford,
> Thank you very much for agreeing to participate in the Wireless Panel
> during 15 Nov 2000 at the Taj Mahal in Atlantic City as part of the
> International Wire and Cable Symposium (IWCS). We have commitments from 3
> other presenters as shown in the attached agenda. <<iwcspan00.doc>> The
> symposium is attended by 1200 engineers in the wire and cable industry.
> We will be expecting about a 25 minute presentation (we can discuss
> content more) followed by a question and answer period after all speakers
> are finished. In 2 or 3 weeks we will need a short abstract and bio for
> the proceedings.
>
> You can find more about the symposium through the website
> http://www.iwcs.org. Although this symposium is geared to the wire and
> cable industry there is a growing interest in the wireless area. We
> actually have 3 events directed at the wireless subject- our panel, a full
> day seminar that is more tutorial (attached below) and a technical session
> entitled, "Cables for Wireless Applications".
>
I have asked Tony Dentino to send you our announcement regarding a new
Bluetooth application program.
> Thank you for your efforts.
>
> Dr. Howard Wichansky <<iwcssem2000.doc>>
> US Army CECOM
> ATTN: AMSEL-RD-ST-WL-AW
> Fort Monmouth, NJ 07703
>
> 732-427-4713

## Slide 3: Wireless Access Systems - An Alternative to Wireline Solutions Panel
Dr. Howard Wichansky, Panel Chairman
Bluetooth, A Cable Replacement Overview - Ian C. Gifford, Vice Chair IEEE 802.15 Wireless Personal Area Network, M/A-COM, Inc
  1011 Pawtucket Boulevard, Lowell, MA 01853
  978-442-4650
The Hows and Whys of Broadband Fixed Wireless Access - Christopher Leising, Telcordia Technologies, Inc
  331 Newman Springs Road, Red Bank, NJ 07701
  732-758-5218
Strategic Wireless Analysis: When and Where to Deploy Wireless Services or Technology - Howard Sherry, Telcordia Technologies, Inc
  331 Newman Springs Road, Red Bank, NJ 07701
  732-758-2208
HDR (High Data Rate): A Wireless Solution for Internet Access - Michael A. Lapadula, QUALCOMM
  6455 Lusk Boulevard, San Diego CA 92121
  858-658-2722
Notes: Final
Session 12, Wednesday, November 15, 2000, 2:00-4:30 PM
Wireless Access Systems - An Alternative to Wireline Solutions Panel
Dr. Howard Wichansky, Panel Chairman
·Bluetooth, A Cable Replacement Overview -
Ian C. Gifford, Vice Chair IEEE 802.15 Wireless Personal Area Network, M/A-COM, Inc
1011 Pawtucket Boulevard, Lowell, MA 01853
978-442-4650
·The Hows and Whys of Broadband Fixed Wireless Access -
Christopher Leising, Telcordia Technologies, Inc
331 Newman Springs Road, Red Bank, NJ 07701
732-758-5218
·Strategic Wireless Analysis: When and Where to Deploy Wireless Services or Technology - Howard Sherry, Telcordia Technologies, Inc
331 Newman Springs Road, Red Bank, NJ 07701
732-758-2208
·HDR (High Data Rate): A Wireless Solution for Internet Access -
Michael A. Lapadula, QUALCOMM
6455 Lusk Boulevard, San Diego CA 92121
858-658-2722

## Slide 4: Contents
Summary
Background
Overview
  Bluetooth™ SIG
  IEEE 802.15 WG for WPANs™
Conclusion

## Slide 5: Summary
A primary goal for Bluetooth™ and WPANs™ is to replace all the cables the mobile worker has today i.e., cell phone to laptop/PDA, cell phone to headset, etc.
This pitch will provide an overview of the Bluetooth™ SIG Foundation Specifciation and the IEEE WPAN™ “derivative work” based on the same.

## Slide 6: OSI Reference Model
wireless
application
presentation
session
transport
network
data link
physical
application
presentation
session
transport
network
data link
physical
application
presentation
session
transport
network
data link
physical
TCP connection

## Slide 7: OSI to 802 LAN/MAN Model
application
presentation
session
transport
network
data link
physical

## Slide 8
Consumer Wireless - Portable, Unlicensed, Accessible
10K
(b/sec.)
100K
1M
10M
  BOM. Cost (Dollars - Y2000)
10
100
IrDA 1.0
IrDA 1.1
ISM Spread Spectrum
w/ Access Point
Cellular
PCS
Satellite
Multimedia System
Wireless LANs
Bluetooth
1,000
Home RF
Wireless Modems
Data Rates
?
HomeRF Multimedia - TBD
AIR
W/o Access point
AirPort
Source: Walt Davis, Motorola, Mar00 IEEE 802.15 Plenary Meeting http://grouper.ieee.org/groups/802/15/pub/2000/Mar00/00086r1P802-15_HRSG-Wireless-Multimedia-Application-Motorola.ppt
Data Rate Vs. Cost

## Slide 9
10K
(b/sec.)
100K
1M
10M
Distance (feet)
100
1,000
10,000’s
IrDA 1.0
IrDA 1.1
ISM Spread Spectrum
WLAN w/beam
Cellular
LAN w/ Patch Antenna
PCS
Satellite
Multimedia System
Wireless LANs
WLAN 11 Mbps Modulation
Bluetooth
Data Rates
Wireless Modems
HomeRF
16 Mbps IrDA
(Apple/Lucent “AirPort”)
Source: Walt Davis, Motorola, Mar00 IEEE 802.15 Plenary Meeting http://grouper.ieee.org/groups/802/15/pub/2000/Mar00/00086r1P802-15_HRSG-Wireless-Multimedia-Application-Motorola.ppt
Data Rate Vs. Distance

## Slide 10: Major opportunities and convergence scenario
Source: Marc de Courville, Motorola, May00 IEEE 802.15 Plenary Meeting http://grouper.ieee.org/groups/802/15/pub/2000/Mar00/00128r0P802-15_TG3-OFDM-HIPERPAN.ppt

## Slide 11: Bluetooth™ v1.0B Specs 1522 Pgs. IEEE D0.7.3 Std 773 Pgs.
Core Specification
Pgs. 1082
Profiles Specification
Pgs. 440
802.15.1 Standard
Pgs. 773 (D0.7.3)
These documents are very detailed and offer an unparalleled source of information on the
Bluetooth Technology. However, additional collateral help with technology adoption.

## Slide 12: Bluetooth™ Special Interest Group Overview
c/o Jim Kardach, BSIG Chairman
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 13: Bluetooth is…
The best low-cost radio link technology
Perfect for mobile devices – small, low power, and low cost, but good performance
Open, royalty free specification
From Intel, IBM, Ericsson, Nokia, Toshiba, Lucent, Motorola, 3COM, Microsoft
>1,900 more Bluetooth SIG members: Compaq, Dell, Motorola, Qualcomm, Psion, Xircom, Philips, Texas Instruments, Sony, Sprint PCS, Seiko-Epson, Conexant, BMW, Puma, NEC, Saab, Starfish, Casio, NTT DoCoMo, Boeing, Bang & Olafsen...
IEEE Standard (via the 802.15.1 working group)
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt
Notes: <number>
July 29, 2026
Ericsson, IBM, Intel, Nokia, and Toshiba are the founding members of the Bluetooth Special Interest Group (SIG), which was formed in early 1998.
In the three weeks following the Bluetooth public launch in May 1998 more than 150 companies joined or started the process of joining the Bluetooth SIG.

## Slide 14: Bluetooth-integrated Cable Replacement Tech
Technology targeted at mobile users
  Goes where users go (global use, 2.4GHz ISM band, airline safe)
  Highly secure (business data)
  High capacity (High interference immunity to itself and others)
  Integrated feature in notebooks, cell-phones and handhelds (low cost, very small, low power)
  Replace the cables common to mobile devices (short range)
25 mm dia
17x33mm
36x43mm
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 15: Bluetooth Vision
Personal Ad-hoc Networks
Cable Replacement
Universal Data/Voice Access Points
Landline
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 16: Data Access Points
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 17: Cable Replacement
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 18: Ad-Hoc Networking
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 19: What Does Bluetooth Do?
Cable Replacement
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 20: Mobile Computer Market
Mobile Computer Total Available Market (TAM)
  16M ’98, 18M ’99
Intel to provide Bluetooth solutions in the PC space
  Drivers and binaries
  Bluetooth modules for notebook integration
Bluetooth penetration
  IBM&Toshiba 1H’99
  Rest of NB OEMs 2H’99
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 21: Who Is Bluetooth?
Harald Blaatand “Bluetooth” II
  King of Denmark 940-981
    Son of Gorm the Old (King of Denmark) and Thyra Danebod (daughter of King Ethelred of England)
This is one of two Runic stones erected in his capitol city of Jelling (central Jutland)
  This is the front of the stone depicting the chivalry of Harald.
  The stone’s inscription (“runes”) say:
    Harald christianized the Danes
    Harald controlled Denmark and Norway
    Harald thinks notebooks and cellular phones should seamlessly communicate
Source: Jim Kardach, Intel, [MobileDemo.ppt] 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 22: Bluetooth SIG Structure
BQRB = Bluetooth Qualification Review Board
BTAB = Bluetooth Technical Advisor Board
BQA = Bluetooth Qualification Administrator
BQB = Bluetooth Qualification Body
Source: Jim Kardach, Intel, 8Jun00 IEEE ComSoc http://grouper.ieee.org/groups/802/15/pub/2000/Jul00/00184r0P802-15_TG1-Bluetooth_IEEE-ComSoc-Pitch-8Jun00.ppt

## Slide 23: IEEE, IEEE 802, and 802.15 WG for WPANs™
Ian Gifford

## Slide 24: About IEEE
The IEEE ("eye-triple-E"), The Institute of Electrical and Electronics Engineers, Inc., helps advance global prosperity by promoting the engineering process of creating, developing, integrating, sharing, and applying knowledge about electrical and information technologies and sciences for the benefit of humanity and the profession.

## Slide 25: IEEE
IEEE Established in 1884 (AIEE & IRE)
IEEE September 2000 Membership was 368,225; 66% USA & 33% Non-USA
IEEE produces 30 percent of the world's published literature in electrical engineering, computers and control technology,
IEEE holds annually more than 300 major conferences and
IEEE has more than 800 active standards with 700 under development.

## Slide 26: IEEE-SA
IEEE-SA now has a total of 5,969 members.
IEEE-SA standards production has a run-rate of about 75 standards per year, a typical year.
IEEE-SA electronic balloting is becoming more accepted and there was discussion of making electronic balloting either mandatory or the default method.
IEEE-SA is working a MoU with the ITU-R that will facilitate the exchange of technical information and the cross-referencing of each others work. This signals both the importance of IEEE standards work in the field of wireless communications and the importance of communication standards in the IEEE.
Europe's ETSI and the IEEE are expanding cooperation under their existing MoU to: 802.11a/HiperLAN2 at 5 GHz and 802.16/ETSI-BRAN for fixed wireless.

## Slide 27: IEEE SA and IEEE 802
Chair
SEC (17)
VOTING MEMBERSHIP (500)
IEEE 802
SPONSOR
US TAG
ISO/IEC
JTC1/SC6
APPEALS
PRESS RELEASES
RULES
COMPUTER
SOCIETY SAB
NESCOM – PARS
REVCOM – STDS
PATENTS
IEEE-SA STDS BD
IEEE-SA BD OF GOV
PUBLISHING
LMSC BALLOTS
SUPPORT
TRAINING
IEEE STDS
STAFF

## Slide 28: IEEE 802 Local and Metropolitan Area Network Standards Committee
Accredited by ANSI, Sponsored by IEEE Computer Society
  Ethernet, Token Ring, Wireless, Cable Modem Standards
  Bridging, VLAN, Security Upper Layer Standards
Meets three times per year (400 individuals, 15% non-US)
Develops equivalent IEC/ISO JTC 1 standards
  JTC 1 series of equivalent standards are known as ISO 8802-nnn
IEEE 802 web site at http://ieee802.org/
Chair: Jim Carlo (jcarlo@ti.com) PHONE:1-214-853-5274

## Slide 29: Objectives of IEEE 802
Enable IEEE 802 to develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of due process, consensus,openness, balance and rights of appeal.
Electronic distribution of standards.

## Slide 30: IEEE 802 Organization
Executive Officers
Working Group Officers
= Active
= Hibernation
= Disbanded
= Wireless

## Slide 31: IEEE 802 Family & Wireless
802.10 SECURITY
*802 OVERVIEW & ARCHITECTURE
802.1 MANAGEMENT
802.2 LOGICAL LINK CONTROL
802.1 BRIDGING
802.9
MAC
802.9
PHY
802.11
MAC
802.11
PHY
802.12
MAC
802.12
PHY
802.14
MAC
802.14
PHY
802.15
MAC
802.15
PHY
802.3
MAC
802.3
PHY
802.4
MAC
802.4
PHY
802.5
MAC
802.5
PHY
802.6
MAC
802.6
PHY
DATA
LINK
LAYER
PHY
LAYER
802.16
MAC
802.16
PHY
Source: IEEE Std P802.15.1 D0.8
802.17
MAC
802.17
PHY

## Slide 32: Wired & Wireless
WAN (Wide Area Network)
  WANs interconnect facilities in different parts of a country or of the world
MAN (Metropolitan Area Network)
  MANs shall be capable of operating over an area up to 50 Km in diameter
LAN (Local Area Network)
  LANs shall be capable of supporting segments at least 100 meters in length. LANs composed of segments connected by physical layer inter-networking devices, shall be capable of operating over a physical medium that is at least 2 Km in length.
PAN (Personal Area Network)
  PANs shall be capable of supporting segments at least 10 meters in length.

## Slide 33: 802.11 WLANs
802.11b-cor, Corr. of 802.11b's MIB
802.11d, Update of Regulatory Domains
802.11e, MAC Enhancements
802.11f, IAPP Inter AP Protocol
802.11g, Higher Rate Ext to 802.11b
802.11h, Spectrum Managed 802.11a
Regulatory activities
Publicity Committee

## Slide 34: 802.11 WLANs
802.11d
802.11b-cor1
802.11e
802.11f
Liaison and Contact w/
Regulatory agencies
802.11g HR 802.11b
802.11h SMa 802.11a

## Slide 35: 802.16 WMANs
802.16.1 (Standard)
  Air Interface for Fixed Broadband Wireless Access Systems (10-66 GHz)
802.16.2 (Recommend Practice)
  Coexistence of Broadband Wireless Access Systems
802.16.3 (Standard)
  Air Interface for Fixed Broadband Wireless Access
  Licensed bands, 2-11 GHz
802.16.1b (Standard) WirelessHUMAN
  broadband fixed wireless access in the 5-6 GHz
  Unlicensed bands, 2-11 GHz

## Slide 36: 802.16 WMANs
802.16.2 Coexistence
Notes: Session #9 of the IEEE 802.16 Working Group on Broadband Wireless Access took place on 11-15 September 2000 in Denver, Colorado, USA. The meeting was notable for major progress in all Task Groups and for a Working Group decision to use a single MAC across all projects.
802.16 to Use a Single MAC Layer
Based on an original motion of Task Group 3, 802.16 unanimously adopted a motion to establish a common 802.16 medium access control layer (MAC) based on the Task Group 1 MAC, requiring each 802.16 Task Group to define its mandatory and optional sub-sets of the common MAC. Backward compatibility and maintenance of the common MAC will be ensured, and 802.16 will strive for forward compatibility.

## Slide 37: 802.15 WPANs™
802.15.1 (Standard)
  Bluetooth™-WPAN™ derivative in WG Draft Ballot
802.15.2 (Recommended Practice)
  Coexistence MAC & PHY Modeling
802.15.3 (Standard)
  WPAN-HR, High Rate >20Mbps commenced Draft
802.15.4 (Standard)
  WPAN-LR, Low Rate 2Kb/sec to 200Kb/sec
Publicity Committee
  Provide MARCOM for above

## Slide 38: 802.15 WPANs™
802.15.2 Coexistence
5GHz option
WPAN-HR
Study Group?

## Slide 39: IEEE 802.15
Standards for Wireless Personal Area Networks (WPANs™)
Short-range
Low Power
Low Cost
Small networks (e.g. 8-16 nodes)
Communication of devices within a Personal Operating Space

## Slide 40: IEEE 802.15 Functional Chart

## Slide 41: IEEE 802.15 Org Chart

## Slide 42: IEEE 802.15 Process Status
Idea for standard
Find Sponsor
Submit PAR
Approve PAR
Organize Task Group
Develop draft standard
Ballot draft standard
Approve draft standard
Publish approved standard
Task Group 4
Task Group 3
Task Group 2
Task Group 1

## Slide 43: IEEE 802.15 Draft Status
Write scope and purpose
Examine related standards and publications
Draft outline
Fill in outline
Revise, revise, revise
Finalize document
Task Group 4
Task Group 3
Task Group 2
Task Group 1

## Slide 44: IEEE 802.15.1 Task Group 1
IEEE 802.15.1 Task Group 1 is licensed to create a derivative work from the Bluetooth™ Specification v1.x
Convert to IEEE Format
Adding Service Access Points (SAPs) and Specification and Description Language (SDL)
  Std ~1052 Pages & SDL Model 462 Pages
IEEE Peer Review via Letter Ballots, Comments, and Comment Resolution provides input to Bluetooth™ Errata DB and continuous improvement loop.
Notes: Note: IEEE Std 802.15.1-[2001] Draft 0.7.2 is 773 pages of which 183 (pages 487-670) are SDL Model. If we assume the remaining 590 are the Draft Std Text and that it stays relatively the same from IEEE Std 802.15.1-[2001] Draft 0.7.2 to IEEE Std 802.15.1-[2001] Draft 0.8. Also, that the current SDL Model –00/202r3 is 462 pages. Then IEEE Std 802.15.1-[2001] Draft 0.8 will be approximately 1052 pages. This is an increase of 279 pages – all in SDL graphics. Finally, that the TG1 is working from D0.7.3 a “smoothed” version from IEEE-SA.

## Slide 45: Current Balloting Planning
2000
2001
J
J
A
S
O
N
D
J
F
M
A
M
J
J
Copyright Addendum Signed
D
J
F
M
A
M
+ Rev 1.0 B spec
- FM Source 3Dec99
A
S
O
N
StB 4-6Dec01
Working Group
Sponsor
+ Rev 1.1 spec
- FM Source ~1Jan01
+ LB3 Balloted/Applied
-24May00 – 6Nov00
StB 11-13Sep01
+ SB(2)
-1May – 15May
+ SB(3)
-15May – 31May
+ LB(6) Recirc.
-01Jan – 15Jan01
+ Rev 1.2 spec
- FM Source ~Jun01
+ Rev 1.x specs
Draft Deadline 3Aug01
Draft Deadline 26Oct01
You are here
+ LB(7) Recirc.
-22Jan01 – 31Jan01
+ SB(1)
-16Mar – 30Apr
Notes: <number>
July 29, 2026
From: Tom Siep [siep@ti.com]
Sent: Thursday, November 02, 2000 12:32 PM
To: Task Group 1
Subject: 802.15.1 Version 1.1 not available
Importance: High
I just spoke to Cathy Hughes of the Open Group. There has been a MAJOR retrenchment: the TROFF version has been abandoned. They will RE-IMPLEMENT Errata against the original v1.0b and stay in FrameMaker.
Details
1.. The Open Group has had static from the SIG about "Conversion Errors" from FrameMaker to TROFF (Cathy says there were 5 in the 1600 pages, 4 of which were TROFF coding errors, one was a figure)
2.. Open Group will use a consultant to apply the Errata
3.. Cathy had made both editorial and technical changes
4.. The techinal changes will be reapplied
5.. The editorial changes likely will be lost.
6.. Kennith Wilson (the consultant) will be seeing the FM source for the first time tomorrow.
7.. The desired delivery for the updated FM is 24November
8.. It is not known at this time how long the SIG will need to review the new document, but 30 or even 40 days seems reasonable to both Cathy and me.
9.. It seems likely that v1.1 will not be ready for the BT DevCon (4-7 Dec 00)
Implications for TG1 (as I see them)
1.. Earliest possible editorial changes on Clauses 7-11 is 1December
2.. Earliest possible start time for comment resolution is 1January01
3.. No impact on Clauses 1-6
4.. No impact on magnitude of changes to base document; we can determine with what we know whether we need to do a reconsider (40 day) or confirmation (15 day) ballot -- I think 15 day will do.
5.. No impact on responding to comments that were rejected
Other thoughts?
--
Tom Siep
Wireless Communications Business Unit
Texas Instruments
(214) 480-6786
(972) 761-5581 FAX
(214) 808-2642 cell
siep@ti.com

## Slide 46: Q&A

## Slide 47: More Info
IEEE 802.15 WG for WPANs™
  http://ieee802.org/15/
IEEE-SA
  http://standards.ieee.org/
Bluetooth™ SIG
  http://www.opengroup.org/bluetooth/
HomeRF Working Group
  http://www.homerf.org
Firefly-RF
  http://www.firefly-rf.org/

## Slide 48
Ian C. Gifford - IEEE 802.15 Vice Chair
  giffordi@amp.com
  Tel: +1 978 442 4650
James Kardach, Bluetooth SIG Chair
  Jim.Kardach@intel.com
  +1 408 765 4469
Jim Carlo, IEEE802 LAN/MAN Standards Committee, Chair
  jcarlo@ti.com
  +1 214 853 5274
Susan Tatiner, IEEE-SA Director Standards Publishing Programs
  s.tatiner@ieee.org
  Tel: +1 732 562 3830
Contact Information