## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Supergold Encoding for High Rate WPAN Physical Layer ]
Date Submitted: [ 19 September 2000 ]
Source: [ T O’Farrell & L.E. Aguado] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 2332052 ], FAX: [ +44 113 2332032 ], E-Mail:[ tim.ofarrell@supergold.com ]
Re: [ Physical layer modulation proposal for the IEEE P802.15.3 High Rate Wireless Personal Area Networks Standard.ref 00210P802.15]
Abstract: [ This contribution presents a coded modulation proposal for the physical layer part of the High Rate WPAN standard. This scheme is evaluated based on the Pugh criteria. ]
Purpose: [ Proposal for PHY part of IEEE P802.15.3 standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Supergold Communication
Supergold Communication is a campus start up company that specialises in solutions for wireless communications:
  Sequence Coded Modulation
  Sequence/Code Design
  Synchronisation
By efficiently exploiting the distance properties of sequences/codes, Supergold’s solutions balance the trade-off between bandwidth efficiency, BER performance and complexity.
Supergold’s solutions can be beneficially applied in
  WPAN
  WLAN
  Wireless Infrared
  Cellular Mobile

## Slide 3: Sequence Coded Modulation for High Rate WPAN PHY
M-ary symbol modulation using QPSK chip modulation
  near constant amplitude
  3 dB PA back-off and low power consumption
  robust in multipath fading up to 30 ns rms delay spread
Single-error-correcting concatenated RS(127,125) code
  RS code matched to M-ary modulation
  very simple Berlekamp-Massey hard-decision decoding
  very high rate code (0.98)
> 3 dB coding gain over QPSK @ 10-6 BER
High spectral efficiency: 21.53 Mbit/s data rate in 22MHz

## Slide 4: Properties of the sequence coded modulation (cont.)
Based on pre-existing technology
  Feasible solution
  Short Development time
  Dual mode 802.15.1 / 802.15.3 using common RF blocks
Works in the 2.4 GHz ISM band with 802.11 channelisation
  Uses a 12.5 Mchip/s chipping rate
  Allows for 802.11b - 802.15.1 and 802.15.3 co-existence
  Can operate in 5 GHz band
Very low baseband complexity
Uses Clear Channel Assessment (CCA) as in 802.11b

## Slide 5: Example of Link Budget for Two-Ray Model
[based on: IEEE 802.15-00/050r1, Rick Roberts]
Rx Noise Figure: 15 dB (inexpensive implementation)
Rx Noise Bandwidth: 15.625 MHz
Rx Noise Floor: -174+10*log(15.625*106)+15  -87 dBm
Implementation Loss Margin: 6 dB
Antenna Gain: 0 dB

## Slide 6: Example of Link Budget for Two-Ray Model (Cont.)
Maximum Second Ray Delay: 25 ns
Maximum Second Ray Refflection Coefficient: -6 dB
Required Direct Ray Range: 10 m
Loss Equation (dB): L = 32.5+20log(dmeters)+20log(FGHz)
At 2.4 GHz, assuming the direct ray is blocked, the loss of the reflected ray path (17.4 m) is:
L = 32.5+24.8+7.6+6  71dB (6 dB reflection coefficient)
Including antenna gain and implementation loss:
Total Loss Budget: L + 2x0 + 6 = 77 dB
Rx Sensitivity is -75 dBm for an operating SNR of 10 dB at 10 -6 BER
Tx Power: Noise Floor + SNR + Loss = -87 dBm + 10 dB + 77 dB
Tx Power  0 dBm

## Slide 7
PHY Functional Schematic
BPF
BPF
BPF
BPF
LNA
IF
Amp
PA
RF
Synthesiser
IF
Synthesiser
0o / 90o
LPF
LPF
LPF
LPF
ADC
ADC
DAC
DAC
ADC
BB
Processing
AGC
Rx I
Rx Q
Tx Q
Tx I
RSSI
50MHz
Oscillator
Band
Filter
Image
Reject
Filter
MAC
802.15.3 IF Filter
SAW
802.15.1 IF Filter

## Slide 8
Baseband Processor — M-ary Sequence Coded Modem
Fast Transform Correlator
Maximum Likelyhood Detector
RS Decoder
Select 1 of 128 Sequences
RS Encoder
DATA IN
1
d
c
7
xI
xQ
8
8
I OUT
Q OUT
8
8
7
1
1
1
Rx I IN
Rx Q IN
rI
rQ
c’
DATA OUT
y

## Slide 9
RF Functionality
  All RF blocks shared between 802.15.1 and 802.15.3 modes. Except IF filters
  Transmit power = 0 dBm
  RFPA efficiency of 33%, 3 dB RFPA back-off
  CMOS technology
BB Functionality
  Fast transform correlators - 12.5 Mchips/s rate
  3-bit Rx ADCs - 50 Msample/s rate
  6-bit Tx DACs - 50 Msample/s rate
  6-bit AGC ADC
  16-tap digital raised-cosine pulse shaping filter
  30K gates for BB processing
  0.18u CMOS process in a dedicated ASIC
1 chip implementation, 1 crystal, 4 filters (front-end, IF x 2, Tx IRF)

## Slide 10
Characteristic of pulse shape digital raised-cosine filter

## Slide 11: General Solution Criteria
2.1. Unit Manufacturing Cost
Similar to 802.15.1 equivalent UMC at 2H 2000
  Similar architecture to IEEE 802.11b
  Much simpler baseband processing than 802.11b (30K gates)
  Low power PA (0 dBm Tx Power)
  Shared RF architecture for 802.15.1 and 802.15.3 modes
  1 Chip RF / BB implementation + 5 external components

## Slide 12: General Solution Criteria
2.2. Signal Robustness
2.2.2. Interference and Susceptibility
  BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S (MAI) = -6 dB co-channel
    J/S (CW) = -7 dB co-channel
  Adjacent+1 channel power attenuation > 50 dBc min.
   In-band interference protection > 40 dBc
  Out-of-band attenuation > 80 dBc
   Complies with 802.15.1 out-of-band blocking

## Slide 13: General Solution Criteria
2.2.2. Interference and Susceptibility (cont.)
System performance in the presence of interference

## Slide 14: General Solution Criteria
2.2.3. Intermodulation Resistance:
IP3 Specification of RF Front-end
BPF
BPF
LNA
Band
Filter
RF
Mixer
SAW
IF Channel
Filter
Gain (dB) -2 +15 +10 -10
IP3 (dBm)  -4 +5 
IP3TOT referred to the input = -9 dBm

## Slide 15
General Solution Criteria
2.2.3. Intermodulation Resistance:
Intermodulating signal
The receiver can tolerate intermodulating signals of up to -34dBm whilst retaining a BER=10-6 with 3 dB Eb/N0 loss. Input IP2 = +16.6 dBm.
2412
Ch1
2432
Ch5
2452
Ch9
2472
Ch13
S + 3 dB
-34 dBm
IM
Freq MHz
Sensitivity S = -75 dB, C/I = 10 dB, Corr = 10log(103/10-1) = 0 dB, IP3 = -9 dBm
IM3TOT = -85.8 dBm
IM = [2.IP3 +(S - C/I +Corr)]/3 = -34 dBm

## Slide 16: General Solution Criteria
2.2.4. Jamming Resistance
  1. Microwave oven interference:
  Interference bandwidth = 2450 to 2460 MHz. CCA would detect jammer and select clear channel. Two free channel are available from 3 non-over-lapping channels while three free channels are available from 4 overlapping channels.
  2-3. 802.15.1 piconet
  802.15.1 randomly hops over 78 1MHz-bands. 802.15.3 is jammed by hops into 15.625 MHz jamming sensitive area; jamming prob  15.625 / 78  20 %.
  4. 802.15.3 transmitting MPG2-DVD
  DVD bit stream takes  30% of channel throughput. If 2 un-coordinated WPANs share the 1 channel with CCA-deferred access then >50% throughput expected.
  Otherwise CCA in subject WPAN would select clear channel.
  5. 802.11a network
  Working on a disjoint frequency band  no jamming.
  6. 802.11b network
  CCA in subject WPAN would select clear channel.

## Slide 17: General Solution Criteria
2.2.5. Multiple Access
  21.53 Mbit/s bit rate  Throughput in [15, 20] Mbit/s range.
  Coordinated time-multiplexing used for multiple access to shared channel.
  No constraint when multiplexing an MPEG2 stream (4.5 Mbit/s) with 512-byte asynchronous packets (max. 273s).
    CASE 1: three MPEG2 streams (at 4.5Mbit/s) share the total throughput (min.) 15 Mbit/s.
    CASE 2 and 3: one MPEG2 stream takes 4.5 Mbit/s whilst the asynchronous services share the remaining throughput in a time-multiplexing manner.

## Slide 18: General Solution Criteria
2.2.6. Coexistence
  802.15.1 piconet scenario:
  IC1 & IC2: x = 7 m
  IC3: x = 97 m
  IC4 & IC5: x = 47 m
A1
A2
B2
B1
3m
3m
x m
Physical Layout
802.15.3
802.15.1
< 0.5 m

## Slide 19
802.15.1 Devices Tx at 1 mW
A1 will interfere with B1 but not B2 while A2 will interfere with B1 and B2.
B1 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B1) ~ 50 dB; Rx Pwr at B1 due to A1 ~ -50 dBm in 15.625 MHz channel bandwidth; i.e. a power density of -61.5 dBm/MHz
- A2 interferes with B1 in the same manner as A1
- B2 Tx Pwr = 0 dBm; Pathloss(B2-B1) ~ 60dB; Rx Pwr at B1 due to B2 ~ -60 dBm
C/I ~ -60 - (-50 +3) ~ -13 dB ,  B1 jams when signals collide
B2 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B2) ~ 62.4 dB; Rx Pwr at B2 due to A1 ~ -62.4 dBm in 15.625 MHz channel bandwidth; i.e. a power density of -74.3 dBm/MHz
- A2 Tx Pwr = 0 dBm; Pahtloss(A2-B2) ~ 57 dB; Rx Pwr at B2 due to A2 ~ -57 dBm in 15.625 MHz channel bandwidth; i.e. a power density of -69 dBm/MHz
- B1 Tx Pwr = 0 dBm; Pathloss(B1-B2) ~ 60dB; Rx Pwr at B2 due to B1 ~ -60 dBm
C/I ~ -60 - 10log(10-6.9+10-7.43) ~ 7.9 dB ,  B2 jams when signals collide
General Solution Criteria
2.2.6. Coexistence cont.

## Slide 20
802.15.1 Devices Tx at 100 mW
Neither A1 nor A2 will not interfere with either B1 or B2
B1 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B1) ~ 50 dB; Rx Pwr at B1 due to A1 ~ -50 dBm in 15.625 MHz channel bandwidth; i.e. a power density of -61.5 dBm/MHz
- A2 interferes with B1 in the same manner as A1
- B2 Tx Pwr = 20 dBm; Pathloss(B2-B1) ~ 60dB; Rx Pwr at B1 due to B2 ~ -40 dBm
C/I ~ -40 - (-61.5 +3) ~ 18.5 dB ,  B1 does not jam when signals collide
B2 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B2) ~ 62.4 dB; Rx Pwr at B2 due to A1 ~ -62.4 dBm in 15.625 MHz channel bandwidth; i.e. a power density of -74.3 dBm/MHz
- A2 Tx Pwr = 0 dBm; Pahtloss(A2-B2) ~ 57 dB; Rx Pwr at B2 due to A2 ~ -57 dBm in 15.625 MHz channel bandwidth; i.e. a power density of -69 dBm/MHz
- B1 Tx Pwr = 20 dBm; Pathloss(B1-B2) ~ 60dB; Rx Pwr at B2 due to B1 ~ -40 dBm
C/I ~ -40 - 10log(10-6.9+10-7.43) ~ 27.9 dB ,  B2 does not jam when signals collide
General Solution Criteria
2.2.6. Coexistence cont.

## Slide 21: General Solution Criteria
2.2.6. Coexistence cont.
  IC1 & IC2 - 802.15.1 network at 0 dBm Tx Power
  Probability of 802.15.1 hopping into 802.15.3 15.625 MHz channel is
  P(interf.) = 15.625 / 78 = 20%  802.15.1 throughput over 80 %
  IC1 & IC2 - 802.15.1 network at 20 dBm Tx Power
  As neither device is jammed the throughput is always 100 %
  IC3 & IC5 - 802.11b network:
  Different channels would be selected for each network via CCA
  IC4 - 802.11a network
  802.15.3 and 802.11a use different frequency bands and would be able to co-exist without interfering with each other.

## Slide 22
2.3. Interoperability
  The 802.15.3 WPAN implements a dual mode radio with shared RF blocks for interoperability with 802.15.1.
  Rx shared components include band filter, LNA, RF mixer and synthesiser, IF amplifier, IF mixer and synthesiser, anti-aliasing filters, ADCs and baseband processing unit.
  Tx shared components include band filter, PA, RF mixer and Synthesiser, image rejection filter, IF mixer and synthesiser, smoothing filters, DACs and baseband processing unit.
  A dedicated IF channel filter matched to the 802.25.1 channel bandwidth is required in addition to the 802.11.3 IF channel filter.
General Solution Criteria

## Slide 23: General Solution Criteria
2.4. Technical Feasibility
2.4.1. Manufactureability
  System architecture utilises pre-existing 802.11b and 802.15.1 technology.
  Baseband processing functionality similar to existing solutions such as MBOK and CCK.
2.4.2. Time to Market
  Pre-existence of technology will ensure short development cycle
  Only PHY part proposed
  Available earlier than 1Q2002

## Slide 24: General Solution Criteria
2.4.3. Regulatory Impact
  The proposed scheme is compliant with regulatory standards FCC(25.249), ETSI 300-328 and ARIB STD-T66.
2.4.4. Maturity of Solution
  The system utilises existing 802.11b and 802.15.1 technology
  Underlying modulation is constant amplitude QPSK
  Baseband processing less complicated than CCK
  Baseband scheme tested in a general purpose hardware demonstrator

## Slide 25: General Solution Criteria
2.5. Scalability
2.5.1.1. Power Consumption
  Transmit power can be changed with impact on either range or throughput (through change in coding rate).
2.5.1.2. Data Rate
  Coding level can be adjusted to fit power and channel conditions.
2.5.1.3. Frequency Band of Operation
  This modulation scheme can be applied at both 2.4 GHz and 5 GHz
2.5.1.4. Cost
  Changing the level of coding or power would not significantly affect the unit cost.
2.5.1.5. Function
  Equalisation can be introduced into the scheme inorder to enhance resistance to time dispersive channels with large delay spreads.

## Slide 26: PHY Layer Criteria
4.1. Size and Form Factor
  Dual mode RF / BB parts integrated in one PHY chip.
  Five external components: crystal oscillator, band filter, 802.15.1 IF filter, 802.15.3 SAW IF filter, Tx image rejection filter.
  One chip for dual mode 802.15.1 / 802.15.3 MAC.
  0.18  CMOS process
  Size smaller than a Compact Flash Type 1 card.

## Slide 27: PHY Layer Criteria
4.2. MAC/PHY Throughput
4.2.1. Minimum MAC/PHY Throughput
  Offered data rate = 2 x 12.5x106 x (7/8) x (125/127) = 21.531 Mbit/s
  PHY overhead due to coding = 1 - (7/8 x 125/127) = 13.88%
  minimum MAC/PHY throughput is met for services that use a MAC overhead of less than or equal to 8%
4.2.2. High End MAC/PHY Throughput
  One throughput level is offered

## Slide 28
4.2. MAC/PHY Throughput cont.
PLCP Packet Format
PHY Layer Criteria
Sync
2*64 chips
SFD
16 bits
PSDU
PLCP Preamble
PLCP Header
Signal
8 bits
Service
8 bits
Length
16 bits
CRC
16 bits
PPDU
T1
T2
T3
2*12.5 Mchip/s
QPSK
21.531 Mb/s
QPSK
21.531 Mb/s
QPSK
T1 = 128/25000000 = 5.12 us
T2 = 16/21531000 = 0.74 us
T3 = 48/215310000 = 2.23 us

## Slide 29
4.2. MAC/PHY Throughput cont.
PLCP Packet Parameters
PHY Layer Criteria
PLCP Preamble: = T1 + T2 = 5.12 + 0.74 = 5.86 us
PLCP Header: = T3 = 2.23 us
aSIFSTIME: = 10.00 us
aslotTIME: = 20.00 us

## Slide 30: PHY Layer Criteria
4.3. Frequency Band
  This proposal is aimed at the 2.4 GHz ISM band, but is also applicable to the 5GHz ISM band.
4.4. Number of Simultaneously Operating Full Throughput PANs
  The IEEE 802.11b channelisation is adopted which provides for 14 overlapping channels
  With non-overlapping channels, up to 3 co-located networks can share the 2.4 GHz ISM band without co-channel interference, (3 non-overlapping 25 MHz channels , fc= 2412, 2437, 2462 MHz).
  With overlapping channels, up to 4 co-located networks can share the 2.4 GHz ISM band without significant co-channel interference, (4 overlapping 20 MHz channels, fc = 2412, 2432, 2452, 2472M Hz).
  Up to 5 co-located networks could share the 5 GHz ISM band with no co-channel interference

## Slide 31
PHY Layer Criteria
4.4. Cont.
A2
B1
A1
1m
10m
Physical Layout
802.15.3
2.412 GHz
802.15.3
2.432 GHz
- A1 Tx Pwr = 0dBm; Pahtloss(A1-A2) ~60 dB;
- Pathloss(B1-A2) ~ 40 dB and Pathloss(B2-A2) ~ 40 dB (avoids IM3 effects)
- For 20 MHz channel separation the adjacent channel interference (ACI) produced by the filtered signals at 1 m is 3+ACI(0m) - pathloss(1m)  3 - 89 - 40 = -126 dBm
- As the receiver sensitivity is -75 dBm, then the C/I margin is at least 50 dB
- Hence there is no significant impact on throughput due to ACI nor associated IM3.
802.15.3
2.432 GHz
4.6. Range
  For 0 dBm Tx. Power, range > 10 m (for link budget presented)
B2
1m
802.15.3
2.452 GHz

## Slide 32: PHY Layer Criteria
4.7. Sensitivity
BER v. Eb/N0 Performance in the AWGN channel

## Slide 33: PHY Layer Criteria
4.7. Sensitivity
BER v. SNR Performance in the AWGN channel

## Slide 34: PHY Layer Criteria
4.7. Sensitivity
PER v. SNR Performance in the AWGN channel

## Slide 35: PHY Layer Criteria
4.8.2. Delay Spread Tolerance
System Performance in the multipath channel for TRMS = 25 ns

## Slide 36: PHY Layer Criteria
4.8.2. Delay Spread Tolerance
  The BER criterion = 10-3 is met for TRMS = 25 ns with no equalisation
  A delay spread of 30ns is tolerated for more than 90% of the channels with FER < 1% at Eb/N0 = 17.5 dB
  No equalisation required

## Slide 37: PHY Layer Criteria
4.9. Power Consumption
  0 dBm transmitted power
  QPSK: near constant amplitude and 3 dB RFPA back-off.
  Low baseband processor complexity
    low complexity fast transform correlation detection and FEC
    no equaliser
    30k BB processing gate count
    Dedicated ASIC using 0.18 u CMOS process
 PHY peak power consumption is 330 mW excluding MAC.

## Slide 38
Transmitter
PA (33% eff, 3dB back-off) 10*
RF up-mixer 30
RF Synthesiser 25
IF up-mixer 20
IF Synthesiser 15
Smoothing Filters (I&Q) 10
DACs (I&Q) 40
BB Processing (ASIC) 125
* 2dB band filter loss
Tx Total 275
4.9. Power Consumption Budget in mW for 0.18 u Technology
Receiver
LNA 10
RF down-mixer 30
RF Synthesiser 25
IF Amp 10
IF down-mixer 20
IF Synthesiser 15
Anti-aliasing Filters (I&Q) 10
ADCs (I&Q) 40
ADC (RSSI) 20
BB Processing (ASIC) 150
Rx Total 330

## Slide 39: Pugh Matrix - General Solution Criteria

## Slide 40: Pugh Matrix - General Solution Criteria

## Slide 41: Pugh Matrix - PHY Layer Criteria

## Slide 42: Pugh Matrix - PHY Layer Criteria