## Slide 1: TI proposal
Symbol rate is 11 MSPS (same as 802.11b)
Data rates
  22 Mbps QPSK uncoded
  22 Mbps 16 QAM, rate 1/2 coding (TBD)
  33 Mbps 16 QAM, rate 3/4 coding (TBD)
  44 Mbps (exact modulation and coding TBD)

## Slide 2: TI proposal
Scalability
  Fixed symbol rate of 11 MSPS
  The system design for baseline 22 Mbps can be reused for the 33 and 44 Mbps higher rates.
  Incremental additional cost to implement the higher rates of 33 and 44 Mbps.
Reusability of system design
  From baseline 22 Mbps to 33, 44 Mbps
Implementation: Can be built using either discrete or integrated components.

## Slide 3: TI Proposal
TI has clearly demonstrated flexibility to address the concerns of the committee/other proposers.
  We have agreed to an evaluation of different coding techniques including Turbo codes /TCM/ MBCK/ Reed Solomon
  We have agreed to an evaluation of coded 44 Mbps.

## Slide 4: GMSK
  Not scalable: 22Mbps GMSK is not scalable to higher data rates of 33, 44 Mbps.
  Inconsistent: The symbol rate and modulation schemes (22 MSPS, GMSK) for the baseline are completely different than those of the higher data rates (11 MSPS, QAM)
  No cost advantage: Exactly the same cost as 11 MSPS QPSK.
  Needs equalization: TI simulations (and IEEE papers) show that without equalization, hits an error floor of 10-1.