## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Supergold Encoding for High Rate WPAN Physical Layer ]
Date Submitted: [ 27 October 2000 ]
Source: [ T. O’Farrell, L.E. Aguado & C. Caldwell] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 2332052 ], FAX: [ +44 113 2332032 ], E-Mail:[ tim.ofarrell@supergold.com ]
Re: [ Physical layer modulation proposal for the IEEE P802.15.3 High Rate Wireless Personal Area Networks Standard.ref 00210P802.15]
Abstract: [ This contribution is a final presentation of Supergold’s coded modulation proposal for the physical layer part of the High Rate WPAN standard as evaluated by the Pugh criteria. ]
Purpose: [ Proposal for PHY part of IEEE P802.15.3 standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline of the Presentation
Supergold’s approach
M-ary Bi-Code Keying: Supergold’s solution for WPAN
PHY Specification
Options
Conclusions

## Slide 3: M-ary Bi-Code Keying: A Solution for WPANs
The critical principle behind Supergold’s solution for WPANs is to:
Meet the performance criteria by
A straight forward application of direct sequence techniques
With minimal implementation complexity

## Slide 4: M-ary Bi-Code Keying: A Solution for WPANs
The PHY architecture evaluated is based on
A simple heterodyne radio
Incorporating RF, IF and BB processing functions
And minimal external filtering functions
MBCK without equalisation is implemented in the BB processing function

## Slide 5
BPF
BPF
BPF
BPF
LNA
IF
Amp
PA
RF
Synthesiser
IF
Synthesiser
0o / 90o
LPF
LPF
LPF
LPF
ADC
ADC
DAC
DAC
ADC
BB
Processing
AGC
Rx I
Rx Q
Tx Q
Tx I
RSSI
50MHz
Oscillator
Band
Filter
Image
Reject
Filter
MAC
802.15.3 IF Filter
SAW
802.15.1 IF Filter
PHY Architecture Evaluated

## Slide 6
M-ary Bi-Code Keying: A Solution for WPANs
This is an established principle:
Quote “DSSS for 802.11c, CCK for 802.11b and M-ary Bi-Orthogonal Keying (MBOK) are schemes that
Benefit from processing gain and inherent coding gain that
Give robust performance in noisy channels, flat fading channels, and ISI channels without the need for complex
Equalisers or channel selectivity techniques
Code and Go

## Slide 7
M-ary Bi-Code Keying: A Solution for WPANs
M-ary Bi-Code Keying is a member of the family of direct sequence coding schemes that specifically
Addresses the issue of high data rates
By carrying more bits per binary symbol
But retains low sequence cross-correlations
Hence robust performance in interference and ISI

## Slide 8
M-ary Bi-Code Keying: A Solution for WPANs
By packing more bits per symbol, M-ary Bi-Code Keying uses more symbols which nominally increases complexity in a conventional receiver.
Supergold’s detection scheme solves the complexity bottleneck
By using unique decoding techniques
And simple Fast Correlator Transform processing which is similar to the Fast Hadamard Transform
Supergold’s 128-ary Bi-Code Keying is less complex than 8-ary Bi-Orthogonal Keying, carries >twice the data and has a similar BER performance

## Slide 9
M-ary Bi-Code Keying: A Solution for WPANs
In Supergold’s solution, M-ary Bi-Code Keying is concatenated with a Reed-Solomon code to:
Enhance the overall coding gain,
Protect against random and burst errors and
Provide rate adaptation – more coding gain at low data rates
Supergold’s proposal was evaluated at the maximum PHY data rate of 21.53 Mb/s using an RS(127,125) code.

## Slide 10
RS – MBCK Encoding Chain
Fast Correlator Transform
Maximum Likelihood Detector
RS Decoder
7
1
1
1
Rx I IN
Rx Q IN
rI
rQ
c’
DATA OUT
y
MBCK
Select 1 of 128 Sequences
RS Encoder
DATA IN
1
d
c
7
xI
xQ
8
I OUT
Q OUT
1
1

## Slide 11
PLCP Packet Format
T1 = 128/25000000 = 5.12 us
T2 = 16/25000000 = 0.64 us
T3 = 40/25000000 = 1.60 us
Sync
2*64 chips
SFD
16 bits
PSDU
PLCP Preamble
PLCP Header
Signal
4 bits
Service
4 bits
Length
16 bits
CRC
16 bits
PPDU
T1
T2
T3
2*12.5 Mchip/s
QPSK
25 Mb/s
QPSK
25 Mb/s
QPSK
Tpsdu
21.531 Mb/s
QPSK

## Slide 12
PHY Subcommittee Evaluation - 1
PHY subcommittee evaluation as supported by at least 00210r9P802.15_TG3
 | Criteria Ref. | Criteria | Outcome
General Solution | 2.1 | Unit Manufacturing Cost | 1
 | 2.2.2 | Interference & Susceptibility | 1
 | 2.2.3 | Intermodulation Resistance | 1
 | 2.2.4 | Jamming Resistance | 1
 | 2.2.5 | Multiple Access | 1
 | 2.2.6 | Coexistence | 1
 | 2.3 | Interoperability | 0
 | 2.4.1 | Manufacturability | 1
 | 2.4.2 | Time to Market | 1
 | 2.4.3 | Regulatory Impact | 0
 | 2.4.4 | Maturity of Solution | 1
 | 2.5 | Scalability | 1
 | 2.6 | Location Awareness | 0

## Slide 13
 | Criteria Ref. | Criteria | Outcome
PHY | 4.1 | Size & Form Factor | 1
 | 4.2.1 | Minimum MAC/PHY Throughput | -1
 | 4.2.2 | High-end MAC/PHY Throughput | 0
 | 4.3 | Frequency Band | 0
 | 4.4 | Number of Simultaneously Operating Full Throughput PANs | 0
 | 4.5 | Signal Acquisition Method | 0
 | 4.6 | Range | 0
 | 4.7 | Sensitivity | 0
 | 4.8.2 | Delay Spread Tolerance | 0
 | 4.9 | Power Consumption | 1
Overall Totals |  | Total –’s | 1
(Gen + PHY) |  | Total 0’s | 10
 |  | Total +’s | 12
Simple but Effective
PHY Subcommittee Evaluation - 2

## Slide 14
PHY System Specification - 1
Parameter | Symbol | Test Condition | Value | Units
Frequency band |  | 2400 – 2483.5 MHz ISM Band | 2.4 | GHz
Number of frequency channels |  | 2412, 2417, 2422, 2427, 2432, 2437, 2442, 2447, 2452, 2457, 2462, 2467, 2472, 2483 | 14 | 
Channel bandwidth | B | Null-to-null, 25% root raised cosine filter | 16 | MHz
Chip rate | Rchip | 1.5625 Msymbols/s, 8 chips/symbol | 12.5 | Mchip/s
Data rate | R | Unencoded Encoded | 25 21.53 | Mb/s Mb/s
Spectral efficiency 3 PANs 4 PANs |  | 21.53 Mb/s data rate per PAN in 2400 – 2483.5 MHz ISM Band | 76 100 | % %
Delay spread tolerance | TRMS | 95% channels @ FER  1%, No Equaliser | 33 | ns

## Slide 15
Parameter | Symbol | Test Condition | Value | Units
Range | d | Up to | 10 | m
Power consumption |  | Maximum, 3.3 V Supply | 330 | mW
Implementation loss margin | Lsys |  | 6 | dB
Regulatory impact |  | Conforms to FCC 25.249, ETSI 300-328 and ARIB STD-T66 | None | 
Dual mode radio |  | 802.15.3 and 802.15.1 interoperability | Yes | 
Clear channel assessment |  |  | Yes | 
CMOS process |  |  | 0.18 | um
Component count |  | Single chip solution, 5 external components | 6 | 
Availability |  | First Quarter | 2002 | 
PHY System Specification - 2

## Slide 16: PHY System Specification - 3
Delay Spread Tolerance (new criteria)
The system tolerates a multipath TRMS greater than 25 ns
  > 95% channels @ FER  1% for TRMS MAX = 33 ns
  > 99% channels @ FER  1% for TRMS = 25 ns
  Eb/N0(TRMS = 25ns) = 5 dB + Eb/N0, S for 95% channels @ FER  1%
  Eb/N0(TRMS = 10ns) = 4 dB + Eb/N0 ,S for 95% channels @ FER  1%
  Simulation Conditions:
  Eb/N0,S (FER(AWGN) = 1%) = 7.5 dB (i.e. sensitivity)
  Fading multipath channels as in 4.8.1
  Direct measurement of FER
  No equalisation

## Slide 17
PHY Encoding Specification - 1
Parameter | Symbol | Test Condition | Value | Units
Sequence coding | MBCK | 128-ary bi-code keying Binary sequences of length 8 chips |  | 
Implementation |  | Fast correlator transform |  | 
Data bits/sequence | k |  | 7 | 
FEC |  | Reed Solomon RS(127,125) Single error correcting |  | 
Overall coding rate | r | (7/8)*(125/127) | 0.86 | 
Coding gain |  | Over QPSK at 10-6 BER | 3 | dB
PLCP: Preamble duration Header duration |  |  | 5.76 1.60 | us us
aSIFTime | Tsif |  | <11 | us
aSLOTTime | Tslot |  | <13 | us

## Slide 18
PHY RF Specification - 1
Parameter | Symbol | Test Condition | Value | Units
Modulation |  |  | QPSK | 
Transmit power | PTx | At antenna | 0 | dBm
PA back-off |  |  | 3 | dB
PA efficiency | E |  | 33 | %
Noise figure | NF | Receiver input | 15 | dB
Sensitivity | S | 21.53 Mb/s, 10-6 BER | -75 | dBm
RF antenna gain | G | Transmit and receive | 0 | dB
IF frequency |  |  | 280 | MHz
IF bandwidth |  |  | 17 | MHz
Rx/Tx swt. speed |  |  | 1 | us

## Slide 19
PHY RF Specification - 2
Parameter | Symbol | Test Condition | Value | Units
Interference susceptibility |  | In band interference protection Out of band interference rejection Adjacent channel + 1 rejection | >40 >80 >55 | dBc dBc dBc
IM tolerance |  | Maximum IM level that can be tolerated | -34 | dBm
Input IP3 | IIP3 |  | -9 | dBm
Spectral mask requirement |  | @ 11 MHz @ 22 MHz | -30 -50 | dBc dBc

## Slide 20
PHY BB Specification - 1
Parameter | Symbol | Test Condition | Value | Units
Clock rates | clk bb | Master BB processing | 50 12.5 | MHz MHz
Samples/chip | Ts | To meet root raised cosine filter spec. | 4 | 
RRCF |  | Root raised cosine filter, 25% excess B/W | 22 | taps
ADC precision |  | 50 Msamples/s | 3 | bits
DAC precision |  | 50 Msamples/s | 6 | bits
RSSI ADC |  | 12.5 Msamples/s | 6 | bits
BB processing |  | Altera Flex EPF 10k100A MBCK + Sync functionality only | 30,000 | gates

## Slide 21
Options - 1
MBCK can be used with a number of modulation schemes while retaining its robust tolerance to interference and delay spread. Candidate modulation schemes include
BPSK
OQPSK
GMSK
All of these modulation schemes will offer a delay spread tolerance of 33 ns when used with MBCK

## Slide 22
Options - 2
An equaliser may be optionally used in order to achieve even greater delay spread tolerances.
MBCK plus equalisation can tolerate delay spreads in excess of 50 ns
Alternate FEC schemes can be used with MBCK such as:
Convolutional codes
Turbo codes
Trellis coded modulation

## Slide 23
Options - 3
An MBCK code for use with 16-QAM exists. When concatenated with a RS(63,55) code and an equaliser, the code provides a:
33 Mb/s data rate;
10-6 BER at Eb/No = 8 dB in AWGN;
tolerance to delay spread > 50 ns.
low complexity detection algorithm
This scheme has not been evaluated by the PHY sub-committee.

## Slide 24
Conclusions
MBCK is a straight forward coding scheme which meets the robustness requirements of a WPAN
It is implementable now using discrete chips sets and can be made available as a single chip device
MBCK can be used either as a standalone solution for the WPAN or as one of a bouquet of coding methods for small, medium & high data rates
MBCK will be an inexpensive solution for WPAN
The adoption of MBCK in 802.15.3 and its commercialisation be fully supported by Supergold.

## Slide 25: Appendix

## Slide 26: Sequence Coded Modulation for High Rate WPAN PHY
M-ary symbol modulation using QPSK chip modulation
  near constant amplitude
  3 dB PA back-off and low power consumption
  robust in multipath fading up to 30 ns rms delay spread
Single-error-correcting concatenated RS(127,125) code
  RS code matched to M-ary modulation
  very simple Berlekamp-Massey hard-decision decoding
  very high rate code (0.98)
> 3 dB coding gain over QPSK @ 10-6 BER
High spectral efficiency: 21.53 Mbit/s data rate in 22MHz

## Slide 27: Properties of the sequence coded modulation
Based on pre-existing technology
  Feasible solution
  Short Development time
  Dual mode 802.15.1 / 802.15.3 using common RF blocks
Works in the 2.4 GHz ISM band with 802.11 channelisation
  Uses a 12.5 Mchip/s chipping rate
  Allows for 802.11b - 802.15.1 and 802.15.3 co-existence
  Can operate in 5 GHz band
Very low baseband complexity
Uses Clear Channel Assessment (CCA) as in 802.11b

## Slide 28: Example of Link Budget for Two-Ray Model
[based on: IEEE 802.15-00/050r1, Rick Roberts]
Rx Noise Figure: 15 dB (inexpensive implementation)
Rx Noise Bandwidth: 16 MHz
Rx Noise Floor: -174+10*log(16*106)+15  -87 dBm
Implementation Loss Margin: 6 dB
Antenna Gain: 0 dB

## Slide 29: Example of Link Budget for Two-Ray Model (Cont.)
Maximum Second Ray Delay: 25 ns
Maximum Second Ray Reflection Coefficient: -6 dB
Required Direct Ray Range: 10 m
Loss Equation (dB): L = 32.5+20log(dmeters)+20log(FGHz)
At 2.4 GHz, assuming the direct ray is blocked, the loss of the reflected ray path (17.4 m) is:
L = 32.5+24.8+7.6+6  71dB (6 dB reflection coefficient)
Including antenna gain and implementation loss:
Total Loss Budget: L + 2x0 + 5 = 77 dB
Rx Sensitivity is -75 dBm for an operating SNR of 10 dB at 10 -6 BER
Tx Power: Noise Floor + SNR + Loss = -87 dBm + 10 dB + 77 dB
Tx Power  0 dBm

## Slide 30
RF Functionality
  All RF blocks shared between 802.15.1 and 802.15.3 modes. Except IF filters
  Transmit power = 0 dBm
  RFPA efficiency of 33%, 3 dB RFPA back-off
  CMOS technology
BB Functionality
  Fast transform correlators - 12.5 Mchips/s rate
  3-bit Rx ADCs - 50 Msample/s rate
  6-bit Tx DACs - 50 Msample/s rate
  6-bit AGC ADC – 12.5 Msamples/s rate
  22-tap digital root raised-cosine pulse shaping filter (25% roll off factor)
  30K gates for BB processing
  0.18u CMOS process in a dedicated ASIC
1 chip implementation, 1 crystal, 4 filters (front-end, IF x 2, Tx IRF)

## Slide 31
Frequency transfer function of root raised cosine filter
25% roll-off factor, 22 taps

## Slide 32
Filter response of root raised cosine filter
to data showing RF Mask
Relative magnitude (dBc)
Frequency (Hz)
RF Mask
-30 dBc
-50 dBc

## Slide 33: General Solution Criteria
2.1. Unit Manufacturing Cost
Similar to 802.15.1 equivalent UMC at 2H 2000
  Similar architecture to IEEE 802.11b
  Much simpler baseband processing than 802.11b (30K gates)
  Low power PA (0 dBm Tx Power)
  Shared RF architecture for 802.15.1 and 802.15.3 modes
  1 Chip RF / BB implementation + 5 external components

## Slide 34: General Solution Criteria
2.2. Signal Robustness
2.2.2. Interference and Susceptibility
  BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S (MAI) = -6 dB co-channel
    J/S (CW) = -7 dB co-channel
  Adjacent+1 channel power attenuation > 50 dBc min.
   In-band interference protection > 40 dBc
  Out-of-band attenuation > 80 dBc
   Complies with 802.15.1 out-of-band blocking

## Slide 35: General Solution Criteria
2.2.2. Interference and Susceptibility (cont.)
System performance in the presence of interference

## Slide 36: General Solution Criteria
2.2.3. Intermodulation Resistance:
IP3 Specification of RF Front-end
BPF
BPF
LNA
Band
Filter
RF
Mixer
SAW
IF Channel
Filter
Gain (dB) -2 +15 +10 -10
IP3 (dBm)  -4 +5 
IP3TOT referred to the input = -9 dBm

## Slide 37
General Solution Criteria
2.2.3. Intermodulation Resistance:
Intermodulating signal
The receiver can tolerate intermodulating signals of up to -34dBm whilst retaining a BER=10-6 with 3 dB Eb/N0 loss. Input IP2 = +16.6 dBm.
2412
Ch1
2432
Ch5
2452
Ch9
2472
Ch13
S + 3 dB
-34 dBm
IM
Freq MHz
Sensitivity S = -75 dB, C/I = 10 dB, Corr = 10log(103/10-1) = 0 dB, IP3 = -9 dBm
IM3TOT = -85.8 dBm
IM = [2.IP3 +(S - C/I +Corr)]/3 = -34 dBm

## Slide 38: General Solution Criteria
2.2.4. Jamming Resistance
  1. Microwave oven interference:
  Interference bandwidth = 2450 to 2460 MHz. CCA would detect jammer and select clear channel. Two free channels are available from 3 non-overlapping channels while three free channels are available from 4 tightly packed channels.
  2-3. 802.15.1 piconet
  802.15.1 randomly hops over 79 1MHz-bands. 802.15.3 is jammed by hops into 16 MHz jamming sensitive area; jamming prob  16 / 79  20 %.
  4. 802.15.3 transmitting MPG2-DVD
  DVD bit stream takes  30% of channel throughput. If 2 un-coordinated WPANs share the 1 channel with CCA-deferred access then >50% throughput expected.
  Otherwise CCA in subject WPAN would select clear channel.
  5. 802.11a network
  Working on a disjoint frequency band  no jamming.
  6. 802.11b network
  CCA in subject WPAN would select clear channel.

## Slide 39: General Solution Criteria
2.2.5. Multiple Access
  21.53 Mbit/s maximum bit rate  Throughput in [15, 20] Mbit/s range.
  Coordinated time-multiplexing used for multiple access to shared channel.
  No constraint when multiplexing an MPEG2 stream (4.5 Mbit/s) with 512-byte asynchronous packets (max. 273s).
    CASE 1: three MPEG2 streams (at 4.5Mbit/s) share the total throughput (min.) 15 Mbit/s.
    CASE 2 and 3: one MPEG2 stream takes 4.5 Mbit/s whilst the asynchronous services share the remaining throughput in a time-multiplexing manner.

## Slide 40: General Solution Criteria
2.2.6. Coexistence
  802.15.1 piconet scenario:
A1
A2
B2
B1
3m
3m
x m
Physical Layout
802.15.3
802.15.1
< 0.5 m
IC1 & IC2: x = 7 m
IC3: x = 97 m
IC4 & IC5: x = 47 m

## Slide 41
802.15.1 Devices Tx at 1 maw
A1 will interfere with B1 but not B2 while A2 will interfere with B1 and B2.
B1 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B1) ~ 50 dB; Rx Pwr at B1 due to A1 ~ -50 dBm in 16 MHz channel bandwidth; i.e. a power density of -61.5 dBm/MHz
- A2 interferes with B1 in the same manner as A1
- B2 Tx Pwr = 0 dBm; Pathloss(B2-B1) ~ 60dB; Rx Pwr at B1 due to B2 ~ -60 dBm
C/I ~ -60 - (-50 +3) ~ -13 dB ,  B1 jams when signals collide
B2 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B2) ~ 62.4 dB; Rx Pwr at B2 due to A1 ~ -62.4 dBm in 16 MHz channel bandwidth; i.e. a power density of -74.3 dBm/MHz
- A2 Tx Pwr = 0 dBm; Pahtloss(A2-B2) ~ 57 dB; Rx Pwr at B2 due to A2 ~ -57 dBm in 16 MHz channel bandwidth; i.e. a power density of -69 dBm/MHz
- B1 Tx Pwr = 0 dBm; Pathloss(B1-B2) ~ 60dB; Rx Pwr at B2 due to B1 ~ -60 dBm
C/I ~ -60 - 10log(10-6.9+10-7.43) ~ 7.9 dB ,  B2 jams when signals collide
General Solution Criteria
2.2.6. Coexistence cont.

## Slide 42
802.15.1 Devices Tx at 100 maw
Neither A1 nor A2 will not interfere with either B1 or B2
B1 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B1) ~ 50 dB; Rx Pwr at B1 due to A1 ~ -50 dBm in 16 MHz channel bandwidth; i.e. a power density of -61.5 dBm/MHz
- A2 interferes with B1 in the same manner as A1
- B2 Tx Pwr = 20 dBm; Pathloss(B2-B1) ~ 60dB; Rx Pwr at B1 due to B2 ~ -40 dBm
C/I ~ -40 - (-61.5 +3) ~ 18.5 dB ,  B1 does not jam when signals collide
B2 Rx
- A1 Tx Pwr = 0 dBm; Pahtloss(A1-B2) ~ 62.4 dB; Rx Pwr at B2 due to A1 ~ -62.4 dBm in 16 MHz channel bandwidth; i.e. a power density of -74.3 dBm/MHz
- A2 Tx Pwr = 0 dBm; Pahtloss(A2-B2) ~ 57 dB; Rx Pwr at B2 due to A2 ~ -57 dBm in 16 MHz channel bandwidth; i.e. a power density of -69 dBm/MHz
- B1 Tx Pwr = 20 dBm; Pathloss(B1-B2) ~ 60dB; Rx Pwr at B2 due to B1 ~ -40 dBm
C/I ~ -40 - 10log(10-6.9+10-7.43) ~ 27.9 dB ,  B2 does not jam when signals collide
General Solution Criteria
2.2.6. Coexistence cont.

## Slide 43: General Solution Criteria
2.2.6. Coexistence cont.
  IC1 & IC2 - 802.15.1 network at 0 dBm Tx Power
  Probability of 802.15.1 hopping into 802.15.3 16 MHz channel is
  P(interf.) = 16 / 79 = 20%  802.15.1 throughput over 80 %
  IC1 & IC2 - 802.15.1 network at 20 dBm Tx Power
  As neither device is jammed the throughput is always 100 %
  IC3 & IC5 - 802.11b network:
  Different channels would be selected for each network via CCA
  IC4 - 802.11a network
  802.15.3 and 802.11a use different frequency bands and would be able to co-exist without interfering with each other.

## Slide 44
2.3. Interoperability
  The 802.15.3 WPAN implements a dual mode radio with shared RF blocks for interoperability with 802.15.1.
  Rx shared components include band filter, LNA, RF mixer and synthesiser, IF amplifier, IF mixer and synthesiser, anti-aliasing filters, ADCs and baseband processing unit.
  Tx shared components include band filter, PA, RF mixer and Synthesiser, image rejection filter, IF mixer and synthesiser, smoothing filters, DACs and baseband processing unit.
  A dedicated IF channel filter matched to the 802.25.1 channel bandwidth is required in addition to the 802.11.3 IF channel filter.
General Solution Criteria

## Slide 45: General Solution Criteria
2.4. Technical Feasibility
2.4.1. Manufacturability
  System architecture utilises pre-existing 802.11b and 802.15.1 technology.
  Baseband processing functionality similar to existing solutions such as MBOK and CCK.
2.4.2. Time to Market
  Pre-existence of technology will ensure short development cycle
  Only PHY part proposed
  Available earlier than 1Q2002

## Slide 46: General Solution Criteria
2.4.3. Regulatory Impact
  The proposed scheme is compliant with regulatory standards FCC(25.249), ETSI 300-328 and ARIB STD-T66.
2.4.4. Maturity of Solution
  The system utilises existing 802.11b and 802.15.1 technology
  Underlying modulation is constant amplitude QPSK
  Baseband processing less complicated than CCK
  Baseband scheme tested in a general purpose hardware demonstrator

## Slide 47: General Solution Criteria
2.5. Scalability
2.5.1.1. Power Consumption
  Transmit power can be changed with impact on either range or throughput (through change in coding rate).
2.5.1.2. Data Rate
  Coding level can be adjusted to fit power and channel conditions.
2.5.1.3. Frequency Band of Operation
  This modulation scheme can be applied at both 2.4 GHz and 5 GHz
2.5.1.4. Cost
  Changing the level of coding or power would not significantly affect the unit cost.
2.5.1.5. Function
  Equalisation can be introduced into the scheme in order to enhance resistance to time dispersive channels with large delay spreads.

## Slide 48: PHY Layer Criteria
4.1. Size and Form Factor
  Dual mode RF / BB parts integrated in one PHY chip.
  Five external components: crystal oscillator, band filter, 802.15.1 IF filter, 802.15.3 SAW IF filter, Tx image rejection filter.
  One chip for dual mode 802.15.1 / 802.15.3 MAC.
  0.18  CMOS process
  Size smaller than a Compact Flash Type 1 card.

## Slide 49: PHY Layer Criteria
4.2. MAC/PHY Throughput
4.2.1. Minimum MAC/PHY Throughput
  Offered data rate = 2 x 12.5x106 x (7/8) x (125/127) = 21.531 Mbit/s
  PHY overhead due to coding = 1 - (7/8 x 125/127) = 13.88%
  minimum MAC/PHY throughput is met for services that use a MAC overhead of less than or equal to 8%
4.2.2. High End MAC/PHY Throughput
  One throughput level is offered

## Slide 50
4.2. MAC/PHY Throughput Cont: PLCP Packet Format
PHY Layer Criteria
T1 = 128/25000000 = 5.12 us
T2 = 16/25000000 = 0.64 us
T3 = 40/25000000 = 1.60 us
Sync
2*64 chips
SFD
16 bits
PSDU
PLCP Preamble
PLCP Header
Signal
4 bits
Service
4 bits
Length
16 bits
CRC
16 bits
PPDU
T1
T2
T3
2*12.5 Mchip/s
QPSK
25 Mb/s
QPSK
25 Mb/s
QPSK
Tpsdu
21.531 Mb/s
QPSK

## Slide 51
4.2. MAC/PHY Throughput cont.: PHY-SAP Parameters
PHY Layer Criteria
PLCP Preamble: = T1 + T2 = 5.12 + 0.64 = 5.76 us
PLCP Header: = T3 = 1.60 us
aRxPLCPDelay = 7.36 us
aTxRxTurnround/ aRxTxTurnround  1.00 us
aRxRfDelay/aTxRfDelay  0.25 us
aCCADelay  2.00 us
aCCATime = aCCADelay + aRxRfDelay + aRxPLCPDelay  10.00 us
aAirPropagationTime  0.03 us
aMACProcessingTime  2.00 us
aSIFSTIME = aRxRfDelay + aRxPLCPDelay + aMACProcessingTime + aTxRxTurnround  11.00 us
aSLOTTIME = aCCATime + aRxTxTurnround + aAirPropagationTime + aMACProcessingTime  13.00 us

## Slide 52: PHY Layer Criteria
4.3. Frequency Band
  This proposal is aimed at the 2.4 GHz ISM band, but is also applicable to the 5GHz ISM band.
4.4. Number of Simultaneously Operating Full Throughput PANs
  The IEEE 802.11b channelisation is adopted which provides for 14 overlapping channels
  For a 25 MHz channel spacing, up to 3 co-located networks can share the 2.4 GHz ISM band without significant adjacent channel interference, (i.e. channel fc= 2412, 2437, 2462 MHz).
  For a 20 MHz channel spacing, up to 4 co-located networks can share the 2.4 GHz ISM band without significant adjacent channel interference, (i.e channel fc = 2412, 2432, 2452, 2472M Hz).
  Up to 5 co-located networks may share the 5 GHz ISM band without significant adjacent channel interference

## Slide 53
PHY Layer Criteria
4.4. Cont. Adjacent Channel Interference Effects
- A1 Tx Pwr = 0dBm; Pahtloss(A1-A2) ~60 dB;
Pathloss(B1-A2) ~ 40 dB and Pathloss(B2-A2) ~ 40 dB
For 20 MHz channel separation the adjacent channel interference (ACI) produced by the filtered signals at 1 m is 3+ACI(0m) - pathloss(1m)  3 - 55 - 40 = -92 dBm
Rx Pwr at A1 due to A2 ~ -60 dBm, then the C/I margin is at least 32 dB
For a Rx Pwr of -75 dBm (= sensitivity), then the C/I margin is at least 17 dB
- As the modulation scheme can tolerate co-channel interference up to -6 dB then -17 dB of interference will not substantially degrade the system throughput.
A2
B1
A1
1m
10m
Physical Layout
802.15.3
2.412 GHz
802.15.3
2.432 GHz
802.15.3
2.432 GHz
B2
1m
802.15.3
2.452 GHz

## Slide 54
PHY Layer Criteria
4.4. Cont. IM3 Effects
- Pathloss(B1-A2) ~ 40 dB and Pathloss(B2-A2) ~ 40 dB
- IM at A2 due to B1 and B2 is -40 dBm each
- From slides 15 & 16, the maximum IM that can be tolerated is –34 dBm
- Therefore IM3 effects are avoided.
A2
B1
A1
1m
10m
Physical Layout
802.15.3
2.432 GHz
802.15.3
2.412 GHz
802.15.3
2.412 GHz
B2
1m
802.15.3
2.452 GHz

## Slide 55
PHY Layer Criteria
4.4. Cont.: Baseband Channel Selectivity for 25 MHz Channel Separation
0
20
25
10
15
5
Freq (MHz)
0
-20
-40
-60
-80
-100
-120
Relative magnitude (dBc)

## Slide 56
PHY Layer Criteria
4.4. Cont.: Baseband Channel Selectivity for 20 MHz Channel Separation
0
20
25
10
15
5
Freq (MHz)
0
-20
-40
-60
-80
-100
-120
Relative magnitude (dBc)

## Slide 57
4.6. Range
  For 0 dBm Tx. Power, range > 10 m (for link budget presented)
4.4 Cont.
The spectral efficiency of an 802.11 channelisation scheme is low because the channel bandwidth allocation is over dimensioned. A channel separation of 25 MHz can support a Nyquist bandwidth of 12.5 MHz while a chipping rate of 12.5 Mchip/s requires a Nyquist bandwidth of 6.25 MHz. Though undesirable to fully occupy the available Nyquist bandwidth, it is possible to increase the occupancy by reducing the separation between channels. A Root Raised Cosine Filter with 25% roll-off factor and half-amplitude frequency of 6.25 MHz can support a channel separation of 20 MHz without a substantial loss of performance. This allows 4 full throughput wireless PANs to transmit simultaneously in the ISM band at 2.4 GHz.
For a channel separation of 25 MHz, a Root Raised Cosine Filter with 25% roll-off factor and half-amplitude frequency of 6.25 MHz introduced about -55 dBc of ACI. The frequency separation between main-lobes is about 9 MHz and there is no overlap between 1st and 2nd sidelobes. For a channel separation of 20 MHz, the same filter introduces the same level of ACI. The frequency separation between main lobes is reduced to 4 MHz and there is overlap of the 1st and 2nd sidelobes but not the main-lobes. The small power in the sidelobes together with their further attenuation by the SAW channel select filter substantially reduces their contribution to the interference budget.

## Slide 58: PHY Layer Criteria
4.7. Sensitivity
BER v. Eb/N0 Performance in the AWGN channel

## Slide 59: PHY Layer Criteria
4.7. Sensitivity
BER v. SNR Performance in the AWGN channel

## Slide 60: PHY Layer Criteria
4.7. Sensitivity
PER v. SNR Performance in the AWGN channel

## Slide 61: PHY Layer Criteria
4.8.2. Delay Spread Tolerance
System Performance in the multipath channel for TRMS = 25 ns

## Slide 62: PHY Layer Criteria
4.8.2. Delay Spread Tolerance (new criteria)
Rating: TRUE, the system tolerates a multipath TRMS greater than 25 ns
  > 95% channels @ FER  1% for TRMS MAX = 33 ns
  > 99% channels @ FER  1% for TRMS = 25 ns
  Eb/N0(TRMS = 25ns) = 5 dB + Eb/N0 ,S for 95% channels @ FER  1%
  Eb/N0(TRMS = 10ns) = 4 dB + Eb/N0 ,S for 95% channels @ FER  1%
  Simulation Conditions:
  Eb/N0 ,S(FER(AWGN) = 1%) = 7.5 dB (i.e. Sensitivity)
  Fading multipath channels as in 4.8.1
  Direct measurement of FER
  No equalisation

## Slide 63: PHY Layer Criteria
4.9. Power Consumption
  QPSK with 0 dBm transmitted power
  RF PA efficiency = 33%, 3 dB back-off.
  Low baseband processor complexity
    low complexity fast transform correlation detection and FEC
    no equaliser
    30k BB processing gate count
    Dedicated ASIC using 0.18 u CMOS process
 PHY peak power consumption is 330 maw excluding MAC (i.e 100mA drain for 3.3V supply).

## Slide 64
Transmitter
PA (33% eff, 3dB back-off) 10*
RF up-mixer 30
RF Synthesiser 25
IF up-mixer 20
IF Synthesiser 15
Smoothing Filters (I&Q) 10
DACs (I&Q) 40
BB Processing (ASIC) 125
* 2dB band filter loss
Tx Total 275
4.9. Power Consumption Budget in maw for 0.18 u Technology
Receiver
LNA 10
RF down-mixer 30
RF Synthesiser 25
IF Amp 10
IF down-mixer 20
IF Synthesiser 15
Anti-aliasing Filters (I&Q) 10
ADCs (I&Q) 40
ADC (RSSI) 20
BB Processing (ASIC) 150
Rx Total 330

## Slide 65: Pugh Matrix - General Solution Criteria

## Slide 66: Pugh Matrix - General Solution Criteria

## Slide 67: Pugh Matrix - PHY Layer Criteria

## Slide 68: Pugh Matrix - PHY Layer Criteria